Specifications. (from 9/2021 on)

BMW iX3.

|  |  | BMW iX3 |
| --- | --- | --- |
| Vehicle category |  |  |
| Drive type / body style |  | Battery electric vehicle (BEV) / Sports Activity Vehicle (SAV) |
| Body |  |  |
| No of doors/seats |  | 5 / 5 |
| Length/width/height (unladen) | mm | 4734 / 1891 / 1668 |
| Wheelbase | mm | 2864 |
| Turning circle | m | 12.1 |
| Weight, unladen (DIN/EU) | kg | 2185 / 2260 |
| Weight distribution (unladen), front/rear | % / % | 43 / 57 |
| Max load to DIN | kg | 540 |
| Max permissible weight | kg | 2725 |
| Max axle load, front/rear | kg | 940 / 1040 |
| Max trailer load, braked (12%)/unbraked | kg | 750 / 750 |
| Max roofload/max towbar download | kg | 100 / 75 |
| Luggage comp capacity | l | 510 – 1560 |
| Air resistance | cd x A | 0.29 x 2.65 |
| Electric Motor |  |  |
| Motor technology |  | Fifth-generation BMW eDrive technology: current-excited synchronous electric motor, power electronics and single-speed transmission sharing the same housing, generator function for recuperating energy |
| Max output | kW/hp | 210 / 286 |
| at | rpm | 6000 |
| Continuous output | kW/hp | 80 / 109 |
| Max torque | Nm | 400 |
| Max rev speed | rpm | 17,000 |
| Max recuperation | kW | 134 |
| High-voltage Battery |  |  |
| Storage technology |  | Lithium-ion |
| Installation |  | Underfloor |
| Voltage | V | 400 |
| Battery capacity | Ah | 232 |
| Energy capacity, gross | kWh | 80.0 |
| Energy capacity, net | kWh | 74.0 |
| Charging 0-100% |  | 7.5 h at 11 kW (16 A / 230 V, three-phase AC) |
| Charging 10-80% |  | 32 min at 150 kW DC |
| Range per 10mins charging | km | 100 (for 150kW DC charging) |
| Charging unit |  |  |
| Type |  | Combined Charging Unit (CCU) with built-in 4 kW voltage transformer for supplying power to the 12 V electrical system |
| Max charging rate alternating current (AC), single-phase | kW | 7.4 |
| Max charging rate alternating current (AC), three-phase | kW | 11.0 |
| Max charging rate direct current (DC) | kW | 150 |

|  |  | BMW iX3 |
| --- | --- | --- |
| Driving Dynamics and Safety |  |  |
| Suspension, front |  | Double-joint spring strut axle in aluminium construction |
| Suspension, rear |  | Five-link axle in lightweight steel construction |
| Brakes, front |  | Vented disc brakes, with single-piston floating callipers |
| Brakes, rear |  | Vented disc brakes, with single-piston floating callipers |
| Driving stability systems |  | Standard: DSC incl. ABS, ASC and DTC (Dynamic Traction Control), ARB (near-actuator wheel slip limitation) technology, CBC (Cornering Brake Control), DBC (Dynamic Brake Control), Dry Braking function, fading compensation, Start-Off Assistant, trailer stability control, Performance Control, adaptive suspension |
| Safety equipment |  | Standard: airbags for driver and front passenger, side airbags for driver and front passenger, head airbags for front and rear seats, three-point inertia-reel seatbelts on all seats with belt stopper, belt tensioner and belt force limiter in the front, crash sensors, tyre pressure indicator |
| Steering |  | Electric Power Steering (EPS) with Servotronic function |
| Steering ratio, overall | :1 | 16.8 |
| Tyres, front/rear |  | 245/50 R19 105W XL |
| Rims, front/rear |  | 7.5J x 19 aluminium |
| Transmission |  |  |
| Type of transmission |  | Automatic transmission, single-speed with fixed ratio |
| Ratio | :1 | 11.115 |
| Final drive | :1 | 1.0 |
| Performance |  |  |
| Power-to-weight ratio (DIN, based on max output) | kg/kW | 10.4 |
| Acceleration 0–100 km/h | s | 6.8 |
| Acceleration 0-60 km/h | s | 3.7 |
| Acceleration 80-120 km/h | s | 4,1 |
| Top speed | km/h | 180 (electronically limited) |
| Off-road characteristics |  |  |
| Angle of approach/departure | ° | 23.1 / 20.9 |
| Breakover angle | ° | 14.8 |
| Ground clearance when unladen | mm | 179 |
| Fording depth (at 7 km/h) | mm | 500 |
| Electric power consumption / range in WLTP test cycle |  |  |
| Electric power consumption combined | kWh/100 km | 19.5 – 18.5 |
| Range | km | up to 460 |
| Environmental characteristics |  |  |
| Emissions rating |  | Electric vehicle |
| C02 Life Cycle Assessment when charging with green electricity for the use phase, compared to BMW X3 20d |  | 60% |
| CO2 Life Cycle Assessment when charging with EU28 electricity mix for the use phase, compared to BMW X3 20d |  | 30% |

The fuel consumption, CO2 emissions, electric power consumption and operating range figures are determined according to the European WLTP Regulation (EC) 715/2007 in the version applicable. The figures refer to a vehicle with basic configuration in the EU. The range shown considers the different sizes of the selected wheels/tyres and the selected items of optional equipment, and may vary during configuration.

Further information on official fuel consumption figures and specific CO2 emission values of new passenger cars is included in the following guideline: 'Leitfaden über den Kraftstoffverbrauch, die CO2-Emissionen und den Stromverbrauch neuer Personenkraftwagen' (Guide to the fuel economy, CO2 emissions and electric power consumption of new passenger cars), which can be obtained free of charge from all dealerships, from Deutsche Automobil Treuhand GmbH (DAT), Hellmuth-Hirth-Str. 1, 73760 Ostfildern-Scharnhausen and at https://www.dat.de/co2/.