Specifications BMW 1 Series Five-Door.
120i, 130i

|  |  | BMW 120i |  | BMW 130i |
| --- | --- | --- | --- | --- |
| Body |  |  |  |  |
| No of doors/seats |  | 5 / 5 |  | 5 / 5 |
| Length/width/height (unladen) | mm | 4 239 / 1748 / 1421 |  | 4 239 / 1748 / 1421 |
| Wheelbase | mm | 2 660 |  | 2 660 |
| Track, front/rear | mm | 1480 / 1493 |  | 1474 / 1487 |
| Ground clearance | mm | 145 |  | 145 |
| Turning circle | m | 10.7 |  | 10.7 |
| Tank capacity | app ltr | 53 |  | 53 |
| Cooling system incl heater | ltr | 7.3 (7.9) |  | 8.2 (8.5) |
| Engine oil1) | ltr | 4.25 |  | 6.5 |
| Weight, unladen, to DIN/EU | kg | 1300/1375 (1320/1395) |  | 1385/1460 (1410/1485) |
| Max load to DIN | kg | 500 |  | 500 |
| Max permissible | kg | 1800 (1820) |  | 1885 (1910) |
| Max axle load, front/rear | kg | 875/1020 |  | 920/1045 |
| Max trailer load (12%), braked/unbraked | kg | 1200/680 |  | 1200/725 |
| Max roofload/max towbar downl | kg | 75 / 75 |  | 75 / 75 |
| Luggage com capacity | ltr | 330-1150 |  | 330-1150 |
| Air drag | Cd x A | 0.30 x 2.09 |  | 0.32 x 2.09 |
| Power Unit |  |  |  |  |
| Config/No of cyls/valves |  | Straight-four / 4 |  | Straight-six / 4 |
| Engine technology |  | Second-generation direct injection (High Precision Injection) with lean burn mode |  | Fully-variable valve management (VALVETRONIC), dual-VANOS |
| Capacity, effective | cc | 1995 |  | 2996 |
| Stroke / bore | mm | 90 / 84 |  | 88 / 85 |
| Compression ratio | :1 | 12.0 |  | 10.7 |
| Fuel |  | RON 91-98 |  | RON 91-98 |
| Max output | kW/hp | 125 / 170 |  | 190 / 258 |
| at | rpm | 6700 |  | 6600 |
| Max torque | Nm/lb-ft | 210/155 |  | 310/228 |
| at | rpm | 4250 |  | 2600-3000 |
| Electrical System |  |  |  |  |
| Battery/location | Ah/– | 80 (70) / luggage comp |  | 70 / luggage comp |
| Alternator | A/W | 180 / 2520 |  | 180 / 2520 |
| Driving Dynamics and Safety |  |
| Suspension, front |  | Double-joint tiebar spring strut axle, aluminium |
| Suspension, rear |  | Five-arm axle, lightweight steel |
| Brakes, front |  | Single-piston swing-calliper disc brakes |
| Diameter | mm | 300 x 24 / vented |  | 330 x 24 / vented |
| Brakes, rear |  | Single-piston swing-calliper disc brakes |
| Diameter | mm | 296 x 10.5 |  | 300 x 20 / vented |
| Driving stability systems |  | Standard: DSC incl ABS and DTC (Dynamic Traction Control), CBC Cornering Brake Control, DBC Dynamic Brake Control, BMW 130i also with Dry Braking, Fading Compensation, Start-Off Assistant and electronic locking function on the rear axle differential |
| Safety equipment |  | Standard: airbags for driver and front passenger (two-stage), side airbags for driver and front passenger, head airbags front and rear, three-point inertia-reel seat belts on all seats, with belt retainer, belt latch tensioner and belt force limiter at the front, crash sensors, Tyre Defect Indicator |
| Steering |  | Rack-and-pinion steering; 3.0 turns; EPS Electronic Power Steering |
| Steering transmission, overall | :1 | 16.0 | 16.0 | 16.0 |
| Tyres, front/rear |  | 205/55R16 87V |  | 205/50R17 89W RSC |
| Rims, front/rear |  | 7J x 16 steel |  | 7J x 17 light-alloy |

Specifications BMW 1 Series Five-Door.

|  |  | BMW 120i |  | BMW 130i |
| --- | --- | --- | --- | --- |
| BMW ConnectedDrive |  |  |  |  |
| Comfort |  | Optional: BMW Assist including features such as enquiry service, remote-control function and V-Info+, BMW TeleServices, integration of mobile terminals |
| Infotainment |  | Optional: access to the internet, BMW Online including features such as Parkinfo, Nationalinfo, Google directory service, News, realtime weather, Office functions, BMW Routes and online music title update |
| Safety |  | Optional: Adaptive Headlights with Bending Lights, High-Beam Assistant, Park Distance Control, cruise control, Automatic/Enhanced Emergency Call |
| Transmission |  |  |  |  |
| Type of transmission |  | Six-speed manual (optional: six-speed automatic transmission) |
| Gear ratios I | :1 | 4.323 (4.171) |  | 4.350 (4.065) |
| II | :1 | 2.456 (2.340) |  | 2.496 (2.371) |
| III | :1 | 1.659 (1.521) |  | 1.665 (1.551) |
| IV | :1 | 1.230 (1.143) |  | 1.230 (1.157) |
| V | :1 | 1.000 (0.867) |  | 1.000 (0.853) |
| VI | :1 | 0.848 (0.691) |  | 0.851 (0.674) |
| Reverse | :1 | 3.938 (3.403) |  | 3.926 (3.200) |
| Final drive | :1 | 3.727 (3.909) |  | 3.462 (3.636) |
| Performance |  |  |  |  |
| Power-to-weight ratio | kg/kW | 10.4 (10.6) |  | 7.3 (7.4) |
| Output per litre | kW/hp | 62.7/88.3 |  | 63.4/86.2 |
| Acceleration 0–100 km/h | sec | 7.8 (8.4) ( |  | 6.1 (6.3) |
| Standing-start km | sec | 28.4 (28.9) |  | 25.5 (25.6) |
| In 4th/5th gear 80–120 km/h | sec | 7.5/9.6 |  | 5.7/7.0 |
| Top speed | km/h | 224 (222) |  | 250 |
| BMW EfficientDynamics |  |  |  |  |
| BMW EfficientDynamics standard features |  | Brake Energy Regeneration, Electronic Power Steering, Auto Start Stop and Gearshift Point Indicator (manual gearbox models), tyres with reduced roll resistance, intelligent lightweight technology, air flap control, map-controlled oil pump, a/c compressor detachable |
| Fuel Consump in EU Cycle |  |  |  |  |
| Urban | ltr/100 km | 8.6 (8.9) |  | 12.4 (12.5) |
| Extra-urban | ltr/100 km | 5.4 (5.3) |  | 6.3 (6.2) |
| Combined | ltr/100 km | 6.6 |  | 8.5 |
| CO2 | g/km | 153 (155) |  | 199 |
| Emission rating |  | EU5 |  | EU5 |

Specifications applicable to ACEA markets/homologation data applicable in part only to Germany (weight).

Figures in brackets apply to automatic transmission models.

1)  Oil change