Specifications BMW Z4.
Z4 sDrive23i, Z4 sDrive30i, Z4 sDrive35i

|  |  | BMW Z4 sDrive23i | BMW Z4 sDrive30i | BMW Z4 sDrive35i |
| --- | --- | --- | --- | --- |
| Body |  |  |  |  |
| No of doors / seats |  | 2 / 2 | 2 / 2 | 2 / 2 |
| Length/width/height (unladen) | mm | 4239 / 1790 / 1291 | 4239 / 1790 / 1291 | 4239 / 1790 / 1291 |
| Wheelbase | mm | 2496 | 2496 | 2496 |
| Track, front/rear | mm | 1511 / 1559 | 1511 / 1559 | 1511 / 1537 |
| Ground clearance | mm | 130 | 130 | 130 |
| Turning circle | m | 10.7 | 10.7 | 10.7 |
| Tank capacity | approx ltr | 55 | 55 | 55 |
| Cooling system incl heater | ltr | 8.2 (8.5) | 8.2 (8.5) | 8.2 (8.5) |
| Engine oil1) | ltr | 6.5 | 6.5 | 6.5 |
| Weight, unladen, to DIN/EU | kg | 1405 / 1480 (1430 / 1505) | 1415 / 1490 (1430 / 1505) | 1505 / 1580 (1525 / 1600) |
| Max load to DIN | kg | 330 | 330 | 330 |
| Max permissible | kg | 1735 (1760) | 1745 (1760) | 1835 (1855) |
| Max axle load, front/rear | kg | 800 / 970 | 800 / 970 | 870 / 1000 |
| Luggage comp capacity | ltr | 180-310 | 180-310 | 180-310 |
| Air resistance | cD x A | 0.34 x 1.96 | 0.34 x 1.96 | 0.35 x 1.96 |
| Power Unit |  |  |  |  |
| Configuration/No of cyls/valves |  | Straight-6 / 4 | Straight-6 / 4 | Straight-6 / 4 |
| Engine technology |  | Fully variable valve management (VALVETRONIC), double-Vanos | Fully variable valve management (VALVETRONIC), double-Vanos | BMW Twin Turbo, second-generation direct injection (High Precision Injection) |
| Capacity, effective | cc | 2497 | 2996 | 2979 |
| Stroke/bore | mm | 78.8 / 82.0 | 88.0 / 85.0 | 89.6 / 84.0 |
| Compression ratio | :1 | 11.0 | 10.7 | 10.2 |
| Fuel grade |  | min RON 91 | min RON 91 | min RON 95 |
| Max output | kW/hp | 150 / 204 | 190 / 258 | 225 / 306 |
| at | rpm | 6400 | 6600 | 5800 |
| Max torque | Nm / lb-ft | 250 / 184 | 310 / 228 | 400 / 295 |
| at | rpm | 2750 | 2600 | 1300-5000 |
| Electrical System |  |  |  |  |
| Battery/installation | Ah/– | 70 / luggage compartment | 70 / luggage compartment | 70 / luggage compartment |
| Alternator | A/W | 170 / 2380 | 170 / 2380 | 170 / 2380 |
| Driving Dynamics and Safety |  |
| Suspension, front |  | Double-joint tiebar spring strut axle, aluminium, displaced castor, small positive steering roll radius, compensation of lateral forces, anti-dive |
| Suspension, rear |  | Central-arm axle, separate springs and dampers, anti-squat and anti-dive |
| Brakes, front |  | Single-piston swing-calliper disc brakes | Single-piston frame- calliper disc brakes |
| Diameter | mm | 300 x 24 / vented | 330 x 24 / vented | 348 x 30 / vented |
| Brakes, rear |  | Single-piston swing-calliper disc brakes |
| Diameter | mm | 300 x 20 / vented | 300 x 20 / vented | 324 x 20 / vented |
| Driving stability systems |  | Standard: DSC incl ABS and DTC (Dynamic Traction Control), CBC Cornering Brake Control, DBC Dynamic Brake Control, Dry Braking, Fading Compensation, Start-Off Assistant |
| Safety features |  | Standard: airbags for driver and passenger, seat-integrated side airbags for driver and passenger, three-point inertia-reel seat belts with belt latch tensioner and belt force limiter, crash sensors, tyre defect indicator |
| Steering |  | Power steering, electromechanical (EPS), optional: Servotronic |
| Transmission ratio, overall | :1 | 14.4 | 14.4 | 14.4 |
| Tyres, front/rear |  | 225/45 R17 91W RSC | 225/45 R17 91W RSC | 225/45 R17 91W RSC / 255/40 R17 94W RSC |
| Rims, front/rear |  | 8J x 17 light-alloy | 8J x 17 light-alloy | 8J/8.5J x 17 light-alloy |

Specifications BMW Z4.

|  |  | BMW Z4 sDrive23i | BMW Z4 sDrive30i | BMW Z4 sDrive35i |
| --- | --- | --- | --- | --- |
| BMW ConnectedDrive |  |  |  |  |
| Comfort |  | Optional: BMW Assist incl Enquiry Service, remote-control functions and V-Info+, BMW TeleServices, Integration of mobile terminals |
| Infotainment |  | Optional: access to the internet, BMW Online incl Parkinfo, National Info, Google Directory Service, News, real-time weather, office functions, BMW Routes and online music title update |
| Safety |  | Optional: Adaptive Headlights with Bending Lights, High-Beam Assistant, Park Distance Control, Active Cruise Control with brake function, Automatic/Enhanced Emergency Call |
| Transmission |  |  |  |  |
| Type |  | Six-speed manual (optional: six-speed automatic, BMW Z4 sDrive35i: seven-speed double-clutch gearbox) |
| Gear ratios I | :1 | 4.323 (4.171) | 4.498 (4.171) | 4.055 (4.780) |
| II | :1 | 2.456 (2.340) | 2.005 (2.340) | 2.396 (3.056) |
| III | :1 | 1.659 (1.521) | 1.313 (1.521) | 1.582 (2.153) |
| IV | :1 | 1.230 (1.143) | 1.000 (1.143) | 1.192 (1.678) |
| V | :1 | 1.000 (0.867) | 0.809 (0.867) | 1.000 (1.390) |
| VI | :1 | 0.848 (0.691) | 0.701 (0.691) | 0.872 (1.203) |
| VII | :1 |  |  | (1.000) |
| Reverse | :1 | 3.938 (3.403) | 3.187 (3.403) | 3.677 (4.454) |
| Final drive ratio |  | 3.636 (3.727) | 4.273 (3.636) | 3.077 (2.563) |
| Performance |  |  |  |  |
| Power-to-weight ratio | kg/kW | 9.4 (9.5) | 7.4 (7.5) | 6.7 (6.8) |
| Output per litre | kW/hp | 60.1 / 81.7 | 63.4 / 86.2 | 75.5 / 102.7 |
| Acceleration 0–100 km/h | sec | 6.6 (7.3) | 5.8 (6.1) | 5.2 (5.1) |
| Standing-start km | sec | 26.9 (27.7) | 25.2 (25.6) | 24.4 (24.2) |
| In 4th/5th gear 80–120 km/h | sec | 6.4 / 7.8 (-) | 5.3 / 6.8 (-) | 4.9 / 5.7 (-) |
| Top speed | km/h | 242 (239) | 250 | 250 |
| BMW EfficientDynamics |  |  |  |  |
| BMW EfficientDynamics, standard features |  | Brake Energy Regeneration, electromechanical power steering, gearshift point indicator (manual model), tyres with reduced roll resistance, (BMW Z4 sDrive23i and BMW Z4 sDrive30i), intelligent lightweight construction, on-demand control of ancillary units, on-demand control of oil pump (BMW Z4 sDrive23i and BMW Z4 sDrive30i), a/c compressor detachable |
| Fuel Con in EU Cycle |  |  |  |
| Urban | ltr/100km | 12.4 (11.8) | 12.4 (11.9) | 13.5 (12.6) |
| Extra-urban | ltr/100km | 6.2 (6.1) | 6.2 8.5 | 7.0 (6.9) |
| Combined | ltr/100km | 8.5 (8.2) | 8.5 (8.3) | 9.4 (9.0) |
| CO2 | g/km | 199 (192) | 199 (195) | 219 (210) |
| Emission rating |  | EU5 | EU5 | EU5 |

Specifications apply to ACEA markets/homologation data apply in part only to Germany (weight).

Figures in brackets apply to models with automatic transmission.

1)  Oil change