Specifications BMW 3 Series Sedan.
318i, 320i

|  |  | BMW 318i Saloon |  | BMW 320i Saloon |
| --- | --- | --- | --- | --- |
| Body |  |  |  |  |
| No of doors / seats |  | 4 / 5 |  | 4 / 5 |
| Length/width/height (unladen) | mm | 4531 / 1817 / 1421 |  | 4531 / 1817 / 1421 |
| Wheelbase | mm | 2760 |  | 2760 |
| Track front/rear | mm | 1506 / 1535 |  | 1506 / 1535 |
| Ground clearance | mm | 144 |  | 144 |
| Turning circle | m | 11.0 |  | 11.0 |
| Tank capacity | approx ltr | 63 |  | 63 |
| Cooling system incl heater | ltr | 8.4 (9.2) |  | 8.4 (9.2) |
| Engine oil1) | ltr | 4.25 |  | 4.25 |
| Weight, unladen, to DIN/EU | kg | 1360 / 1435 (1390 / 1465) |  | 1370 / 1445 (1400 / 1475) |
| Max load to DIN | kg | 520 |  | 520 |
| Max permissible | kg | 1880 (1910) |  | 1890 (1920) |
| Max axle load, front/rear | kg | 895 / 1060 |  | 895 / 1060 |
| Max trailer load (12%), braked/unbraked | kg | 1250 (1400) / 695 |  | 1400 (1500) / 695 |
| Max roofload/towbar download | kg | 75 / 75 |  | 75 / 75 |
| Luggage comp capacity | ltr | 460 |  | 460 |
| Air resistance | cD x A | 0.26 x 2.17 |  | 0.26 x 2.17 |
| Power Unit |  |  |  |  |
| Configuration/No of cyls/valves |  | Straight-4 / 4 |  | Straight-4 / 4 |
| Engine technology |  | Second-generation direct injection (High Precision Injection), lean burn |  | Second-generation direct injection (High Precision Injection), lean burn |
| Capacity, effective | cc | 1995 |  | 1995 |
| Stroke/bore | mm | 90.0 / 84.0 |  | 90.0 / 84.0 |
| Compression ratio | :1 | 12.0 |  | 12.0 |
| Fuel grade |  | min RON 91 |  | min RON 91 |
| Max output | kW/hp | 105 / 143 |  | 125 / 170 |
| at | rpm | 6000 |  | 6700 |
| Max torque | Nm / lb-ft | 190 / 140 |  | 210 / 155 |
| at | rpm | 4250 |  | 4250 |
| Electrical System |  |  |  |  |
| Battery/installation | Ah/– | 90 (70) / luggage compartment |  | 90 (70) / luggage compartment |
| Alternator | A/W | 180 / 2520 |  | 180 / 2520 |
| Driving Dynamics and Safety |  |
| Suspension, front |  | Double-joint spring strut axle, aluminium, displaced castor, small positive steering roll radius, compensation of lateral forces, anti-dive |
| Suspension, rear |  | Five-arm axle in lightweight steel construction |
| Brakes, front |  | Single-piston swing-calliper disc brakes |
| Diameter | mm | 300 x 24 / vented |  | 300 x 24 / vented |
| Brakes, rear |  | Single-piston swing-calliper disc brakes |
| Diameter | mm | 300 x 20 / vented |  | 300 x 20 / vented |
| Driving stability systems |  | Standard: DSC incl ABS and DTC (Dynamic Traction Control), CBC Cornering Brake Control, DBC Dynamic Brake Control |
| Safety features |  | Standard: airbags for driver and front passenger, side airbags for driver and front passenger, head airbags front and rear, three-point inertia-reel seat belts on all seats, with belt restrainer, belt latch tensioner and belt force limiter at the front, crash-activated headrests at the front, crash sensors, tyre defect indicator |
| Steering |  | Electromechanical power steering |
| Transmission ratio, overall | :1 | 16.0 |  | 16.0 |
| Tyres, front/rear |  | 205/55 R16 91H |  | 205/55 R16 91H |
| Rims, front/rear |  | 7J x 16 steel |  | 7J x 16 steel |

Specifications BMW 3 Series Saloon.

|  |  | BMW 318i Saloon |  | BMW 320i Saloon |
| --- | --- | --- | --- | --- |
| BMW ConnectedDrive |  |  |  |  |
| Comfort |  | Optional: BMW Assist incl Enquiry Service, remote-control functions and V-Info+, BMW TeleServices, Integration of mobile terminals |
| Infotainment |  | Optional: access to the internet, BMW Online incl Parkinfo, National Info, Google Directory Service, News, real-time weather, office functions, BMW Routes and online music title update |
| Safety |  | Optional: Adaptive Headlights with Bending Lights, High-Beam Assistant, Park Distance Control, Cruise Control, Automatic/Enhanced Emergency Call |
| Transmission |  |  |  |  |
| Type |  | Six-speed manual (optional: six-speed automatic) |
| Gear ratios I | :1 | 4.323 (4.171) |  | 4.323 (4.171) |
| II | :1 | 2.456 (2.340) |  | 2.456 (2.340) |
| III | :1 | 1.659 (1.521) |  | 1.659 (1.521) |
| IV | :1 | 1.230 (1.143) |  | 1.230 (1.143) |
| V | :1 | 1.000 (0.867) |  | 1.000 (0.867) |
| VI | :1 | 0.848 (0.691) |  | 0.848 (0.691) |
| R | :1 | 3.938 (3.403) |  | 3.938 (3.403) |
| Final drive ratio | :1 | 3.385 (3.909) |  | 3.455 (3.909) |
| Performance |  |  |  |  |
| Power-to-weight ratio | kg/kW | 13.0 (13.2) |  | 11.0 (11.2) |
| Output per litre | kW/hp | 52.6 / 71.5 |  | 62.7 / 85.3 |
| Acceleration 0–100 km/h | sec | 9.1 (9.9) |  | 8.2 (8.9) |
| Standing-start km | sec | 30.1 (30.7) |  | 28.9 (29.4) |
| In 4th/5th gear 80–120 km/h | sec | 9.4 / 12.4 (-) |  | 8.3 / 11.0 (-) |
| Top speed | km/h | 210 |  | 228 (226) |
| BMW EfficientDynamics |  |  |  |  |
| BMW EfficientDynamics, standard features |  | Brake Energy Regeneration, electromechanical power steering, Auto Start Stop function and gearshift point indicator (manual model), ancillary units controlled on demand, tyres with reduced roll resistance, intelligent lightweight construction, oil pump with map control, a/c compressor detachable |
| Fuel Con in EU Cycle |  |  |  |
| Urban | ltr/100km | 8.1 (8.7) |  | 8.3 (9.3) |
| Extra-urban | ltr/100km | 5.3 (5.4) |  | 5.3 |
| Combined | ltr/100km | 6.3 (6.6) |  | 6.4 (6.8) |
| CO2 | g/km | 146 (155) |  | 148 (159) |
| Emission rating |  | EU5 |  | EU5 |

Specifications apply to ACEA markets/homologation data apply in part only to Germany (weight).

Figures in brackets apply to models with automatic transmission.

1)  Oil change