Specifications BMW 3 Series Sedan xDrive.
320d xDrive, 330d xDrive

|  |  | BMW 320d xDrive Saloon |  | BMW 330d xDrive Saloon |
| --- | --- | --- | --- | --- |
| Body |  |  |  |  |
| No of doors / seats |  | 4 / 5 |  | 4 / 5 |
| Length/width/height (unladen) | mm | 4531 / 1817 / 1421 |  | 4531 / 1817 / 1421 |
| Wheelbase | mm | 2760 |  | 2760 |
| Track, front/rear | mm | 1506 / 1535 |  | 1500 / 1529 |
| Ground clearance | mm | 140 |  | 140 |
| Turning circle | m | 11.8 |  | 11.8 |
| Tank capacity | approx ltr | 61 |  | 61 |
| Cooling system incl heater | ltr | 7.5 (7.9) |  | 7.9 |
| Engine oil1) | ltr | 5.2 |  | 7.2 |
| Weight, unladen, to DIN/EU | kg | 1525 / 1600 (1540 / 1615) |  | 1635 / 1710 (1650 / 1725) |
| Max load to DIN | kg | 520 |  | 520 |
| Max permissible | kg | 2045 (2060) |  | 2155 (2170) |
| Max axle load, front/rear | kg | 995 / 1105 |  | 1085 / 1125 |
| Max trailer load (12%), braked/unbraked | kg | 1600 / 745 |  | 1800 / 750 |
| Max roofload/towbar download | kg | 75 / 75 |  | 75 / 75 |
| Luggage comp capacity | ltr | 460 |  | 460 |
| Air resistance | cD x A | 0.30 x 2.17 |  | 0.30 x 2.17 |
| Power Unit |  |  |  |  |
| Configuration/No of cyls/valves |  | Straight-4 / 4 |  | Straight-6 / 4 |
| Engine technology |  | Common-rail direct injection, turbocharger with variable intake geometry |  | Common-rail direct injection, turbocharger with variable intake geometry |
| Capacity, effective | cc | 1995 |  | 2993 |
| Stroke/bore | mm | 90.0 / 84.0 |  | 90.0 / 84.0 |
| Compression ratio | :1 | 16.0 |  | 16.5 |
| Fuel grade |  | Diesel |  | Diesel |
| Max output | kW/hp | 130 / 177 |  | 180 / 245 |
| at | rpm | 4000 |  | 4000 |
| Max torque | Nm / lb-ft | 350 / 258 |  | 520 / 383 |
| at | rpm | 1750-3000 |  | 1750-3000 |
| Electrical System |  |  |  |  |
| Battery/installation | Ah/– | 90 (80) / luggage compartment |  | 90 / luggage compartment |
| Alternator | A/W | 180 / 2520 |  | 180 / 2520 |
| Driving Dynamics and Safety |  |
| Suspension, front |  | Double-joint spring strut axle, aluminium, displaced castor, small positive steering roll radius, compensation of lateral forces, anti-dive Five-arm axle in lightweight steel construction |
| Suspension, rear |  | Five-arm axle in lightweight steel construction |
| Brakes, front |  | Single-piston swing-calliper disc brakes |
| Diameter | mm | 312 x 24 / vented |  | 348 x 30 / vented |
| Brakes, rear |  | Single-piston swing-calliper disc brakes |
| Diameter | mm | 330 x 20 / vented |  | 336 x 22 / vented |
| Driving stability systems |  | Standard: DSC incl ABS and DTC (Dynamic Traction Control), CBC Cornering Brake Control, DBC Dynamic Brake Control, BMW 330d also with Dry Braking, Fading Compensation and Start-Off Assistant, interaction of DSC and xDrive through Integrated Chassis Management (ICM) |
| Safety features |  | Standard: airbags for driver and front passenger, side airbags for driver and front passenger, head airbags front and rear, three-point inertia-reel seat belts on all seats, belt restrainer, belt latch tensioner and belt force limiter at the front, crash-activated headrests at the front, crash sensors, tyre defect indicator |
| Steering |  | Rack-and-pinion power steering |
| Transmission ratio, overall | :1 | 18.2 |  | 18.2 |
| Tyres, front/rear |  | 205/55 R16 91V |  | 225/45 R17 91W RSC |
| Rims, front/rear |  | 7J x 16 light-alloy |  | 8J x 17 light-alloy |

Specifications BMW 3 Series Saloon xDrive.

|  |  | BMW 320d xDrive Saloon |  | BMW 330d xDrive Saloon |
| --- | --- | --- | --- | --- |
| BMW ConnectedDrive |  |  |  |  |
| Comfort |  | Optional: BMW Assist incl Enquiry Service, remote-control functions and V-Info+, BMW TeleServices, integration of mobile terminals |
| Infotainment |  | Optional: access to the internet, BMW Online incl Parkinfo, National Info, Google Directory Service, News, real-time weather, office functions, BMW Routes and online music title update |
| Safety |  | Optional: Adaptive Headlights with Bending Lights, High-Beam Assistant, Park Distance Control, Active Cruise Control with Stop & Go, Automatic/Enhanced Emergency Call |
| Transmission |  |  |  |  |
| Type |  | Six-speed manual (optional: six-speed automatic) |
| Gear ratios I | :1 | 5.140 (4.171) |  | 5.080 (4.171) |
| II | :1 | 2.830 (2.340) |  | 2.804 (2.340) |
| III | :1 | 1.804 (1.521) |  | 1.783 (1.521) |
| IV | :1 | 1.257 (1.143) |  | 1.260 (1.143) |
| V | :1 | 1.000 (0.867) |  | 1.000 (0.867) |
| VI | :1 | 0.831 (0.691) |  | 0.835 (0.691) |
| R | :1 | 4.638 (3.403) |  | 4.607 (3.403) |
| Final drive ratio | :1 | 2.640 (3.154) |  | 2.471 (2.929) |
| Performance |  |  |  |  |
| Power-to-weight ratio | kg/kW | 11.7 (11.8) |  | 9.1 (9.2) |
| Output per litre | kW/hp | 65.2 / 88.7 |  | 60.1 / 81.7 |
| Acceleration 0–100 km/h | sec | 8.2 (8.3) |  | 5.9 (6.0) |
| Standing-start km | sec | 29.2 (29.3) |  | 26.1 (26.2) |
| In 4th/5th gear 80–120 km/h | sec | 6.9 / 8.7 (-) |  | 5.1 / 6.5 (-) |
| Top speed | km/h | 224 (222) |  | 247 |
| BMW EfficientDynamics |  |  |  |  |
| BMW EfficientDynamics, standard features |  | Brake Energy Regeneration, Auto Start Stop function (BMW 320d manual model), gearshift point indicator (manual model), ancillary units controlled on demand, intelligent lightweight construction, tyres with reduced roll resistance, a/c compressor detachable |
| Fuel Con in EU Cycle |  |  |  |
| Urban | ltr/100km | 6.7 (7.9) |  | 8.3 (8.8) |
| Extra-urban | ltr/100km | 4.6 (4.8) |  | 5.5 (5.7) |
| Combined | ltr/100km | 5.4 (5.9) |  | 6.5 (6.8) |
| CO2 | g/km | 143 (156) |  | 171 (178) |
| Emission rating |  | EU4 |  | EU5 |

Specifications apply to ACEA markets/homologation data apply in part only to Germany (weight).

Figures in brackets apply to models with automatic transmission.

1)  Oil change