Specifications BMW 3 Series Sedan.
325d, 330d, 335d

|  |  | BMW 325d Saloon | BMW 330d Saloon | BMW 335d Saloon |
| --- | --- | --- | --- | --- |
| Body |  |  |  |  |
| No of doors / seats |  | 4 / 5 | 4 / 5 | 4 / 5 |
| Length/width/height (unladen) | mm | 4531 / 1817 / 1421 | 4531 / 1817 / 1421 | 4531 / 1817 / 1421 |
| Wheelbase | mm | 2760 | 2760 | 2760 |
| Track, front/rear | mm | 1500 / 1529 | 1500 / 1529 | 1500 / 1529 |
| Ground clearance | mm | 144 | 144 | 144 |
| Turning circle | m | 11.0 | 11.0 | 11.0 |
| Tank capacity | approx ltr | 61 | 61 | 61 |
| Cooling system incl heater | ltr | 7.9 (8.2) | 7.9 | 8.2 |
| Engine oil1) | ltr | 7.5 | 7.2 | 7.5 |
| Weight, unladen, to DIN/EU | kg | 1525 / 1600 (1535 / 1610) | 1535 / 1610 (1550 / 1625) | 1550 / 1625 |
| Max load to DIN | kg | 520 | 520 | 520 |
| Max permissible | kg | 2045 (2055) | 2055 (2070) | 2100 |
| Max axle load, front/rear | kg | 985 / 1105 | 995 / 1110 | 1015 / 1120 |
| Max trailer load (12%), braked/unbraked | kg | 1800 / 750 | 1800 / 750 | 1800 / 750 |
| Max roofload/towbar download | kg | 75 / 75 | 75 / 75 | 75 / 75 |
| Luggage comp capacity | ltr | 460 | 460 | 450 |
| Air resistance | cD x A | 0.28 x 2.17 | 0.28 x 2.17 | 0.30 x 2.17 |
| Power Unit |  |  |  |  |
| Configuration/No of cyls/valves |  | Straight-6 / 4 | Straight-6 / 4 | Straight-6 / 4 |
| Engine technology |  | Common-rail direct injection, turbocharger with variable intake geometry | Common-rail direct injection, turbocharger with variable intake geometry | Common-rail direct injection, Variable Twin Turbo |
| Capacity, effective | cc | 2993 | 2993 | 2993 |
| Stroke/bore | mm | 90.0 / 84.0 | 90.0 / 84.0 | 90.0 / 84.0 |
| Compression ratio | :1 | 17.0 | 16.5 | 17.0 |
| Fuel grade |  | Diesel | Diesel | Diesel |
| Max output | kW/hp | 145 / 197 | 180 / 245 | 210 / 286 |
| at | rpm | 4000 | 4000 | 4400 |
| Max torque | Nm / lb-ft | 400 / 295 | 520 / 383 | 580 / 427 |
| at | rpm | 1300-3250 | 1750-3000 | 1750-2250 |
| Electrical System |  |  |  |  |
| Battery/installation | Ah/– | 90 / luggage compartment | 90 / luggage compartment | 90 / luggage compartment |
| Alternator | A/W | 150 / 2100 | 180 / 2520 | 180 / 2520 |
| Driving Dynamics and Safety |  |
| Suspension, front |  | Double-joint spring strut axle, aluminium, displaced castor, small positive steering roll radius, compensation of lateral forces, anti-dive |
| Suspension, rear |  | Five-arm axle in lightweight steel construction |
| Brakes, front |  | Single-piston swing-calliper disc brakes |
| Diameter | mm | 330 x 24 / vented | 348 x 30 / vented | 348 x 30 / vented |
| Brakes, rear |  | Single-piston swing-calliper disc brakes |
| Diameter | mm | 336 x 22 / vented | 336 x 22 / vented | 336 x 22 / vented |
| Driving stability systems |  | Standard: DSC incl ABS and DTC (Dynamic Traction Control), CBC Cornering Brake Control, DBC Dynamic Brake Control, Dry Braking, Fading Compensation, Start-Off Assistant |
| Safety features |  | Standard: airbags for driver and front passenger, side airbags for driver and front passenger, head airbags front and rear, three-point inertia-reel seat belts on all seats, with belt restrainer, belt latch tensioner and belt force limiter at the front, crash-activated headrests at the front, crash sensors, tyre defect indicator |
| Steering |  | Rack-and-pinion power steering |
| Transmission ratio, overall | :1 | 16.0 | 16.0 | 16.0 |
| Tyres, front/rear |  | 225/45 R17 91W RSC | 225/45 R17 91W RSC | 225/45 R17 91W RSC |
| Rims, front/rear |  | 8J x 17 light-alloy | 8J x 17 light-alloy | 8J x 17 light-alloy |

Specifications BMW 3 Series Saloon.

|  |  | BMW 325d Saloon | BMW 330d Saloon | BMW 335d Saloon |
| --- | --- | --- | --- | --- |
| BMW ConnectedDrive |  |  |  |  |
| Comfort |  | Optional: BMW Assist incl Enquiry Service, remote-control functions and V-Info+, BMW TeleServices, Integration of mobile terminals |
| Infotainment |  | Optional: access to the internet, BMW Online incl Parkinfo, National Info, Google Directory Service, News, real-time weather, office functions, BMW Routes and online music title update |
| Safety |  | Optional: Adaptive Headlights with Bending Lights, High-Beam Assistant, Park Distance Control, Cruise Control, Automatic/Enhanced Emergency Call |
| Transmission |  |  |  |  |
| Type |  | Six-speed manual (optional: six-speed automatic) | Six-speed automatic |
| Gear ratios I | :1 | 5.080 (4.171) | 5.080 (4.171) | 4.171 |
| II | :1 | 2.804 (2.340) | 2.804 (2.340) | 2.340 |
| III | :1 | 1.783 (1.521) | 1.783 (1.521) | 1.521 |
| IV | :1 | 1.260 (1.143) | 1.260 (1.143) | 1.143 |
| V | :1 | 1.000 (0.867) | 1.000 (0.867) | 0.867 |
| VI | :1 | 0.835 (0.691) | 0.835 (0.691) | 0.691 |
| R | :1 | 4.607 (3.403) | 4.607 (3.403) | 3.403 |
| Final drive ratio | :1 | 2.353 (2.786) | 2.353 (2.813) | 2.813 |
| Performance |  |  |  |  |
| Power-to-weight ratio | kg/kW | 10.5 (10.6) | 8.5 (8.6) | 7.5 |
| Output per litre | kW/hp | 48.4 / 65.8 | 60.1 / 81.7 | 70.2 / 95.5 |
| Acceleration 0–100 km/h | sec | 7.4 (7.6) | 6.1 (6.2) | 6.0 |
| Standing-start km | sec | 27.9 (27.8) | 25.8 (26.0) | 25.2 |
| In 4th/5th gear 80–120 km/h | sec | 6.4 / 8.2 (-) | 4.8 / 6.1 (-) | - |
| Top speed | km/h | 235 (233) | 250 | 250 |
| BMW EfficientDynamics |  |  |  |  |
| BMW EfficientDynamics, standard features |  | Brake Energy Regeneration, gearshift point indicator (manual model), ancillary units controlled on demand, intelligent lightweight construction, active air flap control (BMW 325d and BMW 330d), tyres with reduced roll resistance, oil pump with map control, a/c compressor detachable |
| Fuel Con in EU Cycle |  |  |  |
| Urban | ltr/100km | 7.6 (8.1) | 7.3 (8.0) | 9.1 |
| Extra-urban | ltr/100km | 4.6 (5.1) | 4.8 (5.2) | 5.3 |
| Combined | ltr/100km | 5.7 (6.2) | 5.7 (6.2) | 6.7 |
| CO2 | g/km | 153 (164) | 152 (164) | 177 |
| Emission rating |  | EU4 | EU5 | EU4 |

Specifications apply to ACEA markets/homologation data apply in part only to Germany (weight).

Figures in brackets apply to models with automatic transmission.

1)  Oil change