Specifications BMW 3 Series Sedan.
325i xDrive, 330i xDrive, 335i xDrive

|  |  | BMW 325i xDrive Saloon | BMW 330i xDrive Saloon | BMW 335i xDrive Saloon |
| --- | --- | --- | --- | --- |
| Body |  |  |  |  |
| No of doors / seats |  | 4 / 5 | 4 / 5 | 4 / 5 |
| Length/width/height (unladen) | mm | 4531 / 1817 / 1421 | 4531 / 1817 / 1421 | 4531 / 1817 / 1421 |
| Wheelbase | mm | 2760 | 2760 | 2760 |
| Track, front/rear | mm | 1506 / 1535 | 1500 / 1529 | 1500 / 1529 |
| Ground clearance | mm | 140 | 140 | 140 |
| Turning circle | m | 11.8 | 11.8 | 11.8 |
| Tank capacity | approx ltr | 63 | 63 | 63 |
| Cooling system incl heater | ltr | 8.2 (8.5) | 8.2 (8.5) | 8.2 (8.5) |
| Engine oil1) | ltr | 6.5 | 6.5 | 6.5 |
| Weight, unladen, to DIN/EU | kg | 1540 / 1615 (1560 / 1635) | 1575 / 1650 (1590 / 1665) | 1645 / 1720 (1660 / 1735) |
| Max load to DIN | kg | 520 | 520 | 520 |
| Max permissible | kg | 2060 (2080) | 2100 (2115) | 2165 (2180) |
| Max axle load, front/rear | kg | 1020 / 1105 | 1035 (1110) | 1095 (1135) |
| Max trailer load (12%), braked/unbraked | kg | 1700 / 750 | 1800 / 750 | 1800 / 750 |
| Max roofload/towbar download | kg | 75 / 75 | 75 / 75 | 75 / 75 |
| Luggage comp capacity | ltr | 460 | 460 | 450 |
| Air resistance | cD x A | 0.30 x 2.17 | 0.31 x 2.17 | 0.32 x 2.17 |
| Power Unit |  |  |  |  |
| Configuration/No of cyls/valves |  | Straight-6 / 4 | Straight-6 / 4 | Straight-6 / 4 |
| Engine technology |  | Second-generation direct injection (High Precision Injection), lean burn | Second-generation direct injection (High Precision Injection), lean burn | BMW Twin Turbo second-generation direct injection (High Precision Injection) |
| Capacity, effective | cc | 2996 | 2996 | 2979 |
| Stroke/bore | mm | 88.0 / 85.0 | 88.0 / 85.0 | 89.6 / 84.0 |
| Compression ratio | :1 | 12.0 | 12.0 | 10.2 |
| Fuel grade |  | min RON 91 | min RON 91 | min RON 95 |
| Max output | kW/hp | 160 / 218 | 200 / 272 | 225 / 306 |
| at | rpm | 6100 | 6700 | 5800 |
| Max torque | Nm / lb-ft | 270 / 199 | 320 / 236 | 400 / 295 |
| at | rpm | 2400-4200 | 2750-3000 | 1300-5000 |
| Electrical System |  |  |  |  |
| Battery/installation | Ah/– | 80 / luggage compartment | 80 / luggage compartment | 80 / luggage compartment |
| Alternator | A/W | 150 / 2100 (180 / 2520) | 150 / 2100 (180 / 2520) | 180 / 2520 |
| Driving Dynamics and Safety |  |
| Suspension, front |  | Double-joint spring strut axle, aluminium, displaced castor, small positive steering roll radius, compensation of lateral forces, anti-dive Five-arm axle in lightweight steel construction |
| Suspension, rear |  | Five-arm axle in lightweight steel construction |
| Brakes, front |  | Single-piston swing-calliper disc brakes |
| Diameter | mm | 312 x 24 / vented | 330 x 24 / vented | 348 x 30 / vented |
| Brakes, rear |  | Single-piston swing-calliper disc brakes |
| Diameter | mm | 300 x 20 / vented | 336 x 22 / vented | 336 x 22 / vented |
| Driving stability systems |  | Standard: DSC incl ABS and DTC (Dynamic Traction Control), CBC Cornering Brake Control, DBC Dynamic Brake Control, Dry Braking, Fading Compensation, Start-Off Assistant, interaction of DSC and xDrive through Integrated Chassis Management (ICM) |
| Safety features |  | Standard: airbags for driver and front passenger, side airbags for driver and front passenger, head airbags front and rear, three-point inertia-reel seat belts on all seats, belt restrainer, belt latch tensioner and belt force limiter at the front, crash-activated headrests at the front, crash sensors, tyre defect indicator |
| Steering |  | Rack-and-pinion power steering |
| Transmission ratio, overall | :1 | 18.2 | 18.2 | 18.2 |
| Tyres, front/rear |  | 205/55 R16 91W | 225/45 R17 91W RSC | 225/45 R17 91W RSC |
| Rims, front/rear |  | 7J x 16 light-alloy | 8J x 17 light-alloy | 8J x 17 light-alloy |

Specifications BMW 3 Series Saloon xDrive.

|  |  | BMW 325i xDrive Saloon | BMW 330i xDrive Saloon | BMW 335i xDrive Saloon |
| --- | --- | --- | --- | --- |
| BMW ConnectedDrive |  |  |  |  |
| Comfort |  | Optional: BMW Assist incl Enquiry Service, remote-control functions and V-Info+, BMW TeleServices, Integration of mobile terminals |
| Infotainment |  | Optional: access to the internet, BMW Online incl Parkinfo, National Info, Google Directory Service, News, real-time weather, office functions, BMW Routes and online music title update |
| Safety |  | Optional: Adaptive Headlights with Bending Lights, High-Beam Assistant, Park Distance Control, Active Cruise Control, Automatic/Enhanced Emergency Call |
| Transmission |  |  |  |  |
| Type |  | Six-speed manual (optional: six-speed automatic) |
| Gear ratios I | :1 | 4.350 (4.171) | 4.350 (4.171) | 4.055 (4.171) |
| II | :1 | 2.496 (2.340) | 2.496 (2.340) | 2.396 (2.340) |
| III | :1 | 1.665 (1.521) | 1.665 (1.521) | 1.582 (1.521) |
| IV | :1 | 1.230 (1.143) | 1.230 (1.143) | 1.192 (1.143) |
| V | :1 | 1.000 (0.867) | 1.000 (0.867) | 1.000 (0.867) |
| VI | :1 | 0.851 (0.691) | 0.851 (0.691) | 0.872 (0.691) |
| R | :1 | 3.926 (3.403) | 3.926 (3.403) | 3.677 (3.403) |
| Final drive ratio | :1 | 3.071 (3.462) | 3.154 (3.636) | 3.077 (3.462) |
| Performance |  |  |  |  |
| Power-to-weight ratio | kg/kW | 9.6 (9.8) | 7.9 (8.0) | 7.3 (7.4) |
| Output per litre | kW/hp | 53.4 / 72.6 | 66.8 / 90.8 | 75.5 / 102.7 |
| Acceleration 0–100 km/h | sec | 7.3 (7.7) | 6.2 (6.4) | 5.5 (5.6) |
| Standing-start km | sec | 27.8 (28.1) | 26.1 (26.2) | 25.1 |
| In 4th/5th gear 80–120 km/h | sec | 8.3 / 10.2 (-) | 7.0 / 9.0 (-) | 5.9 / 7.1 (-) |
| Top speed | km/h | 244 (242) | 250 | 250 |
| BMW EfficientDynamics |  |  |  |  |
| BMW EfficientDynamics, standard features |  | Brake Energy Regeneration,, gearshift point indicator (manual model), on-demand control of ancillary units, intelligent lightweight construction, tyres with reduced roll resistance, on-demand control of oil pump, a/c compressor detachable |
| Fuel Con in EU Cycle |  |  |  |
| Urban | ltr/100km | 11.0 (11.1) | 11.1 (11.2) | 14.1 (13.8) |
| Extra-urban | ltr/100km | 6.4 (6.5) | 6.5 (6.6) | 7.1 (7.3) |
| Combined | ltr/100km | 8.1 (8.2) | 8.2 (8.3) | 9.7 |
| CO2 | g/km | 188 (192) | 191 (193) | 232 |
| Emission rating |  | EU5 | EU5 | EU4 |

Specifications apply to ACEA markets/homologation data apply in part only to Germany (weight).

Figures in brackets apply to models with automatic transmission.

1)  Oil change