Technical Specifications.
The New BMW 5 Series Touring.
520d, 530d.

|  |  | BMW 520d Touring |  | BMW 530d Touring |
| --- | --- | --- | --- | --- |
| Body |  |  |  |  |
| No of doors/seats |  | 5/5 |  | 5/5 |
| Length/width/height (unladen) | mm | 4907/1860/1462 1) |  | 4907/1860/1462 1) |
| Wheelbase | mm | 2968 |  | 2968 |
| Track, front/rear | mm | 1600/1626 |  | 1600/1626 |
| Ground clearance |  | 141 |  | 141 |
| Turning circle | m | 11.95 |  | 11.95 |
| Tank capacity | app ltr | 70 |  | 70 |
| Cooling system incl heater | ltr | 7.0 |  | 8.0 |
| Engine oil2) | ltr | 5.2 |  | 7.2 |
| Weight, unladen, to DIN/EU | kg | 1710/1785 (1715/1790) |  | 1800/1875 (1805/1880) |
| Max load to DIN | kg | 650 |  | 650 |
| Max permissible | kg | 2360 (2365) |  | 2450 (2455) |
| Max axle load, front/rear | kg | 1060/1400 |  | 1125/1400 |
| Max trailer load (12%), braked/unbraked | kg | 2000/750 |  | 2000/750 |
| Max roofload/max towbar dwnl | kg | 100/90 |  | 100/90 |
| Luggage comp capacity | ltr | 560-1670 |  | 560-1670 |
| Air resistance | Cd x A | 0.31 x 2.35 |  | 0.31 x 2.35 |
| Power Unit |  |  |  |  |
| Config/No of cyls/valves |  | Straight-six / 4 / 4 |  | Straight-six / 6 / 4 |
| Engine technology |  | Common Rail direct fuel injection, turbocharger with variable intake geometry |  | Common Rail direct fuel injection, turbocharger with variable intake geometry |
| Capacity, effective | cc | 1995 |  | 2993 |
| Stroke / bore | mm | 90.0/84.0 |  | 90.0/84.0 |
| Compression ratio | :1 | 16.5 |  | 16.5 |
| Fuel grade |  | Diesel |  | Diesel |
| Max output | kW/bhp | 135/184 |  | 180/245 |
| at | rpm | 4000 |  | 4000 |
| Max torque | Nm/lb-ft | 380/280 |  | 540/398 |
| at | rpm | 1750-2750 |  | 1750-3000 |
| Electrical System |  |  |  |  |
| Battery/installation | Ah/– | 80 (90) / luggage comp |  | 90 / luggage comp |
| Alternator | A/W | 180 / 2520 |  | 180 / 2520 |
| Driving Dynamics and Safety |  |
| Suspension, front |  | Double-track control arm axle with separate lower track arm level, aluminium, small steering roll radius, anti-dive |
| Suspension, rear |  | Integral V multi-arm axle, aluminium, with steering function, anti-squat and anti-dive, double acoustic separation, self-levelling air suspension |
| Brakes, front |  | Single-piston aluminium swing-calliper disc brakes in frame structure |
| Diameter | mm | 330 x 24/inner-vented |  | 348 x 30/inner-vented |
| Brakes, rear |  | Single-piston swing-calliper disc brakes |
| Diameter | mm | 330 x 20/inner-vented |  | 330 x 20/inner-vented |
| Driving stability systems |  | Standard: DSC incl ABS and DTC Dynamic Traction Control, CBC Cornering Brake Control, DBC Dynamic Brake Control, Dry Braking function, Fading Compensation, Start-Off Assistant; optional: Dynamic Damper Control (BMW 523i), Adaptive Drive (BMW 535i) |
| Safety equipment |  | Standard: airbags for driver and front passenger, side airbags for driver and front passenger, head airbags for front and rear seats, three-point inertia-reel belts on all seats with belt stopper, belt tightener and belt force limiter at the front, crash-activated headrests at the front, crash sensors, Tyre Defect Indicator |
| Steering |  | Electric Power Steering (EPS) with Servotronic; optional: Integral Active Steering |
| Steering transmission, overall | :1 | 17.1 |  | 17.1 |
| Tyres, front/rear |  | 225/55 R17 97W |  | 225/55 R17 97W |
| Rims, front/rear |  | 8J x 17 light-alloy |  | 8J x 17 light-alloy |

Technical Specifications.
The New BMW 5 Series Touring.
520d, 530d.

|  |  | BMW 520d Touring |  | BMW 530d Touring |
| --- | --- | --- | --- | --- |
| BMW ConnectedDrive |  |  |  |  |
| Comfort |  | Optional: BMW Assist including Enquiry Service, remote-control functions and V-Info+, BMW TeleServices, integration of mobile terminals |
| Infotainment |  | Optional: access to the internet, BMW Online including Parkinfo, National Info, Google Directory Service, News, Weather Realtime, office functions, Bluetooth Audio Streaming, BMW Routes |
| Safety |  | Optional: Adaptive Headlights with Bending Lights, variable light distribution and adaptive headlight range control, High-Beam Assistant, Park Distance Control, back-up camera, Surround View including Side View and Top View, BMW Night Vision with detection of persons, Head-Up Display, Parking Assistant, collision warning with brake activation function in combination with Active Cruise Control with Stop & Go, Lane Change Warning, Lane Departure Warning, Speed Limit Info, Speed Limit Device, Automatic/Enhanced Emergency Call |
| Transmission |  |  |  |  |
| Type of gearbox |  | Six-speed manual (optional: 8-speed automatic with Steptronic) |
| Gear ratios I |  | 4.110 (4.714) |  | 5.080 (4.714) |
| II | :1 | 2.248 (3.143) |  | 2.804 (3.143) |
| III | :1 | 1.403 (2.106) |  | 1.783 (2.106) |
| IV | :1 | 1.000 (1.667) |  | 1.260 (1.667) |
| V | :1 | 0.802 (1.285) |  | 1.000 (1.285) |
| VI | :1 | 0.659 (1.000) |  | 0.835 (1.000) |
| VII | :1 | – (0.839) |  | – (0.839) |
| VIII | :1 | – (0.667) |  | – (0.667) |
| R | :1 | 3.727 (3.295) |  | 4.607 (3.317) |
| Final drive | :1 | 3.462 (3.077) |  | 2.563 (2.471) |
| Performance |  |  |  |  |
| Power-to-weight ratio | kg/kW | 12.7 (12.7) |  | 10.0 (10.0) |
| Output per litre | kW/ltr | 67.7 |  | 60.1 |
| Acceleration 0–100 km/h | sec | 8.3 (8.3) |  | 6.4 (6.4) |
| 0–1000 m | sec | 29.3 (29.4) |  | 26.8 (26.7) |
| in 4th gear 80–120 km/h | sec | 7.1 (–) |  | 5.3 (–) |
| Top speed | km/h | 222 (220) |  | 243 (242) |
| BMW EfficientDynamics |  |  |  |  |
| BMW EfficientDynamics, standard features |  | Brake Energy Regeneration with recuperation display, gearshift point indicator (on manual gearbox models), intelligent lightweight construction, on-demand operation of ancillary units, air flap control, Electric Power Steering (EPS), detachable a/c compressor, tyres with reduced roll resistance |
| Fuel Consump in EU Cycle |  |  |  |  |
| Urban | ltr/100 km | 6.2 (6.5) |  | 8.1 (8.0) |
| Extra-urban | ltr/100 km | 4.5 (4.6) |  | 5.3 (5.3) |
| Combined | ltr/100 km | 5.1 (5.3) |  | 6.4 (6.3) |
| CO2 | g/km | 135 (139) |  | 169 (165) |
| Emission rating |  | EU5 |  | EU53) |
| Insurance classification |  |  |  |  |
| KH / VK / TK |  | 19 / 25 / 28 |  | 20 / 26 / 28 |

Specifications applicable to ACEA markets, data relevant to homologation applicable in part only to Germany (weight)

Figures in brackets apply to automatic transmission models

1)  With roof aerial: 1488 mm

2)  Oil filling quantity

3)  EU6 with optional BMW BluePerformance technology