Specifications.
The new Long-Wheelbase BMW 5 Series Sedan.
523Li, 528Li, 535Li.

|  |  | BMW 523Li | BMW 528Li | BMW 535Li |
| --- | --- | --- | --- | --- |
| Body |  |  |  |  |
| No of doors / seats |  | 4 / 5 | 4 / 5 | 4 / 5 |
| Length/width/height (unladen) | mm | 5039 / 1860 / 14711) | 5039 / 1860 / 14711) | 5039 / 1860 / 14711) |
| Wheelbase | mm | 3108 | 3108 | 3108 |
| Track, front/rear | mm | 1600 / 1627 | 1600 / 1627 | 1600 / 1627 |
| Ground clearance | mm | 149 | 149 | 149 |
| Turning circle | m | 12.45 | 12.45 | 12.45 |
| Tank capacity | approx ltr | 70 | 70 | 70 |
| Cooling system incl heater | ltr | 9.0 | 9.0 | 9.3 |
| Engine oil1) | ltr | 6.5 | 6.5 | 6.5 |
| Weight, unladen, to DIN/EU | kg | 1750 / 1825 | 1780 / 1855 | 1860 / 1935 |
| Max load to DIN | kg | 480 | 480 | 480 |
| Max permissible | kg | 2230 | 2260 | 2340 |
| Max axle load, front/rear | kg | 1070 / 1270 | 1070 / 1270 | 1100 / 1275 |
| Max trailer load (12%), braked/unbraked | kg | - / - | - / - | - / - |
| Max roofload/towbar download | kg | 100/ - | 100/ - | 100/ - |
| Luggage comp capacity | ltr | 520 | 520 | 520 |
| Air resistance | cD x A | 0.29 x 2.35 | 0.29 x 2.35 | 0.30 x 2.35 |
| Power Unit |  |  |  |  |
| Configuration/No of cyls/valves |  | Straight-6 / 4 | Straight-6 / 4 | Straight-6 / 4 |
| Engine technology |  | Fully-variable valve management (VALVETRONIC), double-Vanos | Fully-variable valve management (VALVETRONIC), double-Vanos | BMW TwinPower Turbo, second-gen direct injection (High Precision Injection), fully-variable valve management (VALVETRONIC) |
| Capacity, effective | cc | 2497 | 2996 | 2979 |
| Stroke/bore | mm | 78.8 / 82.0 | 88.0 / 85.0 | 89.6 / 84.0 |
| Compression ratio | :1 | 11.0 | 10.7 | 10.2 |
| Fuel grade |  | min RON 91 | min RON 91 | min RON 91 |
| Max output | kW/hp | 150 / 204 | 190 / 258 | 225 / 306 |
| at | rpm | 6300 | 6600 | 5800 |
| Max torque | Nm / lb-ft | 250 / 184 | 310 / 228 | 400 / 295 |
| at | rpm | 2750-3000 | 2600-3000 | 1200-5000 |
| Electrical System |  |  |  |  |
| Battery/installation | Ah/– | 90 / luggage comp | 90 / luggage comp | 90 / luggage comp |
| Alternator | A/W | 210 / 2940 | 210 / 2940 | 180 / 2520 |
| Driving Dynamics and Safety |  |
| Suspension, front |  | Double-wishbone axle with separate lower arm level, aluminium, small steering roll radius, anti-dive |
| Suspension, rear |  | Integral-IV multi-arm axle, aluminium, multi-dimensional suspension with anti-squat and anti-dive, double acoustic insulation |
| Brakes, front |  | Single-piston swing-calliper disc brakes, aluminium, in frame construction |
| Diameter | mm | 330 x 24 / vented | 330 x 24 / vented | 348 x 30 / vented |
| Brakes, rear |  | Single-piston swing-calliper disc brakes, aluminium |
| Diameter | mm | 330 x 20 / vented | 330 x 20 / vented | 330 x 20 / vented |
| Driving stability systems |  | Standard: DSC incl ABS and DTC (Dynamic Traction Control), CBC Cornering Brake Control, DBC Dynamic Brake Control, Dry Braking, Fading Compensation, Start-Off Assistant |
| Safety features |  | Standard: airbags and side airbags for driver and front passenger, head airbags front and rear, three-point inertia-reel seat belts on all seats with belt limiter, belt latch tensioner and belt force limiter at the front, crash-activated headrests at the front, crash sensors, tyre defect indicator |
| Steering |  | EPS Electric Power Steering with Servotronic |
| Transmission ratio, overall | :1 | 17.1 | 17.1 | 17.1 |
| Tyres, front/rear |  | 225/55 R17 97Y RSC | 225/55 R17 97Y RSC | 225/55 R18 96Y RSC |
| Rims, front/rear |  | 8J x 17 light-alloy | 8J x 17 light-alloy | 8J x 18 light-alloy |

Specifications.
The new Long-Wheelbase BMW 5 Series Sedan.
523Li, 528Li, 535Li.

|  |  | BMW 523Li | BMW 528Li | BMW 535Li |
| --- | --- | --- | --- | --- |
| BMW ConnectedDrive |  |  |  |  |
| Comfort and infotainment |  | Optional: Rear Seat Entertainment, integration of mobile terminals and devices |
| Safety |  | Optional: Adaptive Headlights with Bending Lights, variable light distribution and adaptive headlight range, High-Beam Assistant, Park Distance Control, back-up camera, Surround View incl Side View and Top View, BMW Night Vision also for individual persons, Head-Up Display, Parking Assistant, Lane Departure Warning, |
| Transmission |  |  |  |  |
| Type |  | Eight-speed automatic with Steptronic |
| Gear ratios I | :1 | 4.714 | 4.714 | 4.714 |
| II | :1 | 3.143 | 3.143 | 3.143 |
| III | :1 | 2.106 | 2.106 | 2.106 |
| IV | :1 | 1.667 | 1.667 | 1.667 |
| V | :1 | 1.285 | 1.285 | 1.285 |
| VI | :1 | 1.000 | 1.000 | 1.000 |
| VII | :1 | 0.839 | 0.839 | 0.839 |
| VIII | :1 | 0.667 | 0.667 | 0.667 |
| R | :1 | 3.295 | 3.295 | 3.295 |
| Final drive ratio | :1 | 3.385 | 3.385 | 3.077 |
| Performance |  |  |  |  |
| Power-to-weight ratio | kg/kW | 11.7 | 9.4 | 8.3 |
| Output per litre | kW/hp | 60.1/ 81.7 | 63.4 / 86.2 | 75.5/102.7 |
| Acceleration 0–100 km/h | sec | 8.6 | 6.9 | 6.2 |
| Standing-start km | sec | 29.5 | 26.9 | 26.0 |
| Top speed | km/h | 234 | 250 | 250 |
| BMW EfficientDynamics |  |  |  |  |
| BMW EfficientDynamics, standard features |  | Brake Energy Regeneration with recuperation indicator, intelligent lightweight construction, on-demand control of ancillary units, active air flap control, EPS Electric Power Steering |
| Fuel Con in EU Cycle |  |  |  |  |
| Urban | ltr/100km | 3) | 3) | 3) |
| Extra-urban | ltr/100km | 3) | 3) | 3) |
| Combined | ltr/100km | 7.9 | 8.1 | 8.7 |
| CO2 | g/km | 187 | 192 | 206 |
| Emission rating |  | EU4 | EU4 | EU4 |

Provisional specifications for the Chinese market.

1)  Height with roof aerial 1481 mm

2)  Oil change

3)  Specifications not yet available