Specifications BMW X1.
X1 sDrive18d, X1 sDrive20d

|  |  | BMW X1 sDrive18d |  | BMW X1 sDrive20d |
| --- | --- | --- | --- | --- |
| Body |  |  |  |  |
| No of doors/seats |  | 5 / 5 |  | 5 / 5 |
| Length/width/height (unladen) | mm | 4454 / 1798 / 1545 |  | 4454 / 1798 / 1545 |
| Wheelbase | mm | 2 760 |  | 2 760 |
| Track, front/rear | mm | 1500 / 1529 |  | 1500 / 1529 |
| Turning circle | m | 11.3 |  | 11.3 |
| Tank capacity, approx | ltr | 61 |  | 61 |
| Cooling system incl heater | ltr | 7.2 (7.5) |  | 7.2 (7.5) |
| Engine oil1) | ltr | 5.2 |  | 5.2 |
| Weight, unladen, to DIN/EU | kg | 1470 / 1545 (1495 / 1570) |  | 1490 / 1565 (1500 / 1575) |
| Max load to DIN | kg | 550 |  | 550 |
| Max permissible | kg | 2030 (2055) |  | 2045 (2060) |
| Max axle load, front/rear | kg | 940 / 1155 |  | 940 / 1160 |
| Max trailer load (12%), braked/unbraked | kg | 1800 / 750 |  | 1800 / 750 |
| Max roofload/max download | kg | 75 / 80 |  | 75 / 80 |
| Luggage capacity | ltr | 420 – 1350 |  | 420 – 1350 |
| Air drag | cd x A | 0.32 x 2.34 |  | 0.32 x 2.34 |
| Power Unit |  |  |  |  |
| Config/No of cyls/valves |  | Straight-four / 4 |  | Straight-four / 4 |
| Engine technology |  | Common-rail direct fuel injection, turbocharger with variable intake geometry |  | Common-rail direct fuel injection, turbocharger with variable intake geometry |
| Capacity, effective | cc | 1995 |  | 1995 |
| Stroke / bore | mm | 90.0 / 84.0 |  | 90.0 / 84.0 |
| Compression ratio | :1 | 16.5 |  | 16.5 |
| Fuel grade |  | Diesel |  | Diesel |
| Max output | kW/hp | 105 / 143 |  | 130 / 177 |
| at | rpm | 4000 |  | 4000 |
| Max torque | Nm/lb-ft | 320/236 |  | 350/258 |
| at | rpm | 1750 – 2500 |  | 1750 – 3000 |
| Electrical System |  |  |  |  |
| Battery/location | Ah/– | 80 / luggage comp |  | 80 / luggage comp |
| Alternator | A/W | 180 / 2520 |  | 180 / 2520 |
| Driving Dynamics and Safety |  |
| Suspension, front |  | Aluminium double-joint thrust axle |
| Suspension, rear |  | Five-arm axle with longitudinal arm and double track control arm |
| Brakes, front |  | Single-piston swing-calliper disc brakes |
| diameter | mm | 312 x 24 / vented |  | 312 x 24 / vented |
| Brakes, rear |  | Single-piston swing-calliper disc brakes |
| diameter | mm | 300 x 20 / vented |  | 300 x 20 / vented |
| Driving stability systems |  | Standard: DSC incl ABS and DTC Dynamic Traction Control, CBC Cornering Brake Control, DBC Dynamic Brake Control |
| Safety equipment |  | Standard: Airbags for driver and front passenger, side airbags for driver and front passenger, head airbags front and rear, three-point inertia-reel belts on all seats, with belt latch tensioner and belt force limiter at the front, crash sensors, Tyre Defect Indicator |
| Steering |  | Rack-and-pinion power steering |
| Steering transmission, overall | :1 | 16.13 |  | 16.13 |
| Tyres, front/rear |  | 225/50 R17 94H |  | 225/50 R17 94H |
| Wheels, front/rear |  | 7.5J x 17 steel |  | 7.5J x 17 steel |

Specifications BMW X1.

|  |  | BMW X1 sDrive18d |  | BMW X1 sDrive20d |
| --- | --- | --- | --- | --- |
| BMW ConnectedDrive |  |  |  |  |
| Comfort |  | Optional: BMW Assist including Enquiry Service, remote control functions and V-Info+, BMW TeleServices, integration of mobile terminals |
| Infotainment |  | Optional: Access to the Internet, BMW Online including Parkinfo, National Info, Google Directory Search, News, Realtime Weather, BMW Routes, Office Functions, Bluetooth Audio Streaming and online music title update |
| Safety |  | Optional: Adaptive Headlights with Bending Lights, High-Beam Assistant, Park Distance Control, back-up camera, cruise control with brake function, automatic/enhanced emergency call function |
| Transmission |  |  |  |  |
| Type of transmission |  | Six-speed manual (optional: six-speed automatic with Steptronic) |
| Gear ratios I | :1 | 4.002 (4.171) |  | 5.140 (4.171) |
| II | :1 | 2.108 (2.340) |  | 2.830 (2.340) |
| III | :1 | 1.380 (1.521) |  | 1.804 (1.521) |
| IV | :1 | 1.000 (1.143) |  | 1.257 (1.143) |
| V | :1 | 0.780 (0.867) |  | 1.000 (0.867) |
| VI | :1 | 0.645 (0.691) |  | 0.831 (0.691) |
| R | :1 | 3.187 (3.403) |  | 4.638 (3.403) |
| Final drive | :1 | 3.231 (3.462) |  | 2.643 (3.385) |
| Performance |  |  |  |  |
| Power-to-weight ratio | kg/kW | 14.0 (14.2) |  | 11.5 (11.5) |
| Output per litre | kW/hp | 52.6/71.5 |  | 65.2/88.7 |
| Acceleration 0–100 km/h | sec | 9.6 (9.9) |  | 8.1 (8.3) |
| standing start km | sec | 30.8 (31.4) |  | 28.8 (29.3) |
| In 4th/5th gear 80–120 km/h | sec | 8.2 / 10.9 (– / –) |  | 7.0 / 8.9 (– / –) |
| Top speed | km/h | 200 (200) |  | 218 (218) |
| Offroad Features |  |  |  |  |
| Overhang angle, front/rear | ° | 18.0 / 22.2 |  | 18.0 / 22.2 |
| Ramp angle | ° | 16.8 |  | 16.8 |
| Ground clearance, unladen | mm | 194 |  | 194 |
| BMW EfficientDynamics |  |  |  |  |
| BMW EfficientDynamics, standard |  | Brake Energy Regeneration, Auto Start Stop and gearshift point indicator (manual models), on-demand management of ancillary units, final dive with optimised warm-up behaviour, intelligent lightweight construction, a/c compressor detachable |
| Fuel Consumption in EU Cycle |  |  |  |  |
| Urban | ltr/100 km | 6.1 (7.1) |  | 6.4 (7.1) |
| Extra-urban | ltr/100 km | 4.7 (5.2) |  | 4.7 (5.2) |
| Combined | ltr/100 km | 5.2 (5.9) |  | 5.3 (5.9) |
| CO2 | g/km | 136 (155) |  | 139 (155) |
| Emission rating |  | EU5 |  | EU5 |

Specifications apply to ACEA markets/homologation data apply in part only to Germany (weight).

Figures in brackets apply to models with automatic transmission.

1)   Oil change