Specifications BMW X1.
X1 sDrive18i

|  |  | BMW X1 sDrive18i |  |  |
| --- | --- | --- | --- | --- |
| Body |  |  |  |  |
| No of doors/seats |  | 5 / 5 |  |  |
| Length/width/height (unladen) | mm | 4454 / 1798 / 1545 |  |  |
| Wheelbase | mm | 2760 |  |  |
| Track, front/rear | mm | 1500 / 1529 |  |  |
| Turning circle | m | 11.3 |  |  |
| Tank capacity, approx | ltr | 63 |  |  |
| Cooling system incl heater | ltr | 7.3 (7.9) |  |  |
| Engine oil1) | ltr | 4.3 |  |  |
| Weight, unladen, to DIN/EU | kg | 1430 / 1505 (1455 / 1530) |  |  |
| Max load to DIN | kg | 550 |  |  |
| Max permissible | kg | 1990 (2010) |  |  |
| Max axle load, front/rear | kg | 915 /1135 |  |  |
| Max trailer load (12%), braked/unbraked | kg | 1700 / 750 |  |  |
| Max roofload/max download | kg | 75 / 80 |  |  |
| Luggage capacity | ltr | 420 – 1350 |  |  |
| Air drag | cd x A | 0.32 x 2.34 |  |  |
| Power Unit |  |  |  |  |
| Config/No of cyls/valves |  | Straight-four / 4 |  |  |
| Engine technology |  | Fully variable valve management (VALVETRONIC), double-Vanos |
| Capacity, effective | cc | 1995 |  |  |
| Stroke / bore | mm | 90.0 / 84.0 |  |  |
| Compression ratio | :1 | 10.5 |  |  |
| Fuel grade |  | min RON 91 |  |  |
| Max output | kW/hp | 110 / 150 |  |  |
| at | rpm | 6400 |  |  |
| Max torque | Nm/lb-ft | 200/147 |  |  |
| at | rpm | 3600 |  |  |
| Electrical System |  |  |  |  |
| Battery/location | Ah/– | 70 / luggage comp |  |  |
| Alternator | A/W | 180 / 2520 |  |  |
| Driving Dynamics and Safety |  |
| Suspension, front |  | Aluminium double-joint thrust axle |
| Suspension, rear |  | Five-arm axle with longitudinal arm and double track control arm |
| Brakes, front |  | Single-piston swing-calliper disc brakes |
| diameter | mm | 312 x 24 / vented |  |  |
| Brakes, rear |  | Single-piston swing-calliper disc brakes |
| diameter | mm | 300 x 20 / vented |  |  |
| Driving stability systems |  | Standard: DSC incl ABS and DTC Dynamic Traction Control, CBC Cornering Brake Control, DBC Dynamic Brake Control |
| Safety equipment |  | Standard: Airbags for driver and front passenger, side airbags for driver and front passenger, head airbags front and rear, three-point inertia-reel belts on all seats, with belt latch tensioner and belt force limiter at the front, crash sensors, Tyre Defect Indicator |
| Steering |  | Rack-and-pinion power steering, optional: Servotronic |
| Steering transmission, overall | :1 | 16.13 |  |  |
| Tyres, front/rear |  | 225/50 R17 94H |  |  |
| Wheels, front/rear |  | 7.5J x 17 steel |  |  |

Specifications BMW X1.

|  |  | BMW X1 sDrive18i |  |  |
| --- | --- | --- | --- | --- |
| BMW ConnectedDrive |  |  |  |  |
| Comfort |  | Optional: BMW Assist including Enquiry Service, remote control functions and V-Info+, BMW TeleServices, integration of mobile terminals |
| Infotainment |  | Optional: Access to the Internet, BMW Online including Parkinfo, National Info, Google Directory Search, News, Realtime Weather, BMW Routes, Office Functions, Bluetooth Audio Streaming and online music title update |
| Safety |  | Optional: Adaptive Headlights with Bending Lights, High-Beam Assistant, Park Distance Control, back-up camera, cruise control with brake function, automatic/enhanced emergency call function |
| Transmission |  |  |  |  |
| Type of transmission |  | Six-speed manual (optional: six-speed automatic with Steptronic) |
| Gear ratios I | :1 | 4.323 (4.065) |  |  |
| II | :1 | 2.456 (2.371) |  |  |
| III | :1 | 1.659 (1.551) |  |  |
| IV | :1 | 1.230 (1.157) |  |  |
| V | :1 | 1.000 (0.853) |  |  |
| VI | :1 | 0.848 (0.674) |  |  |
| R | :1 | 3.938 (3.200) |  |  |
| Final drive | :1 | 3.727 (4.444) |  |  |
| Performance |  |  |  |  |
| Power-to-weight ratio | kg/kW | 13.0 (13.2) |  |  |
| Output per litre | kW/hp | 55.1/74.9 |  |  |
| Acceleration 0–100 km/h | sec | 9.7 (10.4) |  |  |
| standing start km | sec | 31.0 (31.9) |  |  |
| In 4th/5th gear 80–120 km/h | sec | 9.4 / 12.2 (– / –) |  |  |
| Top speed | km/h | 202 (200) |  |  |
| Offroad Features |  |  |  |  |
| Overhang angle, front/rear | ° | 18.0/21.5 |  |  |
| Ramp angle | ° | 16.8 |  |  |
| Ground clearance, unladen | mm | 194 |  |  |
| BMW EfficientDynamics |  |  |  |  |
| BMW EfficientDynamics, standard |  | VALVETRONIC, double-Vanos, on-demand management of ancillary units, intelligent lightweight construction |
| Fuel Consumption in EU Cycle |  |  |  |  |
| Urban | ltr/100 km | 11.3 (11.5) |  |  |
| Extra-urban | ltr/100 km | 6.4 (6.6) |  |  |
| Combined | ltr/100 km | 8.2 (8.4) |  |  |
| CO2 | g/km | 191 (195) |  |  |
| Emission rating |  | EU5 |  |  |

Specifications apply to ACEA markets/homologation data apply in part only to Germany (weight).

Figures in brackets apply to models with automatic transmission.

1)   Oil change