Specifications BMW X1.
X1 xDrive18d, X1 xDrive20d, X1 xDrive23d

|  |  | BMW X1 xDrive18d | BMW X1 xDrive20d | BMW X1 xDrive23d |
| --- | --- | --- | --- | --- |
| Body |  |  |  |  |
| No of doors/seats |  | 5 / 5 | 5 / 5 | 5 / 5 |
| Length/width/height (unladen) | mm | 4454 / 1798 / 1545 | 4454 / 1798 / 1545 | 4454 / 1798 / 1545 |
| Wheelbase | mm | 2760 | 2 760 | 2 760 |
| Track, front/rear | mm | 1500 / 1529 | 1500 / 1529 | 1500 / 1529 |
| Turning circle | m | 11.8 | 11.8 | 11.8 |
| Tank capacity, approx | ltr | 61 | 61 | 61 |
| Cooling system incl heater | ltr | 7.2 (7.5) | 7.2 (7.9) | 7.9 |
| Engine oil1) | ltr | 5.2 | 5.2 | 5.2 |
| Weight, unladen, to DIN/EU | kg | 1540 / 1615 (1575 / 1650) | 1575 / 1650 (1585 / 1660) | 1585 / 1660 (1595 / 1670) |
| Max load to DIN | kg | 550 | 550 | 550 |
| Max permissible | kg | 2120 (2140) | 2130 (2145) | 2150 (2160) |
| Max axle load, front/rear | kg | 1010 / 1170 | 1010 / 1165 | 1015 / 1160 |
| Max trailer load (12%), braked/unbraked | kg | 1800 / 750 | 2000 / 750 | 2000 / 750 |
| Max roofload/max download | kg | 75 / 80 | 75 / 80 | 75 / 80 |
| Luggage capacity | ltr | 420 – 1350 | 420 – 1350 | 420 – 1350 |
| Air drag | cd x A | 0.32 x 2.34 | 0.33 x 2.34 | 0.33 x 2.34 |
| Power Unit |  |  |  |  |
| Config/No of cyls/valves |  | Straight-four / 4 | Straight-four / 4 | Straight-four / 4 |
| Engine technology |  | Common-rail direct fuel injection, turbocharger with variable intake geometry | Common-rail direct fuel injection, turbocharger with variable intake geometry | Common-rail direct fuel injection, BMW TwinPower Turbo (Variable Twin Turbo) |
| Capacity, effective | cc | 1995 | 1995 | 1995 |
| Stroke / bore | mm | 90.0 / 84.0 | 90.0 / 84.0 | 90.0 / 84.0 |
| Compression ratio | :1 | 16.5 | 16.5 | 16.5 |
| Fuel grade |  | Diesel | Diesel | Diesel |
| Max output | kW/hp | 105 / 143 | 130 / 177 | 150 / 204 |
| at | rpm | 4000 | 4000 | 4400 |
| Max torque | Nm/lb-ft | 320/236 | 350/258 | 400/295 |
| at | rpm | 1750 – 2500 | 1750 – 3000 | 2000 – 2250 |
| Electrical System |  |  |  |  |
| Battery/location | Ah/– | 80 / luggage comp | 80 / luggage comp | 80 / luggage comp |
| Alternator | A/W | 180 / 2520 | 180 / 2520 | 180 / 2520 |
| Driving Dynamics and Safety |  |
| Suspension, front |  | Double-joint spring-strut thrust bar axle |
| Suspension, rear |  | Five-arm axle with longitudinal arm and double track control arm |
| Brakes, front |  | Single-piston swing-calliper disc brakes |
| diameter |  | 312 x 24 / vented | 312 x 24 / vented | 330 x 24 / vented |
| Brakes, rear |  | Single-piston swing-calliper disc brakes |
| diameter |  | 300 x 20 / vented | 300 x 20 / vented | 300 x 20 / vented |
| Driving stability systems |  | Standard: DSC incl ABS and DTC Dynamic Traction Control, CBC Cornering Brake Control, DBC Dynamic Brake Control, DSC networked with xDrive all-wheel drive, HDC Hill Descent Control; optional: Performance Control |
| Safety equipment |  | Standard: Airbags for driver and front passenger, side airbags for driver and front passenger, head airbags front and rear, three-point inertia-reel belts on all seats, with belt latch tensioner and belt force limiter at the front, crash sensors, Tyre Defect Indicator |
| Steering |  | Rack-and-pinion power steering, optional: Servotronic |
| Steering transmission, overall | :1 | 18.46 | 18.46 | 18.46 |
| Tyres, front/rear |  | 225/50 R17 94H | 225/50 R17 94H | 225/50 R17 94H |
| Wheels, front/rear |  | 7.5J x 17 steel | 7.5J x 17 light-alloy | 7.5J x 17 light-alloy |

Specifications BMW X1.

|  |  | BMW X1 xDrive18d | BMW X1 xDrive20d | BMW X1 xDrive23d |
| --- | --- | --- | --- | --- |
| BMW ConnectedDrive |  |  |  |  |
| Comfort |  | Optional: BMW Assist including Enquiry Service, remote control functions and V-Info+, BMW TeleServices, integration of mobile terminals |
| Infotainment |  | Optional: Access to the Internet, BMW Online including Parkinfo, National Info, Google Directory Search, News, Realtime Weather BMW Routes, Office Functions, Bluetooth Audio Streaming and online music title update |
| Safety |  | Optional: Adaptive Headlights with Bending Lights, High-Beam Assistant, Park Distance Control, back-up camera, cruise control with brake function, automatic/enhanced emergency call function |
| Transmission |  |  |  |  |
| Type of transmission |  | Six-speed manual (optional: six-speed automatic with Steptronic) |
| Gear ratios I | :1 | 5.140 (4.171) | 5.140 (4.171) | 4.110 (4.171) |
| II | :1 | 2.830 (2.340) | 2.830 (2.340) | 2.248 (2.340) |
| III | :1 | 1.804 (1.521) | 1.804 (1.521) | 1.403 (1.521) |
| IV | :1 | 1.257 (1.143) | 1.257 (1.143) | 1.000 (1.143) |
| V | :1 | 1.000 (0.867) | 1.000 (0.867) | 0.802 (0.867) |
| VI | :1 | 0.831 (0.691) | 0.831 (0.691) | 0.659 (0.691) |
| R | :1 | 4.638 (3.403) | 4.638 (3.403) | 3.727 (3.403) |
| Final drive | :1 | 2.786 (3.636) | 2.786 (3.462) | 3.636 (3.636) |
| Performance |  |  |  |  |
| Power-to-weight ratio | kg/kW | 14.7 (15.0) | 12.1 (12.2) | 10.6 (10.6) |
| Output per litre | kW/hp | 52.6/71.5 | 65.2/88.7 | 75.2/102.3 |
| Acceleration 0–100 km/h | sec | 10.1 (10.3) | 8.4 (8.6) | 7.3 (7.3) |
| standing start km | sec | 31.7 (31.9) | 29.5 (29.7) | 28.2 (28.2) |
| In 4th/5th gear 80–120 km/h | sec | 8.7 / 10.2 (– / –) | 7.2 / 9.1 (– / –) | 6.0 / 7.6 (– / –) |
| Top speed | km/h | 195 (195) | 213 (213) | 223 (223) |
| Offroad Features |  |  |  |  |
| Overhang angle, front/rear | ° | 18.0/22.2 | 18.0/22.2 | 18.0/22.2 |
| Ramp angle | ° | 16.8 | 16.8 | 16.8 |
| Ground clearance, unladen | mm | 194 | 194 | 194 |
| BMW EfficientDynamics |  |  |  |  |
| BMW EfficientDynamics, standard |  | Brake Energy Regeneration, Auto Start Stop function and gearshift point indicator (manual models) on-demand management of ancillary units, final drive with optimised warm-up behaviour, intelligent lightweight construction, a/c compressor detachable |
| Fuel Consumption in EU Cycle |  |  |  |  |
| Urban | ltr/100 km | 6.7 (7.7) | 7.0 (7.7) | 7.3 (7.8) |
| Extra-urban | ltr/100 km | 5.1 (5.4) | 5.1 (5.4) | 5.2 (5.5) |
| Combined | ltr/100 km | 5.7 (6.2) | 5.8 (6.2) | 6.0 (6.3) |
| CO2 | g/km | 150 (164) | 153 (164) | 158 (167) |
| Emission rating |  | EU5 | EU5 | EU5 |

Specifications apply to ACEA markets/homologation data apply in part only to Germany (weight).

Figures in brackets apply to models with automatic transmission.

- Oil change