Specifications BMW 3 Series Convertible.
318i, 320i

|  |  | BMW 318i Convertible |  | BMW 320i Convertible |
| --- | --- | --- | --- | --- |
| Body |  |  |  |  |
| No of doors / seats |  | 2 / 4 |  | 2 / 4 |
| Length/width/height (unladen) | mm | 4612 / 1782 / 1384 |  | 4612 / 1782 / 1384 |
| Wheelbase | mm | 2760 |  | 2760 |
| Track, front/rear | mm | 1506 / 1519 |  | 1500 / 1513 |
| Ground clearance |  | 138 |  | 138 |
| Turning circle | m | 11.0 |  | 11.0 |
| Tank capacity appr ltr | 63 |  | 63 |
| Cooling system incl heater | ltr | 8.4 |  | 8.4 (9.1) |
| Engine oil1) | ltr | 4.3 |  | 4.3 |
| Weight, unladen, to DIN/EU | kg | 1595 / 1670 |  | 1595 / 1670 (1625 / 1700) |
| Max load to DIN | kg | 430 |  | 430 |
| Max permissible | kg | 2025 |  | 2025 (2055) |
| Max axle load, front / rear | kg | 915 / 1155 |  | 915 / 1160 |
| Max trailer load (12%), braked / unbraked | kg | 1400 / 695 |  | 1400 (1500) / 695 |
| Max roofload / max download | kg | - / 75 |  | - / 75 |
| Luggage comp | ltr | 210-350 |  | 210-350 |
| Air drag | cd x A | 0.27 x 2.08 |  | 0.27 x 2.08 |
| Power Unit |  |  |  |  |
| Configuration/No of cyls/valves |  | Straight-4 / 4 |  | Straight-4 / 4 |
| Engine technology |  | Second-generation direct fuel injection (High Precision Injection) with lean burn |  | Second-generation direct fuel injection (High Precision Injection) with lean burn |
| Capacity, effective | cc | 1995 |  | 1995 |
| Stroke / bore | mm | 90.0 / 84.0 |  | 90.0 / 84.0 |
| Compression ratio | :1 | 12.0 |  | 12.0 |
| Fuel |  | min 91 RON |  | min 91 RON |
| Max output | kW/hp | 105 / 143 |  | 125 / 170 |
| at | rpm | 6000 |  | 6700 |
| Max torque | Nm/lb-ft | 190 / 140 |  | 210 / 155 |
| at | rpm | 4250 |  | 4250 |
| Electrical System |  |  |  |  |
| Battery / installation | Ah/– | 90 / luggage compartment |  | 90 / luggage compartment |
| Alternator | A/W | 180 / 2520 |  | 180 / 2520 |
| Driving Dynamics and Safety |  |
| Suspension, front |  | Double-joint spring strut axle in aluminium with displaced castor, small positive steering roll radius, compensation of lateral forces, anti-dive |
| Suspension, rear |  | Five-arm axle in lightweight steel |
| Brakes, front |  | Single-piston swing-calliper disc brakes |
| Diameter | mm | 312 x 24 / vented |  | 312 x 24 / vented |
| Brakes, rear |  | Single-piston swing-calliper disc brakes |
| Diameter | mm | 300 x 20 / vented |  | 300 x 20 / vented |
| Driving stability systems |  | Standard: DSC incl ABS and DTC Dynamic Traction Control, CBC Cornering Brake Control, DBC Brake Assistant |
| Safety |  | Standard: airbags for driver and front passenger, side airbags for driver and front passenger with combined head airbags, three-point inertia-reel belts on all seats, integrated on front seats with belt retainer, belt latch tensioner and belt force limiter, crash-activated headrests at the front, crash sensors, rollover safety system, Tyre Defect Indicator |
| Steering |  | Electric Power Steering |
| Steering ratio, overall | :1 | 16.0 |  | 16.0 |
| Tyres, front/rear |  | 205/55 R16 91H RSC |  | 225/45 R17 91W RSC |
| Wheels, front/rear |  | 7J x 16 LM |  | 8J x 17 light-alloy |

Specifications BMW 3 Series Convertible.

|  |  | BMW 318i Convertible |  | BMW 320i Convertible |
| --- | --- | --- | --- | --- |
| BMW ConnectedDrive |  |  |  |  |
| Comfort |  | Optional: BMW Assist incl Enquiry Service, remote control functions and V- Info+, BMW TeleServices, integration of mobile terminals |
| Infotainment |  | Optional: access to the internet, BMW Online incl Parkinfo, National Info, Google directory search, news, realtime weather, BMW Routes, office functions, Bluetooth audio streaming and music title update online |
| Safety |  | Optional: Adaptive Headlights with Bending Lights, High-Beam Assistant, Park Distance Control, cruise control, automatic/enhanced emergency call function |
| Transmission |  |  |  |  |
| Type of transmission |  | Six-speed manual (optional on BMW 320i: six-speed automatic) |
| Gear ratios I | :1 | 4.323 |  | 4.323 (4.171) |
| II | :1 | 2.456 |  | 2.456 (2.340) |
| III | :1 | 1.659 |  | 1.659 (1.521) |
| IV | :1 | 1.230 |  | 1.230 (1.143) |
| V | :1 | 1.000 |  | 1.000 (0.867) |
| VI | :1 | 0.848 |  | 0.848 (0.691) |
| R | :1 | 3.938 |  | 3.938 (3.403) |
| Final drive | :1 | 3.455 |  | 3.636 (4.100) |
| Performance |  |  |  |  |
| Power-to-weight ratio | kg/kW | 15.2 |  | 12.8 (13.0) |
| Output per litre | kW/hp | 52.6 / 71.5 |  | 62.7 / 85.3 |
| Acceleration 0–100 km/h | sec | 10.3 |  | 9.1 (9.8) |
| standing-start | sec | 31.4 |  | 30.0 (30.5) |
| In 4th/5th gear 80–120 km/h | sec | 10.6 / 13.9 |  | 9.3 / 12.0 (-) |
| Top speed | km/h | 210 |  | 228 (226) |
| BMW EfficientDynamics |  |  |  |  |
| BMW EfficientDynamics, standard features |  | Brake Energy Regeneration, Auto Start Stop and gearshift point indicator (manual gearbox models), Electric Power Steering, on-demand management of ancillary units, tyres with reduced roll resistance, intelligent lightweight construction, oil pump with map control, a/c compressor detachable |
| Fuel Consump in EU Cycle |  |  |  |  |
| Urban | ltr/100km | 8.4 |  | 8.8 (9.8) |
| Extra-urban | ltr/100km | 5.6 |  | 5.6 (5.8) |
| Combined | ltr/100km | 6.6 |  | 6.8 (7.3) |
| CO2 | g/km | 154 |  | 159 (169) |
| Emission rating |  | EU5 |  | EU5 |

Specifications apply to ACEA markets/data relevant to homologation apply in part only to Germany (weight)

Figures in brackets apply to models with automatic transmission

1)  Oil change