Specifications BMW X3.
X3 xDrive35i, X3 xDrive20d

|  |  | BMW X3 xDrive35i |  | BMW X3 xDrive20d |
| --- | --- | --- | --- | --- |
| Body |  |  |  |  |
| Number of doors/seats |  | 5 / 5 |  | 5 / 5 |
| Length/Width/Height (unladen) | mm | 4648 / 1881 / 1661 1) |  | 4648 / 1881 / 1661 1) |
| Wheelbase | mm | 2810 |  | 2810 |
| Track front/rear | mm | 1594 / 1610 |  | 1616 / 1632 |
| Turning cycle | m | 11,9 |  | 11,9 |
| Tank capacity | appr ltr | 67 |  | 67 |
| Cooling system incl. heating | ltr | 3) |  | 3) |
| Engine oil 2) | ltr | 6,5 |  | 5,2 |
| Weight, unladen, to DIN/EU | Kg | 1805 / 1880 |  | 1715 / 1790 (1725 / 1800) |
| Max. load to DIN | kg | 560 |  | 575 |
| Max. perm. weight, overall | kg | 2365 |  | 2290 (2300) |
| Max perm axle load front/rear | kg | 1130 / 1290 |  | 1080 / 1280 |
| Max perm trailer load (12 %) braked/unbraked | kg | 2400 / 750 |  | 2000 (2400) / 750 |
| Perm roof load/trail download | kg | 100 / 100 |  | 100 / 100 |
| Luggage capacity | ltr | 550–1600 |  | 550–1600 |
| Air resistance | cd x A | 0.35 x 2.65 |  | 0.33 x 2.65 |
| Engine |  |  |  |  |
| Config/no of cyls/valves |  | R / 6 / 4 |  | R / 4 / 4 |
| Engine technology |  | BMW TwinPower Turbo, direct injection, fully variable valve control (VALVETRONIC) |  | Turbocharger with variable intake geometry, Common Rail direct injection with piezo injectors (max. injection pressure: 1800 bar) |
| Capacity | cc | 2979 |  | 1995 |
| Stroke/bore | mm | 89.6 / 84.0 |  | 90.0 / 84.0 |
| Compression ratio | :1 | 10.2 |  | 16.5 |
| Fuel grade |  | At least RON 91 |  | Diesel |
| Max output | kW/bhp | 225 / 306 |  | 135 / 184 |
| At rpm | rpm | 5800 |  | 4000 |
| Torque | Nm | 400 |  | 380 |
| At rpm | rpm | 1200-5000 |  | 1750-2750 |
| Electrical system |  |  |  |  |
| Battery/installation | Ah/– | 90 / luggage comp |  | 90 / luggage comp |
| Alternator | A/W | 210 / 2940 |  | 180 / 2520 (210 / 2940) |
| Driving dynamics and safety |  |
| Suspension, front |  | Double-joint tension-rod spring-strut suspension, anti-dive |
| Suspension, rear |  | Five-link rear axle, spatial suspension with anti-squat and anti-dive |
| Brakes, front |  | Single-piston floating-caliper disc brakes |
| Diameter | mm | 328 / vented |  | 328 / vented |
| Brakes, rear |  | Single-piston floating-caliper disc brakes |
| Diameter | mm | 330 / vented |  | 330 / vented |
| Driving stability systems |  | Fitted as standard: DSC incl. ABS and DTC (Dynamic Traction Control), CBC Cornering Brake Control, DBC Dynamic Brake Control, rain brake support, fading compensation, hill-start assistant; DSC networked with xDrive four-wheel drive, HDC Hill Descent Control, optional: Dynamic Damper Control, Performance Control |
| Safety features |  | Fitted as standard: Airbags for driver and front seat passenger, side airbags for driver and front seat passenger, head airbags for the first and second seat row, crash-active headrests at the front, three-point automatic belts on all seats, on the front seats with pretensioners, belt-force limiters and belt stoppers, crash sensors, tyre defect indicator |
| Steering |  | EPS Electric Power Steering with Servotronic function, optional: variable sports steering |
| Overall steering transmission | :1 | 3) |  | 3) |
| Tyres front/rear | 245/50 R18 100 W |  | 225/60 R17 99 V |
| Wheels front/rear |  | 8J x 18 LM |  | 7.5J x 17 LM |

Specifications BMW X3.

|  |  | BMW X3 xDrive35i |  | BMW X3 xDrive20d |
| --- | --- | --- | --- | --- |
| BMW ConnectedDrive |  |  |  |  |
| Comfort |  | Optional extras: BMW Assist featuring, inter alia, information service, remote functions and traffic info+, BMW TeleServices, integration of mobile devices |
| Infotainment |  | Optional extras: Internet access, BMW Online featuring, inter alia, parking info, country-relevant info, Google search by type of business, news, weather realtime, BMW Routes, office functions, Bluetooth audio streaming and online update of music tracks |
| Safety |  | Adaptive Cornering Headlights with variable light distribution and adaptive levelling, High-beam Assistant, Park Distance Control, reversing camera with Top View, Head-up Display, speed control with braking function, automatic/advanced emergency call |
| Transmission |  |  |  |  |
| Type |  | 8-speed automatic transmission with Steptronic | 6-speed manual transmission (optional: 8-speed automatic transmission with Steptronic) |
| Gear ratios I | :1 | 4.714 |  | 4.110 (4.714) |
| II | :1 | 3.143 |  | 2.248 (3.143) |
| III | :1 | 2.106 |  | 1.403 (2.106) |
| IV | :1 | 1.667 |  | 1.000 (1.667) |
| V | :1 | 1.285 |  | 0.802 (1.285) |
| VI | :1 | 1.000 |  | 0.659 (1.000) |
| VII | :1 | 0.839 |  | – (0.839) |
| VIII | :1 | 0.667 |  | – (0.667) |
| R | :1 | 3.295 |  | 3.727 (3.295) |
| Final Drive | :1 | 3.385 |  | 3.727 (3.077) |
| Performance |  |  |  |  |
| Power-to-weight ratio | kg/kW | 8.0 |  | 12.7 (12.8) |
| Output per litre | kW/ltr | 75.5 |  | 67.7 |
| Acceleration 0–100 km/h | s | 5.7 |  | 8.5 (8.5) |
| 0–1000 m | s | 25.5 |  | 29.7 (29.7) |
| in 4th/5th gear 80–120 km/h | s | – |  | 6.9 / 9.0 (–) |
| Top speed | km/h | 245 |  | 210 (210) |
| Off-road characteristics |  |  |  |  |
| Overhang angle front/rear | ° | 25.7 / 22.6 |  | 25.7 / 22.6 |
| Ramp angle | ° | 19.4 |  | 19.4 |
| Ground-clearance when unladen | mm | 212 |  | 212 |
| Wading depth | mm | 500 |  | 500 |
| BMW EfficientDynamics |  |  |  |  |
| BMW EfficientDynamics measures as standard |  | Brake Energy Regeneration with recuperation display, EPS Electric Power Steering), Auto Start Stop function, gear shift indicator (BMW X3 xDrive20d manual transmission), demand-controlled ancillary components, map-controlled oil pump (BMW X3 xDrive35i) intelligent lightweight construction, final drive with optimised warm-up behaviour, tyres with reduced rolling resistance |
| Fuel con in the EU cycle |  |  |  |  |
| Urban | ltr/100 km | 11.2 |  | 6.7 (6.1) |
| Extra-urban | ltr/100 km | 7.4 |  | 5.0 (5.3) |
| Composite | ltr/100 km | 8.8 |  | 5.6 (5.6) |
| CO2 | g/km | 204 |  | 149 (147) |
| Emission classification |  | EU5 |  | EU5 |

Technical data valid for ACEA markets/Part of registration-specific data only apply to Germany (weights, top speed)

BMW X3 xDrive20d: Data in parentheses apply to automatic transmission

- Height without roof aerial: 1675 mm

- Oil filling quantity

- Data not yet available