Specifications BMW X1.
X1 xDrive28i

|  |  | BMW X1 xDrive28i |  |  |
| --- | --- | --- | --- | --- |
| Body |  |  |  |  |
| No of doors/seats |  | 5 / 5 |  |  |
| Length/width/height (unladen) | mm | 4454 / 1798 / 1545 |  |  |
| Wheelbase | mm | 2760 |  |  |
| Track, front/rear | mm | 1500 / 1529 |  |  |
| Turning circle | m | 11,8 |  |  |
| Tank capacity | app ltr | 63 |  |  |
| Cooling system incl heater | ltr | 8,5 |  |  |
| Engine oil1) | ltr | 6,5 |  |  |
| Weight, unladen, to DIN/EU | kg | 1610 / 1685 |  |  |
| Max load to DIN | kg | 550 |  |  |
| Max permissible | kg | 2180 |  |  |
| Max axle load, front/rear | kg | 1030 / 1180 |  |  |
| Max trailer load (12%), braked/unbraked | kg | 2000 / 750 |  |  |
| Max roofload/max towbar downl | kg | 75 / 80 |  |  |
| Luggage comp capacity | ltr | 420 – 1350 |  |  |
| Air drag | Cd x A | 0,33 x 2,34 |  |  |
| Power Unit |  |  |  |  |
| Power Unit |  |  |  |  |
| Config/No of cyls/valves |  | R / 6 / 4 |  |  |
| Engine technology |  | Fully variable valve actuation (VALVETRONIC), Double-Vanos |
| Capacity, effective | cc | 2996 |  |  |
| Stroke / bore | mm | 88,0 / 85,0 |  |  |
| Compression ratio | :1 | 10,7 |  |  |
| Fuel |  | min ROZ 91 |  |  |
| Max output | kW/hp | 190 / 258 |  |  |
| at | rpm | 6600 |  |  |
| Max torque | Nm/lb-ft | 310 |  |  |
| at | rpm | 2600 – 3000 |  |  |
| Electrical System |  |  |  |  |
| Battery/location | Ah/– | 80 / luggage comp |  |  |
| Alternator | A/W | 180 / 2520 |  |  |
| Driving Dynamics and Safety |  |
| Suspension, front |  | Aluminium double-joint tie bar axle |
| Suspension, rear |  | Double-wishbone five-link axle with trailing arm |
| Brakes, front |  | Single-piston swing-calliper disc brakes |
| Diameter | mm | 348 x 30 / vented |  |  |
| Brakes, rear |  | Single-piston swing-calliper disc brakes |
| Diameter | mm | 336 x 22 / vented |  |  |
| Driving stability systems |  | Standard: DSC incl ABS and DTC Dynamic Traction Control, CBC Cornering Brake Control, DBC Dynamic Brake Control, DSC linked with xDrive, Hill Descent Control HDC, optional: Performance Control |
| Safety equipment |  | Standard: airbags for driver and front passenger, side airbags for driver and front passenger, head airbags front and rear, active headrests at the front, three-point inertia-reel seat belts on all seats, belt latch tensioners at the front, crash sensors, roll-over sensors, Tyre Defect Indicator |
| Steering |  | Rack-and-pinion power steering, optional: Servotronic |
| Steering transmission, overall | :1 | 18,46 |  |  |
| Tyres, front/rear |  | 225/50 R17 94H |  |  |
| Rims, front/rear |  | 7,5J x 17 LM |  |  |

Specifications BMW X1.
X1 xDrive28i

|  |  | BMW X1 sDrive18d |  |  |
| --- | --- | --- | --- | --- |
| BMW ConnectedDrive |  |  |  |  |
| Comfort |  | Optional: BMW Assist including Enquiry Service, remote-control function and V-Info+, BMW TeleServices, integration of mobile terminals |
| Infotainment |  | Optional: access to the internet, BMW Online including features such as Parkinfo, Nationalinfo, Google directory service, News, realtime weather, Office functions, BMW Routes and online music title update |
| Safety |  | Optional: Adaptive Headlights with Bending Lights, High-Beam Assistant, Park Distance Control, back-up camera, Head-Up Display, Active Cruise Control with Stop & Go, Automatic/Enhanced Emergency Call |
| Transmission |  |  |  |  |
| Type of transmission |  | Manual six-speed transmission |
| Gear ratios I | :1 | 5,140 |  |  |
| II | :1 | 2,830 |  |  |
| III | :1 | 1,804 |  |  |
| IV | :1 | 1,257 |  |  |
| V | :1 | 1,000 |  |  |
| VI | :1 | 0,831 |  |  |
| Reverse | :1 | 4,638 |  |  |
| Final drive | :1 | 3,071 |  |  |
| Performance |  |  |  |  |
| Power-to-weight ratio | kg/kW | 11,3 |  |  |
| Output per litre | kW/hp | 53,5 |  |  |
| Acceleration 0–100 km/h | sec | 7,4 (7,7) |  |  |
| Standing-start km | sec | 28,0 (28,4) |  |  |
| In 4th / 5th gear 80-120km/h | sec | 5,7 / 6,9 (-) |  |  |
| Top speed | km/h | 210 / 2202 |  |  |
| Offroad characteristics |  |  |  |  |
| Overhang angle front / rear | ° | 18,0/21,5 |  |  |
| Ramp breakover angle | ° | 16,8 |  |  |
| Ground cleerance | mm | 194 |  |  |
| BMW EfficientDynamics |  |  |  |  |
| BMW EfficientDynamics standard features |  | Brake energy regeneration, Intelligent lightweight technology, on-demand fuel pump, on-demand coolant pump, Auto Start Stop function and gearshift indicator, final drive with optimised thermal management ,a/c compressor detachable |
| Fuel Consumption in EU Cycle |  |  |  |  |
| Urban | ltr/100 km | 13,0 |  |  |
| Extra-urban | ltr/100 km | 7,3 |  |  |
| Combined | ltr/100 km | 9,4 |  |  |
| CO2 | g/km | 219 |  |  |
| Emission rating |  | EU5 |  |  |

Specifications applicable to ACEA markets/homologation data applicable in part only to Germany (weight),

- Oil change

- With high speed setup (depending on market)