Specifications BMW 1 Series Five-Door.
116i, 118i

|  |  | BMW 116i | BMW 116i | BMW 118i |
| --- | --- | --- | --- | --- |
|  |  | (other EU-Markets incl. Germany and NL) | (IT, GR, NL, PT, HU, JP, Baltic States) |  |
| Body |  |  |  |  |
| No of doors/seats |  | 5 / 5 | 5 / 5 | 5 / 5 |
| Length/width/height (unladen) | mm | 4 239 / 1748 / 1421 | 4 239 / 1748 / 1421 | 4 239 / 1748 / 1421 |
| Wheelbase | mm | 2 660 | 2 660 | 2 660 |
| Track, front/rear | mm | 1484 / 1497 | 1484 / 1497 | 1484 / 1497 |
| Ground clearance | mm | 145 | 145 | 145 |
| Turning circle | m | 10.7 | 10.7 | 10.7 |
| Tank capacity | app ltr | 53 | 53 | 53 |
| Cooling system incl heater | ltr | 7.0 (7.6) | 7.0 (7.6) | 7.3 (7.9) |
| Engine oil1) | ltr | 4.25 | 4.25 | 4.25 |
| Weight, unladen, to DIN/EU | kg | 1275/1350 (1300/1375) | 1265/1340 (1290/1365) | 1275/1350 (1300/1375) |
| Max load to DIN | kg | 500 | 500 | 500 |
| Max permissible | kg | 1775 (1800) | 1765 (1790) | 1775 (1800) |
| Max axle load, front/rear | kg | 855 / 1020 | 855 / 1020 | 855 / 1020 |
| Max trailer load (12%), braked/unbraked | kg | 1200 / 650 | 1200 / 650 | 1200 / 670 |
| Max roofload/max towbar downl | kg | 75 / 75 | 75 / 75 | 75 / 75 |
| Luggage comp capacity | ltr | 330-1150 | 330-1150 | 330-1150 |
| Air drag | Cd x A | 0.29 x 2.09 | 0.29 x 2.09 | 0.30 x 2.09 |
| Power Unit |  |  |  |  |
| Config/No of cyls/valves |  | Straight-four / 4 | Straight-four / 4 | Straight-four / 4 |
| Engine technology |  | Second-generation direct fuel injection (High Precision Injection) with lean burn mode |
| Capacity, effective | Cc | 1995 | 1599 | 1995 |
| Stroke / bore | Mm | 90 / 84 | 75.7 / 82 | 90 / 84 |
| Compression ratio | :1 | 12.0 | 12.0 | 12.0 |
| Fuel |  | RON 91-98 | RON 91-98 | RON 91-98 |
| Max output | kW/hp | 902) / 122 | 90 / 122 | 105 / 143 |
| at | rpm | 6 000 | 6 000 | 6000 |
| Max torque | Nm/lb-ft | 185/136 | 160/118 | 190/140 |
| at | rpm | 3000 – 4250 | 4250 | 4250 |
| Electrical System |  |  |  |  |
| Battery/location | Ah/– | 80 (70) / luggage comp | 80 (70) / luggage comp | 80 (70) / luggage comp |
| Alternator | A/W | 180 / 2520 | 180 / 2520 | 180 / 2520 |
| Driving Dynamics and Safety |  |
| Suspension, front |  | Double-joint tiebar spring strut axle, aluminium |
| Suspension, rear |  | Five-arm axle, lightweight steel |
| Brakes, front |  | Single-piston swing-calliper disc brakes |
| Diameter | mm | 284 x 22 / vented | 284 x 22 / vented | 292 x 22 / vented |
| Brakes, rear |  | Single-piston swing-calliper disc brakes |
| Diameter | mm | 280 x 10 | 280 x 10 | 296 x 10.5 |
| Driving stability systems |  | Standard: DSC incl ABS and DTC (Dynamic Traction Control), CBC Cornering Brake Control, DBC Dynamic Brake Control |
| Safety equipment |  | Standard: airbags for driver and front passenger (two-stage), side airbags for driver and front passenger, head airbags front and rear, three-point inertia-reel seat belts on all seats, with belt retainer, belt latch tensioner and belt force limiter at the front, crash sensors, Tyre Defect Indicator |
| Steering |  | Rack-and-pinion steering; 3.0 turns; EPS Electronic Power Steering |
| Steering transmission, overall | :1 | 16.0 | 16.0 | 16.0 |
| Tyres, front/rear |  | 195/55 R16 87H | 195/55 R16 87H | 195/55 R16 87H |
| Rims, front/rear |  | 6.5J x 16 steel | 6.5J x 16 steel | 6.5J x 16 steel |

Specifications BMW 1 Series Five-Door.

|  |  | BMW 116i | BMW 116i | BMW 118i |
| --- | --- | --- | --- | --- |
|  |  | (Germany, Romania) | (Other EU markets) |  |
| BMW ConnectedDrive |  |  |  |  |
| Comfort |  | Optional: BMW Assist including features such as enquiry service, remote-control function and V-Info+, BMW TeleServices, integration of mobile terminals |
| Infotainment |  | Optional: access to the internet, BMW Online including features such as Parkinfo, Nationalinfo, Google directory service, News, realtime weather, Office functions, BMW Routes and online music title update |
| Safety |  | Optional: Adaptive Headlights with Bending Lights, High-Beam Assistant, Park Distance Control, cruise control, Automatic/Enhanced Emergency Call |
| Transmission |  |  |  |  |
| Type of transmission |  | Six-speed manual gearbox (optional: six-speed automatic transmission) |
| Gear ratios I |  | 4.323 (4.171) | 4.323 (4.171) | 4.323 (4.171) |
| II |  | 2.456 (2.340) | 2.456 (2.340) | 2.456 (2.340) |
| III |  | 1.659 (1.521) | 1.659 (1.521) | 1.659 (1.521) |
| IV |  | 1.230 (1.143) | 1.230 (1.143) | 1.230 (1.143) |
| V |  | 1.000 (0.867) | 1.000 (0.867) | 1.000 (0.867) |
| VI |  | 0.848 (0.691) | 0.848 (0.691) | 0.848 (0.691) |
| Reverse |  | 3.938 (3.403) | 3.938 (3.403) | 3.938 (3.403) |
| Final drive | :1 | 3.380 (3.910) | 3.636 (4.100) | 3.385 (3.909) |
| Performance |  |  |  |  |
| Power-to-weight ratio | kg/kW | 14.2 (14.4) | 14.1 (14.3) | 12.1 (12.4) |
| Output per litre | kW/hp | 45.1/61.3 | 56.3/78.6 | 52.6/71.5 |
| Acceleration 0–100 km/h | sec | 9.9 (10.8) | 10.2 (11.2) | 8.8 (9.3) |
| Standing-start km | sec | 31.3 (30.0) | 31.4 (32.3) | 29.8 (30.2) |
| In 4th/5th gear 80–120 km/h | sec | 9.2/11.8 | 10.0/13.3) | 9.0/11.6 |
| Top speed | km/h | 204 (202) | 204 (202) | 210 |
| BMW EfficientDynamics |  |  |  |  |
| BMW EfficientDynamics standard features |  | Brake Energy Regeneration, Electronic Power Steering, Auto Start Stop and Gearshift Point Indicator (manual gearbox models), tyres with reduced roll resistance, intelligent lightweight technology, air flap control, map-controlled oil pump, a/c compressor detachable |
| Fuel Consump in EU Cycle |  |  |  |  |
| Urban | ltr/100 km | 7.9 (8.7) | 7.9 (8.9) | 7.9 (8.7) |
| Extra-urban | ltr/100 km | 5.1 (5.4) | 5.1 (5.5) | 5.1 (5.4) |
| Combined | ltr/100 km | 6.1 (6.6) | 6.1 (6.8) | 6.1 (6.6) |
| CO2 | g/km | 143 (154) | 143 (158) | 143 (154) |
| Emission rating |  | EU5 | EU5 | EU5 |

Specifications applicable to ACEA markets/homologation data applicable in part only to Germany (weight).

Figures in brackets apply to automatic transmission models.

1)  Oil change

2)  BMW 116i in Austria: 89 kW/121 hp