Specifications BMW X1.
X1 xDrive25i, X1 xDrive28i

|  |  | BMW X1 xDrive25i |  | BMW X1 xDrive28i |
| --- | --- | --- | --- | --- |
| Body |  |  |  |  |
| No of doors/seats |  | 5 / 5 |  | 5 / 5 |
| Length/width/height (unladen) | mm | 4454 / 1798 / 1545 |  | 4454 / 1798 / 1545 |
| Wheelbase | mm | 2760 |  | 2760 |
| Track, front/rear | mm | 1500 / 1529 |  | 1500 / 1529 |
| Turning circle | m | 11.8 |  | 11.8 |
| Tank capacity, approx | ltr | 63 |  | 63 |
| Cooling system incl heater | ltr | 8.5 |  | 8.5 |
| Engine oil1) | ltr | 6.5 |  | 6.5 |
| Weight, unladen, to DIN/EU | kg | 1600 / 1675 |  | 1610 / 1685 |
| Max load to DIN | kg | 550 |  | 550 |
| Max permissible | kg | 2180 |  | 2180 |
| Max axle load, front/rear | kg | 1030 / 1180 |  | 1030 / 1180 |
| Max trailer load (12%), braked/unbraked | kg | 2000 / 750 |  | 2000 / 750 |
| Max roofload/max download | kg | 75 / 80 |  | 75 / 80 |
| Luggage capacity | ltr | 420 – 1350 |  | 420 – 1350 |
| Air drag | cd x A | 0.33 x 2.34 |  | 0.33 x 2.34 |
| Power Unit |  |  |  |  |
| Config/No of cyls/valves |  | Straight / 6 / 4 |  | Straight / 6 / 4 |
| Engine technology |  | Fully variable valve management (VALVETRONIC), double-Vanos |
| Capacity, effective | cc | 2996 |  | 2996 |
| Stroke / bore | mm | 88.0 / 85.0 |  | 88.0 / 85.0 |
| Compression ratio | :1 | 10.7 |  | 10.7 |
| Fuel grade |  | min 91 RON |  | min 91 RON |
| Max output | kW/hp | 160 / 218 |  | 190 / 258 |
| at | rpm | 6100 |  | 6600 |
| Max torque | Nm/lb-ft | 280/207 |  | 310/228 |
| at | rpm | 2500 – 3500 |  | 2600 – 3000 |
| Electrical System |  |  |  |  |
| Battery/location | Ah/– | 80 / luggage comp |  | 80 / luggage comp |
| Alternator | A/W | 180 / 2520 |  | 180 / 2520 |
| Driving Dynamics and Safety |  |
| Suspension, front |  | Double-joint spring-strut thrust bar axle |
| Suspension, rear |  | Five-arm axle with longitudinal arm and double track control arm |
| Brakes, front |  | Single-piston swing-calliper disc brakes |  | Single-piston frame-calliper disc brakes |
| diameter | mm | 330 x 24 / vented |  | 348 x 30 / vented |
| Brakes, rear |  | Single-piston swing-calliper disc brakes |
| diameter | mm | 300 x 20 / vented |  | 336 x 22 / vented |
| Driving stability systems |  | Standard: DSC incl ABS and DTC Dynamic Traction Control, CBC Cornering Brake Control, DBC Brake Assistant, Dry Braking, Fading Compensation, Start-Off Assistant, DSC networked with xDrive, HDC Hill Descent Control, optional: Performance Control |
| Safety equipment |  | Standard: Airbags for driver and front passenger, side airbags for driver and front passenger, head airbags front and rear, three-point inertia-reel belts on all seats, with belt latch tensioner and belt force limiter at the front, crash sensors, Tyre Defect Indicator |
| Steering |  | Rack-and-pinion power steering, optional: Servotronic |
| Steering transmission, overall | :1 | 18.46 |  | 18.46 |
| Tyres, front/rear |  | 225/50 R17 94H |  | 225/50 R17 94H |
| Wheels, front/rear |  | 7.5J x 17 light-alloy |  | 7.5J x 17 light-alloy |

Specifications BMW X1.

|  |  | BMW X1 xDrive25i |  | BMW X1 xDrive28i |
| --- | --- | --- | --- | --- |
| BMW ConnectedDrive |  |  |  |  |
| Comfort |  | Optional: BMW Assist including Enquiry Service, remote control functions and V-Info+, BMW TeleServices, integration of mobile terminals |
| Infotainment |  | Optional: Access to the Internet, BMW Online including Parkinfo, National Info, Google directory search, news, realtime weather, office functions, BMW Routes and music title online update |
| Safety |  | Optional: Adaptive Headlights with Bending Lights, High-Beam Assistant, Park Distance Control, back-up camera, cruise control with brake function, automatic/enhanced emergency call function |
| Transmission |  |  |  |  |
| Type of transmission |  | Six-speed automatic |
| Gear ratios I | :1 | 4.065 |  | 4.065 |
| II | :1 | 2.371 |  | 2.371 |
| III | :1 | 1.551 |  | 1.551 |
| IV | :1 | 1.157 |  | 1.157 |
| V | :1 | 0.853 |  | 0.853 |
| VI | :1 | 0.674 |  | 0.674 |
| R | :1 | 3.200 |  | 3.200 |
| Final drive | :1 | 3.909 |  | 3.909 |
| Performance |  |  |  |  |
| Power-to-weight ratio | kg/kW | 10.0 |  | 8.5 |
| Output per litre | kW/hp | 53.4/72.6 |  | 63.4/86.2 |
| Acceleration 0–100 km/h | sec | 7.9 |  | 6.8 |
| standing start km | sec | 28.6 |  | 27.0 |
| In 4th/5th gear 80–120 km/h | sec | - |  | - |
| Top speed | km/h | 223 |  | 230 |
| Offroad Features |  |  |  |  |
| Overhang angle, front/rear | ° | 18.0/21.5 |  | 18.0/21.5 |
| Ramp angle | ° | 16.8 |  | 16.8 |
| Ground clearance, unladen | mm | 194 |  | 194 |
| BMW EfficientDynamics |  |  |  |  |
| BMW EfficientDynamics, standard |  | Brake Energy Regeneration, on-demand management of ancillary units, final drive with optimised warm-up behaviour, intelligent lightweight construction, oil pump with map control |
| Fuel Consumption in EU Cycle |  |  |  |  |
| Urban | ltr/100 km | 12.9 |  | 13.0 |
| Extra-urban | ltr/100 km | 7.2 |  | 7.3 |
| Combined | ltr/100 km | 9.3 |  | 9.4 |
| CO2 | g/km | 217 |  | 219 |
| Emission rating |  | EU5 |  | EU5 |

Specifications apply to ACEA markets/homologation data apply in part only to Germany (weight).

- Oil change