Specifications BMW 3 Series Convertible.
320d, 325d, 330d

|  |  | BMW 320d Convertible | BMW 325d Convertible | BMW 330d Convertible |
| --- | --- | --- | --- | --- |
| Body |  |  |  |  |
| No of doors / seats |  | 2 / 4 | 2 / 4 | 2 / 4 |
| Length/width/height (unladen) | mm | 4612 / 1782 / 1384 | 4612 / 1782 / 1384 | 4612 / 1782 / 1384 |
| Wheelbase | mm | 2760 | 2760 | 2760 |
| Track, front/rear | mm | 1500 / 1513 | 1500 / 1513 | 1500 / 1513 |
| Ground clearance |  | 138 | 138 | 138 |
| Turning circle | m | 11.0 | 11.0 | 11.0 |
| Tank capacity appr ltr | 61 | 61 | 61 |
| Cooling system incl heater | ltr | 7.2 (7.5) | 7.9 (8.2) | 7.9 (8.2) |
| Engine oil1) | ltr | 5.2 | 7.5 | 7.5 |
| Weight, unladen, to DIN/EU | kg | 1655 / 1730 (1670 / 1745) | 1740 / 1815 (1755 / 1830) | 1750 / 1825 (1765 / 1840) |
| Max load to DIN | kg | 430 | 430 | 430 |
| Max permissible | kg | 2085 (2100) | 2170 (2180) | 2180 (2195) |
| Max axle load, front / rear | kg | 920 / 1185 | 1005 / 1200 | 1005 / 1200 |
| Max trailer load (12%), braked / unbraked | kg | 1600 / 745 | 1800 / 750 | 1800 / 750 |
| Max roofload / max download | kg | - / 75 | - / 75 | - / 75 |
| Luggage comp | ltr | 210-350 | 210-350 | 210-350 |
| Air drag | cd x A | 0.28 x 2.08 | 0.28 x 2.08 | 0.28 x 2.08 |
| Power Unit |  |  |  |  |
| Configuration/No of cyls/valves |  | Straight-4 / 4 | Straight-6 / 4 | Straight-6 / 4 |
| Engine technology |  | Common-rail direct fuel injection, turbocharger with variable intake geometry | Common-rail direct fuel injection, turbocharger with variable intake geometry | Common-rail direct fuel injection, turbocharger with variable intake geometry |
| Capacity, effective | cc | 1995 | 2993 | 2993 |
| Stroke / bore | mm | 90.0 / 84.0 | 90.0 / 84.0 | 90.0 / 84.0 |
| Compression ratio | :1 | 16.5 | 16,5 | 16.5 |
| Fuel |  | Diesel | Diesel | Diesel |
| Max output | kW/hp | 135 / 184 | 150 / 204 | 180 / 245 |
| at | rpm | 4000 | 3750 | 4000 |
| Max torque | Nm/lb-ft | 380 / 280 | 430 / 317 | 520 / 383 |
| at | rpm | 1750-2750 | 1750 | 1750-3000 |
| Electrical System |  |  |  |  |
| Battery / installation | Ah/– | 90 (80) / luggage comp | 90 / luggage comp | 90 / luggage comp |
| Alternator | A/W | 180 / 2520 | 180 / 2520 | 180 / 2520 |
| Driving Dynamics and Safety |  |
| Suspension, front |  | Double-joint spring strut axle in aluminium with displaced castor, small positive steering roll radius, compensation of lateral forces, anti-dive |
| Suspension, rear |  | Five-arm axle in lightweight steel |
| Brakes, front |  | Single-piston swing-calliper disc brakes |
| Diameter | mm | 312 x 24 / vented | 330 x 24 / vented | 348 x 30 / vented |
| Brakes, rear |  | Single-piston swing-calliper disc brakes |
| Diameter | mm | 300 x 20 / vented | 336 x 22 / vented | 336 x 22 / vented |
| Driving stability systems |  | Standard: DSC incl ABS and DTC Dynamic Traction Control, CBC Cornering Brake Control, DBC Brake Assistant, BMW 325d and BMW 330d also with Dry Braking, Fading Compensation, Start-Off Assistant |
| Safety |  | Standard: airbags for driver and front passenger, side airbags for driver and front passenger with combined head airbags, three-point inertia-reel belts on all seats, integrated on front seats with belt retainer, belt latch tensioner and belt force limiter, crash-activated headrests at the front, crash sensors, rollover safety system, Tyre Defect Indicator |
| Steering |  | Electric Power Steering |
| Steering ratio, overall | :1 | 16.0 | 16.0 | 16.0 |
| Tyres, front/rear |  | 225/45 R17 91W RSC | 225/45 R17 91W RSC | 225/45 R17 91Y RSC |
| Wheels, front/rear |  | 8J x 17 light-alloy | 8J x 17 light-alloy | 8J x 17 light-alloy |

Specifications BMW 3 Series Convertible.

|  |  | BMW 320d Convertible | BMW 325d Convertible Convertible Cabrio | BMW 330d Convertible |
| --- | --- | --- | --- | --- |
| BMW ConnectedDrive |  |  |  |  |
| Comfort |  | Optional: BMW Assist incl Enquiry Service, remote control functions and V- Info+, BMW TeleServices, integration of mobile terminals |
| Infotainment |  | Optional: access to the internet, BMW Online incl Parkinfo, National Info, Google directory search, news, realtime weather, BMW Routes, office functions, Bluetooth audio streaming and music title update online |
| Safety |  | Optional: Adaptive Headlights with Bending Lights, High-Beam Assistant, Park Distance Control, cruise control, automatic/enhanced emergency call function |
| Transmission |  |  |  |  |
| Type of transmission |  | Six-speed manual (optional: six-speed automatic) |
| Gear ratios I | :1 | 4.110 (4.171) | 5.080 (4.171) | 5.080 (4.171) |
| II | :1 | 2.248 (2.340) | 2.804 (2.340) | 2.804 (2.340) |
| III | :1 | 1.403 (1.521) | 1.783 (1.521) | 1.783 (1.521) |
| IV | :1 | 1.000 (1.143) | 1.260 (1.143) | 1.260 (1.143) |
| V | :1 | 0.802 (0.867) | 1.000 (0.867) | 1.000 (0.867) |
| VI | :1 | 0.659 (0.691) | 0.835 (0.691) | 0.835 (0.691) |
| R | :1 | 3.727 (3.403) | 4.607 (3.403) | 4.607 (3.403) |
| Final drive | :1 | 3.385 (3.154) | 2.471 (2.929) | 2.471 (2.929) |
| Performance |  |  |  |  |
| Power-to-weight ratio | kg/kW | 12.3 (12.4) | 11.6 (11.7) | 9.7 (9.8) |
| Output per litre | kW/hp | 67.7 / 92.1 | 50.1 / 68.1 | 60.1 / 81.7 |
| Acceleration 0–100 km/h | sec | 8.3 (8.4) | 7.5 (7.6) | 6.4 (6.5) |
| standing-start | sec | 29.1 (29.3) | 28.0 (28.1) | 26.5 (26.7) |
| In 4th/5th gear 80–120 km/h | sec | 6.6 / 8.4 (-) | 6.3 / 7.9 (-) | 5.2 / 6.6 (-) |
| Top speed | km/h | 228 (226) | 238 (236) | 250 |
| BMW EfficientDynamics |  |  |  |  |
| BMW EfficientDynamics, standard features |  | Brake Energy Regeneration, Auto Start Stop (on BMW 320d manual), gearshift point indicator (manual gearbox models), Electric Power Steering, on-demand management of ancillary units, intelligent lightweight construction, tyres with reduced roll resistance, a/c compressor detachable |
| Fuel Consump in EU Cycle |  |  |  |  |
| Urban | ltr/100km | 6.3 (7.1) | 7.7 (8.2) | 7.7 (8.2) |
| Extra-urban | ltr/100km | 4.4 (4.7) | 5.2 (5.4) | 5.2 (5.4) |
| Combined | ltr/100km | 5.1 (5.6) | 6.1 (6.4) | 6.1 (6.4) |
| CO2 | g/km | 135 (149) | 160 (168) | 162 (170) |
| Emission rating |  | EU5 | EU5 | EU5 |

Specifications apply to ACEA markets/data relevant to homologation apply in part only to Germany (weight)

Figures in brackets apply to models with automatic transmission

1)  Oil change