Specifications BMW 3 Series Convertible.
325i, 330i, 335i

|  |  | BMW 325i Convertible | BMW 330i Convertible | BMW 335i Convertible |
| --- | --- | --- | --- | --- |
| Body |  |  |  |  |
| No of doors / seats |  | 2 / 4 |  | 2 / 4 |
| Length/width/height (unladen) | mm | 4612 / 1782 / 1384 | 4612 / 1782 / 1384 | 4612 / 1782 / 1384 |
| Wheelbase | mm | 2760 | 2760 | 2760 |
| Track, front/rear | mm | 1500 / 1513 | 1500 / 1513 | 1500 / 1507 |
| Ground clearance |  | 138 | 138 | 138 |
| Turning circle | m | 11.0 | 11.0 | 11.0 |
| Tank capacity appr ltr ca. l | 63 | 63 | 63 |
| Cooling system incl heater | ltr | 8.2 (8.5) | 8.2 (8.5) | 8.2 (8,5) |
| Engine oil1) | ltr | 6.5 | 6.5 | 6.5 |
| Weight, unladen, to DIN/EU | kg | 1655 / 1730 (1685 / 1760) | 1705 / 1780 (1720 / 1795) | 1735 / 1810 (1750 / 1825) |
| Max load to DIN | kg | 430 | 430 | 430 |
| Max permissible | kg | 2085 (2115) | 2135 (2150) | 2165 (2180) |
| Max axle load, front / rear | kg | 945 / 1180 | 960 / 1200 | 990 / 1200 |
| Max trailer load (12%), braked / unbraked | kg | 1600 / 745 | 1700 / 750 | 1700 / 750 |
| Max roofload / max download | kg | - / 75 | - / 75 | - / 75 |
| Luggage comp | ltr | 210-350 | 210-350 | 210-350 |
| Air drag | cd x A | 0.28 x 2.08 | 0.28 x 2.08 | 0.31 x 2.08 |
| Power Unit |  |  |  |  |
| Configuration/No of cyls/valves |  | Straight-6 / 4 | Straight-6 / 4 | Straight-6 / 4 |
| Engine technology |  | Second-generation direct fuel injection (High Precision Injection) with lean burn | Second-generation direct fuel injection (High Precision Injection) with lean burn | BMW TwinPower Turbo, second-generation direct fuel injection (High Precision Injection), fully variable valve management (VALVETRONIC) |
| Capacity, effective | cc | 2996 | 2996 | 2979 |
| Stroke / bore | mm | 88.0 / 85.0 | 88.0 / 85.0 | 89.6 / 84.0 |
| Compression ratio | :1 | 12.0 | 12.0 | 10.2 |
| Fuel |  | min 91 RON | min 91 RON | min 91 RON |
| Max output | kW/hp | 160 / 218 | 200 / 272 | 225 / 306 |
| at | rpm | 6100 | 6700 | 5800 |
| Max torque | Nm/lb-ft | 270 / 200 | 320 / 236 | 400 / 295 |
| at | rpm | 2400-4200 | 2750-3000 | 1200-5000 |
| Electrical System |  |  |  |  |
| Battery / installation | Ah/– | 90 / luggage compartment | 90 / luggage comp | 90 (80) / luggage comp |
| Alternator | A/W | 180 / 2520 | 180 / 2520 | 180 / 2520 |
| Driving Dynamics and Safety |  |
| Suspension, front |  | Double-joint spring strut axle in aluminium with displaced castor, small positive steering roll radius, compensation of lateral forces, anti-dive |
| Suspension, rear |  | Five-arm axle in lightweight steel |
| Brakes, front |  | Single-piston swing-calliper disc brakes |
| Diameter | mm | 330 x 24 / vented | 348 x 30 / vented | 348 x 30 / vented |
| Brakes, rear |  | Single-piston swing-calliper disc brakes |
| Diameter | mm | 300 x 20 / vented | 336 x 22 / vented | 336 x 22 / vented |
| Driving stability systems |  | Standard: DSC incl ABS and DTC Dynamic Traction Control, CBC Cornering Brake Control, DBC Brake Assistant, Dry Braking, Fading Compensation, Start-Off Assistant |
| Safety |  | Standard: airbags for driver and front passenger, side airbags for driver and front passenger with combined head airbags, three-point inertia-reel belts on all seats, integrated on front seats with belt retainer, belt latch tensioner and belt force limiter, crash-activated headrests at the front, crash sensors, rollover safety system, Tyre Defect Indicator |
| Steering |  | Electric Power Steering | Hydraulic rack-and-pinion power steering |
| Steering ratio, overall | :1 | 16.0 | 16.0 | 16.0 |
| Tyres, front/rear |  | 225/45 R17 91W RSC | 225/45 R17 91Y RSC | 225/45 R17 91W RSC / 255/40 R17 94W RSC |
| Wheels, front/rear |  | 8J x 17 light-alloy | 8J x 17 light-alloy | 8J/8.5J x 17 light-alloy |

Specifications BMW 3 Series Convertible.

|  |  | BMW 325i Convertible | BMW 330i Convertible | BMW 335i Convertible |
| --- | --- | --- | --- | --- |
| BMW ConnectedDrive |  |  |  |  |
| Comfort |  | Optional: BMW Assist incl Enquiry Service, remote control functions and V- Info+, BMW TeleServices, integration of mobile terminals |
| Infotainment |  | Optional: access to the internet, BMW Online incl Parkinfo, National Info, Google directory search, news, realtime weather, BMW Routes, office functions, Bluetooth audio streaming and music title update online |
| Safety |  | Optional: Adaptive Headlights with Bending Lights, High-Beam Assistant, Park Distance Control, cruise control, automatic/enhanced emergency call function |
| Transmission |  |  |  |  |
| Type of transmission |  | Six-speed manual (optional: six-speed automatic, BMW 335i: seven-speed double-clutch) |
| Gear ratios I | :1 | 4.323 (4.171) | 4.350 (4.171) | 4.110 (4.780) |
| II | :1 | 2.456 (2.340) | 2.496 (2.340) | 2.315 (3.056) |
| III | :1 | 1.659 (1.521) | 1.665 (1.521) | 1.542 (2.153) |
| IV | :1 | 1.230 (1.143) | 1.230 (1.143) | 1.179 (1.678) |
| V | :1 | 1.000 (0.867) | 1.000 (0.867) | 1.000 (1.390) |
| VI | :1 | 0.848 (0.691) | 0.851 (0.691) | 0.846 (1.203) |
| VII | :1 |  |  | (1.000) |
| R | :1 | 3.938 (3.403) | 3.926 (3.403) | 3.727 (4.454) |
| Final drive | :1 | 3.154 (3.636) | 3.154 (3.727) | 3.154 (2.563) |
| Performance |  |  |  |  |
| Power-to-weight ratio | kg/kW | 10.3 (10.5) | 8.5 (8.6) | 7.7 (7.8) |
| Output per litre | kW/hp | 53.4 / 72.6 | 66.8 / 90.8 | 75.5 / 102.7 |
| Acceleration 0–100 km/h | sec | 7.6 (8.1) | 6.5 (6.7) | 5.8 (5.7) |
| standing-start | sec | 28.1 (28.5) | 26.4 | 25.2 (25.1) |
| In 4th/5th gear 80–120 km/h | sec | 8.3 / 10.5 (-) | 7.1 / 9.0 (-) | 5.9 / 6.9 (-) |
| Top speed | km/h | 245 (243) | 250 | 250 |
| BMW EfficientDynamics |  |  |  |  |
| BMW EfficientDynamics. standard features |  |  |  |  |
|  |  | Brake Energy Regeneration, gearshift point indicator (manual gearbox models), Electric Power Steering (BMW 325i and BMW 330i), on-demand management of ancillary units, intelligent lightweight construction, tyres with reduced roll resistance, oil pump with map control, a/c compressor detachable |
| Fuel Consump in EU Cycle |  |  |  |  |
| Urban | ltr/100km |  |  |  |
| Extra-urban | ltr/100km | 10.2 (10.6) | 10.5 (11.1) | 12.4 (12.2) |
| Combined | ltr/100km | 5.9 (6.3) | 6.2 (6.5) | 6.7 (6.8) |
| CO2 | g/km | 7.5 (7.9) | 7.8 (8.2) | 8.8 (8.8) |
| Emission rating |  | 176 (185) | 182 (190) | 205 (205) |
|  |  | EU5 | EU5 | EU5 |

Specifications apply to ACEA markets/data relevant to homologation apply in part only to Germany (weight)

Figures in brackets apply to models with automatic transmission

1)  Oil change