Specifications MINI Cooper. (May 2007)

| Body d Anzahl Türen / s |  | MINI Cooper | MINI Cooper Automatic |  |
| --- | --- | --- | --- | --- |
| No of doors/seats L |  | 3/4 | 3/4 |  |
| Length/width/height (unladen) ) | mm | 3699/ 1683 / 1407 | 3699 / 1683 / 1407 |  |
| Wheelbase | mm | 2 467 | 2 467 |  |
| Track front/rear wgsdfg | mm | 1459 / 1467 | 1459 / 1467 |  |
| Turning circle | m | 10,07 | 10,07 |  |
| Fuel tank capacity | approx. ltr | 40 | 40 |  |
| Cooling system including heater l | ltr | 5,2 | 5,2 |  |
| Engine oil Getriebeöl | ltr | 4,2 | 4,2 |  |
| Transmission fluid incl final drive | ltr | Permanent filling | Permanent filling |  |
| Weight, unladen, according to DIN/EU1 | kg | 1065 / 1140 | 1105 / 1180 |  |
| Max load according to DIN | kg | 450 | 450 |  |
| Max permissible weight to DIN | kg | 1515 | 1550 |  |
| Max permissible axle load front/rear | kg | 855 / 740 | 855 / 740 |  |
| Max permissible trailer load |  |  |  |  |
| braked (12%)/unbraked | kg | 750 / 500 | 750 / 500 |  |
| Max roof load / max towbar download | kg | 75 / 50 | 75 / 50 |  |
| Luggage compartment according to DIN | l | 160-680 | 160-680 |  |
| Air resistance | cX x A | 0,33 x 1,97 | 0,33 x 1,97 |  |
| Engine |  |  |  |  |
| Configuration/No of cylinders/valves Zylinder/Ventile |  | Inline/ 4/ 4 | Inline / 4/ 4 |  |
| Engine management |  | MEV 17.2 | MEV 17.2 |  |
| Capacity | cc | 1598 | 1598 |  |
| Bore/stroke | mm | 77 / 85,8 | 77 / 85,8 |  |
| Compression ratio | :1 | 11:1 | 11:1 |  |
| Fuel | RON | From 91 ROZ | From 91 ROZ |  |
| Max output | kW/bhp | 88 / 120 | 88 / 120 |  |
| at | rpm | 6 000 | 6 000 |  |
| Max torque | Nm | 160 | 160 |  |
| at | rpm | 4 000 | 4 000 |  |
| Electrical system |  |  |  |  |
| Battery/installation | Ah/– | 46 / in front | 55 / in front |  |
| Alternator | A/W | 120 / 1680 | 120 / 1680 |  |
| Chassis and suspension |  |  |  |  |
| Front suspension | Singe-joint Mc Pherson spring strut axle with anti-dive |  |
| Rear suspension | Longitudinal struts with centrally-pivoted control arms, Z-axle |  |
| Brake, front |  | Disc, vented | Disc, vented |  |
| Diameter | mm | 280 | 280 |  |
| Brake, rear |  | Disc brake | Disc brake |  |
| Diameter | mm | 259 | 259 |  |
| Driving stability systems | Hydraulic two-circuit brake system with anti-lock brakes (ABS), Electronic Brake Force Distribution (EBD), Cornering Brake Control (CBC) and Brake Assistant. Optional: ASC+T traction control, Dynamic Stability Control (DSC) with Hill Start Assistant, Limited-slip differential. EHPAS |  |
| Steering | Electric power steering (EPS)) |  |
| Overall transmission ratio | :1 | 14,1 | 14,1 |  |
| Type of transmission |  | 6-gear-maunal | 6-gear-automatic |  |
| Gear ratios I | :1 | 3,214 | 4,148 |  |
| II | :1 | 1,792 | 2,370 |  |
| III | :1 | 1,194 | 1,556 |  |
| IV | :1 | 0,914 | 1,155 |  |
| V | :1 | 0,784 | 0,859 |  |
| VI | :1 | 0,683 | 0,686 |  |
| R | :1 | 3,143 | 3,394 |  |
| Final drive ratio | :1 | 4,353 | 4,103 |  |
| Tyres |  | 175 / 65 R15 84H | 175 / 65 R15 84H |  |
| Wheels |  | 5,5Jx15 Alloy | 5,5Jx15 Alloy |  |
| Performance |  |  |  |  |
| Power-to-weight ratio, DIN | kg/kW | 12,1 | 12,6 |  |
| Output per litre | kW/ltr | 55,1 | 55,1 |  |
| Acceleration 0–62 mph | s | 9,1 | 10,4 |  |
| 0–1000 m | s | 30,3 | 31,4 |  |
| in 4th/5th gear 50–75 mph | s | 9,6 / 12,1 | - |  |
| Top speed | km/h | 203 | 197 |  |
| Consumption in the EU cycle |  |  |  |  |
| Urban | ltr/100 km | 6.9 | 9,1 |  |
| Extra-urban | ltr/100 km | 4,5 | 5,0 |  |
| Combined | ltr/100 km | 5,4 | 6,5 |  |
| CO2 | g/km | 129 | 156 |  |
| Miscellaneous |  |  |  |  |
| Emission category | – | EU4 | EU4 |  |
| Ground clearance | mm | 139 | 139 |  |