Specifications MINI Cooper D. (May 2007)

| Body d Anzahl Türen / s |  | MINI Cooper D | MINI Cooper D Automatic |  |
| --- | --- | --- | --- | --- |
| No of doors/seats L |  | 3/4 | 3/4 |  |
| Length/width/height (unladen) ) | mm | 3709 / 1683/ 1407 | 3709 / 1683/ 1407 |  |
| Wheelbase | mm | 2 467 | 2 467 |  |
| Track front/rear wgsdfg | mm | 1459 / 1467 | 1459 / 1467 |  |
| Turning circle | m | 10,7 | 10,7 |  |
| Fuel tank capacity | approx. ltr | 40 | 40 |  |
| Cooling system including heater l | ltr | 5,4 | 5,4 |  |
| Engine oil Getriebeöl | ltr |  |  |  |
| Transmission fluid incl final drive | ltr | Permanent filling | Permanent filling |  |
| Weight, unladen, according to DIN/EU1 | kg | 1090 / 1165 | 1120 / 1195 |  |
| Max load according to DIN | kg | 450 | 450 |  |
| Max permissible weight to DIN | kg | 1540 | 1570 |  |
| Max permissible axle load front/rear | kg | 885 / 720 | 885 / 720 |  |
| Max permissible trailer load |  |  |  |  |
| braked (12%)/unbraked | kg | 750 / 500 | 750 / 500 |  |
| Max roof load / max towbar download | kg | 75 / 50 | 75 / 50 |  |
| Luggage compartment according to DIN | l | 160-680 | 160-680 |  |
| Air resistance | cX x A | 0,32 x 1,97 | 0,32 x 1,97 |  |
| Engine |  |  |  |  |
| Configuration/No of cylinders/valves Zylinder/Ventile |  | Inline/ 4/ 4 | Inline/ 4/ 4 |  |
| Engine management |  | DDE 6.08 | DDE 6.08 |  |
| Capacity | cc | 1560 | 1560 |  |
| Bore/stroke | mm | 75 / 88,3 | 75 / 88,3 |  |
| Compression ratio | :1 | 18:1 | 18:1 |  |
| Fuel |  | Diesel | Diesel |  |
| Max output | kW/bhp | 80/ 110 | 80/ 110 |  |
| at | rpm | 4 000 | 4 000 |  |
| Max torque | Nm | 240 | 240 |  |
| at | rpm | 1750-2000 | 1750-2000 |  |
| Electrical system |  |  |  |  |
| Battery/installation | Ah/– | 70 / front | 70 / front |  |
| Alternator | A/W | 154/ 2156 | 154/ 2156 |  |
| Chassis andsuspension |  |  |  |  |
| Front suspension | Singe-joint Mc Pherson spring strut axle with anti-dive |  |
| Rear suspension | Longitudinal struts with centrally-pivoted control arms, Z-axle |  |
| Brake, front |  | Disc, vented | Disc, vented |  |
| Diameter | mm | 280 | 280 |  |
| Brake, rear |  | Disc brake | Disc brake |  |
| Diameter | mm | 259 | 259 |  |
| Driving stability systems | Hydraulic two-circuit brake system with anti-lock brakes (ABS), Electronic Brake Force Distribution (EBD), Cornering Brake Control (CBC) and Brake Assistant. Optional: ASC+T traction control, Dynamic Stability Control (DSC) with Hill Start Assistant, Limited-slip differential. . EHPAS |  |
| Steering | Electric power steering (EPS |  |
| Overall transmission ratio | :1 | 14,1 | 14,1 |  |
| Type of transmission |  | 6-gear-maunal | 6-gear-automatic |  |
| Gear ratios I | :1 | 3,308 | 4,044 |  |
| II | :1 | 1,870 | 2,371 |  |
| III | :1 | 1,194 | 1,556 |  |
| IV | :1 | 0,872 | 1,159 |  |
| V | :1 | 0,721 | 0,852 |  |
| VI | :1 | 0,596 | 0,672 |  |
| R | :1 | 3,231 | 3,193 |  |
| Final drive ratio | :1 | 3,706 | 3,683 |  |
| Tyres |  | 175/65 R15 84H | 175/65 R15 84H |  |
| Wheels |  | 5,5Jx15 Alloy | 5,5Jx15 Alloy |  |
| Performance |  |  |  |  |
| Power-to-weight ratio, DIN | kg/kW | 13,6 | 14,0 |  |
| Output per litre | kW/ltr | 51,3 | 51,3 |  |
| Acceleration 0–62 mph | s | 9,9 | 10,3 |  |
| 0–1000 m | s | 32,3 | 32,5 |  |
| in 4th/5th/6th gear 50–75 mph | s | 7,4 / 9,5 | - |  |
| Top speed | km/h | 195 | 190 |  |
| Consumption in the EU cycle |  |  |  |  |
| Urban | ltr/100 km | 4,7 | 6,5 |  |
| Extra-urban | ltr/100 km | 3,5 | 4,2 |  |
| Combined | ltr/100 km | 3,9 | 5,0 |  |
| CO2 | g/km | 104 | 134 |  |
| Miscellaneous |  |  |  |  |
| Emission category | – | EU4 | EU4 |  |
| Ground clearance | mm | 139 | 139 |  |