Specifications BMW 1 Series Five-Door.
120d, 123d

|  |  | BMW 120d |  | BMW 123d |
| --- | --- | --- | --- | --- |
| Body |  |  |  |  |
| No of doors/seats |  | 5 / 5 |  | 5 / 5 |
| Length/width/height (unladen) | mm | 4239 / 1748 / 1421 |  | 4239 / 1748 / 1421 |
| Wheelbase | mm | 2660 |  | 2660 |
| Track, front/rear | mm | 1480 / 1493 |  | 1474/ 1487 |
| Ground clearance | mm | 145 |  | 145 |
| Turning circle | m | 10.7 |  | 10.7 |
| Tank capacity | app ltr | 51 |  | 51 |
| Cooling system incl heater | ltr | 7.2 (7.5) |  | 7.2 (7.5) |
| Engine oil1) | ltr | 5.5 |  | 5.5 |
| Weight, unladen, to DIN/EU | kg | 1375 / 1450 |  | 1420 / 1495 |
| Max load to DIN | kg | 500 |  | 500 |
| Max permissible | kg | 1875 |  | 1920 |
| Max axle load, front/rear | kg | 905 / 1050 |  | 920 / 1060 |
| Max trailer load (12%), braked/unbraked | kg | 1200 / 720 |  | 1200 / 740 |
| Max roofload/max towbar downl | kg | 75 / 75 |  | 75 / 75 |
| Luggage comp capacity | ltr | 330-1150 |  | 330-1150 |
| Air drag | Cd x A | 0.30 x 2.09 |  | 0.31 x 2.09 |
| Power Unit |  |  |  |  |
| Power Unit |  |  |  |  |
| Config/No of cyls/valves |  | Straight-four / 4 |  | Straight-four / 4 |
| Engine technology |  | Common-rail direct injection, turbocharger with variable intake geometry |  | Common-rail direct injection, BMW TwinPower Turbo (Variable Twin Turbo) |
| Capacity, effective | cc | 1995 |  | 1995 |
| Stroke / bore | mm | 90/84 |  | 90/84 |
| Compression ratio | :1 | 16.0 |  | 16.0 |
| Fuel |  | Diesel |  | Diesel |
| Max output | kW/hp | 130 / 177 |  | 150 / 204 |
| at | rpm | 4000 |  | 4400 |
| Max torque | Nm/lb-ft | 350/258 |  | 400/295 |
| at | rpm | 1750-3000 |  | 2000-2250 |
| Electrical System |  |  |  |  |
| Battery/location | Ah/– | 80 / luggage comp |  | 80 / luggage comp |
| Alternator | A/W | 180 / 2520 |  | 180 / 2520 |
| Driving Dynamics and Safety |  |
| Suspension, front |  | Double-joint tiebar spring strut axle, aluminium |
| Suspension, rear |  | Five-arm axle, lightweight steel |
| Brakes, front |  | Single-piston swing-calliper disc brakes |
| Diameter | mm | 300 x 24 / vented |  | 330 x 24 / vented |
| Brakes, rear |  | Single-piston swing-calliper disc brakes |
| Diameter | mm | 300 x 20 / vented |  | 300 x 20 / vented |
| Driving stability systems |  | Standard: DSC incl ABS and DTC (Dynamic Traction Control), CBC Cornering Brake Control, DBC Dynamic Brake Control, BMW 123d with electronic locking function on the rear axle differential |
| Safety equipment |  | Standard: airbags for driver and front passenger (two-stage), side airbags for driver and front passenger, head airbags front and rear, three-point inertia-reel seat belts on all seats, with belt retainer, belt latch tensioner and belt force limiter at the front, crash sensors, Tyre Defect Indicator |
| Steering |  | Rack-and-pinion steering; 3.0 turns; EPS Electronic Power Steering |
| Steering transmission, overall | :1 | 16.0 |  | 16.0 |
| Tyres, front/rear |  | 205/55 R16 87V |  | 205/50 R17 89W RSC |
| Rims, front/rear |  | 7J x 16 steel |  | 7J x 17 light-alloy |

Specifications BMW 1 Series Five-Door.

|  |  | BMW 120d |  | BMW 123d |
| --- | --- | --- | --- | --- |
| BMW ConnectedDrive |  |  |  |  |
| Comfort |  | Optional: BMW Assist including features such as enquiry service, remote-control function and V-Info+, BMW TeleServices, integration of mobile terminals |
| Infotainment |  | Optional: access to the internet, BMW Online including features such as Parkinfo, Nationalinfo, Google directory service, News, realtime weather, Office functions, BMW Routes and online music title update |
| Safety |  | Optional: Adaptive Headlights with Bending Lights, High-Beam Assistant, Park Distance Control, cruise control, Automatic/Enhanced Emergency Call |
| Transmission |  |  |  |  |
| Type of transmission |  | Six-speed manual (optional: six-speed automatic transmission) |
| Gear ratios I | :1 | 5.140 (4.171) |  | 5.080 (4.171) |
| II | :1 | 2.830 (2.340) |  | 2.804 (2.340) |
| III | :1 | 1.804 (1.521) |  | 1.783 (1.521) |
| IV | :1 | 1.257 (1.143) |  | 1.260 (1.143) |
| V | :1 | 1.000 (0.867) |  | 1.000 (0.867) |
| VI | :1 | 0.831 (0.691) |  | 0.835 (0.691) |
| Reverse | :1 | 4.638 (3.403) |  | 4.607 (3.403) |
| Final drive | :1 | 2.563 (3.154) |  | 2.813 (3.154) |
| Performance |  |  |  |  |
| Power-to-weight ratio | kg/kW | 10.6 |  | 9.5 |
| Output per litre | kW/hp | 65.2 |  | 75.2 |
| Acceleration 0–100 km/h | sec | 7.6 (7.8) |  | 7.0 (7.1) |
| Standing-start km | sec | 28.2 (28.1) |  | 27.3 (27.1) |
| In 4th/5th gear 80–120 km/h | sec | 6.4/8.0 |  | 5.5/6.6 |
| Top speed | km/h | 228 (226) |  | 238 (236) |
| BMW EfficientDynamics |  |  |  |  |
| BMW EfficientDynamics standard features |  | Brake Energy Regeneration, Electronic Power Steering, Auto Start Stop and Gearshift Point Indicator (manual gearbox models), tyres with reduced roll resistance, intelligent lightweight technology, air flap control, map-controlled oil pump, a/c compressor detachable |
| Fuel Consump in EU Cycle |  |  |  |  |
| Urban | ltr/100 km | 6.1 (7.2) |  | 6.5 (7.3) |
| Extra-urban | ltr/100 km | 4.1 (4.4) |  | 4.4 (4.6) |
| Combined | ltr/100 km | 4.8 (5.4) |  | 5.2 (5.6) |
| CO2 | g/km | 128 (144) |  | 138 (148) |
| Emission rating |  | EU5 |  | EU5 |

Specifications applicable to ACEA markets/homologation data applicable in part only to Germany (weight).

Figures in brackets apply to automatic transmission models.

1)  Oil change