BMW 650i
Contents.

1.	BMW 650i
Coupé and Convertible get a new 8-cylinder Power Unit. 	 2

2. 	Technical Specifications. 	 4

1.	BMW 650i:                                                      New 270kW V8 Power Unit for Coupe & Convertible

BMW’s new 4.8-litre eight-cylinder developing a maximum output of 
270 kW, and just released in the new BMW 550i, has already made a great name for itself in the BMW 750i. Now this new power unit, developing maximum torque of 490 Nm, is available in the BMW 6 Series Coupé and Convertible. The two new BMW 650i models replace the BMW 645Ci.

Even better performance, similar fuel consumption.

Featuring 25 kW more power and an increase in torque of 40 Nm give BMW’s two large sports cars even more dynamic performance and supremacy on the road: The new BMW 650i Coupé accelerates from standstill to 100 km/h in 5.4 seconds, while its open-air counterpart completes the same exercise in 5.7 seconds.

Passing another vehicle in fourth gear of the six-speed manual gearbox featured as standard (an optional six-speed Steptronic automatic transmission is available) takes the 650i Coupé just 4.7 seconds, with the 650i Convertible requiring only 0.2 seconds more. Top speed of both models is limited electronically to 250 km/h.

Despite its remarkable performance, the new eight-cylinder coupé consumes just 11.9 litres of fuel per 100 kilometres, while the corresponding figure on the 650i Convertible is 12.9 litres/100 km.

Best-in-class up to 5.0 litres.

Offering truly outstanding power and performance, the 650i featuring BMW VALVETRONIC and double-VANOS, ensures exceptional engine response and rapid reaction in all driving situations, offering ample power and performance reserves whenever and wherever required.

Again reflecting that typical BMW style, the eight-cylinder revs up quickly and smoothly like a turbine, giving both the driver and the passengers an extremely sporting and dynamic driving experience based on supreme agility and nimble handling.

From outside both of the new models remain very discreet in showing how new they really are: Only two new exterior colours – Monaco Blue and 
Barbera Red – as well as a new 19-inch wheel design with different-sized tyres (245/40 R 19 at the front, 275/35 R 19 at the rear) show the connoisseur 
that these are indeed BMW’s new 650i models.

A further sign of distinction underlining the two cars’ powerful look is the wider track at the rear, up by 8 millimetres.

Moving on to the elegant but sporting interior, the colour world now in black replacing the former grey colour scheme, the new design of the iDrive 
Controller as well as start/stop button on the instrument panel are the most striking points. Comfort Access comes as an option.

It almost goes without saying that the two new BMW 650i models feature BMW’s latest generation of DSC Dynamic Stability Control offering the driver a whole range of new safety functions such as Hill Start Assist, Brake Standby 
in dangerous situations, Dry Braking in the wet, Fading Compensation and Soft-Stop.

Pricing

BMW 650i Coupe						R751 000.00

BMW 650i Coupe Steptronic					R765 400.00

BMW 650i Convertible					R826 500.00

BMW 650i Convertible Steptronic				R840 900.00

###

For media enquiries

Guy Kilfoil

Manager: Automotive Communications

Email: guy.kilfoil@bmw.co.za

Tel: +2712 522 2227

Fax: +2711 805 2775

Mobile: +2782 583 6262

www.press.bmwgroup.com

www.quickpic.co.za

www.bmw.co.za

2. Technical Specifications

| Body |  | 650i Coupe | 650i Convertible |
| --- | --- | --- | --- |
| No. of doors/seats L |  | 2/2 + 2 | 2/2 + 2 |
| Length/width/height (unladen) ) | mm | 4,820/1,855/1,373 | 4,820/1,855/1,373 |
| Wheelbase | mm | 2,780 | 2,780 |
| Track, front/rear | mm | 1,558/1,592 | 1,558/1,592 |
| Turning circle | m | 11.4 | 11.4 |
| Tank capacity | approx ltr | 70 | 70 |
| Cooling system incl heater | ltr | 14.2 | 14.2 |
| Engine oil | ltr | 8.0 | 8.0 |
| Transmission fluid | ltr | 1.8 | 1.8 |
| Final drive fluid | ltr | 1.2 | 1.2 |
| Weight, unladen, to DIN1 | kg | 1,640 | 1,850 |
| Max. load to DIN | kg | 450 | 400 |
| Max. permissible weight to DIN | kg | 2,090 | 2,250 |
| Max. axle load front/rear | kg | 1,060/1,170 | 1,100/1,270 |
| Max. trailer load |  |  |  |
| braked (12%); unbraked | kg | – | – |
| Max. roofload/max towbar download | kg | – | – |
| Luggage comp to VDA | ltr | 450 | 300-350 |
| Air resistance | cX x A | 0.29 x 2.15 | 0.29 x 2.15 |
| Engine |  |  |  |
| Configuration/No. of cyls/valves |  | V 90/8/4 | V 90/8/4 |
| Engine management |  | Bosch ME 9.2.1 | Bosch ME 9.2.1 |
| Capacity | cc | 4,799 | 4,799 |
| Bore/stroke | mm | 92.0/82.7 | 92.0/82.7 |
| Compression ratio | :1 | 10.5 | 10.5 |
| Fuel grade | RON | 91–98 | 91–98 |
| Max. output | kW | 270 | 270 |
| at speed | rpm | 6,300 | 6,300 |
| Torque | Nm | 490 | 490 |
| at speed | Rpm | 3,400 – 3,750 | 3,400 – 3,750 |
| Electrical system |  |  |  |
| Battery/installation | Ah/– | 110/luggage comp | 110/luggage comp |
| Alternator | A/W | 170/2,380 | 170/2,380 |
| Chassis and suspension |  |  |  |
| Suspension, front |  | Double-joint spring strut axle with track control arms and tiebars |
| Suspension, rear |  | Integral axle |
| Brakes, front |  | Single-piston swing-calliper disc brakes |
| Diameter | mm | 348, vented | 348, vented |
| Brakes, rear |  | Single-piston swing-calliper disc brakes |
| Diameter | mm | 345, vented | 345, vented |
| Driving stability systems |  | ABS, CBC, ASC, DSC, DTC, DBC; optional: Dynamic Drive |
| Steering |  | Rack-and-pinion power steering, optional: Active Steering |
| Transmission ratio, steering, overall | :1 | 14.4 | 14.4 |
| Type of transmission |  | 6-speed manual (6-speed Steptronic automatic) |
| Gear ratios | 1st | :1 | 4.055 (4.17) | 4.055 (4.17) |
|  | 2nd | :1 | 2.396 (2.34) | 2.396 (2.34) |
|  | 3rd | :1 | 1.582 (1.52) | 1.582 (1.52) |
|  | 4th | :1 | 1.192 (1.14) | 1.192 (1.14) |
|  | 5th | :1 | 1.0 (0.87) | 1.0 (0.87) |
|  | 6th | :1 | 0.872 (0.69) | 0.872 (0.69) |
|  | Rev | :1 | 3.677 (3.40) | 3.677 (3.40) |
| Final drive ratio | :1 | 3.23 (3.46) | 3.46 (3.46) |
| Tyres, front |  | 245/45 R 18 96W RSC | 245/45 R 18 96W RSC |
| Tyres, rear |  | 245/45 R 18 96W RSC | 245/45 R 18 96W RSC |
| Rims, front |  | 8 J x 18 alu | 8 J x 18 alu |
| Rims, rear |  | 8 J x 18 alu | 8 J x 18 alu |
| Performance |  |  |  |
| Power-to-weight ratio (DIN) | kg/kW | 6.07 | 6.85 |
| Output per litre | kW/ltr | 56.26 | 56.26 |
| Acceleration 0–100 km/h | sec | 5.4 (5.5) | 5.7 (5.8) |
| in 4th gear 80–120 km/h | sec | 4.7 | 4.9 |
| Top speed | km/h | 250 | 250 |
| Fuel consumption, EU cycle |  |  |  |
| Urban | ltr/100 km | 17.6 (16.3) | 19.1 (17.2) |
| Extra-urban | ltr/100 km | 8.6 (8.1) | 9.3 (8.5) |
| Composite | ltr/100 km | 11.9 (11.1) | 12.9 (11.7) |
| CO2 | g/km | 286 (267) | 310 (281) |
| Miscellaneous |  |  |  |
| Emission category |  | EU4 | EU4 |