Specifications.

The BMW 5 Series Sedan.

530i.

|  |  | BMW 530i Sedan |  |
| --- | --- | --- | --- |
| Body |  |  |
| No of doors/seats |  | 4/5 |  |
| Length/width/height (unladen) | mm | 4936/1868/1479 |  |
| Wheelbase | mm | 2975 |  |
| Track, front/rear | mm | 1605/1630 |  |
| Ground clearance | mm | 144 |  |
| Turning circle | m | 12.05 |  |
| Fuel tank capacity | approx. ltr | 68 |  |
| Engine oil1) | ltr | 5.25 |  |
| Weight, unladen, to DIN/EU | kg | 1540/1615 |  |
| Max load to DIN | kg | 660 |  |
| Max permissible weight | kg | 2200 |  |
| Max axle load, front/rear | kg | 1045/1250 |  |
| Max trailer load, Braked (12%)/unbraked | kg | 2000/750 |  |
| Max roofload/max towbar download | kg | 100/90 |  |
| Luggage comp capacity | ltr | 530 |  |
| Air resistance | cd x A | 0.24 x 2.35 |  |
| Power Unit |  |  |
| Config/No of cyls/valves |  | In-line/4/4 |  |
| Engine technology |  | BMW TwinPower Turbo technology: TwinScroll turbocharger, High Precision Direct Injection, VALVETRONIC fully variable valve control, Double-VANOS variable camshaft timing |
| Effective capacity | cc | 1998 |  |
| Stroke/bore | mm | 94.6/82.0 |  |
| Compression ratio | :1 | 10.2 |  |
| Fuel |  | min. RON 91 |  |
| Max output | kW/hp | 185/252 |  |
| at | rpm | 5200–6500 |  |
| Max torque | Nm/lb-ft | 350/258 |  |
| at | rpm | 1450–4800 |  |
| Electrical System |  |
| Battery/installation | Ah/– | 90/Luggage compartment |  |
| Alternator | A/W | n.b. |  |
| Driving Dynamics and Safety |  |  |
| Suspension, front |  | Aluminium double track control arm axle with separate lower track arm level, small steering roll radius, traverse force compensation, anti-dive |
| Suspension, rear |  | Five-link axle in aluminium lightweight construction |
| Brakes, front |  | Four-piston fixed-calliper disc brakes / vented |
| Brakes, rear |  | Single-piston floating-calliper disc brakes / vented |
| Driving stability systems |  | Standard: DSC incl. ABS and DTC (Dynamic Traction Control), CBC (Cornering Brake Control), DBC (Dynamic Brake Control), Dry Braking function, Fading Compensation, Start-Off Assistant. Optional: Dynamic Damper Control, Drive Performance Control |
| Safety equipment |  | Standard: airbags for driver and front passenger, side airbags for driver and front passenger, head airbags for front and rear seats, three-point inertia-reel seatbelts on all seats with belt latch tensioner and belt force limiter at the front seats, crash sensors, tyre defect indicator |
| Steering |  | Electric Power Steering (EPS) Optional: Integral Active Steering |
| Steering ratio, overall | :1 | 16.3 |  |
| Tyres, front/rear |  | 225/55 R17 97Y |  |
| Rims, front/rear |  | 7.5J x 17 light alloy |  |

|  |  | BMW 530i Sedan |  |
| --- | --- | --- | --- |
| Transmission |  |  |
| Type of transmission |  | 8-speed Steptronic |  |
| Gear ratios I | :1 | 5.000 |  |
| II | :1 | 3.200 |  |
| III | :1 | 2.143 |  |
| IV | :1 | 1.720 |  |
| V | :1 | 1.314 |  |
| VI | :1 | 1.000 |  |
| VII | :1 | 0.822 |  |
| VIII | :1 | 0.640 |  |
| R | :1 | 3.456 |  |
| Final drive | :1 | 2.929 |  |
| Performance |  |  |
| Power-to-weight ratio | kg/kW | 8.3 |  |
| Output per litre | kW/ltr | 92.6 |  |
| Acceleration 0–100 km/h | sec | 6.2 |  |
| In 5th gear 80–120 km/h | sec | -- |  |
| Top speed | km/h | 250 |  |
| BMW EfficientDynamics |  |  |
| BMW EfficientDynamics standard features |  | Brake Energy Regeneration, electromechanical power steering, Automatic Start/Stop function, ECO PRO mode, coasting function, intelligent lightweight construction, optimised aerodynamic attributes, on-demand operation of ancillary units, map-regulated oil pump, differential with optimised warm-up behaviour, tyres with reduced rolling resistance |
| Fuel Consumption ECE2) |
| Urban | ltr/100 km | 7.3–6.9 |  |
| Extra-urban | ltr/100 km | 5.2–4.7 |  |
| Combined | ltr/100 km | 5.9–5.5 |  |
| CO2 | g/km | 136–126 |  |
| Emission rating |  | EU6 |  |

Specifications apply to ACEA markets/data relevant to homologation applies in part only to Germany (weight)

1) Oil change

2) Fuel consumption and CO2 emissions depend on the selected tyre format

The BMW 5 Series Sedan.

540i.

|  |  | BMW 540i Sedan |  |
| --- | --- | --- | --- |
| Body |  |  |
| No of doors/seats |  | 4/5 |  |
| Length/width/height (unladen) | mm | 4936/1868/1479 |  |
| Wheelbase | mm | 2975 |  |
| Track, front/rear | mm | 1605/1630 |  |
| Ground clearance | mm | 144 |  |
| Turning circle | m | 12.05 |  |
| Fuel tank capacity | approx. ltr | 68 |  |
| Engine oil1) | ltr | 6.5 |  |
| Weight, unladen, to DIN/EU | kg | 1595/1670 |  |
| Max load to DIN | kg | 675 |  |
| Max permissible weight | kg | 2270 |  |
| Max axle load, front/rear | kg | 1110/1260 |  |
| Max trailer load, Braked (12%)/unbraked | kg | 2000/750 |  |
| Max roofload/max towbar download | kg | 100/90 |  |
| Luggage comp capacity | ltr | 530 |  |
| Air resistance | cd x A | 0.25 x 2.35 |  |
| Power Unit |  |  |
| Config/No of cyls/valves |  | In-line/6/4 |  |
| Engine technology |  | BMW TwinPower Turbo technology: TwinScroll turbocharger, High Precision Direct Injection, VALVETRONIC fully variable valve control, Double-VANOS variable camshaft timing |
| Effective capacity | cc | 2998 |  |
| Stroke/bore | mm | 94.6/82.0 |  |
| Compression ratio | :1 | 11.0 |  |
| Fuel |  | min. RON 91 |  |
| Max output | kW/hp | 250/340 |  |
| at | rpm | 5500–6500 |  |
| Max torque | Nm/lb-ft | 450/332 |  |
| at | rpm | 1380–5200 |  |
| Electrical System |  |
| Battery/installation | Ah/– | 105/Luggage compartment |  |
| Alternator | A/W | n.b. |  |
| Driving Dynamics and Safety |  |  |
| Suspension, front |  | Aluminium double track control arm axle with separate lower track arm level, small steering roll radius, traverse force compensation, anti-dive |
| Suspension, rear |  | Five-link axle in aluminium lightweight construction |
| Brakes, front |  | Four-piston fixed-calliper disc brakes / vented |
| Brakes, rear |  | Single-piston floating-calliper disc brakes / vented |
| Driving stability systems |  | Standard: DSC incl. ABS and DTC (Dynamic Traction Control), CBC (Cornering Brake Control), DBC (Dynamic Brake Control), Dry Braking function, Fading Compensation, Start-Off Assistant. Optional: Dynamic Damper Control, Drive Performance Control |
| Safety equipment |  | Standard: airbags for driver and front passenger, side airbags for driver and front passenger, head airbags for front and rear seats, three-point inertia-reel seatbelts on all seats with belt latch tensioner and belt force limiter at the front seats, crash sensors, tyre defect indicator |
| Steering |  | Electric Power Steering (EPS) Optional: Integral Active Steering |
| Steering ratio, overall | :1 | 16.3 |  |
| Tyres, front/rear |  | 225/55 R17 97Y |  |
| Rims, front/rear |  | 7.5J x 17 light alloy |  |

|  |  | BMW 540i Sedan |  |
| --- | --- | --- | --- |
| Transmission |  |  |
| Type of transmission |  | 8-speed Steptronic |  |
| Gear ratios I | :1 | 5.000 |  |
| II | :1 | 3.200 |  |
| III | :1 | 2.143 |  |
| IV | :1 | 1.720 |  |
| V | :1 | 1.314 |  |
| VI | :1 | 1.000 |  |
| VII | :1 | 0.822 |  |
| VIII | :1 | 0.640 |  |
| R | :1 | 3.456 |  |
| Final drive | :1 | 2.929 |  |
| Performance |  |  |
| Power-to-weight ratio | kg/kW | 6.4 |  |
| Output per litre | kW/ltr | 83.4 |  |
| Acceleration 0–100 km/h | sec | 5.1 |  |
| In 5th gear 80–120 km/h | sec | -- |  |
| Top speed | km/h | 250 |  |
| BMW EfficientDynamics |  |  |
| BMW EfficientDynamics standard features |  | Brake Energy Regeneration, electromechanical power steering, Automatic Start/Stop function, ECO PRO mode, coasting function, intelligent lightweight construction, optimised aerodynamic attributes, on-demand operation of ancillary units, map-regulated oil pump, differential with optimised warm-up behaviour, tyres with reduced rolling resistance |
| Fuel Consumption ECE2) |
| Urban | ltr/100 km | 9.2–8.9 |  |
| Extra-urban | ltr/100 km | 5.6–5.2 |  |
| Combined | ltr/100 km | 6.9–6.5 |  |
| CO2 | g/km | 159–149 |  |
| Emission rating |  | EU6 |  |

Specifications apply to ACEA markets/data relevant to homologation applies in part only to Germany (weight)

1) Oil change

2) Fuel consumption and CO2 emissions depend on the selected tyre format

The BMW 5 Series Sedan.

520d.

|  |  | BMW 520d Sedan |  |
| --- | --- | --- | --- |
| Body |  |  |
| No of doors/seats |  | 4/5 |  |
| Length/width/height (unladen) | mm | 4936/1868/1479 |  |
| Wheelbase | mm | 2975 |  |
| Track, front/rear | mm | 1605/1630 |  |
| Ground clearance | mm | 144 |  |
| Turning circle | m | 12.05 |  |
| Fuel tank capacity | approx. ltr | 66 |  |
| Engine oil1) | ltr | 5.0 |  |
| Weight, unladen, to DIN/EU | kg | 1540/1615 (1560/1635) |  |
| Max load to DIN | kg | 685 |  |
| Max permissible weight | kg | 2230 (2245) |  |
| Max axle load, front/rear | kg | 1045/1280 (1055/1280) |  |
| Max trailer load, Braked (12%)/unbraked | kg | 1800 (2000)/750 |  |
| Max roofload/max towbar download | kg | 100/90 |  |
| Luggage comp capacity | ltr | 530 |  |
| Air resistance | cd x A | 0.24 x 2.35 |  |
| Power Unit |  |  |
| Config/No of cyls/valves |  | In-line/4/4 |  |
| Engine technology |  | BMW TwinPower Turbo technology: variable-geometry turbocharger, common-rail direct injection |
| Effective capacity | cc | 1995 |  |
| Stroke/bore | mm | 90.0/84.0 |  |
| Compression ratio | :1 | 16.5 |  |
| Fuel |  | Diesel |  |
| Max output | kW/hp | 140/190 |  |
| at | rpm | 4000 |  |
| Max torque | Nm/lb-ft | 400/295 |  |
| at | rpm | 1750–2500 |  |
| Electrical System |  |
| Battery/installation | Ah/– | 90/Luggage compartment |  |
| Alternator | A/W | n.b. |  |
| Driving Dynamics and Safety |  |  |
| Suspension, front |  | Aluminium double track control arm axle with separate lower track arm level, small steering roll radius, traverse force compensation, anti-dive |
| Suspension, rear |  | Five-link axle in aluminium lightweight construction |
| Brakes, front |  | Four-piston fixed-calliper disc brakes / vented |
| Brakes, rear |  | Single-piston floating-calliper disc brakes / vented |
| Driving stability systems |  | Standard: DSC incl. ABS and DTC (Dynamic Traction Control), CBC (Cornering Brake Control), DBC (Dynamic Brake Control), Dry Braking function, Fading Compensation, Start-Off Assistant. Optional: Dynamic Damper Control, Drive Performance Control |
| Safety equipment |  | Standard: airbags for driver and front passenger, side airbags for driver and front passenger, head airbags for front and rear seats, three-point inertia-reel seatbelts on all seats with belt latch tensioner and belt force limiter at the front seats, crash sensors, tyre defect indicator |
| Steering |  | Electric Power Steering (EPS) Optional: Integral Active Steering |
| Steering ratio, overall | :1 | 16.3 |  |
| Tyres, front/rear |  | 225/55 R17 97Y |  |
| Rims, front/rear |  | 7.5J x 17 light alloy |  |

|  |  | BMW 520d Sedan |  |
| --- | --- | --- | --- |
| Transmission |  |  |
| Type of transmission |  | 6-speed manual (Optional: 8-speed Steptronic) |  |
| Gear ratios I | :1 | 4.110 (5.000) |  |
| II | :1 | 2.248 (3.200) |  |
| III | :1 | 1.403 (2.143) |  |
| IV | :1 | 1.000 (1.720) |  |
| V | :1 | 0.802 (1.314) |  |
| VI | :1 | 0.659 (1.000) |  |
| VII | :1 | -- (0.822) |  |
| VIII | :1 | -- (0.640) |  |
| R | :1 | 3.727 (3.456) |  |
| Final drive | :1 | 3.231 (2.929) |  |
| Performance |  |  |
| Power-to-weight ratio | kg/kW | 11.0 (11.1) |  |
| Output per litre | kW/ltr | 70.2 |  |
| Acceleration 0–100 km/h | sec | 7.7 (7.5) |  |
| In 5th gear 80–120 km/h | sec | 8.4 (--) |  |
| Top speed | km/h | 238 (235) |  |
| BMW EfficientDynamics |  |  |
| BMW EfficientDynamics standard features |  | Brake Energy Regeneration, electromechanical power steering, Automatic Start/Stop function, Optimum Shift Indicator (manual gearbox), ECO PRO mode, coasting function (automatic), intelligent lightweight construction, optimised aerodynamic attributes, on-demand operation of ancillary units, map-regulated oil pump, differential with optimised warm-up behaviour, tyres with reduced rolling resistance |
| Fuel Consumption ECE2) |
| Urban | ltr/100 km | 5.2–4.9 (5.0–4.7) |  |
| Extra-urban | ltr/100 km | 4.1–3.7 (5.1–3.8) |  |
| Combined | ltr/100 km | 4.5–4.2 (4.5–4.1) |  |
| CO2 | g/km | 119–109 (118–108) |  |
| Emission rating |  | EU6 |  |

Specifications apply to ACEA markets/data relevant to homologation applies in part only to Germany (weight)

Figures in brackets apply to models with automatic transmission

1) Oil change

2) Fuel consumption and CO2 emissions depend on the selected tyre format

The BMW 5 Series Sedan.

530d.

|  |  | BMW 530d Sedan | BMW 530d xDrive Sedan |
| --- | --- | --- | --- |
| Body |  |  |
| No of doors/seats |  | 4/5 |  |
| Length/width/height (unladen) | mm | 4936/1868/1479 |  |
| Wheelbase | mm | 2975 |  |
| Track, front/rear | mm | 1605/1630 |  |
| Ground clearance | mm | 144 |  |
| Turning circle | m | 12.05 |  |
| Fuel tank capacity | approx. ltr | 66 |  |
| Engine oil1) | ltr | 6.5 |  |
| Weight, unladen, to DIN/EU | kg | 1640/1715 |  |
| Max load to DIN | kg | 705 |  |
| Max permissible weight | kg | 2345 |  |
| Max axle load, front/rear | kg | 1125/1310 |  |
| Max trailer load, Braked (12%)/unbraked | kg | 2000/750 |  |
| Max roofload/max towbar download | kg | 100/90 |  |
| Luggage comp capacity | ltr | 530 |  |
| Air resistance | cd x A | 0.24 x 2.35 |  |
| Power Unit |  |  |
| Config/No of cyls/valves |  | In-line/6/4 |  |
| Engine technology |  | BMW TwinPower Turbo technology: variable-geometry turbocharger, common-rail direct injection |
| Effective capacity | cc | 2993 |  |
| Stroke/bore | mm | 90.0/84.0 |  |
| Compression ratio | :1 | 16.5 |  |
| Fuel |  | Diesel |  |
| Max output | kW/hp | 195/265 |  |
| at | rpm | 4000 |  |
| Max torque | Nm/lb-ft | 620/457 |  |
| at | rpm | 2000–2500 |  |
| Electrical System |  |
| Battery/installation | Ah/– | 105/Luggage compartment |  |
| Alternator | A/W | n.b. |  |
| Driving Dynamics and Safety |  |  |
| Suspension, front |  | Aluminium double track control arm axle with separate lower track arm level, small steering roll radius, traverse force compensation, anti-dive |
| Suspension, rear |  | Five-link axle in aluminium lightweight construction |
| Brakes, front |  | Four-piston fixed-calliper disc brakes / vented |
| Brakes, rear |  | Single-piston floating-calliper disc brakes / vented |
| Driving stability systems |  | Standard: DSC incl. ABS and DTC (Dynamic Traction Control), CBC (Cornering Brake Control), DBC (Dynamic Brake Control), Dry Braking function, Fading Compensation, Start-Off Assistant. Optional: Dynamic Damper Control, Drive Performance Control |
| Safety equipment |  | Standard: airbags for driver and front passenger, side airbags for driver and front passenger, head airbags for front and rear seats, three-point inertia-reel seatbelts on all seats with belt latch tensioner and belt force limiter at the front seats, crash sensors, tyre defect indicator |
| Steering |  | Electric Power Steering (EPS) Optional: Integral Active Steering |
| Steering ratio, overall | :1 | 16.3 |  |
| Tyres, front/rear |  | 225/55 R17 97Y |  |
| Rims, front/rear |  | 7.5J x 17 light alloy |  |

|  |  | BMW 530d Sedan |  |
| --- | --- | --- | --- |
| Transmission |  |  |
| Type of transmission |  | 8-speed Steptronic |  |
| Gear ratios I | :1 | 5.000 |  |
| II | :1 | 3.200 |  |
| III | :1 | 2.143 |  |
| IV | :1 | 1.720 |  |
| V | :1 | 1.313 |  |
| VI | :1 | 1.000 |  |
| VII | :1 | 0.823 |  |
| VIII | :1 | 0.640 |  |
| R | :1 | 3.478 |  |
| Final drive | :1 | 2.471 |  |
| Performance |  |  |
| Power-to-weight ratio | kg/kW | 8.4 |  |
| Output per litre | kW/ltr | 65.2 |  |
| Acceleration 0–100 km/h | sec | 5.7 |  |
| In 5th gear 80–120 km/h | sec | -- |  |
| Top speed | km/h | 250 |  |
| BMW EfficientDynamics |  |  |
| BMW EfficientDynamics standard features |  | Brake Energy Regeneration, electromechanical power steering, Automatic Start/Stop function, ECO PRO mode, coasting function, intelligent lightweight construction, optimised aerodynamic attributes, on-demand operation of ancillary units, map-regulated oil pump, differential with optimised warm-up behaviour, tyres with reduced rolling resistance |
| Fuel Consumption ECE2) |
| Urban | ltr/100 km | 5.6–5.3 |  |
| Extra-urban | ltr/100 km | 4.4–4.1 |  |
| Combined | ltr/100 km | 4.9–4.5 |  |
| CO2 | g/km | 128–118 |  |
| Emission rating |  | EU6 |  |

Specifications apply to ACEA markets/data relevant to homologation applies in part only to Germany (weight)

1) Oil change

2) Fuel consumption and CO2 emissions depend on the selected tyre format

Output and torque diagrams.
The BMW 5 Series Sedan.
530i.

The BMW 5 Series Sedan.
540i.

The BMW 5 Series Sedan.
520d.

The BMW 5 Series Sedan.
530d.

Exterior and interior dimensions.
The BMW 5 Series Sedan.