The BMW 2 Series Coupe.
220i, 230i.

|  |  | BMW 220i Coupe | BMW 230i Coupe |
| --- | --- | --- | --- |
| Body |  |  |  |
| No. of doors/seats |  | 2 / 4 | 2 / 4 |
| Length/width/height 1 (unladen) | mm | 4432 / 1774 / 1418 | 4432 / 1774 / 1418 |
| Wheelbase | mm | 2690 | 2690 |
| Front/rear track | mm | 1521 / 1556 | 1521 / 1556 |
| Ground clearance | mm | 140 | 140 |
| Turning circle | m | 10.9 | 10.9 |
| Fuel tank capacity | approx. l | 52 | 52 |
| Engine oil 2) | l | 5.25 | 5.25 |
| Weight, unladen (DIN/EU) | kg | 1405 / 1480 | 1430 / 1505 |
| Max. load to DIN | kg | 510 | 510 |
| Max. permissible weight | kg | 1910 | 1935 |
| Max. axle load, front/rear | kg | 905 / 1065 | 915 / 1085 |
| Max. trailer load (12%) braked/unbraked | kg | 1500 / 680 | 1500 / 715 |
| Max. roof load/max towbar download | kg | 75 / 75 | 75 / 75 |
| Luggage comp. capacity | l | 390 | 390 |
| Air resistance | Cd x A | 0.29 x 2.14 | 0.29 x 2.14 |
| Engine |  |  |  |
| Type/no. of cylinders/valves |  | in-line / 4 / 4 | in-line / 4 / 4 |
| Engine technology |  | BMW TwinPower Turbo technology: twin-scroll turbocharger, direct injection system High Precision Injection, fully variable valve control (VALVETRONIC) and double VANOS variable camshaft timing |
| Effective capacity | cc | 1998 | 1998 |
| Stroke/bore | mm | 94.6 / 82.0 | 94.6 / 82.0 |
| Compression ratio | :1 | 11.0 | 10.2 |
| Fuel type |  | min RON 91 | min RON 91 |
| Output | kW/hp | 135 / 184 | 185 / 252 |
| at rpm |  | 5000 | 5200 |
| Torque | Nm | 270 | 350 |
| at rpm |  | 1350 – 4600 | 1450 – 4800 |
| Electrical |  |  |  |
| Battery charge/location | Ah/– | 80 / luggage compartment | 80 / luggage compartment |
| Driving Dynamics and Safety |  |
| Front suspension |  | Aluminium double-joint spring strut axle |
| Rear suspension |  | Five-link axle in lightweight steel construction with double elastic bearing |
| Front brakes |  | Single-piston floating-calliper disc brakes |
| Rear brakes |  | Single-piston floating-calliper disc brakes |
| Driving stability systems |  | Standard: DSC incl. ABS, ASC and DTC (Dynamic Traction Control), CBC Cornering Brake Control, DBC Dynamic Brake Control, brake drying function, fading compensation, start-off assistant |
| Safety equipment |  | Standard: airbags for driver and front passenger, side airbags for driver and front passenger, head airbags front and rear, three-point inertia-reel seatbelts on all seats with belt tensioner and belt force limiter at the front, crash sensors, Tyre Defect Indicator |
| Steering |  | Electromechanical rack-and-pinion power steering (EPS); optional: Servotronic function, variable sport steering |
| Overall steering ratio | :1 | 15.0 | 15.0 |
| Front/rear tyres |  | 205/55 R16 91V | 205/50 R17 89Y |
| Front/rear wheels |  | 7J x 16 light-alloy | 7J x 17 light-alloy |

|  |  | BMW 220i Coupe | BMW 230i Coupe |
| --- | --- | --- | --- |
| Transmission |  |  |  |
| Type of gearbox |  | 8-speed Steptronic |
| Gear ratios I | :1 | 5.000 | 5.000 |
| II | :1 | 3.200 | 3.200 |
| III | :1 | 2.143 | 2.143 |
| IV | :1 | 1.720 | 1.720 |
| V | :1 | 1.314 | 1.314 |
| VI | :1 | 1.000 | 1.000 |
| VII | :1 | 0.822 | 0.822 |
| VIII | :1 | 0.640 | 0.640 |
| R | :1 | 3.456 | 3.456 |
| Final drive | :1 | 2.813 | 2.813 |
| Performance |  |  |  |
| Weight-to-power ratio (DIN unladen) | kg/kW | 10.4 | 7.7 |
| Specific power output | kW/l | 67.6 | 92.6 |
| Acceleration 0–100 km/h | sec | 7.2 | 5.6 |
| in 5th gear 80–120 km/h | sec | – | – |
| Max. speed | km/h | 230 | 250 |
| BMW EfficientDynamics |  |  |  |
| BMW EfficientDynamics Features included as standard |  | Brake Energy Regeneration with recuperation display, electric power steering (EPS), Auto Start Stop function, ECO PRO mode with coasting function, intelligent lightweight construction, optimised aerodynamic attributes, on-demand operation of ancillary units, map-controlled oil pump, differential with optimised warm-up behaviour, tyres with reduced rolling resistance |
| Fuel consumption (EU) 3) |  |  |  |
| with standard wheels and tyres: 7J x 16‘‘ rims and 205/55 R16 tyres (BMW 220i Coupe), 7J x 17’’ rims and 205/50 R17 tyres (BMW 230i Coupe) |
| Urban | l/100 km | 7.0 | 7.3 |
| Extra-urban | l/100 km | 4.7 | 4.8 |
| Total | l/100 km | 5.5 | 5.7 |
| CO2 emissions | g/km | 127 | 131 |
| with 7J x 17‘‘ rims and 205/50 R17 tyres (BMW 220i Coupe), with 7.5J x 17 rims and 225/45 R 17 tyres, with 7.5J x 17‘‘ front rims, 8J x 17‘‘ rear rims and 225/45 R17 front tyres, 245/40 R17 rear tyres |
| Urban | l/100 km | 7.4 | 7.4 |
| Extra-urban | l/100 km | 5.0 | 5.1 |
| Total | l/100 km | 5.9 | 5.9 |
| CO2 emissions | g/km | 134 | 134 |
| with 7.5J x 18‘‘ front rims, 8J x 18‘‘ rear rims and 225/40 R18 front tyres, 245/35 R18 rear tyres and with winter tyres |
| Urban | l/100 km | 7.4 | 7.4 |
| Extra-urban | l/100 km | 5.1 | 5.1 |
| Total | l/100 km | 5.9 | 5.9 |
| CO2 emissions | g/km | 136 | 134 |
| Emissions standard |  | EU6 | EU6 |

Technical data valid for ACEA countries/Some permitted weights valid only for Germany

1) Height including roof aerial

2) Oil change volume

3) Fuel consumption and CO2 emissions depend on the selected tyre format

The BMW 2 Series Coupe.
M240i.

|  |  |  | BMW M240i Coupe |  |
| --- | --- | --- | --- | --- |
| Body |  |  |  |  |
| No. of doors/seats |  |  | 2 / 4 |  |
| Length/width/height1) (unladen) | mm |  | 4454 / 1774 / 1408 |  |
| Wheelbase | mm |  | 2690 |  |
| Track, front/rear | mm |  | 1516 / 1534 |  |
| Ground clearance | mm |  | 130 |  |
| Turning circle | m |  | 10.9 |  |
| Tank capacity | approx. ltr |  | 52 |  |
| Engine oil2) | ltr |  | 6.5 |  |
| Weight, unladen, to DIN/EU | kg |  | 1475 / 1550 (1490 / 1565) |  |
| Max. load to DIN | kg |  | 510 |  |
| Max. permissible weight | kg |  | 1980 (1995) |  |
| Max. axle load, front/rear | kg |  | 975 / 1100 |  |
| Max. trailer load, (12%) braked/unbraked, | kg |  | – / – |  |
| Max. roof load/towbar download | kg |  | 75 / – |  |
| Luggage comp. capacity | ltr |  | 390 |  |
| Air resistance | Cd x A |  | 0.33 x 2.14 |  |
| Engine |  |  |  |  |
| Config./No. of cyls./valves |  |  | in-line / 6 / 4 |  |
| Engine technology |  | M Performance TwinPower Turbo technology with twin-scroll turbocharger, High Precision Direct Injection, fully variable valve control (VALVETRONIC) and double-VANOS variable camshaft control |
| Effective capacity | cc |  | 2998 |  |
| Stroke/bore | mm |  | 94.6 / 82.0 |  |
| Compression ratio | :1 |  | 11.0 |  |
| Fuel grade |  |  | min. RON 91 |  |
| Output | kW/hp |  | 250 / 340 |  |
| at | rpm |  | 5500 |  |
| Torque | Nm |  | 500 |  |
| at | rpm |  | 1520 – 4500 |  |
| Electrical System |  |  |  |  |
| Battery/Installation | Ah/– |  | 80 / luggage comp. |  |
| Driving Dynamics and Safety |  |
| Suspension, front |  | Aluminium double-joint spring strut axle with M-specific elastokinematics |
| Suspension, rear |  | Five-link axle in lightweight steel construction with double elastic bearing |
| Brakes, front |  | Four-piston fixed-calliper disc brakes |
| Brakes, rear |  | Two-piston fixed-calliper disc brakes |
| Driving stability systems |  | Standard: DSC incl. ABS, ASC and DTC (Dynamic Traction Control), CBC (Cornering Brake Control), DBC (Dynamic Brake Control), Dry Braking function, Fading Compensation, Start-Off Assistant |
| Safety equipment |  | Standard: airbags for driver and front passenger, side airbags for driver and front passenger, head airbags front and rear, three-point inertia-reel seatbelts on all seats with belt tensioner and belt force limiter at the front, crash sensors, Tyre Defect Indicator |
| Steering |  | Electric Power Steering (EPS), variable sport steering |
| Steering ratio, overall | :1 |  | 14.5 |  |
| Tyres, front/rear |  |  | 225/40 ZR18 88Y/ 245/35 ZR 18 92Y XL |  |
| Rims, front/rear |  |  | 7.5J x 18 light-alloy/ 8J x 18 light-alloy |  |

|  |  |  | BMW M240i Coupe |  |
| --- | --- | --- | --- | --- |
| Transmission |  |  |  |  |
| Type of gearbox |  | 6-speed manual gearbox (optional: 8-speed Steptronic Sport transmission) |
| Gear ratios I | :1 |  | 4.110 (5.000) |  |
| II | :1 |  | 2.315 (3.200) |  |
| III | :1 |  | 1.542 (2.143) |  |
| IV | :1 |  | 1.179 (1.720) |  |
| V | :1 |  | 1.000 (1.314) |  |
| VI | :1 |  | 0.846 (1.000) |  |
| VII | :1 |  | – (0.822) |  |
| VIII | :1 |  | – (0.640) |  |
| R | :1 |  | 3.727 (3.456) |  |
| Final drive | :1 |  | 3.077 (2.813) |  |
| Performance |  |  |  |  |
| Power-to-weight ratio (DIN) | kg/kW |  | 5.9 (6,0) |  |
| Output per litre | kW/ltr |  | 83.4 |  |
| Acceleration 0–100 km/h | s |  | 4.8 (4.6) |  |
| in 5th gear 80–120 km/h | s |  | 4.8 (–) |  |
| Top speed | km/h |  | 250 (250) |  |
| BMW EfficientDynamics |  |  |  |  |
| BMW EfficientDynamics, standard features |  | Brake Energy Regeneration with recuperation display, Electric Power Steering (EPS), Auto Start Stop function, Optimum Gearshift Indicator, ECO PRO mode with coasting function (automatic), intelligent lightweight construction, optimised aerodynamic attributes, on-demand operation of ancillary units, map-controlled oil pump, differential with optimised warm-up behaviour, tyres with reduced rolling resistance |
| Fuel consumption EU |  |  |  |  |
| Urban | ltr/100 km |  | 10.6 (9.4) |  |
| Extra-urban | ltr/100 km |  | 6.2 (5.8) |  |
| Combined | ltr/100 km |  | 7.8 (7.1) |  |
| CO2 | g/km |  | 179 (163) |  |
| Emission rating |  |  | EU6 |  |

Specifications apply to ACEA markets; data relevant to homologation applicable in part only to Germany (weight)

Figures in brackets apply to automatic transmission

1) Height including roof aerial

2) Oil change volume

The BMW 2 Series Coupe.
218d.

|  |  |  | BMW 218d Coupe |
| --- | --- | --- | --- |
| Body |  |  |  |  |
| No. of doors/seats |  |  | 2 / 4 |  |
| Length/width/height 1) (unladen) | mm |  | 4432 / 1774 / 1418 |  |
| Wheelbase | mm |  | 2690 |  |
| Front/rear track | mm |  | 1521 / 1556 |  |
| Ground clearance | mm |  | 140 |  |
| Turning circle | m |  | 10.9 |  |
| Fuel tank capacity | approx. l |  | 52 |  |
| Engine oil 2) | l |  | 5.0 |  |
| Weight, unladen (DIN/EU) | kg |  | 1380 / 1455 (1400 / 1475) |  |
| Max. load to DIN | kg |  | 510 |  |
| Max. permissible weight | kg |  | 1885 (1905) |  |
| Max. axle load, front/rear | kg |  | 900 / 1055 |  |
| Max. trailer load (12%) braked/unbraked | kg |  | 1500 / 690 |  |
| Max. roof load/max towbar download | kg |  | 75 / 75 |  |
| Luggage comp. capacity | l |  | 390 |  |
| Air resistance | Cd x A |  | 0.29 x 2.14 |  |
| Engine |  |  |  |  |
| Type/no. of cylinders/valves |  |  | in-line / 4 / 4 |  |
| Engine technology |  | BMW TwinPower Turbo technology: variable-geometry turbocharger, Common Rail direct injection with solenoid valve injectors (max. injection pressure: 2000 bar) |
| Effective capacity | cc |  | 1995 |  |
| Stroke/bore | mm |  | 90.0 / 84.0 |  |
| Compression ratio | :1 |  | 16.5 |  |
| Fuel type |  |  | Diesel |  |
| Output | kW/hp |  | 110 / 150 |  |
| at rpm |  |  | 4000 |  |
| Torque | Nm |  | 320 |  |
| at rpm |  |  | 1500 – 3000 |  |
| Electrical |  |  |  |  |
| Battery charge/location | Ah/– |  | 80 (90) / luggage compartment |  |
| Alternator current/output | A/W |  | 150 / 2100 |  |
| Driving Dynamics and Safety |  |
| Front suspension |  | Aluminium double-joint spring strut axle |
| Rear suspension |  | Five-link axle in lightweight steel construction with double elastic bearing |
| Front brakes |  | Single-piston floating-calliper disc brakes |
| Rear brakes |  | Single-piston floating-calliper disc brakes |
| Driving stability systems |  | Standard: DSC incl. ABS, ASC and DTC (Dynamic Traction Control), CBC Cornering Brake Control, DBC Dynamic Brake Control, brake drying function, fading compensation, start-off assistant |
| Safety equipment |  | Standard: driver and front-seat passenger airbags, driver and front-seat passenger side airbags, head airbags front and rear, three-point automatic seatbelts for all seats, seatbelt tensioners and seatbelt force limiters in front seats, crash sensors, Tyre Defect Indicator |
| Steering |  | Electromechanical rack-and-pinion power steering (EPS); optional: Servotronic function, variable sport steering |
| Overall steering ratio | :1 |  | 15.0 |  |
| Front/rear tyres |  |  | 205/55 R16 91V |  |
| Front/rear wheels |  |  | 7J x 16 light-alloy |  |

|  |  |  | BMW 218d Coupe |
| --- | --- | --- | --- |
| Transmission |  |  |  |  |
| Type of gearbox |  | 6-speed manual (optional: 8-speed Steptronic) |
| Gear ratios I | :1 |  | 4.002 (5.000) |  |
| II | :1 |  | 2.109 (3.200) |  |
| III | :1 |  | 1.396 (2.143) |  |
| IV | :1 |  | 1.000 (1.720) |  |
| V | :1 |  | 0.781 (1.314) |  |
| VI | :1 |  | 0.668 (1.000) |  |
| VII | :1 |  | – (0.822) |  |
| VIII | :1 |  | – (0.640) |  |
| R | :1 |  | 3.647 (3.456) |  |
| Final drive | :1 |  | 3.077 (2.647) |  |
| Performance |  |  |  |  |
| Weight-to-power ratio (DIN unladen) | kg/kW |  | 12.5 (12.7) |  |
| Specific power output | kW/l |  | 55.1 |  |
| Acceleration 0–100 km/h | sec. |  | 8.4 (8.2) |  |
| in 5th gear 80–120 km/h | sec. |  | 9.7 (–) |  |
| Max. speed | km/h |  | 213 (213) |  |
| BMW EfficientDynamics |  |  |  |  |
| BMW EfficientDynamics Features included as standard |  | Brake Energy Regeneration with recuperation display, electric power steering (EPS), Auto Start Stop function, Optimum Gearshift Indicator, ECO PRO mode with coasting function (automatic), intelligent lightweight construction, optimised aerodynamic attributes, on-demand operation of ancillary units, map-controlled oil pump, differential with optimised warm-up behaviour, tyres with reduced rolling resistance |
| Fuel consumption (EU) 3) |  |  |  |  |
| with standard wheels and tyres |  |  |  |  |
| Urban | l/100 km |  | 4.8 (4.6) |  |
| Extra-urban | l/100 km |  | 3.6 (3.4) |  |
| Total | l/100 km |  | 4.0 (3.8) |  |
| CO2 emissions | g/km |  | 106 (101) |  |
| with 7J x 17'' rims and 205/50 R17 tyres, with 7.5J x 17'' rims and 225/45 R17 tyres and with winter tyres, with 7.5J x 17'' front rims, 8J x 17'' rear rims, 225/45 R17 front tyres and 245/40 R17 rear tyres |
| Urban | l/100 km |  | 5.1 (4.9) |  |
| Extra-urban | l/100 km |  | 3.8 (3.6) |  |
| Combined | l/100 km |  | 4.3 (4.1) |  |
| CO2 emissions | g/km |  | 113 (108) |  |
| with 7.5J x 18'' front rims, 8J x 18'' rear rims, 225/40 R18 front tyres and 245/35 R18 rear tyres |
| Urban | l/100 km |  | 5.3 (5.0) |  |
| Extra-urban | l/100 km |  | 3.9 (3.8) |  |
| Total | l/100 km |  | 4.4 (4.2) |  |
| CO2 emissions | g/km |  | 116 (111) |  |
| Emissions standard |  |  | EU6 |  |

Technical data valid for ACEA countries/Some permitted weights valid only for Germany

Figures in brackets are for vehicles with automatic transmission

1) Height including roof aerial

2) Oil change volume

3) Fuel consumption and CO2 emissions depend on the selected tyre format

The BMW 2 Series Coupe.
220d.

|  |  | BMW 220d Coupe |  |
| --- | --- | --- | --- |
| Body |  |  |  |
| No. of doors/seats |  | 2 / 4 |  |
| Length/width/height 1 (unladen) | mm | 4432 / 1774 / 1418 |  |
| Wheelbase | mm | 2690 |  |
| Front/rear track | mm | 1522 / 1556 |  |
| Ground clearance | mm | 140 |  |
| Turning circle | m | 10,9 |  |
| Fuel tank capacity | approx. l | 52 |  |
| Engine oil 2) | l | 5,0 |  |
| Weight, unladen (DIN/EU) | kg | 1395 / 1470 (1415 / 1490) |  |
| Max. load to DIN | kg | 510 |  |
| Max. permissible weight | kg | 1900 (1920) |  |
| Max. axle load, front/rear | kg | 905/ 1065 (920 / 1065) |  |
| Max. trailer load (12%) braked/unbraked | kg | 1500 / 725 |  |
| Max. roof load/max towbar download | kg | 75 / 75 |  |
| Luggage comp. capacity | l | 390 |  |
| Air resistance | Cd x A | 0.28 x 2.14 |  |
| Engine |  |  |  |
| Type/no. of cylinders/valves |  | in-line / 4 / 4 |  |
| Engine technology |  | BMW TwinPower Turbo technology: variable-geometry turbocharger, Common Rail direct injection with solenoid valve injectors (max. injection pressure: 2000 bar) |
| Effective capacity | cc | 1995 |  |
| Stroke/bore | mm | 90.0 /84.0 |  |
| Compression ratio | :1 | 16.5 |  |
| Fuel type |  | Diesel |  |
| Output | kW/hp | 140 / 190 |  |
| at rpm |  | 4000 |  |
| Torque | Nm | 400 |  |
| at rpm |  | 1750 – 2500 |  |
| Electrical |  |  |  |
| Battery charge/location | Ah/– | 80 (90) / luggage compartment |  |
| Driving Dynamics and Safety |  |
| Front suspension |  | Aluminium double-joint spring strut axle |
| Rear suspension |  | Five-link axle in lightweight steel construction with double elastic bearing |
| Front brakes |  | Single-piston floating-calliper disc brakes |
| Rear brakes |  | Single-piston floating-calliper disc brakes |
| Driving stability systems |  | Standard: DSC incl. ABS, ASC and DTC (Dynamic Traction Control), CBC Cornering Brake Control, DBC Dynamic Brake Control, brake drying function, fading compensation, start-off assistant; linked to xDrive all-wheel-drive system in Integrated Chassis Management (ICM) (220d xDrive) |
| Safety equipment |  | Standard: airbags for driver and front passenger, side airbags for driver and front passenger, head airbags front and rear, three-point inertia-reel seatbelts on all seats with belt tensioner and belt force limiter at the front, crash sensors, Tyre Defect Indicator |
| Steering |  | Electromechanical rack-and-pinion power steering (EPS); optional: Servotronic function, variable sport steering |
| Overall steering ratio | :1 | 15.0 |  |
| Front/rear tyres |  | 205/55 R16 91V |  |
| Front/rear wheels |  | 7J x 16 light-alloy |  |

|  |  | BMW 220d Coupe |  |
| --- | --- | --- | --- |
| Transmission |  |  |  |
| Type of gearbox |  | 6-speed manual (optional: 8-speed Steptronic) |  |
| Gear ratios I | :1 | 4.110 (5.000) |  |
| II | :1 | 2.247 (3.200) |  |
| III | :1 | 1.403 (2.143) |  |
| IV | :1 | 1.000 (1.720) |  |
| V | :1 | 0.802 (1.314) |  |
| VI | :1 | 0.659 (1.000) |  |
| VII | :1 | – (0.822) |  |
| VIII | :1 | – (0.640) |  |
| R | :1 | 3.727 (3.456) |  |
| Final drive | :1 | 3.077 (2.647) |  |
| Performance |  |  |  |
| Weight-to-power ratio (DIN unladen) | kg/kW | 10.0 (10.1) |  |
| Specific power output | kW/l | 70.2 |  |
| Acceleration 0–100 km/h | sec | 7.1 (7.0) |  |
| in 5th gear 80–120 km/h | sec | 7.2 (–) |  |
| Max. speed | km/h | 230 (230) |  |
| BMW EfficientDynamics |  |  |  |
| BMW EfficientDynamics Features included as standard |  | Brake Energy Regeneration with recuperation display, electric power steering (EPS), Auto Start Stop function, Optimum Gearshift Indicator, ECO PRO mode with coasting function (automatic), intelligent lightweight construction, optimised aerodynamic attributes, on-demand operation of ancillary units, map-controlled oil pump, differential and transfer case with optimised warm-up behaviour, tyres with reduced rolling resistance |
| Fuel consumption (EU) 3) |  |  |  |
| with standard wheels and tyres: 7J x 16‘‘ rims and 205/55 R16 tyres |
| Urban | l/100 km | 5.0 (4.6) |  |
| Extra-urban | l/100 km | 3.5 (3.6) |  |
| Total | l/100 km | 4.1 (4.0) |  |
| CO2 emissions | g/km | 107 (104) |  |
| with 7J x 17‘‘ rims and 205/50 R17 tyres, with 7.5J x 17 rims and 225/45 R 17 tyres, with 7.5J x 17‘‘ front rims, 8J x 17‘‘ rear rims and 225/45 R17 front tyres, 245/40 R17 rear tyres |
| Urban | l/100 km | 5.3 (4.8) |  |
| Extra-urban | l/100 km | 3.7 (3.8) |  |
| Total | l/100 km | 4.3 (4.1) |  |
| CO2 emissions | g/km | 112 (109) |  |
| with 7.5J x 18‘‘ front rims, 8J x 18‘‘ rear rims and 225/40 R18 front tyres, 245/35 R18 rear tyres and with winter tyres |
| Urban | l/100 km | 5.4 (5.0) |  |
| Extra-urban | l/100 km | 3.8 (3.9) |  |
| Total | l/100 km | 4.4 (4.3) |  |
| CO2 emissions | g/km | 115 (113) |  |
| Emissions standard |  | EU6 |  |

Technical data valid for ACEA countries/Some permitted weights valid only for Germany

Figures in brackets are for vehicles with automatic transmission

1) Height including roof aerial

2) Oil change volume

3) Fuel consumption and CO2 emissions depend on the selected tyre format

The BMW 2 Series Convertible.
220i, 230i.

|  |  | BMW 220i Convertible | BMW 230i Convertible |
| --- | --- | --- | --- |
| Body |  |  |  |
| No. of doors/seats |  | 2 / 4 | 2 / 4 |
| Length/width/height (unladen) | mm | 4432 / 1774 / 1413 | 4432 / 1774 / 1413 |
| Wheelbase | mm | 2690 | 2690 |
| Front/rear track | mm | 1521 / 1556 | 1521 / 1556 |
| Ground clearance | mm | 140 | 140 |
| Turning circle | m | 10.9 | 10.9 |
| Fuel tank capacity | approx. l | 52 | 52 |
| Engine oil 1) | l | 5.25 | 5.25 |
| Weight, unladen (DIN/EU) | kg | 1540 / 1615 | 1575 / 1650 |
| Max. load to DIN | kg | 470 | 440 |
| Max. permissible weight | kg | 2010 | 2020 |
| Max. axle load, front/rear | kg | 935 / 1145 | 935 / 1130 |
| Max. trailer load (12%) braked/unbraked | kg | 1500 / 750 | 1500 / 750 |
| Max. roof load/max towbar download | kg | – / 75 | – / 75 |
| Luggage comp. capacity | l | 280 – 335 | 280 – 335 |
| Air resistance | Cd x A | 0.32 x 2.13 | 0.33 x 2.13 |
| Engine |  |  |  |
| Type/no. of cylinders/valves |  | in-line / 4 / 4 | in-line / 4 / 4 |
| Engine technology |  | BMW TwinPower Turbo technology: twin-scroll turbocharger, direct injection system High Precision Injection, fully variable valve control (VALVETRONIC) and double VANOS variable camshaft timing |
| Effective capacity | cc | 1998 | 1998 |
| Stroke/bore | mm | 94.6 / 82.0 | 94.6 / 82.0 |
| Compression ratio | :1 | 11.0 | 10.2 |
| Fuel type |  | min RON 91 | min RON 91 |
| Output | kW/hp | 135 / 184 | 185 / 252 |
| at rpm |  | 5000 | 5200 |
| Torque | Nm | 270 | 350 |
| at rpm |  | 1350 – 4600 | 1450 – 4800 |
| Electrical |  |  |  |
| Battery charge/location | Ah/– | 80 / luggage compartment | 80 / luggage compartment |
| Driving Dynamics and Safety |  |
| Front suspension |  | Aluminium double-joint spring strut axle |
| Rear suspension |  | Five-link axle in lightweight steel construction with double elastic bearing |
| Front brakes |  | Single-piston floating-calliper disc brakes |
| Rear brakes |  | Single-piston floating-calliper disc brakes |
| Driving stability systems |  | Standard: DSC incl. ABS, ASC and DTC (Dynamic Traction Control), CBC Cornering Brake Control, DBC Dynamic Brake Control, brake drying function, fading compensation, start-off assistant |
| Safety equipment |  | Standard: driver and front-seat passenger airbags, driver and front-seat passenger side airbags with combined head airbags, three-point automatic seatbelts for all seats, seatbelt tensioners and seatbelt force limiters in front seats, crash sensors, Tyre Defect Indicator |
| Steering |  | Electromechanical rack-and-pinion power steering (EPS); optional: Servotronic function, variable sport steering |
| Overall steering ratio | :1 | 15.0 | 15.0 |
| Front/rear tyres |  | 205/55 R16 91W | 205/50 R17 89Y |
| Front/rear wheels |  | 7J x 16 light-alloy | 7J x 17 light-alloy |

|  |  | BMW 220i Convertible | BMW 230i Convertible |
| --- | --- | --- | --- |
| Transmission |  |  |  |
| Type of gearbox |  | 8-speed Steptronic |
| Gear ratios I | :1 | 5.000 | 5.000 |
| II | :1 | 3.200 | 3.200 |
| III | :1 | 2.143 | 2.143 |
| IV | :1 | 1.720 | 1.720 |
| V | :1 | 1.314 | 1.314 |
| VI | :1 | 1.000 | 1.000 |
| VII | :1 | 0.822 | 0.822 |
| VIII | :1 | 0.640 | 0.640 |
| R | :1 | 3.456 | 3.456 |
| Final drive | :1 | 2.813 | 2.813 |
| Performance |  |  |  |
| Weight-to-power ratio (DIN unladen) | kg/kW | 11.4 | 8.5 |
| Specific power output | kW/l | 67.6 | 92.6 |
| Acceleration 0–100 km/h | sec | 7.7 | 5.9 |
| in 5th gear 80–120 km/h | sec | – | – |
| Max. speed | km/h | 226 | 250 |
| BMW EfficientDynamics |  |  |  |
| BMW EfficientDynamics Features included as standard |  | Brake Energy Regeneration with recuperation display, electric power steering (EPS), Auto Start Stop function, ECO PRO mode with coasting function, intelligent lightweight construction, optimised aerodynamic attributes, on-demand operation of ancillary units, map-controlled oil pump, differential with optimised warm-up behaviour, tyres with reduced rolling resistance |
| Fuel consumption (EU) 2) |  |  |  |
| with standard wheels and tyres: 7J x 16‘‘ rims and 205/55 R16 tyres (BMW 220i Convertible), 7J x 17’’ rims and 205/50 R17 tyres (BMW 230i Convertible) |
| Urban | l/100 km | 7.2 | 7.5 |
| Extra-urban | l/100 km | 5.0 | 5.2 |
| Total | l/100 km | 5.8 | 6.0 |
| CO2 emissions | g/km | 133 | 138 |
| with 7J x 17‘‘ rims and 205/50 R17 tyres (BMW 220i Convertible), with 7.5J x 17 rims and 225/45 R 17 tyres, with 7.5J x 17‘‘ front rims, 8J x 17‘‘ rear rims and 225/45 R17 front tyres, 245/40 R17 rear tyres |
| Urban | l/100 km | 7.5 | 7.7 |
| Extra-urban | l/100 km | 5.2 | 5.4 |
| Total | l/100 km | 6.1 | 6.2 |
| CO2 emissions | g/km | 139 | 143 |
| with 7.5J x 18‘‘ front rims, 8J x 18‘‘ rear rims and 225/40 R18 front tyres, 245/35 R18 rear tyres and with winter tyres |
| Urban | l/100 km | 7.6 | 7.7 |
| Extra-urban | l/100 km | 5.4 | 5.4 |
| Total | l/100 km | 6.2 | 6.2 |
| CO2 emissions | g/km | 141 | 143 |
| Emissions standard |  | EU6 | EU6 |

Technical data valid for ACEA countries/Some permitted weights valid only for Germany

1)  Oil change volume

2)  Fuel consumption and CO2 emissions depend on the selected tyre format

The BMW 2 Series Convertible.
M240i.

|  |  |  | BMW M240i Convertible |
| --- | --- | --- | --- |
| Body |  |  |  |  |
| No. of doors/seats |  |  | 2 / 4 |  |
| Length/width/height (unladen) | mm |  | 4454 / 1774 / 1403 |  |
| Wheelbase | mm |  | 2690 |  |
| Front/rear track | mm |  | 1516 / 1534 |  |
| Ground clearance | mm |  | 130 |  |
| Turning circle | m |  | 10.9 |  |
| Fuel tank capacity | approx. l |  | 52 |  |
| Engine oil 1) | l |  | 6.5 |  |
| Weight, unladen (DIN/EU) | kg |  | 1620 / 1695 (1635 / 1710) |  |
| Max. load to DIN | kg |  | 430 |  |
| Max. permissible weight | kg |  | 2045 (2060) |  |
| Max. axle load, front/rear | kg |  | 975 / 1145 |  |
| Max. trailer load (12%) braked/unbraked | kg |  | – / – |  |
| Max. roof load/max towbar download | kg |  | – / – |  |
| Luggage comp. capacity | l |  | 280 – 335 |  |
| Air resistance | Cd x A |  | 0.36 x 2.13 |  |
| Engine |  |  |  |  |
| Type/no. of cylinders/valves |  |  | in-line / 6 / 4 |  |
| Engine technology |  | M Performance TwinPower Turbo technology: twin-scroll turbocharger, direct injection system High Precision Injection, fully variable valve control (VALVETRONIC) and double VANOS variable camshaft timing |
| Effective capacity | cc |  | 2998 |  |
| Stroke/bore | mm |  | 94.6 / 82.0 |  |
| Compression ratio | :1 |  | 11.0 |  |
| Fuel type |  |  | min. RON 91 |  |
| Output | kW/hp |  | 250 / 340 |  |
| at rpm |  |  | 5500 |  |
| Torque | Nm |  | 500 |  |
| at rpm |  |  | 1520 – 4500 |  |
| Electrical |  |  |  |  |
| Battery charge/location | Ah/– |  | 80 / luggage compartment |  |
| Driving Dynamics and Safety |  |
| Front suspension |  | Aluminium double-joint spring strut axle with M-specific elastokinematics |
| Rear suspension |  | Five-link axle in lightweight steel construction with double elastic bearing |
| Front brakes |  | Four-piston fixed-calliper disc brakes |
| Rear brakes |  | Two-piston fixed-calliper disc brakes |
| Driving stability systems |  | Standard: DSC incl. ABS, ASC and DTC (Dynamic Traction Control), CBC Cornering Brake Control, DBC Dynamic Brake Control, brake drying function, fading compensation, start-off assistant |
| Safety equipment |  | Standard: driver and front-seat passenger airbags, driver and front-seat passenger side airbags with combined head airbags, three-point automatic seatbelts for all seats, seatbelt tensioners and seatbelt force limiters in front seats, crash sensors, Tyre Defect Indicator |
| Steering |  | Electromechanical rack-and-pinion power steering (EPS), variable sport steering |
| Overall steering ratio | :1 |  | 14.5 |  |
| Front/rear tyres |  |  | 225/40 ZR18 88Y 245/35 ZR 18 92Y XL |  |
| Front/rear wheels |  |  | 7.5J x 18 light-alloy/ 8J x 18 light-alloy |  |

|  |  |  | BMW M240i Convertible |
| --- | --- | --- | --- |
| Transmission |  |  |  |  |
| Type of gearbox |  | 6-speed manual (optional: 8-speed Steptronic Sport transmission) |
| Gear ratios I | :1 |  | 4.110 (5.000) |  |
| II | :1 |  | 2.315 (3.200) |  |
| III | :1 |  | 1.542 (2.143) |  |
| IV | :1 |  | 1.179 (1.720) |  |
| V | :1 |  | 1.000 (1.314) |  |
| VI | :1 |  | 0.846 (1.000) |  |
| VII | :1 |  | – (0.822) |  |
| VIII | :1 |  | – (0.640) |  |
| R | :1 |  | 3.727 (3.456) |  |
| Final drive | :1 |  | 3.077 (2.813) |  |
| Performance |  |  |  |  |
| Weight-to-power ratio (DIN unladen) | kg/kW |  | 6.5 (6.5) |  |
| Specific power output | kW/l |  | 83.4 |  |
| Acceleration 0–100 km/h | sec. |  | 4.9 (4.7) |  |
| in 5th gear 80–120 km/h | sec. |  | 5.3 (–) |  |
| Max. speed | km/h |  | 250 (250) |  |
| BMW EfficientDynamics |  |  |  |  |
| BMW EfficientDynamics Features included as standard |  | Brake Energy Regeneration with recuperation display, electric power steering (EPS), Auto Start Stop function, Optimum Gearshift Indicator, ECO PRO mode with coasting function (automatic), intelligent lightweight construction, optimised aerodynamic attributes, on-demand operation of ancillary units, map-controlled oil pump, differential with optimised warm-up behaviour, tyres with reduced rolling resistance |
| Fuel consumption (EU) |  |  |  |  |
| Urban | l/100 km |  | 11.2 (9.8) |  |
| Extra-urban | l/100 km |  | 6.6 (6.0) |  |
| Total | l/100 km |  | 8.3 (7.4) |  |
| CO2 emissions | g/km |  | 189 (169) |  |
| Emissions standard |  |  | EU6 |  |

Technical data valid for ACEA countries/Some permitted weights valid only for Germany

Figures in brackets are for vehicles with automatic transmission

1)  Oil change volume

Output and torque diagrams.
The BMW 2 Series.
220i.

The BMW 2 Series.
230i.

The BMW 2 Series.
M240i.

The BMW 2 Series.
220d.

Exterior and interior dimensions.
The BMW 2 Series Coupe.

The BMW 2 Series Convertible.