Specifications.

The new BMW 6 Series Gran Turismo.

640i xDrive.

|  |  |  | BMW 640i xDrive Gran Turismo |
| --- | --- | --- | --- |
| Body |  |  |
| No of doors/seats |  |  | 4 / 5 |
| Length/width/height 1) (unladen) | mm |  | 5091 / 1902 / 1540 |
| Wheelbase | mm |  | 3070 |
| Track, front/rear | mm |  | 1615 / 1647 |
| Ground clearance | mm |  | 138 |
| Turning circle | m |  | 12.5 |
| Fuel tank capacity | approx. l |  | 68 |
| Engine oil 2) | l |  | 6.5 |
| Weight, unladen, to DIN/EU | kg |  | 1835 / 1910 |
| Max load to DIN | kg |  | 660 |
| Max permissible weight | kg |  | 2515 |
| Max axle load, front/rear | kg |  | 1220 / 1410 |
| Max trailer load, braked (12%)/unbraked | kg |  | 2100 / 750 |
| Max roofload/max towbar download | kg |  | 75 / 100 |
| Luggage comp capacity | l |  | 610 – 1800 |
| Air resistance | Cd x A |  | 0.27 x 2.54 |
| Power Unit |  |  |
| Config/No of cyls/valves |  |  | in-line / 6 / 4 |
| Engine technology |  | BMW TwinPower Turbo technology: TwinScroll turbocharger, High Precision Direct Injection, VALVETRONIC fully variable valve control, Double-VANOS variable camshaft timing |
| Effective capacity | cc |  | 2998 |
| Stroke/bore | mm |  | 94.6 / 82.0 |
| Compression ratio | :1 |  | 11.0 |
| Fuel |  |  | min. RON 91 |
| Max output | kW/hp |  | 250 / 340 |
| at | rpm |  | 5500 – 6500 |
| Max torque | Nm |  | 450 |
| at | rpm |  | 1380 – 5200 |
| Electrical System |  |
| Battery/installation | Ah/– |  | 90 / Luggage compartment |
| Driving Dynamics and Safety |  |  |
| Suspension, front |  | Aluminium double track control arm axle with separate lower track arm level, small steering roll radius, transverse force compensation, anti-dive |
| Suspension, rear |  | Five-link axle in aluminium lightweight construction, double elastic bearing, air suspension with automatic self-levelling |
| Brakes, front |  | Four-piston fixed-calliper disc brakes / vented |
| Brakes, rear |  | Single-piston floating-calliper disc brakes / vented |
| Driving stability systems |  | Standard: DSC incl. ABS and DTC (Dynamic Traction Control), CBC (Cornering Brake Control), DBC (Dynamic Brake Control), Dry Braking function, Fading Compensation, Start-Off Assistant, DSC networked with xDrive all-wheel-drive system (BMW 640i xDrive); Optional: Dynamic Damper Control, Adaptive Drive |
| Safety equipment |  | Standard: airbags for driver and front passenger, side airbags for driver and front passenger, head airbags for front and rear seats, three-point inertia-reel seatbelts on all seats with belt stopper, belt latch tensioner and belt force limiter at the front seats, crash-active front head restraints, crash sensors, tyre pressure indicator |
| Steering |  | Electric Power Steering (EPS), optional: Integral Active Steering |
| Steering ratio, overall | :1 |  | 16.3 |
| Tyres, front/rear |  |  | 225/60 R17 99Y |
| Rims, front/rear |  |  | 7.5J x 17 light-alloy |

|  |  |  | BMW 640i xDrive Gran Turismo |
| --- | --- | --- | --- |
| Transmission |  |  |
| Type of transmission |  |  | 8-speed Steptronic Transmission |
| Gear ratios I | :1 |  | 5.000 |
| II | :1 |  | 3.200 |
| III | :1 |  | 2.143 |
| IV | :1 |  | 1.720 |
| V | :1 |  | 1.314 |
| VI | :1 |  | 1.000 |
| VII | :1 |  | 0.822 |
| VIII | :1 |  | 0.640 |
| R | :1 |  | 3.456 |
| Final drive | :1 |  | 3.077 |
| Performance |  |  |
| Power-to-weight ratio (DIN) | kg/kW |  | 7.3 |
| Output per litre | kW/l |  | 83.4 |
| Acceleration 0–100 km/h | s |  | 5.3 |
| In 5th gear 80–120 km/h | s |  | – |
| Top speed | km/h |  | 250 |
| BMW EfficientDynamics |  |  |
| BMW EfficientDynamics standard features |  | Brake Energy Regeneration with recuperation display, Electric Power Steering, Auto Start Stop function, Optimum Shift Indicator, ECO PRO mode with coasting function, BMW EfficientLightweight, optimised aerodynamic attributes, active air flap control, automatic rear spoiler, on-demand operation of ancillary units, map-regulated oil pump, differential and transfer case (BMW 640i xDrive) with optimised warm-up behaviour, tyres with reduced rolling resistance |
| Fuel Consumption in EU Cycle 3) |
| With standard tyres |
| Urban | l/100 km |  | 10.5 |
| Extra-urban | l/100 km |  | 6.1 |
| Combined | l/100 km |  | 7.7 |
| CO2 | g/km |  | 177 |
| With 8J x 18 wheels and 245/50 R18 tyres. With 8.5J x 19 wheels and 245/45 R19 tyres |
| Urban | l/100 km |  | 10.8 |
| Extra-urban | l/100 km |  | 6.4 |
| Combined | l/100 km |  | 8.0 |
| CO2 | g/km |  | 183 |
| With 8.5J x 19 wheels (front), 9.5J x 19 wheels (rear) and 245/45 R19 tyres (front), 275/40 R19 tyres (rear), with 8.5J x 20 wheels (front), 10J x 20 wheels (rear) and 245/40 R20 tyres (front), 275/35 R20 tyres (rear), with runflat tyres and with winter tyres |
| Urban | l/100 km |  | 11.1 |
| Extra-urban | l/100 km |  | 6.5 |
| Combined | l/100 km |  | 8.2 |
| CO2 | g/km |  | 187 |
| Emission rating |  |  | EU6 |

Specifications apply to ACEA markets/data relevant to homologation applies in part only to Germany (weight)

1) Height including roof fin

2) Oil change

3) Fuel consumption and CO2 emissions depend on the selected tyre format

The new BMW 6 Series Gran Turismo.
630d, 630d xDrive.

|  |  | BMW 630d Gran Turismo |  |
| --- | --- | --- | --- |
| Body |  |  |
| No of doors/seats |  | 4 / 5 |  |
| Length/width/height 1) (unladen) | mm | 5091 / 1902 / 1538 |  |
| Wheelbase | mm | 3070 |  |
| Track, front/rear | mm | 1615 / 1649 |  |
| Ground clearance | mm | 138 |  |
| Turning circle | m | 12.3 |  |
| Fuel tank capacity | approx. l | 66 |  |
| Engine oil 2) | l | 6.5 |  |
| Weight, unladen, to DIN/EU | kg | 1825 / 1900 |  |
| Max load to DIN | kg | 680 |  |
| Max permissible weight | kg | 2510 |  |
| Max axle load, front/rear | kg | 1180 / 1425 |  |
| Max trailer load, braked (12%)/unbraked | kg | 2100 / 750 |  |
| Max roofload/max towbar download | kg | 75 / 100 |  |
| Luggage comp capacity | l | 610 – 1800 |  |
| Air resistance | Cd x A | 0.25 x 2.54 |  |
| Power Unit |  |  |
| Config/No of cyls/valves |  | in-line / 6 / 4 |  |
| Engine technology |  | BMW TwinPower Turbo technology: turbocharger with variable inlet geometry, common-rail direct injection with piezo injectors (max. injection pressure: 2500 bar) |
| Effective capacity | cc | 2993 |  |
| Stroke/bore | mm | 90.0 / 84.0 |  |
| Compression ratio | :1 | 16.5 |  |
| Fuel |  | Diesel |  |
| Max output | kW/hp | 195 / 265 |  |
| at | rpm | 4000 |  |
| Max torque | Nm | 620 |  |
| at | rpm | 2000 – 2500 |  |
| Electrical System |  |
| Battery/installation | Ah/– | 90 / Luggage compartment |  |
| Driving Dynamics and Safety |  |  |
| Suspension, front |  | Aluminium double track control arm axle with separate lower track arm level, small steering roll radius, transverse force compensation, anti-dive |
| Suspension, rear |  | Five-link axle in aluminium lightweight construction, double elastic bearing, air suspension with automatic self-levelling |
| Brakes, front |  | Four-piston fixed-calliper disc brakes / vented |
| Brakes, rear |  | Single-piston floating-calliper disc brakes / vented |
| Driving stability systems |  | Standard: DSC incl. ABS and DTC (Dynamic Traction Control), CBC (Cornering Brake Control), DBC (Dynamic Brake Control), Dry Braking function, Fading Compensation, Start-Off Assistant, DSC networked with xDrive all-wheel-drive system (BMW 630d xDrive); Optional: Dynamic Damper Control, Adaptive Drive |
| Safety equipment |  | Standard: airbags for driver and front passenger, side airbags for driver and front passenger, head airbags for front and rear seats, three-point inertia-reel seatbelts on all seats with belt stopper, belt latch tensioner and belt force limiter at the front seats, crash-active front head restraints, crash sensors, tyre pressure indicator |
| Steering |  | Electric Power Steering (EPS), optional: Integral Active Steering |
| Steering ratio, overall | :1 | 16.3 |  |
| Tyres, front/rear |  | 225/60 R17 99Y |  |
| Rims, front/rear |  | 7.5J x 17 light-alloy |  |

|  |  | BMW 630d Gran Turismo |  |
| --- | --- | --- | --- |
| Transmission |  |  |
| Type of transmission |  | 8-speed Steptronic Transmission |  |
| Gear ratios I | :1 | 5.000 |  |
| II | :1 | 3.200 |  |
| III | :1 | 2.143 |  |
| IV | :1 | 1.720 |  |
| V | :1 | 1.313 |  |
| VI | :1 | 1.000 |  |
| VII | :1 | 0.823 |  |
| VIII | :1 | 0.640 |  |
| R | :1 | 3.478 |  |
| Final drive | :1 | 2.563 |  |
| Performance |  |  |
| Power-to-weight ratio (DIN) | kg/kW | 9.4 |  |
| Output per litre | kW/l | 65.2 |  |
| Acceleration 0–100 km/h | s | 6.1 |  |
| In 5th gear 80–120 km/h | s | – |  |
| Top speed | km/h | 250 |  |
| BMW EfficientDynamics |  |  |
| BMW EfficientDynamics standard features |  | Brake Energy Regeneration with recuperation display, Electric Power Steering, Auto Start Stop function, Optimum Shift Indicator, ECO PRO mode with coasting function, BMW EfficientLightweight, optimised aerodynamic attributes, active air flap control, automatic rear spoiler, on-demand operation of ancillary units, map-regulated oil pump, differential and transfer case (BMW 630d xDrive) with optimised warm-up behaviour, tyres with reduced rolling resistance, BMW Blue Performance technology |
| Fuel Consumption in EU Cycle 3) |
| With standard tyres |
| Urban | l/100 km | 5.6 |  |
| Extra-urban | l/100 km | 4.5 |  |
| Combined | l/100 km | 4.9 |  |
| CO2 | g/km | 129 |  |
| With 8J x 18 wheels and 245/50 R18 tyres. With 8.5J x 19 wheels and 245/45 R19 tyres |
| Urban | l/100 km | 5.9 |  |
| Extra-urban | l/100 km | 4.7 |  |
| Combined | l/100 km | 5.1 |  |
| CO2 | g/km | 135 |  |
| With 8.5J x 19 wheels (front), 9.5J x 19 wheels (rear) and 245/45 R19 tyres (front), 275/40 R19 tyres (rear), with 8.5J x 20 wheels (front), 10J x 20 wheels (rear) and 245/40 R20 tyres (front), 275/35 R20 tyres (rear), with runflat tyres and with winter tyres |
| Urban | l/100 km | 6.1 |  |
| Extra-urban | l/100 km | 4.9 |  |
| Combined | l/100 km | 5.3 |  |
| CO2 | g/km | 139 |  |
| Emission rating |  | EU6 |  |

Specifications apply to ACEA markets/data relevant to homologation applies in part only to Germany (weight)

1) Height including roof fin

2) Oil change

3) Fuel consumption and CO2 emissions depend on the selected tyre format

Output and torque diagrams.

The new BMW 6 Series Gran Turismo.

640i xDrive.

The new BMW 6 Series Gran Turismo.

630d.

Exterior and interior dimensions.

The new BMW 6 Series Gran Turismo.