Specifications.

BMW i8 Roadster.

|  |  | BMW i8 Roadster |
| --- | --- | --- |
| Body |  |  |
| No of doors/seats |  | 2 / 2 |
| Length/width/height (unladen) | mm | 4689 / 1942 / 1291 |
| Wheelbase | mm | 2800 |
| Track, front/rear | mm | 1644 / 1721 |
| Ground clearance | mm | 117 |
| Turning circle | m | 12.3 |
| Axle load distribution (unladen) f / r | % / % | 49 / 51 |
| Weight, unladen, to DIN/EU | kg | 1595 / 1670 |
| Max load to DIN | kg | 370 |
| Height of centre of gravity | mm | < 460 |
| Luggage comp capacity | l | 88 |
| Air resistance | Cd x A | 0.28 x 2.15 |
| Power unit |  |  |
| Drive concept |  | Hybrid-specific all-wheel drive: combustion engine sends power to the rear wheels, electric motor sends power to the front wheels |
| Maximum system output | kW/hp | 275 / 374 |
| Petrol engine |  |  |
| Engine technology |  | BMW TwinPower Turbo technology: Highly turbocharged engine, High Precision Direct Injection, VALVETRONIC fully variable valve timing |
| Config / no of cyls / valves |  | In-line / 3 / 4 |
| Effective capacity | cc | 1499 |
| Stroke / bore | mm | 94.6 / 82.0 |
| Compression ratio | :1 | 9.5 |
| Fuel |  | Min. RON 91 Data on rated output and fuel consumption is based on RON 98 |
| Output | kW | 170 |
| at | rpm | 5800 |
| Torque | Nm | 320 |
| at | rpm | 3700 |
| Fuel tank capacity | l | 30, optional: 42 |
| Electric motor |  |  |
| Motor technology |  | BMW eDrive technology: Hybrid synchronous electric motor with power electronics, integrated charging module and generator function for energy recuperation |
| Max output | kW/hp | 105 / 143 |
| at | rpm | 4800 |
| Rated output | kW | 75 |
| at | rpm | 4800 |
| Torque | Nm | 250 |
| Recuperation output | kW | 60 |
| High-voltage battery |  |  |
| Storage technology |  | Lithium-ion |
| Voltage | V | 355 |
| Battery cell capacity | Ah | 34 |
| Energy capacity (gross) | kWh | 11.6 |
| Charging time for 80 % charge |  | < 2 h at 3.6 kW (16 A / 230 V) |
| Charging time for 100 % charge |  | < 3 h at 3.6 kW (16 A / 230 V) |
| Charging time for 100 % charge |  | < 4.5 h from domestic power socket (10 A / 230 V) |

|  |  | BMW i8 Roadster |
| --- | --- | --- |
| Driving dynamics |  |  |
| Steering |  | Electric Power Steering (EPS) |
| Steering ratio, overall | :1 | 16.0 |
| Tyres, front/rear |  | 195/50 R20 / 215/45 R20 |
| Rims, front/rear |  | 7J x 20 forged aluminium / 7.5J x 20 forged aluminium |
| Transmission |  |  |
| Type of transmission: combustion engine |  | 6-speed automatic |
| Type of transmission: electric motor |  | 2-speed automatic |
| Performance |  |  |
| Power-to-weight ratio (DIN) | kg / kW | 5.8 |
| Output per litre: petrol engine | kW / l | 113.3 |
| Acceleration 0–100 km/h | s | 4.6 |
| 80–120 km/h | s | 2.6 |
| in 4th/5th gear 80–120 km/h | s | 3.5 / 4.1 |
| Top speed | km/h | 250 (electronically governed) |
| Top speed (electric) | km/h | 120 |
| Total range* | km | 440 (600 with optional 42-litre tank) |
| Electric range* | km | 53 |
| Fuel consumption / emissions in the EU cycle* |  |  |
| Fuel consumption combined | l/100 km | 2.1 |
| CO2 emissions combined | g/km | 46 |
| Electricity consumption combined | kWh/100 km | 14.5 |
| Emission rating |  | EU6 |

Provisional specifications apply to ACEA markets/data relevant to homologation applies in part only to Germany (weight)

*The fuel consumption, CO2 emissions, power consumption and operating range figures were determined according to the European Regulation (EC) 715/2007 in the version applicable. The figures refer to a vehicle with basic configuration in Germany and the range shown considers the different sizes of the selected wheels/tyres and the selected items of optional equipment.

The values are already based on the new WLTP test cycle and are translated back into NEDC-equivalent values in order to ensure comparability between the vehicles. [With respect to these vehicles, for vehicle-related taxes or other duties based (at least inter alia) on CO2 emissions, the CO2 values may differ from the values stated here (depending on national legislation).]

The CO2 efficiency specifications are determined according to Directive 1999/94/EC and the latest version of the Pkw-EnVKV, and based (for classification) on the fuel consumption and CO2 values as per the NEDC cycle.

Further information on official fuel consumption figures and specific CO2 emission values of new passenger cars is included in the following guideline: 'Leitfaden über den Kraftstoffverbrauch, die CO2-Emissionen und den Stromverbrauch neuer Personenkraftwagen' (Guideline for fuel consumption, CO2 emissions and electric power consumption of new passenger cars), which can be obtained free of charge from all dealerships and at https://www.dat.de/en/offers/publications/guideline-for-fuel-consumption.html.