Technical specifications.

The new BMW Z4.

Z4 sDrive20i.

|  |  | BMW Z4 sDrive20i |
| --- | --- | --- |
| Body |  |  |
| No of doors/seats |  | 2 / 2 |
| Length/width/height (unladen) | mm | 4324 / 1864 / 1304 |
| Wheelbase | mm | 2470 |
| Track, front/rear | mm | 1609 / 1616 |
| Ground clearance | mm | 117 |
| Turning circle | m | 11.0 |
| Fuel tank capacity | approx. l | 52 |
| Engine oil 1) | l | 5.25 |
| Weight, unladen, to DIN/EU | kg | 1405 / 1480 |
| Max load to DIN | kg | 335 |
| Max permissible weight | kg | 1740 |
| Max axle load, front/rear | kg | 830 / 935 |
| Max trailer load, braked (12%)/unbraked | kg | – / – |
| Max roofload/max towbar download | kg | – / – |
| Luggage comp capacity | l | 281 |
| Air resistance | cd x A | 0.29 x 2.07 |
| Power Unit |  |  |
| Config/No of cyls/valves |  | In-line / 4 / 4 |
| Engine technology |  | BMW TwinPower Turbo technology: TwinScroll turbocharger, High Precision Direct Injection, VALVETRONIC fully variable valve control, Double-VANOS variable camshaft timing |
| Effective capacity | cc | 1998 |
| Stroke/bore | mm | 94.6 / 82.0 |
| Compression ratio | :1 | 10.2 |
| Fuel |  | Min. RON 91 |
| Max output | kW | 145 |
| at | rpm | 4500 – 6500 |
| Max torque | Nm | 320 |
| at | rpm | 1450 – 4200 |
| Electrical System |  |
| Battery/installation | Ah/– | 80 / luggage compartment |
| Driving Dynamics and Safety |  |  |
| Suspension, front |  | Double-joint spring-strut axle in lightweight aluminium-steel construction, hydraulically damped torque strut bearings |
| Suspension, rear |  | Five-link axle in lightweight aluminium-steel construction |
| Brakes, front |  | Single-piston floating-calliper disc brakes, vented |
| Brakes, rear |  | Single-piston floating-calliper disc brakes, vented |
| Driving stability systems |  | Standard: DSC incl. ABS and DTC (Dynamic Traction Control), CBC (Cornering Brake Control), DBC (Dynamic Brake Control), Dry Braking function, Fading Compensation, Start-Off Assistant; optional: Adaptive M suspension |
| Safety equipment |  | Standard: airbags for driver and front passenger, side airbags for driver and front passenger with combined head airbags, three-point inertia-reel seatbelts with belt stopper, belt latch tensioner and belt force limiter, crash sensors, rollover protection system, tyre pressure indicator |
| Steering |  | Electric Power Steering (EPS) with Servotronic function, variable sport steering |
| Steering ratio, overall | :1 | 15.1 |
| Tyres, front/rear |  | 225/50 R17 98Y XL / 255/45 R17 98Y |
| Rims, front/rear |  | 7.5J x 17 light-alloy / 8.5J x 17 light-alloy |

|  |  | BMW Z4 sDrive20i |
| --- | --- | --- |
| Transmission |  |  |
| Type of transmission |  | Eight-speed Steptronic transmission |
| Gear ratios I | :1 | 5.250 |
| II | :1 | 3.360 |
| III | :1 | 2.172 |
| IV | :1 | 1.720 |
| V | :1 | 1.316 |
| VI | :1 | 1.000 |
| VII | :1 | 0.822 |
| VIII | :1 | 0.640 |
| R | :1 | 3.712 |
| Final drive | :1 | 3.154 |
| Performance |  |  |
| Power-to-weight ratio (DIN) | kg/kW | 9.7 |
| Output per litre | kW/l | 72.6 |
| Acceleration 0–100 km/h | s | 6.6 |
| Top speed | km/h | 240 |
| BMW EfficientDynamics |  |  |
| BMW EfficientDynamics standard features |  | Brake Energy Regeneration with recuperation display, Electric Power Steering (EPS), Auto Start Stop function, Optimum Shift Indicator, ECO PRO mode with coasting function and Proactive Driving Assistant, BMW EfficientLightweight, optimised aerodynamic attributes, active air flap control, on-demand operation of ancillary units, map-regulated oil pump, differential with optimised warm-up behaviour, tyres with reduced rolling resistance |
| Fuel Consumption ECE |
| Urban | l/100 km | 7.4 – 7.3 |
| Extra-urban | l/100 km | 5.4 – 5.0 |
| Combined | l/100 km | 6.1 – 6.0 |
| CO2 | g/km | 139 – 137 |
| Emission rating |  | Euro 6d-TEMP |

Specifications apply to ACEA markets/data relevant to homologation applies in part only to Germany (weight)

1) Oil change

The fuel consumption, CO2 emissions and electric power consumption figures were determined according to the European Regulation (EC) 715/2007 in the version applicable. The figures refer to a vehicle with basic configuration in Germany. The range shown considers the different sizes of the selected wheels/tyres and the selected items of optional equipment, and may vary during configuration.

The values are already based on the new WLTP test cycle and are translated back into NEDC-equivalent values in order to ensure comparability between the vehicles. With respect to these vehicles, for vehicle-related taxes or other duties based (at least inter alia) on CO2 emissions, the CO2 values may differ from the values stated here (depending on national legislation).

Further information on official fuel consumption figures and specific CO2 emission values of new passenger cars is included in the following guideline: 'Leitfaden über den Kraftstoffverbrauch, die CO2-Emissionen und den Stromverbrauch neuer Personenkraftwagen' (Guide to the fuel economy, CO2 emissions and electric power consumption of new passenger cars), which can be obtained free of charge from all dealerships, from Deutsche Automobil Treuhand GmbH (DAT), Hellmuth-Hirth-Str. 1, 73760 Ostfildern-Scharnhausen and at https://www.dat.de/co2/.

The fuel consumption, CO2 emissions and electric power consumption figures were determined according to the European Regulation (EC) 715/2007 in the version applicable. The figures refer to a vehicle with basic configuration in Germany. The range shown considers the different sizes of the selected wheels/tyres and the selected items of optional equipment, and may vary during configuration.

The values are already based on the new WLTP test cycle and are translated back into NEDC-equivalent values in order to ensure comparability between the vehicles. With respect to these vehicles, for vehicle-related taxes or other duties based (at least inter alia) on CO2 emissions, the CO2 values may differ from the values stated here (depending on national legislation).

Further information on official fuel consumption figures and specific CO2 emission values of new passenger cars is included in the following guideline: 'Leitfaden über den Kraftstoffverbrauch, die CO2-Emissionen und den Stromverbrauch neuer Personenkraftwagen' (Guide to the fuel economy, CO2 emissions and electric power consumption of new passenger cars), which can be obtained free of charge from all dealerships, from Deutsche Automobil Treuhand GmbH (DAT), Hellmuth-Hirth-Str. 1, 73760 Ostfildern-Scharnhausen and at https://www.dat.de/co2/.

The new BMW Z4.
Z4 M40i.

|  |  | BMW Z4 M40i |
| --- | --- | --- |
| Body |  |  |
| No of doors/seats |  | 2 / 2 |
| Length/width/height (unladen) | mm | 4324 / 1864 / 1304 |
| Wheelbase | mm | 2470 |
| Track, front/rear | mm | 1594 / 1589 |
| Ground clearance | mm | 114 |
| Turning circle | m | 11.0 |
| Fuel tank capacity | approx. l | 52 |
| Engine oil 1) | l | 6.5 |
| Weight, unladen, to DIN/EU | kg | 1535 / 1610 |
| Max load to DIN | kg | 325 |
| Max permissible weight | kg | 1860 |
| Max axle load, front/rear | kg | 865 / 995 |
| Max trailer load, braked (12%)/unbraked | kg | – / – |
| Max roofload/max towbar download | kg | – / – |
| Luggage comp capacity | l | 281 |
| Air resistance | cd x A | 0.31 x 2.07 |
| Power Unit |  |  |
| Config/No of cyls/valves |  | In-line / 6 / 4 |
| Engine technology |  | M Performance TwinPower Turbo technology: TwinScroll turbocharger, High Precision Direct Injection, VALVETRONIC fully variable valve control, Double-VANOS variable camshaft timing |
| Effective capacity | cc | 2998 |
| Stroke/bore | mm | 94.6 / 82.0 |
| Compression ratio | :1 | 11.0 |
| Fuel |  | Min. RON 91 |
| Max output | kW/hp | 250 / 340 |
| at | rpm | 5000 – 6500 |
| Max torque | Nm | 500 |
| at | rpm | 1600 – 4500 |
| Electrical System |  |
| Battery/installation | Ah/– | 90 / luggage compartment |
| Driving Dynamics and Safety |  |  |
| Suspension, front |  | Double-joint spring-strut axle in lightweight aluminium-steel construction, hydraulically damped torque strut bearings |
| Suspension, rear |  | Five-link axle in lightweight aluminium-steel construction |
| Brakes, front |  | Four-piston fixed-calliper disc brakes, vented |
| Brakes, rear |  | Single-piston floating-calliper disc brakes, vented |
| Driving stability systems |  | Standard: DSC incl. ABS and DTC (Dynamic Traction Control), CBC (Cornering Brake Control), DBC (Dynamic Brake Control), Dry Braking function, Fading Compensation, Start-Off Assistant, Adaptive M suspension, M Sport differential |
| Safety equipment |  | Standard: airbags for driver and front passenger, side airbags for driver and front passenger with combined head airbags, three-point inertia-reel seatbelts with belt stopper, belt latch tensioner and belt force limiter, crash sensors, rollover protection system, tyre pressure indicator |
| Steering |  | Electric Power Steering (EPS) with Servotronic function, variable sport steering |
| Steering ratio, overall | :1 | 15.1 |
| Tyres, front/rear |  | 255/40 ZR18 95Y / 275/40 ZR18 99Y |
| Rims, front/rear |  | 9J x 18 light-alloy / 10J x 18 light-alloy |

|  |  | BMW Z4 M40i |
| --- | --- | --- |
| Transmission |  |  |
| Type of transmission |  | Eight-speed Steptronic transmission |
| Gear ratios I | :1 | 5.250 |
| II | :1 | 3.360 |
| III | :1 | 2.172 |
| IV | :1 | 1.720 |
| V | :1 | 1.316 |
| VI | :1 | 1.000 |
| VII | :1 | 0.822 |
| VIII | :1 | 0.640 |
| R | :1 | 3.712 |
| Final drive | :1 | 3.154 |
| Performance |  |  |
| Power-to-weight ratio (DIN) | kg/kW | 6.1 |
| Output per litre | kW/l | 83.4 |
| Acceleration 0–100 km/h | s | 4.6 |
| Top speed | km/h | 250 |
| BMW EfficientDynamics |  |  |
| BMW EfficientDynamics standard features |  | Brake Energy Regeneration with recuperation display, Electric Power Steering (EPS), Auto Start Stop function, Optimum Shift Indicator, ECO PRO mode with coasting function and Proactive Driving Assistant, BMW EfficientLightweight, optimised aerodynamic attributes, active air flap control, on-demand operation of ancillary units, map-regulated oil pump, differential with optimised warm-up behaviour |
| Fuel Consumption ECE |
| Urban | l/100 km | 9.2 – 9.2 |
| Extra-urban | l/100 km | 6.3 – 5.9 |
| Combined | l/100 km | 7.4 – 7.1 |
| CO2 | g/km | 168 – 162 |
| Emission rating |  | Euro 6d-TEMP |

Specifications apply to ACEA markets/data relevant to homologation applies in part only to Germany (weight)

1) Oil change

The fuel consumption, CO2 emissions and electric power consumption figures were determined according to the European Regulation (EC) 715/2007 in the version applicable. The figures refer to a vehicle with basic configuration in Germany. The range shown considers the different sizes of the selected wheels/tyres and the selected items of optional equipment, and may vary during configuration.

The values are already based on the new WLTP test cycle and are translated back into NEDC-equivalent values in order to ensure comparability between the vehicles. With respect to these vehicles, for vehicle-related taxes or other duties based (at least inter alia) on CO2 emissions, the CO2 values may differ from the values stated here (depending on national legislation).

Further information on official fuel consumption figures and specific CO2 emission values of new passenger cars is included in the following guideline: 'Leitfaden über den Kraftstoffverbrauch, die CO2-Emissionen und den Stromverbrauch neuer Personenkraftwagen' (Guide to the fuel economy, CO2 emissions and electric power consumption of new passenger cars), which can be obtained free of charge from all dealerships, from Deutsche Automobil Treuhand GmbH (DAT), Hellmuth-Hirth-Str. 1, 73760 Ostfildern-Scharnhausen and at https://www.dat.de/co2/.

Output and torque diagrams.

The new BMW Z4.

Z4 sDrive20i.

The new BMW Z4.

Z4 M40i.

Exterior and interior dimensions.

The new BMW X5.

*dimensions in cm