# Technical Specifications

| Body |  | Z4 2.0i | Z4 2.5i | Z4 2.5si | Z4 3.0si |
| --- | --- | --- | --- | --- | --- |
| No of doors/seats l |  | 2/2 | 2/2 | 2/2 | 2/2 |
| Length/width/height (unladen) ) | mm | 4,091/1,781/1,299 | 4,091/1,781/1,299 | 4,091/1,781/1,299 | 4,091/1,781/1,299 |
| Wheelbase | mm | 2,495 | 2,495 | 2,495 | 2,495 |
| Track, front/rear wgsdfg | mm | 1,473/1,523 | 1,473/1,523 | 1,473/1,523 | 1,473/1,523 |
| Turning circle | m | 9.8 | 9.8 | 9.8 | 9.8 |
| Tank capacity | approx. ltr | 55 | 55 | 55 | 55 |
| Cooling system, incl heating l | ltr | 8.0 | 7.6 (8.4) | 7.6(8.4) | 7.6(8.4) |
| Engine oil Getriebeöl | ltr | 4.25 | 6.5 | 6.5 | 6.5 |
| Transmission/final drive | ltr | Liftetime | Lifetime | Lifetime | Lifetime |
| Weight, unladen, to EU1 | kg | 1,295 | 1,345(1,375) | 1,360(1,395) | 1,385(1,415) |
| Max load to DIN | kg | 300 | 300 | 300 | 300 |
| Max permissible weight to DIN | kg | 1,520 | 1,570 (1,600) | 1,585 (1,620) | 1,610 (1,640) |
| Max axle load, front/rear | kg | 750/840 | 780/840 | 780/850 | 790/860 |
| Luggage compartment to VDA | ltr | 240–260 | 240–260 | 240–260 | 240–260 |
| Drag coefficient | cd x A | 0.35 x 1.91 | 0.36 x 1.91 | 0.36 x 1.91 | 0.36 x 1.91 |
| Engine |  |  |  |  |  |
| Config/No of cyls/valves |  | Inline/4/4 | Inline/6/4 | Inline/6/4 | Inline/6/4 |
| Engine management |  | MEV9 | MSV70 | MSV70 | MSV70 |
| Capacity | cc | 1,995 | 2,497 | 2,497 | 2,996 |
| Bore/stroke | mm | 84.0/90.0 | 82.0/78.8 | 82.0/78.8 | 85.0/88.0 |
| Compression ratio | :1 | 10.5 | 11.0 | 11.0 | 10.7 |
| Fuel grade | RON | 91–98 | 91–98³ | 91–98³ | 91–98³ |
| Output | hp | 150 | 177 | 218 | 265 |
| at | rpm | 6,200 | 5,800 | 6,500 | 6,600 |
| Torque | Nm/lb-ft | 200/147 | 230/169 | 250/184 | 315/232 |
| at | rpm | 3,600 | 3,500-5,000 | 2,750-4,250 | 2,750 |
| Electrical system |  |  |  |  |  |
| Battery/installation | Ah/– | 55/Lug comp | 55/Lug comp | 55/Lug comp | 55/Lug comp |
| Alternator | A/W | 110/1,540 | 155/2,170 /1260 | 155/2,170 /1260 | 155/2,170 |
| Chassis and suspension |  |  |  |  |  |
| Suspension, front |  | Single-joint spring strut axle with displaced castor; |
|  |  | small, positive steering roll radius; compensation of lateral forces; anti-dive |
| Suspension, rear |  | Independent, central arm rear axle; |
|  |  | separate springs and dampers; anti-squat and anti-dive |
| Brakes, front |  | Discs |
| Diameter | mm | 286 x 22, vented | 286, vented | 300, vented | 325, vented |
| Brakes, rear |  | Discs |
| Diameter | mm | 280 x 10, vented | 280, vented | 294, vented | 294, vented |
| Driving stability systems |  | ABS, DSC+, DTC |
| Steering |  | Electrical EPS power steering |
| Overall steering ratio | :1 | 16.0 | 14.2 | 14.2 | 14.2 |
| Transmission |  | 6-speed manual | 6-speed manual | 6-speed manual | 6-speed manual |
| Gear ratios I | :1 | 4.32 | 4.32 (4.17) | 4.32 (4.17) | 4.35 (4.17) |
| II | :1 | 2.46 | 2.46 (2.34) | 2.46 (2.34) | 2.50 (2.34) |
| III | :1 | 1.66 | 1.66 (1.52) | 1.66 (1.52) | 1.66 (1.52) |
| IV | :1 | 1.23 | 1.23 (1.14) | 1.23 (1.14) | 1.23 (1.14) |
| V | :1 | 1.00 | 1.00(0.87) | 1.00 (0.87) | 1.00 (0.87) |
| VI | :1 | 0.85 | 0.85(0.69) | 0.85(0.69) | 0.85(0.69) 0,850,85(0,69) 0,825(-) |
| R | :1 | 3.94 | 3.93 (3.40) | 3.93 (3.40) | 3.93 (3.40) |
| Final drive | :1 | 3.38 | 3.38 (3.91) | 3.38 (3.73) | 3.23 (3.64) |
| Tyres |  | 225/50 R 16 91 V | 225/55 R16 92V | 225/55 R16 92V | 225/45 R17 91W |
| Rims |  | 7 J x 16 cast alu | 7 J x 16 cast-alu | 7 J x 16 cast alu | 8 J x 17 cast alu |
| Performance |  |  |  |  |  |
| Power-to-weight ratio, DIN | kg/kW | 11.1 | 9.8(10.0) | 8.0(8.3) | 6.7(6.9) |
| Output per litre | kW/ltr | 55.1 | 52.1 | 64.1 | 65.1 |
| Acceleration 0-62mph | sec | 8.2 | 7.1 (7.7) | 6.5 (6.9) | 5.7 (6.0) |
| Standing-start | sec | – | – | – | – |
| in 4th gear 50-75mph | sec | 8.2 | 7.0 | 6.5 | 5.5 |
| Top speed | mph | 137 | 142 (141) | 149 (149) | 155 (155)* |
| Fuel consumption in EU cycle |  |  |  |  |  |
| Urban | Mpg | 26.2 | 23.9 (23.5) | 23.5 (22.1) | 22.4 (22.1) |
| Extra-urban | Mpg | 50.4 | 46.3 (44.8) | 44.8 (41.5) | 44.8 (41.5) |
| Composite | Mpg | 37.7 | 34.4 (33.6) | 33.6 (31.4) | 32.9 (31.4) |
| CO2 | Mpg | 181 | 197 (202) | 202 (216) | 207 (217) |
| Miscellaneous |  |  |  |  |  |
| Emission level |  | EU4 | EU4 | EU4 | EU4 |

*Electronically limited

| Body |  | Z4 M Roadster |  |  |  |
| --- | --- | --- | --- | --- | --- |
| No of doors/seats |  | 2/2 |  |  |  |
| Length/width/height (unladen) | mm | 4,113/1,781/1,302 |  |  |  |
| Wheelbase | mm | 2,497 |  |  |  |
| Track, front/rear | mm | 1,486/1,516 |  |  |  |
| Turning circle | m | 10.5 |  |  |  |
| Tank capacity | approx. ltr | 55 |  |  |  |
| Cooling system, incl heating | ltr | 10.7 |  |  |  |
| Engine oil | ltr | 7.0 |  |  |  |
| Transmission fluid | ltr | 1.9 |  |  |  |
| Final drive fluid | ltr | 1.2 |  |  |  |
| Weight, unladen, to EU1 | kg | 1,485 |  |  |  |
| Max load to DIN | kg | 295 |  |  |  |
| Max permissible weight to DIN | kg | 1,705 |  |  |  |
| Max axle load, front/rear | kg | 840/910 |  |  |  |
| Luggage compartment to VDA | ltr | 200/220 |  |  |  |
| Air drag | cd x A | 0.37 x 1.92 |  |  |  |
| Engine |  |  |  |  |  |
| Config/No of cylinders/valves |  | In-line/6/4 |  |  |  |
| Engine management |  | MSS70 |  |  |  |
| Capacity | cc | 3,246 |  |  |  |
| Bore/stroke | mm | 87/91 |  |  |  |
| Compression ratio | :1 | 11.5 |  |  |  |
| Fuel grade | RON | 95–98 |  |  |  |
| Output | hp | 343 |  |  |  |
| at | rpm | 7,900 |  |  |  |
| Torque | Nm/lb-ft | 365/269 |  |  |  |
| at | rpm | 4,900 |  |  |  |
| Electrical system |  |  |  |  |  |
| Batteriy/installation | Ah/– | 70 /luggage compartment, right |  |  |  |
| Alternator | A/W | 147/2,058 |  |  |  |
| Chassis and suspension |  |  |  |  |  |
| Suspension, front |  | Single-joint spring strut axle with multiple track control arms; fixed-position |
|  |  | ball joint on guide joint, thrust plate, twin-sleeve gas pressure spring struts |
| Suspension, rear |  | Central arm axle with separate springs/dampers, twin-sleeve gas |
|  |  | Pressure dampers |
| Brakes, front |  | Single-piston swing callipers, compound disc brakes |
| Diameter | mm | 345,0 vented |  |  |  |
| Brakes, rear |  | Single-piston swing callipers, compound disc brakes |
| Diameter | mm | 328,0 vented |  |  |  |
| Driving stability systems |  | ABS, CBC, DSC+, DBC, variable M differential lock |
| Steering |  | Rack-and-pinion steering with hydraulic assistance |
| Overall steering ratio | :1 | 15.4 |  |  |  |
| Transmission |  | Type H manual gearbox HandschaltgetriebeH |  |
| Gear ratios I | :1 | 4.35 |  |  |  |
| II | :1 | 2.496 |  |  |  |
| III | :1 | 1.665 |  |  |  |
| IV | :1 | 1.23 |  |  |  |
| V | :1 | 1.000 |  |  |  |
| VI | :1 | 0.851 |  |  |  |
| R | :1 | 3.926 |  |  |  |
| Final drive | :1 | 3.62 |  |  |  |
| Tyres, front |  | 225/45 ZR18 |  |  |  |
| Tyres, rear |  | 255/40 ZR18 |  |  |  |
| Rims, front |  | 8.0J x 18 EH2 IS42 LM |  |  |  |
| Rims, rear |  | 9.0J x 18 EH2 IS30 LM |  |  |  |
| Performance |  |  |  |  |  |
| Power-to-weight ratio, DIN | kg/kW | 5.6 |  |  |  |
| Output per litre | kW/ltr | 77.6 |  |  |  |
| Acceleration 0-62mph | sec | 5.0 |  |  |  |
| In 4th/5th gear 50-75mph | sec | 5.0/6.5 |  |  |  |
| Top speed | mph | 155* |  |  |  |
| Fuel consumption in EU cycle |  |  |  |  |  |
| Urban | Mpg | 15.9 |  |  |  |
| Extra-urban | Mpg | 32.9 |  |  |  |
| Composite | Mpg | 23.3 |  |  |  |
| CO2 | g/km | 292 |  |  |  |
| Miscellaneous |  |  |  |  |  |
| Emission level |  | EU4 |  |  |  |

* Electronically limited