Specifications. 
MINI Cooper S Clubman.

| Body |  | MINI Cooper S Clubman | MINI Cooper S Clubman Automatic |  |
| --- | --- | --- | --- | --- |
| No of doors/seats |  | 3/4 | 3/4 |  |
| Length/width/heigth (unladen) | mm | 3,958/1,683/1,432 | 3,958/1,683/1,432 |  |
| Wheelbase | mm | 2,547 | 2,547 |  |
| Track, front/rear | mm | 1,453/1,461 | 1,453/1,461 |  |
| Turning circle | m | 11.0 | 11.0 |  |
| Tank capacity | approx ltr | 50 | 50 |  |
| Cooling system including heater | ltr | 5.2 | 5,2 |  |
| Engine oil | ltr | 4.2 | 4,2 |  |
| Transmission fluid incl final drive | ltr | Lifetime | Lifetime |  |
| Weight, unladen, to DIN/EU1 | kg | 1,205/1,280 | 1,230/1,305 |  |
| Max load to DIN | kg | 485 | 485 |  |
| Max permissible weight to DIN | kg | 1,690 | 1,715 |  |
| Max axle load, front/rear | kg | 865/855 | 890/855 |  |
| Max trailer load2, |  |  |  |  |
| braked (12%)/unbraked | kg | No trailer | No trailer |  |
| Max roof load/max download | kg | 75/– | 75/– |  |
| Luggage compartment to DIN | ltr | 260–930 | 260–930 |  |
| Air resistance | cd x A | 0.35 x 2.02 | 0,35 x 2,02 |  |
| Power Unit |  |  |  |  |
| Configuration/No of cyls/valves |  | Straight/4/4 | Straight/4/4 |  |
| Engine management |  | MED 17.2 | MED 17.2 |  |
| Capacity | cc | 1,598 | 1,598 |  |
| Bore/stroke | mm | 77/85.8 | 77/85,8 |  |
| Compression ratio | : 1 | 10.5 : 1 | 10,5 : 1 |  |
| Fuel grade | RON | 91–98 | 91–98 |  |
| Max output | kW/hp | 128/175 / 170 | 128/175 |  |
| at | rpm | 5,500 | 5,500 |  |
| Max torque | Nm/lb-ft | 240/177 (260/192 Overboost) | 240/177 (260/192 Overboost) |  |
| at | rpm | 1,600–5,000 | 1,600–5,000 |  |
| Elektrical System |  |  |  |  |  |  |
| Battery/installation | Ah/– | 46/front | 46/front |  |
| Alternator | A/W | 120/1,680 | 120/1,680 |  |
| Chassis and Suspension |  |  |  |  |
| Suspension, front | Single-joint McPherson spring strut axle with anti-dive |  |
| Suspension, rear | Longitudinal arms with centrally pivoted track arms, z-axle |  |
| Brakes, front |  | Discs, vented | Discs, vented |  |
| Diameter | mm | 294 | 294 |  |
| Brakes, rear |  | Discs | Discs |  |
| Diameter | mm | 259 | 259 |  |
| Driving stability systems | Hydraulic twin-circuit brake system with anti-lock brakes (ABS), Electronic Brake Force Distribution (EBD), Cornering Brake Control (CBC), Dynamic Stability Control (DSC) with hill start-off assistance and traction aid (ASC+T). Optional limited-slip differential. Handbrake acting mechanically in rear wheels. |
| Steering | Rack-and-pinion steering with electrical power assistance (EPAS) |  |
| Steering transmission ratio, overall | : 1 | 14.1 | 14.1 |  |
| Gearbox |  | Six-speed manuall | Six-speed automatic |  |
| Gear ratios I | : 1 | 3.308 | 4.044 |  |
| II | : 1 | 2.130 | 2.371 |  |
| III | : 1 | 1.483 | 1.556 |  |
| IV | : 1 | 1.139 | 1.159 |  |
| V | : 1 | 0.949 | 0.852 |  |
| VI | : 1 | 0.816 | 0.672 |  |
| R | : 1 | 3.231 | 3.193 |  |
| Final drive | : 1 | 3.647 | 3.683 |  |
| Tyres |  | 195/55 R16 87V RSC | 195/55 R16 87V RSC |  |
| Rims |  | 6.5J x 16 light alloy | 6.5J x 16 light alloy |  |
| Performance |  |  |  |  |
| Power-to-weight ratio to DIN | kg/kW | 9.4 | 9.6 |  |
| Output per litre | kW/hp | 80.1/108.9 | 80.1/108.9 |  |
| Acceleration 0–100 km/h | sec | 7.6 | 7.8 |  |
| standing-start km | sec | 28.0 | 28.3 |  |
| In 4th/5th gear 80–120 km/h | sec | 5.9/7.6 | –/– |  |
| Top speed | km/h | 224 | 219 |  |
| Fuel Consumption in EU Cycle |  |  |  |  |
| Urban | ltr/100 km | 8.0 | 9.8 |  |
| Extra-urban | ltr/100 km | 5.3 | 5.4 |  |
| Composite | ltr/100 km | 6.3 | 7.0 |  |
| CO2 | g/km | 150 | 168 |  |
| Miscellaneous |  |  |  |  |
| Emission rating | – | EU4 | EU4 |  |
| Ground clearance | mm | 135 | 135 |  |

1Weight of car in road trim (DIN) plus 75 kg for driver and luggage.

2May be increased under certain conditions.

MINI Cooper Clubman.

| Body |  | MINI Cooper Clubman | MINI Cooper Clubman Automatic |  |
| --- | --- | --- | --- | --- |
| No of doors/seats |  | 3/4 | 3/4 |  |
| Length/width/heigth (unladen) | mm | 3,937/1,683/1,426 | 3,937/1,683/1,426 |  |
| Wheelbase | mm | 2,547 | 2,547 |  |
| Track, front/rear | mm | 1,459/1,467 | 1,459/1,467 |  |
| Turning circle | m | 11.0 | 11.0 |  |
| Tank capacity | approx ltr | 40 | 40 |  |
| Cooling system including heater | ltr | 5.2 | 5.2 |  |
| Engine oil | ltr | 4.2 | 4.2 |  |
| Transmission fluid incl final drive | ltr | Lifetime | Lifetime |  |
| Weight, unladen, to DIN/EU1 | kg | 1,145/1,220 | 1,185/1,260 |  |
| Max load to DIN | kg | 500 | 500 |  |
| Max permissible weight to DIN | kg | 1,645 | 1,685 |  |
| Max axle load, front/rear | kg | 830/850 | 865/850 |  |
| Max trailer load2, |  |  |  |  |
| braked (12%)/unbraked | kg | 750/500 | 750/500 |  |
| Max roof load/max download | kg | 75/50 | 75/50 |  |
| Luggage compartment to DIN | ltr | 260–930 | 260–930 |  |
| Air resistance | cd x A | 0.33 x 2.01 | 0.33 x 2.01 |  |
| Power Unit |  |  |  |  |
| Configuration/No of cyls/valves |  | Straight/4/4 | Straight/4/4 |  |
| Engine management |  | MEV 17.2 | MEV 17.2 |  |
| Capacity | cc | 1,598 | 1,598 |  |
| Bore/stroke | mm | 77/85.8 | 77/85.8 |  |
| Compression ratio | : 1 | 11 : 1 | 11 : 1 |  |
| Fuel grade | RON | 91–98 | 91–98 |  |
| Max output | kW/hp | 88/120 | 88/120 |  |
| at | rpm | 6,000 | 6,000 |  |
| Max torque | Nm/lb-ft | 160/118 | 160/118 |  |
| at | rpm | 4,250 | 4,250 |  |
| Elektrical System |  |  |  |  |
| Battery/installation | Ah/– | 46/front | 46/front |  |
| Alternator | A/W | 120/1,680 | 120/1,680 |  |
| Chassis and Suspension |  |  |  |  |
| Suspension, front | Single-joint Mc Pherson spring strut axle with anti-dive |  |
| Suspension, rear | Longitudinal arms with centrally pivoted track arms, z-axle |  |
| Brakes, front |  | Discs, vented | Discs, vented |  |
| Diameter | mm | 280 | 280 |  |
| Brakes, rear |  | Discs | Discs |  |
| Diameter | mm | 259 | 259 |  |
| Driving stability systems | Hydraulic twin-circuit brake system with anti-lock brakes (ABS), Electronic Brake Force Distribution (EBD), Cornering Brake Control (CBC), Dynamic Stability Control (DSC) with hill start-off assistance and traction aid (ASC+T). Handbrake acting mechanically in rear wheels. |
| Steering | Rack-and-pinion steering with electrical power assistance (EPAS) |  |
| Steering transmission ratio, overall | : 1 | 14.1 | 14.1 |  |
| Gearbox |  | Six-speed manuall | Six-speed automatic |  |
| Gear ratios I | : 1 | 3.214 | 4.148 |  |
| II | : 1 | 1.792 | 2.370 |  |
| III | : 1 | 1.194 | 1.556 |  |
| IV | : 1 | 0.914 | 1.155 |  |
| V | : 1 | 0.784 | 0.859 |  |
| VI | : 1 | 0.683 | 0.686 |  |
| R | : 1 | 3.143 | 3.394 |  |
| Final drive | : 1 | 4.353 | 4.103 |  |
| Tyres |  | 175/65 R15 84H | 175/65 R15 84H |  |
| Rims |  | 5.5J x 15 light alloy | 5.5J x 15 light alloy |  |
| Performance |  |  |  |  |
| Power-to-weight ratio to DIN | kg/kW | 13.0 | 13.5 |  |
| Output per litre | kW/hp | 55.1/74.9 | 55.1/74.9 |  |
| Acceleration 0–100 km/h | sec | 9.8 | 10.9 |  |
| standing-start km | sec | 30.9 | 32.0 |  |
| In 4th/5th gear 80–120 km/h | sec | 10.2/12.7 | – |  |
| Top speed | km/h | 201 | 195 |  |
| Fuel Consumption in EU Cycle |  |  |  |  |
| Urban | ltr/100 km | 7.1 | 9.2 |  |
| Extra-urban | ltr/100 km | 4.5 | 5.1 |  |
| Composite | ltr/100 km | 5.5 | 6.6 |  |
| CO2 | g/km | 132 | 159 |  |
| Miscellaneous |  |  |  |  |
| Emission rating | – | EU4 | EU4 |  |
| Ground clearance | mm | 138 | 138 |  |

1Weight of car in road trim (DIN) plus 75 kg for driver and luggage.

2May be increased under certain conditions.

MINI Cooper D Clubman.

| Body d Anzahl Türen / s |  | MINI Cooper D Clubman | MINI Cooper D Clubman Automatic |  |
| --- | --- | --- | --- | --- |
| No of doors/seats |  | 3/4 | 3/4 |  |
| Length/width/heigth (unladen) | mm | 3,945/1,683/1,426 | 3,945/1,683/1,426 |  |
| Wheelbase | mm | 2,547 | 2,547 |  |
| Track, front/rear | mm | 1,459/1,467 | 1,459/1,467 |  |
| Turning circle | m | 11.0 | 11.0 |  |
| Tank capacity | approx ltr | 40 | 40 |  |
| Cooling system including heater | ltr | 5.4 | 5.4 |  |
| Engine oil | ltr | – | – |  |
| Transmission fluid incl final drive | ltr | Lifetime | Lifetime |  |
| Weight, unladen, to DIN/EU1 | kg | 1,175/1,250 | 1,205/1,280 |  |
| Max load to DIN | kg | 500 | 500 |  |
| Max permissible weight to DIN | kg | 1,675 | 1,705 |  |
| Max axle load, front/rear | kg | 875/840 | 905/840 |  |
| Max trailer load2, |  |  |  |  |
| braked (12%)/unbraked | kg | 750/500 | 750/500 |  |
| Max roof load/max download | kg | 75/50 | 75/50 |  |
| Luggage compartment to DIN | ltr | 260–930 | 260–930 |  |
| Air resistance | cd x A | 0.33 x 2.01 | 0.33 x 2.01 |  |
| Power Unit |  |  |  |  |
| Configuration/No of cyls/valves |  | Straight/4/4 | Straight/4/4 |  |
| Engine management |  | DDE 6,08 | DDE 6,08 |  |
| Capacity | cc | 1,560 | 1,560 |  |
| Bore/stroke | mm | 75.0/88.3 | 75.0/88.3 |  |
| Compression ratio | : 1 | 18 : 1 | 18:1 |  |
| Fuel grade | RON | Diesel | Diesel |  |
| Max output | kW/hp | 80/110 | 80/110 |  |
| at | rpm | 4,000 | 4,000 |  |
| Max torque | Nm/lb-ft | 240/177 (260/192 Overb) | 240/177 (260/192 Overboost) |  |
| at | rpm | 1,750–2,000 | 1,750–2,000 |  |
| Elektrical System |  |  |  |  |
| Battery/installation | Ah/– | 70/front | 70/front |  |
| Alternator | A/W | 154/ 2,156 | 154/ 2,156 |  |
| Chassis and Suspension |  |  |  |  |
| Suspension, front | Single-joint Mc Pherson spring strut axle with anti-dive |  |
| Suspension, rear | Longitudinal arms with centrally pivoted track arms, z-axle |  |
| Brakes, front |  | Discs, vented | Discs, vented |  |
| Diameter | mm | 280 | 280 |  |
| Brakes, rear |  | Discs | Discs |  |
| Diameter | mm | 259 | 259 |  |
| Driving stability systems | Hydraulic twin-circuit brake system with anti-lock brakes (ABS), Electronic Brake Force Distribution (EBD), Cornering Brake Control (CBC), Dynamic Stability Control (DSC) with hill start-off assistance and traction aid (ASC+T). Handbrake acting mechanically in rear wheels. |
| Steering | Rack-and-pinion steering with electrical power assistance (EPAS) |  |
| Steering transmission ratio, overall | : 1 | 14.1 | 14.1 |  |
| Gearbox |  | Six-speed manual | Six-speed automatic |  |
| Gear ratios I | : 1 | 3.308 | 4.044 |  |
| II | : 1 | 1.870 | 2.371 |  |
| III | : 1 | 1.194 | 1.556 |  |
| IV | : 1 | 0.872 | 1.159 |  |
| V | : 1 | 0.721 | 0.852 |  |
| VI | : 1 | 0.596 | 0.672 |  |
| R | : 1 | 3.231 | 3.193 |  |
| Final drive | : 1 | 3.706 | 3.683 |  |
| Tyres |  | 175/65 R15 84H | 175/65 R15 84H |  |
| Rims |  | 5.5J x 15 light alloy | 5.5J x 15 light alloy |  |
| Performance |  |  |  |  |
| Power-to-weight ratio to DIN | kg/kW | 14.7 | 15.1 |  |
| Output per litre | kW/hp | 51.3/69.8 | 51.3/69.8 |  |
| Acceleration 0–100 km/h | sec | 10.4 | 10.9 |  |
| standing-start km | sec | 32.9 | 33.1 |  |
| In 4th/5th gear 80–120 km/h | sec | 7.9/10.2 | – |  |
| Top speed | km/h | 193 | 188 |  |
| Fuel Consumption in EU Cycle |  |  |  |  |
| Urban | ltr/100 km | 4.9 | 6.6 |  |
| Extra-urban | ltr/100 km | 3.6 | 4.2 |  |
| Composite | ltr/100 km | 4.1 | 5.1 |  |
| CO2 | g/km | 109 | 136 |  |
| Miscellaneous |  |  |  |  |
| Emission rating | – | EU4 | EU4 |  |
| Ground clearance | mm | 118 | 118 |  |

1Weight of car in road trim (DIN) plus 75 kg for driver and luggage.

2May be increased under certain conditions.