The new BMW 1 Series Coupé.
Contents.

01.	Description in Brief. 	 2

02.	With Efficiency to Pure Driving Pleasure.
	The new BMW 1 Series Coupé.
	(Short Version)	 5

03.	Concept:
	More Sport in the Compact Class. 	 15

04.	Design:
	Powerful, Striking, Unmistakable. 	 17

05.	Drivetrain:
	Top Performer in Power and Efficiency. 	 23

06.	Chassis and Driver Assistance Systems:
	Dynamics, Comfort and Safety Tailored to the Driver. 	 30

07.	Body and Safety:
	Strength and Protection of the Highest Standard. 	 35

08.	Features and Equipment:
	Driving Pleasure and Premium Quality Included. 	 38

09.	Production:
	Flexible, Efficient, Conscious of the Environment. 	 44

10.	Specifications. 	 47

11.	Exterior and Interior Dimensions. 	 49

12.	Output and Torque Diagrams. 	 51

1.	Description in Brief.

•	Compact, dynamic coupé based on the successful BMW 1 Series, 
four-seater, extremely agile handling with rear-wheel drive.

•	Consistent extension of the BMW 1 Series; following the new presentation of the three- and five-door models in spring 2007, the
new BMW 1 Series Coupé is now entering the market.

•	The focus on supreme driving pleasure in the compact class takes up the heritage of the BMW 02 Series, with values typical of this brand classic being re-interpreted in authentic, modern style; the concept, design and drive technology all ensure superior sporting performance.

•	New chapter in the BMW 1 Series’ international story of success,
with the car’s presence in the market significantly enhanced through
the introduction of the BMW 135i Coupé in the USA.

•	New top-of-the-range BMW 135i Coupé quite unique in the compact class, combining excellent driving dynamics with maximum efficiency; 
3.0-litre straight-six power unit with Twin Turbo and second-generation direct gasoline injection (High Precision Injection), 225 kW/306 hp.

•	World debut of the new 2.0-litre four-cylinder diesel with variable Twin Turbo (VTT), low-weight all-aluminium crankcase and third-generation common-rail fuel injection, BMW 123d Coupé offering a supreme
balance of dynamism and economy.

•	All-round implementation of the BMW EfficientDynamics development strategy as a standard feature incorporating innovations exclusive
to BMW, unparalleled balance of performance and fuel economy quite unique in the segment, appropriate use of Brake Energy Regeneration, Auto Start Stop, energy-saving electromechanical power steering
with integrated Servotronic function, gearshift point indicator, on-demand management of ancillary units, diesel models fitted as standard with particulates filter close to the engine.

•	Unique, dynamic and unmistakable coupé design combining the powerful look of the car’s body with the greenhouse moved far to the rear and offering a particularly light look, short overhang at the front, long engine compartment lid, long wheelbase, striking silhouette, large, frameless doors.

•	Top-of-the range BMW 135i Coupé with modified M Aerodynamics Package carried over from the M Sports Package as a standard feature.

•	Clear and, generous interior design, high-class trim bars and upholstery
in a wide choice of colours and materials, rear seat backrest folding down in a 60 : 40 split featured as standard.

•	Wide range of safety features fitted as standard, airbags, front seat backrests optimised for superior crash safety and headrests reducing
the risk of injury in a collision from the rear, body structure of the
new BMW 1 Series Coupé achieving optimum results in consumer
safety tests the world over.

•	Unique range of audio, communication and navigation options unparalleled in the compact segment, AUX, USB and Bluetooth interfaces for simple and convenient connection of an MP3 player or memory stick.

•	Elaborate chassis with rear-wheel drive, aluminium double-joint tiebar
axle at the front, five-arm rear axle in lightweight steel construction, Dynamic Stability Control (DSC) including Dynamic Traction Control (DTC), energy-saving electromechanical power steering complete with Servotronic, Active Steering exclusive to BMW available as an option, optimisation of traction through electronic differential lock management
in the DSC-Off mode for the BMW 135i Coupé and BMW 123d.

•	Engine variants:
BMW 135i Coupé: straight-six gasoline engine with Twin Turbo
and direct fuel injection (High Precision Injection), 
capacity 2,979 cc, max output 225 kW/306 hp at 5,800 rpm, 
max torque 400 Nm/295 lb-ft from 1,300–5,000 rpm, 
acceleration 0–100 km/h in 5.3 seconds, 
top speed 250 km/h (155 mph) (electronically limited), 
average fuel consumption in the composite EU cycle 9.2 litres/100 kilometres (equal to 30.7 mpg imp), 
CO2 emission rating according to the EU standard 220 g/km.

BMW 123d Coupé: straight-four diesel engine with Variable Twin Turbo and common-rail fuel injection, diesel particulates filter featured as standard,  
capacity 1,995 cc, max output 150 kW/204 hp at 4,400 rpm, 
max torque 400 Nm/295 lb-ft from 2,000–2,250 rpm,
acceleration 0–100 km/h in 7.0 seconds, 
top speed 238 km/h (148 mph), 
average fuel consumption in the composite EU cycle 5.2 litres/100 kilometres (equal to 54.3 mpg imp), 
CO2 emission rating according to the EU standard 138 g/km.

BMW 120d Coupé: straight-four diesel engine with turbocharger and common-rail fuel injection, diesel particulates filter featured as standard,  
capacity 1,995 cc, max output 130 kW/177 hp at 4,000 rpm, 
max torque 350 Nm/258 lb-ft from 1,750–3,000 rpm,
acceleration 0–100 km/h in 7.6 seconds, 
top speed 228 km/h (141 mph), 
average fuel consumption in the composite EU cycle 4.8 litres/100 kilometres (equal to 58.8 mpg imp), 
CO2 emission rating according to the EU standard 128 g/km.