10.	Specifications BMW 1 Series Coupé. 
	135i.

| Body |  | BMW 135i |  |  |  |
| --- | --- | --- | --- | --- | --- |
| No of doors/seats |  | 2/4 |  |  |  |
| Length/width/height (unladen) | mm | 4,360/1,748/1,408 |  |  |  |
| Wheelbase | mm | 2,660 |  |  |  |
| Track, front/rear | mm | 1,470/1,497 |  |  |  |
| Ground clearance | mm | – |  |  |  |
| Turning circle | m | 10.7 |  |  |  |
| Tank capacity | approx ltr | 53 |  |  |  |
| Cooling system incl heater l | ltr | 8.2 |  |  |  |
| Engine oil | ltr | 6.5 |  |  |  |
| Transmission fluid | ltr | Lifetime |  |  |  |
| Final drive fluid | ltr | Lifetime |  |  |  |
| Weight, unladen, to EU1 | kg | 1,560 |  |  |  |
| Max load to DIN | kg | 440 |  |  |  |
| Max permissible weight to DIN | kg | 1,925 |  |  |  |
| Max axle load, front/rear | kg | 945/1,030 |  |  |  |
| Max trailer load2, |  |  |  |  |  |
| braked (12%)/unbraked | kg | –/– |  |  |  |
| Max roof load/max trailer downl | kg | 75 |  |  |  |
| Lug comp capacity ISO 3832 | ltr | 370 |  |  |  |
| Air drag | cd x A | 0.32 x 2.10 |  |  |  |
| Power Unit |  |  |  |  |  |
| Configuration/No of cyls/valves |  | Straight/6/4 |  |  |  |
| Fuel supply |  | MSD80 |  |  |  |
| Capacity, effective | cc | 2,979 |  |  |  |
| Stroke/bore | mm | 89.9/84.0 |  |  |  |
| Compression | : 1 | 10.2 |  |  |  |
| Fuel grade |  | RON 95–98 |  |  |  |
| Max output | kW/hp | 225/306 |  |  |  |
| At | rpm | 5,800 |  |  |  |
| Max torque | Nm/lb-ft | 400/295 |  |  |  |
| At | rpm | 1,300–5,000 |  |  |  |
| Electrical System |  |  |  |  |  |
| Battery/installation | Ah/– | 70/luggage comp |  |  |  |
| Alternator | A/W | 180/2,520 |  |  |  |
| Chassis and Suspension |  |  |  |  |  |
| Suspension, front |  | Double-joint tiebar spring strut axle, aluminium |
| Suspension, rear |  | Five-arm axle, lightweight steel |
| Brakes, front |  | six-piston fixed callipers disc brakes |
| Diameter | mm | Vented/338 x 26 |  |  |  |
| Brakes, rear |  | two-piston fixed callipers disc brakes |
| Diameter | mm | Vented/324 x 22 |  |  |  |
| Driving stability systems |  | ABS, CBC, ASC, DSC, DTC, DBC |
| Steering |  | Rack-and-pinion |  |
| Steering ratio, overall | : 1 | 16.0 |  |  |  |
| Type of steering |  | G |  |
| Gear ratios I | : 1 | 4.055 |  |  |  |
| II | : 1 | 2.396 |  |  |  |
| III | : 1 | 1.582 |  |  |  |
| IV | : 1 | 1.192 |  |  |  |
| V | : 1 | 1.0 |  |  |  |
| VI | : 1 | 0.872 |  |  |  |
| R | : 1 | 3.677 |  |  |  |
| Final drive | : 1 | 3.08 |  |  |  |
| Tyres, front |  | 215/40 R18 85Y RSC |  |  |  |
| Tyres, rear |  | 245/35 R18 88Y RSC |  |  |  |
| Rims, front |  | 7.5J x 18 light-alloy |  |  |  |
| Rims, rear |  | 8.5J x 18 light-alloy |  |  |  |
| Performance |  |  |  |  |  |
| Power-to-weight ratio to DIN | kg/kW | 6.6 |  |  |  |
| Output per litre | kW/hp | 75.5/102.7 |  |  |  |
| Acceleration 0–100 km/h | sec | 5.3 |  |  |  |
| standing start km | sec | 24.6 |  |  |  |
| 80–120 km/h in 4th/5th gear | sec | 5.0/6.0 |  |  |  |
| Top speed | km/h | 250 |  |  |  |
| Fuel Consumption in EU Cycle |  |  |  |  |  |
| Urban | ltr/100 km | 13.0 |  |  |  |
| Extra-urban | ltr/100 km | 7.0 |  |  |  |
| Composite | ltr/100 km | 9.2 |  |  |  |
| CO2 | g/km | 220 |  |  |  |
| Miscellaneous |  |  |  |  |  |
| Emission category |  | EU4 |  |  |  |

Weight of vehicle in road trim  (DIN) plus 75 kg for driver and baggage.		
2May be increased under certain conditions.

Specifications BMW 1 Series Coupé.
120d; 123d.

| Body |  | BMW 120d | BMW 123d |
| --- | --- | --- | --- |
| No of doors/seats |  | 2/4 | 2/4 |
| Length/width/height (unladen) | mm | 4,360/1,748/1,423 | 4,360/1,748/1,423 |
| Wheelbase | mm | 2,660 | 2,660 |
| Track, front/rear | mm | 1,484/1,517 | 1,484/1,517 |
| Ground clearance | mm | – | – |
| Turning circle | m | 10.7 | 10.7 |
| Tank capacity | approx ltr | 51 | 51 |
| Cooling system incl heater l | ltr | 7.2 (7.5) | 7.2 |
| Engine oil | ltr | 5.5 | 5.5 |
| Transmission fluid | ltr | Lifetime | Lifetime |
| Final drive fluid | ltr | Lifetime | Lifetime |
| Weight, unladen, to EU1 | kg | 1,450 (1,455) | 1,495 |
| Max load to DIN | kg | 440 | 440 |
| Max permissible weight to DIN | kg | 1,815 (1,820) | 1,860 |
| Max axle load, front/rear | kg | 895/985 | 925/1,000 |
| Max trailer load2 |  |  |  |
| braked (12%)/unbraked | kg | 1,200/720 | 1,200/740 |
| Max roof load/max trailer downl | kg | 75/75 | 75/75 |
| Lug comp capacity ISO 3832 | ltr | 370 | 370 |
| Air drag | cd x A | 0.30 x 2.10 | 0.30 x 2.10 |
| Power Unit |  |  |  |
| Configuration/No of cyls/valves |  | Straight/4/4 | Straight/4/4 |
| Fuel supply |  | DDE 71 | DDE 71 |
| Capacity, effective | cc | 1,995 | 1,995 |
| Stroke/bore | mm | 90/84 | 90/84 |
| Compression | : 1 | 16.0 | 16.0 |
| Fuel grade |  | Diesel | Diesel |
| Max output | kW/hp | 130/177 | 150/204 |
| at | rpm | 4,000 | 4,400 |
| Max torque | Nm/lb-ft | 350/258 | 400/295 |
| at | rpm | 1,750–3,000 | 2,000–2,250 |
| Electrical System |  |  |  |
| Battery/installation | Ah/– | 80/Luggage comp | 80/Luggage comp |
| Alternator | A/W | 180/2,520 | 180/2,520 |
| Chassis and Suspension |  |  |  |
| Suspension, front |  | Double-joint tiebar spring strut axle, aluminium |
| Suspension, rear |  | Five-arm axle, lightweight steel |
| Brakes, front |  | Single-piston swing-calliper disc brakes |
| Diameter | mm | Vented/300x 24 | Vented/330 x 24 |
| Brakes, rear |  | Single-piston swing-calliper disc brakes |
| Diameter | mm | Vented/300 x 20 | Vented/300 x 20 |
| Driving stability systems |  | ABS, CBC, ASC, DSC, DTC, DBC |
| Steering |  | Rack-and-pinion |
| Steering ratio, overall | : 1 | 16.0 | 16.0 |
| Type of steering |  | H, wide (6HP19TU) | G, wide |
| Gear ratios I | : 1 | 5.140 (4.171) | 5.080 |
| II | : 1 | 2.830 (2.340) | 2.804 |
| III | : 1 | 1.804 (1.521) | 1.783 |
| IV | : 1 | 1.257 (1.143) | 1.260 |
| V | : 1 | 1.000 (0.867) | 1.0 |
| VI | : 1 | 0.831 (0.691) | 0.835 |
| R | : 1 | 4.638(3.403) | 4.607 |
| Final drive | : 1 | 2.56 (3.15) | 2.65 |
| Tyres, front |  | 205/50 R17 89V RSC | 205/50 R17 89W RSC |
| Tyres, rear |  | 205/50 R17 89V RSC | 205/50 R17 89W RSC |
| Rims, front |  | 7J x 17 light-alloy | 7J x 17 light-alloy |
| Rims, rear |  | 7J x 17 light-alloy | 7J x 17 light-alloy |
| Performance |  |  |  |
| Power-to-weight ratio to DIN | kg/kW | 10.6 | 9.5 |
| Output per litre | kW/hp | 65.2/88.7 | 75.2/102.3 |
| Acceleration 0–100 km/h | sec | 7.6 (7.8) | 7.0 |
| standing start km | sec | 28.2 (28.1) | 27.3 |
| 80–120 km/h in 4th/5th gear | sec | 6.4 (-) | 5.5 |
| Top speed | km/h | 228 (226) | 238 |
| Fuel Consumption in EU Cycle |  |  |  |
| Urban | ltr/100 km | 6.1 (7.2) | 6.5 |
| Extra-urban | ltr/100 km | 4.1 (4.4) | 4.4 |
| Composite | ltr/100 km | 4.8 (5.4) | 5.2 |
| CO2 | g/km | 128 (144) | 138 |
| Miscellaneous |  |  |  |
| Emission category |  | EU4 | EU4 |

Figures in brackets apply to models with automatic transmission.

Weight of vehicle in road trim  (DIN) plus 75 kg for driver and baggage.		
2May be increased under certain conditions.