Specifications.

|  |  | X5 M | X6 M |
| --- | --- | --- | --- |
| Body |  |  |  |
| No of doors/seats |  | 5/5 | 5/4 |
| Length/width/height (unladen) | mm | 4,851/1,994/1,764 | 4,876/1,983/1,684 |
| Wheelbase | mm | 2,933 | 2,933 |
| Track, front/rear | mm | 1,660/1,672 | 1,660/1,672 |
| Turning circle | m | 12.8 | 12.8 |
| Tank capacity | approx ltr | 85 | 85 |
| Cooling system incl heater | ltr | 17.0 | 17.0 |
| Engine oil | ltr | 8,5 | 8,5 |
| Transmission fluid |  | Lifelong | Lifelong |
| Final drive fluid |  | Lifelong | Lifelong |
| Weight, unladen, to EU (DIN) | kg | 2,380 (2,305) | 2,380 (2,305) |
| Max load | kg | 600 | 600 |
| Weight, max permissible | kg | 2,905 | 2,905 |
| Max axle load, front/rear | kg | 1,400/1,560 | 1,400/1,520 |
| Max trailer load, braked (12%)/unbraked raked | kg | 3,000/750 | 3,000/750 |
| Max roofload/max towbar downl | kg | 100/120 | 100/120 |
| Luggage comp cap DIN 70020 | ltr | 620–1,750 | 570–1,450 |
| Air drag | Cx x A | 0.38 x 2.90 | 0.38 x 2.85 |
| Power Unit |  |  |  |
| Config/No of cyls/valves |  | V/8/4 | V/8/4 |
| Engine management |  | MSD85.1 | MSD85.1 |
| Engine capacity | cc | 4,395 | 4,395 |
| Bore/stroke | mm | 89.0/88.3 | 89.0/88.3 |
| Compression ratio | :1 | 9.3 | 9.3 |
| Fuel grade1) | RON | min RON 95 | min RON 95 |
| Max output | kW/hp | 408/555 | 408/555 |
| At | rpm | 6,000 | 6,000 |
| Max torque | Nm/lb-ft | 680/501 | 680/501 |
| At | rpm | 1,500–5,650 | 1,500–5,650 |
| Electrical System |  |  |  |
| Battery/location | Ah/– | 90/luggage comp | 90/luggage comp |
| Alternator | A/W | 210/2,940 | 210/2,940 |
| Chassis and Suspension |  |  |  |
| Suspension, front |  | Double track control arm; small, negative steering roll radius, dive reduction |
| Suspension, rear |  | Integral axle; multi-dimensional with anti-squat and anti-dive |
| Disc brakes, front |  | Four-piston fixed callipers |
|  |  | X5 M | X6 M |
| Diameter | mm | 395 x 36, vented | 395 x 36, vented |
| Disc brakes, rear |  | Single-piston fixed callipers |
| Diameter | mm | 385 x 24, vented | 385 x 24, vented |
| Driving stability systems |  | DSC III (HDC, DBC, ABS, ASC-X, ADB-X, DTC, Trailer Stability Control) |
| Steering |  | Rack-and-pinion power steering |
| Steering trans ratio, overall | :1 | 19.5 | 19.5 |
| Transmission |  | Six-speed Sports Automatic with Steptronic, electronic gear select lever and shift paddles on steering wheel |
| Gear ratios I | :1 | 4.171 | 4.171 |
| II | :1 | 2.340 | 2.340 |
| III | :1 | 1.521 | 1.521 |
| IV | :1 | 1.143 | 1.143 |
| V | :1 | 0.867 | 0.867 |
| VI | :1 | 0.691 | 0.691 |
| R | :1 | 3.403 | 3.403 |
| Final drive | : 1 | 3.909 | 3.909 |
| Tyres, front |  | 275/40 R20 106Y XL RSC | 275/40 R20 106Y XL RSC |
| Tyres, rear |  | 315/35 R20 110Y XL RSC | 315/35 R20 110Y XL RSC |
| Rims, front |  | 10J x 20 light-alloy | 10J x 20 light-alloy |
| Rims, rear |  | 11J x 20 light-alloy | 11J x 20 light-alloy |
| Performance |  |  |  |
| Power-weight ratio (DIN unladen) | kg/kW | 5.6 | 5.6 |
| Output per litre | kW/ltr | 92.8 | 92.8 |
| Acceleration 0–100 km/h | sec | 4.7 | 4.7 |
| 0–200 km/h | sec | 16.9 | 16.9 |
| Standing-start km | sec | 23.5 | 23.5 |
| In 4th/5th gear 80–120 km/h | sec | 4.3/5.1 | 4.3/5.1 |
| Top speed | km/h | 250 (2752)) | 250 (2752)) |
| Fuel Consumption in EU Cycle |  |  |  |
| Urban | ltr/100 km | 19.3 | 19.3 |
| Extra-urban | ltr/100 km | 10.8 | 10.8 |
| Combined | ltr/100 km | 13.9 | 13.9 |
| CO2 | g/km | 325 | 325 |
| Miscellaneous |  |  |  |
| Emission rating |  | EU 5 | EU 5 |
| Perm 4WD, power split |  | variable | variable |

Specifications apply to ACEA markets. Some homologation data applies to Germany only (weight).

1) Power and consumption data with RON 98 fuel.

2) With optional M Driver’s Package.