1.  Summary

The original BMW 3 Series Compact was launched in 1994 and proved itself a great success.  More than 400,000 were sold in total, 37,000 of which were in Britain – but more importantly, it brought new buyers to BMW.  Two out of every three Compact owners had not bought a BMW before and 65 per cent of them went on to buy another car in the range.

To continue this success, an all-new Compact will be launched in the UK on 16 August 2001.  It has been completely redesigned from the ground up and is the first BMW to feature the revolutionary, four cylinder VALVETRONIC petrol engine, built in the UK at BMW’s new engine plant at Hams Hall. Its new technology increases power by 10 per cent, while reducing fuel consumption and emissions by the same amount.

The new Compact’s chassis has been developed to be exceptionally responsive, with quick, beautifully weighted steering and suspension based on the widely acclaimed 3 Series range.  The rear benefits particularly from a version of BMW’s exceptional Z-axle.

Three models, with two engine variants will be available at launch; the 316ti and 316ti SE powered by the 115 bhp 1.8 litre, four cylinder VALVETRONIC engine and the 325ti SE with BMW’s fabled straight six cylinder, 192 bhp engine. Two more models will follow in the autumn; a 318ti powered by a 2.0 litre Valvetronic petrol engine and 320td with a four-cylinder common rail 2.0 litre diesel engine.

The main features of the new Compact are summarised as follows:

·	Distinctive new styling gives Compact a new look, different to the rest of 3 Series

·	Three models at launch; 316ti (£16,265), 316ti SE (£17,775) and 325ti SE (£22,640)

·	316ti: 1.8 litre, 115 bhp, 175 Nm, four cylinder engine with new VALVETRONIC technology. Top speed 125 mph, 0-62 mph 10.9 seconds.

·	VALVETRONIC engine increases power by 10 per cent and reduces fuel consumption and emissions by 10 per cent, compared to the previous model (power up from 105 to 115 bhp and fuel consumption improved from 37.2 to 40.9 mpg)

·	325ti: 2.5 litre, 192 bhp, 245 Nm, six cylinder. Top speed 146 mph, 0-62 mph 7.1 seconds.

·	318ti (2.0 litre four cylinder) and 320td (2.0 litre diesel) to follow in the autumn.

·	15 mm higher, 53 mm wider and 52 mm longer than the previous Compact.

·	70 litres more boot space than previously, with a maximum of 1100 litre (with the seats folded).

·	Optional five-speed Steptronic automatic transmission available for the first time on all three models.

·	State-of-the-art driving stability aids as standard; ASC+T (Automatic Stability Control + Traction), CBC (Cornering Braking Control) and EBD (Electronic Brake Distribution).

·	DSC (Dynamic Stability Control) standard on 325ti SE and an option for 316ti, now includes DBC (Dynamic Brake Control) to optimise braking power under heavy braking conditions

·	Passive safety features as standard: six airbags, ABS, seatbelt pretentioners, belt-force limiters, side impact door beams and rigid occupant safety cage.