3.  Drivetrain

There will be two engines available initially – a 1.8 litre four cylinder petrol with new VALVETRONIC technology and a 2.5 litre straight six.  Two more engines will follow later in 2001 – a 2.0 litre, four cylinder petrol and a 2.0 litre common rail diesel.

VALVETRONIC – a world first in the 316ti Compact

The BMW 316ti Compact is the first car in the world to feature an engine controlled by BMW’s new VALVETRONIC system.  Since the dawn of the internal combustion engine a throttle butterfly has regulated air intake which restricts the breathing of the engine and results in a loss of engine efficiency.  VALVETRONIC adjusts intake valve lift infinitely to control the supply of fuel/air mixture to the cylinders which offers a quantum leap forward compared with the move from carburettor to fuel injection.

The major benefit for drivers of the 316ti Compact is the ability to save around ten per cent on fuel consumption with a corresponding reduction in exhaust emissions regardless of fuel quality.

As a result the 115 bhp entry level Compact has a top speed of 125 mph yet consumes a mere 40.9 mpg in the European test cycle - a full 3.8 mpg saving - despite having an engine delivering 10 bhp more, and significantly, up to 15 per cent better than its competitors in this class.

The facts

| Engine size | 1796 |
| --- | --- |
| Power @ rpm | 115 bhp @ 5500 |
| Torque @ rpm | 175 NM @ 3750 |
| 0-62 mph | 10.9 secs |
| Top speed | 125 mph |

Taking nature as the role model

Comparison with a human being’s breathing illustrates how VALVETRONIC works.

Humans breathe deeply when required to exert themselves.  Yet we do not close our nose or mouth when we need less air, but simply breathe in shorter, more gentle rhythms.  A conventional engine with a throttle butterfly is comparable to a human being closing his or her mouth to strangle the air intake.

With its infinitely variable valve lift VALVETRONIC is able to take deep or shallow breaths according to the demands of the driver, just as nature intended.

Double-VANOS variable valve timing

The VALVETRONIC system is based around BMW’s proven double-VANOS which provides infinite camshaft adjustment and, therefore, valve lift.  The variable valve lift adjusts the cam action and, therefore, the duration of the valve opening.

A lever, positioned between camshaft and the intake valves, is operated by an electric motor via an eccentric shaft and has infinite adjustment capacity.  Depending on the position of the VALVETRONIC control system, the lever converts the cam contour to produce greater or smaller valve lift.

All new engine built in Britain

Although the VALVETRONIC technology in the innovative cylinder head attracts the prime focus, this four cylinder 16 valve engine is the first in a completely new range.  This and future variants will be built in BMW’s new UK plant at Hams Hall, Warwickshire which opened in February 2001.

The new engine’s ‘open deck’ crankcase features a new crossflow cooling concept which reduces coolant flow resistance and allows a smaller water pump which uses only 60 per cent of the normal power drain.

The aluminium engine block ends on the centre line of the crankshaft bearings.  A ladder frame between the crankcase and sump connects the lower halves of the bearing bridges to form one unit and also accommodates the balance shaft housing and the two stage oil pump.  This makes the entire unit stiff and robust minimising vibration.

All ancillaries are bolted directly to the crankcase – without elaborate supports – which also contributes to running smoothness with reduced vibration.

BMW’s new four cylinder engine also comes with all modern engine technologies such as:

·	Anti-knock control for running on all fuel grades between 87 and 99 octane.

·	A maintenance-free ignition system with individual coils.

·	Maintenance-free valve drive with automatic hydraulic adjustment.

·	A Service Interval Indicator to keep the cost of service to a minimum.

·	A double-mass flywheel for maximum running smoothness.

·	Valve drive with roller bearings throughout in the interest of minimum friction and fuel consumption.

·	Advanced catalysts near the engine in special manifold design for minimum emissions.

Consumption down by 10 per cent

VALVETRONIC offers the customer direct and immediate benefits of decreased fuel consumption and exhaust emissions, but the dynamic performance and spontaneous response of the engine is still much improved when compared to its predecessor.  Added to this there is the even higher standard of running smoothness, since the valves move less in the precisely-controlled VALVETRONIC process.

The improvement in fuel economy delivered by throttle-free engine load management is approximately 10 per cent in the EU cycle and at least 10 per cent under typical driving conditions encountered by a customer.  Such consumption figures are comparable to the fuel economy that only a diesel engine was able to offer just a few years ago.

At the same time the new four-cylinder is even more dynamic than its predecessor, the 316ti now accelerating well over a second faster to 62 mph in 10.9 seconds.  The standing start kilometre arrives in 31.6 seconds, 1.8 seconds faster than before, and the top speed of the 316ti is now 125 mph, 7 mph faster than the outgoing model.

Another advantage is the instantaneous throttle response of the 316ti Compact.  This is attributable to the simple fact that load control, to use the technical term for pressing the accelerator, now takes place “right where the action is”, that is directly in the combustion chamber.  This eliminates the time lag between the process of touching the throttle and the actual acceleration of the car, an inevitability due to the need to fill the intake manifold between the throttle butterfly and the combustion chamber.

Perfectly suited for all fuel grades, unlike a direct-injection (DI) petrol engine

Another significant advantage is that a VALVETRONIC engine offers at least the same fuel economy as the most advanced direct-injection (DI) petrol engines without the same compromises in terms of emissions.  Accordingly, the 316ti has no need for the elaborate and less reliable emission management technologies still required today on a DI petrol engine.  Furthermore it does not require sulphur-free fuel like a DI petrol engine, its proven technology allows the VALVETRONIC engine to run on all commercially available grades of regular petrol.

In other words, the customer enjoys all the consumption advantages of VALVETRONIC even when driving in countries without a national supply of sulphur-free fuel.  The consumption figures for the 316ti nevertheless relate to the use of premium fuel with an octane rating of 95 RON.  With its 63 litre (13.9 gal) fuel tank the 316ti offers a much longer range than its predecessor, achieving extra-urban fuel consumption in the European EU test cycle of an impressive 53 mpg.  This means that the driver would only have to refuel after a very long journey of 737 miles.

More to come …..

The second engine in the new four cylinder range will arrive in the 318ti Compact in September 2001.  This 2 litre version produces 143 bhp and 200 Nm of torque.

Also new will be the 320td Compact with a thoroughly revised two litre four cylinder common rail diesel engine.  Sporting an additional 14 bhp and a huge 18 per cent uplift in torque to 330 Nm, the 320td will record 51.4 mpg in the EU cycle.

From four to six

Although a six cylinder model in the previous Compact range was sold in Continental Europe, it was never brought to the United Kingdom.  The new Compact, however, will offer BMW’s smooth and powerful 2.5 litre straight six from the very start.  The BMW 325ti SE Compact brings the sophistication of six cylinder driving to the compact segment and with a power-to-weight ratio of 13.6 kgs or under 30 lbs per bhp, perfect 50:50 front to rear balance and the agility package to exploit its chassis dynamics, the 325ti SE Compact is a revelation.

Developing a maximum torque of 245 Nm or 181 lb ft, the 192 bhp straight six has a relatively easy job in handling the agile 3 Series Compact:  acceleration to 62 mph takes 7.1 seconds and its top speed is 146 mph.  Engine flexibility and acceleration at intermediate speeds are also better than before, the new six cylinder Compact accelerating from 50 to 75 mph in a typical overtaking manoeuvre in just 7.6 seconds, again 0.6 seconds faster than the former model.

The 2.5 litre power unit featured in the 325ti SE comes from BMW’s latest generation of straight six engines introduced in September 2000.  Featuring an aluminium crankcase, a cylinder head with double-VANOS and four valve technology, a two stage resonance intake system, adaptive anti-knock control, map-controlled cooling, E-gas and individual coils, this engine continues the history of BMW’s legendary straight six power units.

Despite the increase in output by 22 bhp and the car’s significantly better performance on the road, fuel consumption of the 325ti SE is down versus the former 323ti to 31.7 mpg, a figure which again makes the 325ti SE unique in comparison with other cars in this segment.

Both the 316ti and the 325ti SE have been tuned to please the ear of the driver too, with a sporty crackle from the exhaust when the driver is in an enthusiastic mood!

Transmission:  manual or automatic with Steptronic

The new Compact models come as standard with a manual five speed gearbox featuring a direct 1:1 transmission ratio in fifth gear.  Both the gearbox and the rear axle differential come with a lifelong oil filling, a self-adjusting clutch designed for consistent pedal forces regardless of wear to ensure a perfect match between engine and gearbox.  The clutch is service free throughout its entire running life.

As an option both the 316ti and 325ti SE are available with a five speed automatic transmission – a first for the Compact - featuring Adaptive Transmission Management (ATM).  ATM learns the driver’s style and adapts the shift points accordingly.  It also recognises uphill and downhill gradients as well as bends and prevents the transmission from shifting up unnecessarily before a bend, thereby retaining the correct transmission ratio for accelerating cleanly away.  Further features of the automatic transmission are the fully controlled converter clutch and a lock-up function for optimum fuel economy.  Last, but certainly not least, Steptronic allows the driver to select gears manually via the separate selector lever plane to the left of the automatic mode – briefly flick the selector lever forwards or backwards to move quickly to the next higher or lower gear, just like a manual gearbox.

Lower service costs too

The purchase price of a car is but one element in the cost of ownership.

Of the others perhaps the most significant is the residual value when the owner comes to change.  This is an area where BMW has a justified reputation for excellent value and the Compact range has proved to be one of the most robust models in the second hand car market.

Fuel costs too are rising, hence the importance of much improved economy with all four of the new Compact’s engines.

However, the less obvious costs of ownership such as insurance, road fund licence, service and repair are all important in the whole life costs.

BMW’s engineers are well aware of the significance of such costs and have designed the new Compact with such economies in mind.  For example, service intervals are longer, the target for lower costs of repair in the event of an accident imply lower insurance costs and the low CO2 rating of the 316ti (and 320td) Compact ensures a low VED rating and popularity with company car buyers when the new tax regime arrives in 2002.

Specific contributions towards lower service costs include:

·	Camshaft drive by chain is maintenance free for the entire service life of the engine, just like the ancillary drive system with a ribbed V-belt.

·	Thanks to the hydraulic valve play compensation there is no need to adjust the valve gear.

·	Both the air filter and spark plugs only need replacing after about 62,500 miles.

·	Transmissions and differentials come with a life-long oil filling.

·	Service intervals are not based rigidly on mileage covered or time elapsed, but rather on the vehicle’s actual running conditions determined and calculated individually by the BMW Service Interval Indicator.  This is shown as the remaining mileage until the next service interval.  Under typical running conditions this allows an oil change interval of 18,750 miles.

·	Exhaust system made of corrosion-free stainless steel.

·	Self-adjusting clutch.

·	Continuous brake lining check – without removing the wheels.

·	Brake light switch is a contact-free electronic signal switch without the possibility of mechanical wear.

·	The instrument cluster uses LEDs not conventional bulbs and actuator motors.