4.  Chassis, suspension and safety

All-new suspension and steering

The new Compact is an exceptionally nimble and agile car, yet entirely stable at high speed. This is thanks to a completely redesigned suspension and steering set-up compared to the previous Compact. In fact this arrangement appears for the first time on the Compact, but will be extended across the entire 3 Series range from September 2001.

A quicker steering rack reduces lock to lock wheel twirling to 3.0 turns, making it extremely responsive, and the power steering pump has been redesigned to increase weight and to give greater feel. Spring and damper settings have been adjusted and all mounting points stiffened to reduce the elasticity within the suspension system and unsprung weight has been reduced by 60 kg through the use of alloy components.

Like all BMW models, the Compact has almost perfect 50:50 front to rear weight distribution and of course rear wheel drive, which leaves the front wheels free to do nothing but steer.  Combined with its wide track and stiff anti-roll bars, this makes for an extremely stable chassis during cornering, while the short overhangs front and rear help to sharpen its agility.

In terms of design, the front axle is a spring-strut configuration with forged aluminium track control arms, two-sleeve gas pressure spring struts, rack-and-pinion steering and an anti-roll bar.  At the rear is a version of BMW’s widely acclaimed Z-axle, with two-sleeve gas-pressure dampers and an anti-roll bar.

Long wheelbase, small turning circle

The new car has a 25 mm longer wheelbase than its predecessor (increasing to 2725 mm), which brings advantages on the road in straightline tracking and ride quality.  But it is still extremely agile both on the open road and at lower, manoeuvering speeds with a turning circle of just 10.5 metres (30 cm less than the previous Compact).

Safety

Active safety based on excellent brakes

Large brake discs, vented at the front (and also at the rear on the 325ti SE) with a sophisticated anti-lock system are the basis of the electronic dynamic driving stability systems fitted to the Compact.  They give powerful, adjustable, fade-free stopping power even under extreme driving conditions – on mountain passes or even on track.

ABS and wheel-specific brake force distribution featured as standard

Like all models in the 3 Series, all Compact models are fitted as standard with ASC+T Automatic Stability Control.  This system uses ABS sensors to measure any rear wheel slippage under either acceleration or deceleration and adjusts power accordingly.  The MSR Engine Drag Control system prevents wheel lock-up on slippery surfaces under engine braking, by gently applying a touch of throttle to the locked wheel, to get it rolling again.

Two other developments of ABS anti-lock brakes offered by BMW are Electronic Brake Distribution (EBD) and Cornering Brake Control (CBC).

EBD allows the driver to make best use of the available brake power on all four wheels by monitoring the maximum amount of grip available and distributing braking force accordingly.  CBC gives additional dynamic stability if the driver is forced to brake mid-bend.  Sensors register that the car is cornering and if the brakes are applied, directs more power to the outside wheels, to reduce the risk of oversteer.

DSC Dynamic Stability Control with the ADB Automatic Differential Brake and DBC Dynamic Brake Control

DSC Dynamic Stability Control is BMW’s state-of-the-art electronic active safety system and is an option for the 316ti and 316ti SE, standard on the 325ti SE.  DSC enables even the average driver to keep control of the car, even under extreme emergency-avoidance manoeuvers.  A complex series of sensors measure all the forces acting on the car, the steering and throttle inputs and the level of grip at each wheel.  It can then adjust the attitude of the car by applying braking forces to individual wheels.

DBC Dynamic Brake Control is integrated within the system, accelerating and boosting the build-up of brake pressure in an emergency and keeping stopping distances to a minimum, even when the driver fails to properly press down the brake pedal.  Unlike some other systems on the market, DBC operates according to the hydraulic brake force enhancement principle (as opposed to vacuum boosting), thus ensuring much more effective and quicker brake control in an emergency.

As of September 2000, all 3 Series equipped with DSC Dynamic Stability Control have featured an integrated, electronic ADB Automatic Differential Brake function for optimum traction under all conditions – acting rather like a limited slip differential.  This function is particularly helpful when driving in deep snow, on loose gravel or during hard road or track driving.  The driver activates this mode by pressing the DSC button briefly.  Holding the DSC button down for more than two seconds completely switches off all electronic traction and stability systems.  A light in the instrument panel indicates that one of these modes has been activated.

The BMW Light Control Module (LCM) is a useful satefy aid in the event of a brake light failure.  If such a failure occurs, extra power is fed to the tail lights, so that they effectively act as brake lights. In fact if any of the tail lights, indicators or fog lights fail, the system can select other lights to perform their function.  The driver is made aware of any bulb or electronic failures via the usual warning light system.

Passive safety

Occupant protection is outstanding and the new Compact offers the full array of BMW passive safety systems that have won it many plaudits in recent crash test results.

There are seatbelt tensioners and belt force limiters at the front, as well as airbags at the front and side for both the driver and front passenger (in the latter case with seat occupancy sensing).  In addition there are two ITS head airbags as standard.

Integrated in the roof frame, the head airbag supplements the effect of the sidebags in the doors by expanding diagonally across the side window in a side impact, significantly improving protection levels.  The headbag helps prevent the occupant’s head from striking other objects and reduces the risk of lateral neck-strain injuries.  Activation of the airbags is controlled individually as a function of crash severity, ensuring the best protection for that particular crash situation.