Technical Specifications

| Body |  | 316ti/SE | 316ti/SE Auto | 325ti SE | 325ti SE Auto |
| --- | --- | --- | --- | --- | --- |
| No. of doors/seats |  | 3/5 | 3/5 | 3/5 | 3/5 |
| Length/width/height (unladen) | mm | 4262/1751/1408 | - | 262/1751/1408 | - |
| Wheelbase | mm | 2725 | - | 2725 | - |
| Track, front/rear | mm | 1484/1493 | - | 1474/1483 | - |
| Turning circle | m | 10.5 | - | 10.5 | - |
| Fuel tank capacity/range | ca. ltr | 63 | - | 63 | - |
| Cooling system incl. heating | ltr | 7.0 | - | 8.4 | - |
| Engine oil | ltr | 4.25 | - | 6.5 | - |
| Transmission fluid | ltr | Permanent filling | - | Permanent filling | - |
| Final drive fluid | ltr | Permanent fillling | - | Permanent filling | - |
| Weight, unladen DIN/EU1 | kg | 1300/1375 | 1320/1395 | 1405/1480 | 1430/1505 |
| Max. load (DIN) | kg | 500 | - | 500 | - |
| Max. permissible weight (DIN) | kg | 1,800 | 1,820 | 1905 | 1930 |
| Max. permissible axle load, front/rear | kg | 865/1015 | - | 935/1040 | - |
| Max. trailer load |  |  |  |  |  |
| braked (12%)/unbraked | kg | 1250/670 | 1300/670 | 1600/720 | 1600/720 |
| Max. roof load/trailer nose weight | kg | 75/na | - | 75/na | - |
| Luggage compartment capacity, (VDA) | ltr | 310-1100 | - | 310-1100 | - |
| Drag coefficient | Cd x A | 0.29 x 2.07 | 0.31 x 2.07 | 0.30 x 2.07 | 0.31 x 2.07 |
| Engine |  |  |  |  |  |
| Layout/No. of cylinders/valves |  | Inline /4/16 | - | Inline /6/24 | - |
| Engine management |  | Bosch |  | Siemens MS43 | - |
| Displacement | cc | 1796 | - | 2494 | - |
| Bore/stroke | mm | 84/81 | - | 84/75 | - |
| Compression ratio/fuel grade |  | 10.5/RON 87-98 | - | 10.5/RON 87-98 | - |
| Max. output | kW/bhp | 85/115 | - | 141/192 | - |
| At engine speed | rpm | 5500 | - | 6000 | - |
| Max. torque | Nm/lb-ft | 175 | - | 245 | - |
| At engine speed | rpm | 3750 | - | 3500 | - |
| Electric |  |  |  |  |  |
| Battery/location | Ah/– | 55/engine comp | - | 70/luggage comp | - |
| Alternator | A/W | 90/1260 | 120/1680 | 90/1260 | 120/1680 |
| Chassis |  |  |  |  |  |
| Front suspension |  | Single- joint spring-strut axle with displaced camber; small, positive steering scrub radius; compensation of lateral forces; anti-dive |
| Rear suspension |  | Central-arm axle with longitudinal control arm and double track control arm; anti-squat; anti-dive. |
| Brakes, front |  | Single-piston disc brakes, vented |
| Diameter | mm | 286 | - | 300 | - |
| Brakes, rear |  | Single piston disc brakes |
| Diameter | mm | 280 | - | 294, vented | - |
| Driving stability systems |  | ABS, traction control (ASC+T), wheel selective brake power distribution (EDV, CBC), Dynamic Stability Control (DSC), electronic limited slip differential (ABD), emergency braking detection (DBC). |
| Steering |  | Rack and pinion, servo-assisted; 3.0 turns lock to lock |  |
| Overall ratio | :1 | 13.7 | - | 13.7 | - |
| Type of transmission 5 sp manual gearbox or optional 5 sp auto transmission with steptronic |
| Transmission ratio I |  | 4.23 | 3.42 | 4.23 | 3.67 |
| II |  | 2.52 | 2.22 | 2.52 | 2.00 |
| III |  | 1.66 | 1.60 | 1.66 | 1.41 |
| IV |  | 1.22 | 1.00 | 1.22 | 1.00 |
| V |  | 1.00 | 0.75 | 1.00 | 0.74 |
| R |  | 4.04 | 3.03 | 4.04 | 4.10 |
| Final drive ratio |  | 3.38 | 3.73 | 3.23 | 3.23 |
| Tyres |  | 195/65R15 91 H - 205/55 R16 91 W - |
|  |  | 6.5J x 15 Steel - 7 J x 16 Alloy |
| Performance |  |  |  |  |  |
| Power to weight ratio | bhp/t | 88. | 87.1 | 136.7 | 134.3 |
| Output per litre | bhp/ltr | 64.0 | 64.0 | 77.0 | 77.0 |
| Acceleration 0 – 62 mph | s | 10.9 | 11.9 | 7.1 | 8.2 |
| 0 – 1000 m | s | 31.6 | 33.2 | 27.5 | 29.0 |
| Top speed | mph | 125 | 122 146 | 144 |
| Fuel consumption (EU-cycle) |  |  |  |  |  |
| urban | mpg | 29.1 | 27.2 | 23.0 | 20.9 |
| extra-urban | mpg | 53.3 | 47.1 | 40.4 | 38.7 |
| Combined | mpg | 40.9 | 37.2 | 31.7 | 29.7 |
| CO2 | g/km | 167 | 183 | 215 | 227 |

1 May be increased under certain conditions

2 Performance and fuel consumption figures relate to RON 98 fuel