EMBARGO: October 17

MINI hits new heights for performance and luxury

MINI Cooper S to be unveiled at Tokyo Motor Show

Contents

MINI Cooper S; Overview…………………………………………………………………………… 1

Specification and standard equipment…………………………..………………………3

Power……………………………………………………………………………………………………………….4

Driving dynamics……………………………………………………………………………………………	5

Safety……………………………………………………………………………………………..………………..7

Design………………………………………………………………………………………………………………8

MINI Cooper S overview: Beautifully packaged performance

MINI Cooper S will be unveiled at the 2001 Tokyo Motor Show on October 24, hot on the heels of the successful UK launch of MINI One and MINI Cooper. The flagship model is due to set pulses racing next summer.

The “heart” of the MINI Cooper S is the same compact, transverse,             4-cylinder engine from MINI One and MINI Cooper, but uses state-of-the-art supercharger and intercooler technology to extract an impressive 163 bhp at 6,000 rpm. MINI Cooper S will be the most powerful car in its class breaking the magical 100 bhp per litre mark from its 1.6 litre engine.

Perfectly complementing the uprated engine is a new six-speed version of MINI’s highly-praised short-shifting manual gearbox allied to a carefully tuned sports suspension set up.

MINI Cooper S will be instantly recognisable as the top-of-the-range version. An eye-catching air intake scoop on the re-designed bonnet, re-designed chunky bumpers, centrally mounted twin tailpipes and black side-sills give a clear impression of the car’s power and agility.

Behind the scenes, active and passive safety features, including up to six airbags, and run-flat tyres as standard, ensure the car  is also top of its class for safety.

Trevor Houghton-Berry, MINI’s General Manager in the UK said: “MINI Cooper S is the icing on the cake for everyone working on MINI. The car has a great pedigree, great looks,  a stunningly powerful engine and top-of-the-range refinement. Add this to the superb chassis and handling already experienced on MINI One and MINI Cooper and you have the ingredients of a truly ‘Super’ car in the Supermini segment. It's a great second step in MINI's bright future.”

MINI Cooper S will appear on the market thirty-nine years after the original ’S’ was introduced as the flagship of the Mini range. Owned by celebrities such as Peter Sellers, various Beatles and Steve McQueen, the ’S’ established the Cooper legend.

The Mini Cooper S dominated the Monte Carlo rally in the mid-sixties, winning in’64, ’65 and’67 and, controversially in ’66 when it was subsequently disqualified. Touring car and saloon car victories were also being racked up at this time. The ’S’ was also immortalised in celluloid with the release of The Italian Job in 1969.

Dr Heinrich Petra, Head of the MINI Project said: “The desire to achieve such a well balanced front-wheel drive car, and the fun we had in putting 163 brake horse power into the MINI, produced levels of enthusiasm and motivation I have never before experienced. The team have produced a car that sets new standards in performance and luxury in its class.“

MINI Cooper S specification

Engine					4 cylinders; 4 valves per cylinder

Capacity (cc)					1598

Bore/stroke (mm)				85.8 / 77

Compression ratio				8.3:1

Max. output	(bhp)				163

....at engine speed (rpm)			6,000

Max. torque (lb-ft/Nm)			155 / 210

....at engine speed (rpm)			4,000

Acceleration 0 – 62 mph (sec)		7.4

Top speed (mph)				135

Combined fuel consumption (mpg)	33.6 mpg

Length/height (mm)			3655/	1416

Wheelbase (mm)				2467

Weight (kg)					1140

MINI Cooper S standard equipment (over MINI Cooper)

·	Uprated engine to 163 bhp

·	Sports suspension PLUS

·	6-speed manual gearbox

·	Sixteen inch alloys with run-flat tyres

·	Automatic Stability Control and Traction control (ASC+T)

·	Styling - Air intake scoop, larger front bumper including honeycomb grille, re-designed rear bumper housing chrome plated twin exhaust pipes, re-designed wheel arches, rear roof spoiler, ’S’ badging on side and rear, chrome plated side grille with clear indicators, chrome plated fuel cap, two exclusive metallic colours,

·	Interior -  Chrome door sill strip, brushed aluminium-look dash, sport seats, stainless steel foot rest, leather steering wheel and gear stick

Power: Sets the pulse racing

At just 1,140 kg, MINI Cooper S is a powerful yet agile four-seater, offering a 0 – 62 time of just 7.4 seconds and a top speed of 135 mph.

Acceleration and top speed aren’t everything, however. Pulling power around the dial is crucial to the car’s success and MINI Cooper S produces an impressively “beefy” torque curve with 80 per cent of the maximum torque available between 2,500 and 6,500 rpm.

The torquey 16 valve Pentagon engine is improved through a mechanically driven supercharger and intercooler.  The supercharger compresses the fresh air drawn in by the engine to an overpressure of 0.8 bar, heating the air in the compression process. The intercooler then cools it back down again, without a drop in pressure, before it enters the combustion chambers. Bore and stroke remain unchanged and the result is a stunning increase in engine charge, output and performance.

Power delivery is instant with the tooth belt driven compressor experiencing none of the lag suffered by many turbo driven cars. This system develops torque steadily through the range peaking at 155 lb-ft (210 Nm) at 4,000 rpm.

The exhaust system has been modified for performance and sound and its raucous note sets the pulse racing as soon as the car is fired up.

Modifications to the crankshaft, pistons, valves, radiator and the engine management system also contribute to the car’s extra 48 bhp.

Drive-by-wire throttle technology, as used on all MINIs, ensures the Cooper S is extremely reactive,  utilising an electric motor to operate the throttle butterfly instead of a conventional gas cable. Fuel consumption remains impressive at 33.6 mpg (combined).

Driving dynamics: Twisting turns and open roads taken in its stride

MINI One and MINI Cooper have been praised for their agility and direct handling, but MINI Cooper S drivers will find even more driving enjoyment at their finger-tips.

Sports suspension PLUS (an option on MINI Cooper) and MINI’s direct electrohydraulic steering, with just 2.5 turns of the wheel from lock to lock, offers sharp handling and greater feedback, resulting in a kart-like driving experience.  Reinforced McPherson spring struts with a reinforced anti-roll bar at the front provide outstanding stability on winding roads without compromising motorway refinement.

Directional stability is further guaranteed as both drive shafts are identical in length, unlike on most other Superminis, providing symmetrical feedback during cornering, accelerating and braking.

Automatic Stability Control with Traction Control (ASC + T) as standard ensures that the extra power to the front wheels is conveyed safely to the road at all times and can be deactivated. The system uses the ABS sensors to detect any wheel slippage, automatically cutting power to any spinning wheel until it grips again. It also works under deceleration on a slippery surface if a wheel approaches lock-up due to engine braking.  In this instance power is gently fed to that wheel to get it rolling again and so control is regained.

Dynamic Stability Control (DSC) is available as an option and is an even more advanced system.  It maintains cornering stability at all times, not just under braking, adjusting the attitude of the car through automatic brake applications to individual wheels.

MINI’s multi-arm rear axle is unique in this segment of the market and, again, is supported by a reinforced stabiliser bar ensuring optimum roadholding at all times. Balanced weight distribution, front to rear, also aids the stunning road-holding capabilities and razor-sharp turn-in.

Sixteen inch light-alloy wheels wear 195/55 R 16 tyres as standard and optional 205/45 tyres running on impressive seventeen inch S-spoke wheels are available.

Safety: The best in the business

Supplementing the ABS, Electronic Brake Force Distribution (EBD) and Cornering Brake Control (CBC) systems that are standard on MINI,  the addition of ASC + T and the optional DSC places the new MINI Cooper S as the safest, small driver’s car on the market.

Cornering Braking Control (CBC) tempers the natural tendency for a car to become unstable at the rear if the brakes are applied heavily while cornering.  The system recognises that the car is cornering and feeds more braking force to the outside front wheel and counteracts potential oversteer.  Additionally, more braking force can be fed to the rear brakes slowing the car as fast as possible with maximum stability.

MINI Cooper S is the only car in its class to be fitted with run-flat tyres  offering optimum active safety in the event of a puncture and sparing the driver the trouble, and danger, of changing a wheel on the spot.

Tyre wall reinforcements and heat-proof rubber compounds prevent the tyre walls from rubbing together when deflated, or the tyre from jumping off the rim, and the driver can therefore continue for 90 miles at up to 50 mph. The tyre defect indicator warns the driver of any loss of pressure via a warning light on the speedometer.

MINI Cooper S offers a high standard of passive safety.  Front and side “intelligent” airbags inflate in accordance with the severity of an accident and interact precisely with the pyrotechnical belt latch tensioners and belt force limiters. Side airbags as standard in the seat backrests and the optional Advanced Head Protection System (AHPS 2) ensure a high standard of occupant safety in a collision from the side. With the tubular structure of the head airbags extending from the front to the rear roof pillars, both front and rear occupants are equally well protected.

Design: Distinctive and exclusive, inside and out

MINI Cooper S is instantly recognisable as the flagship model of the acclaimed new car. Badged ‘S’ on the side and rear, the Cooper S styling features give a visual indication of its abilities, but also play a major role in enhancing its driving characteristics and performance.

The air intake scoop is an eye-catching addition to the MINI Cooper S styling and funnels fresh air under the bonnet, cooling the air flowing between the supercharger and the engine.

Brand new, body coloured, front and rear bumpers house an integrated honeycomb grille and two chrome-plated tailpipes respectively. Side-sills and wider wheel arches are finished in black. The roof spoiler completes the impressive styling whilst increasing down forces on the rear axle and improving even further the car’s directional stability and driving characteristics.

A bespoke chrome-plated fuel cap, chrome-plated side grilles and chrome “MINI Cooper S” door sill strips give off an air of exclusivity that is complemented by the brushed aluminium look of the interior facia.

MINI’s unique interior design language is borne out by further high-quality materials and Sport seats come as standard (cloth/leather or leather options). The stainless steel foot rest, and leather steering wheel and gear stick accentuate the quality of this top-of-the-range model.

MINI Cooper S is available in eight exterior colours, two of which are exclusive to this top model: Electric Blue metallic and Dark Silver metallic. The crossbars in the radiator grille and boot grab handle come in body colour, whilst the roof and exterior mirrors are finished in white or black (body coloured roof available as a no cost option).