BMW C1 : Technical detail :

|  |  | C1 | C1 200 |
| --- | --- | --- | --- |
| Engine: Capacity | cc | 125 | 176 |
| Bore / stroke | mm | 56.4 x 50 | 62,0x58,4 |
| Max output / rpm | kW / bhp / rpm | 11 / 15 / 9250 | 13/18/9000 |
| Max torque / rpm | Nm / lb-ft / rpm | 12 / 8.8 / 6500 | 17/6500 |
| Cooling system |  | Water | - |
| No of cylinders |  | One, 4-stroke / fully-controlled catalytic converter | - |
| Compression ratio / fuel grade |  | 13.0:1 / premium unleaded, 95 RON | 11,5:1 Premium unleaded,95 RON |
| Valve / gas cycle control |  | DOHC | - |
| Valves per cylinder |  | 4 | - |
| Intake / outlet dia | mm | 21.2 / 19.0 | - |
| Fuel supply |  | BMW engine controller (BMS) | - |
| No / outlet dia | mm | 1 / 28 | - |
| Service interval | km | 7.500 | - |

Electrical system:

| Ignition |  | BMS | - |
| --- | --- | --- | --- |
| Alternator | W | 400 | - |
| Battery | V / Ah | 12 / 14 | - |
| Headlight (H4) | W | 60 / 55 | - |
| Starter | kW | 0.6 | - |

Power transmission:

| Transmission |  | Automatic | - |
| --- | --- | --- | --- |
| Secondary drive |  | Belt transmission | - |
| Rear-wheel drive |  | Two-stage spur gear layshaft | - |

Chassis:

| Frame |  | Aluminium space frame | - |
| --- | --- | --- | --- |
| Suspension | front | Telelever | - |
|  | rear | Drive unit swinging arm | - |
| Spring travel, front / rear | mm | 75 / 85 | - |
| Castor | mm | 113 | - |
| Wheelbase | mm | 1488 |  |
| Brakes : front, disc brake | mm | dia 220 | - |
| rear, disc brake | mm | dia 220 | - |
| optional |  | ABS | - |
| Wheel | front | 3.5 J x 13 | - |
|  | rear | 3.5 J x 12 | - |
| Tyres | front | 120 / 70 - 13 | - |
|  | rear | 140 / 70 - 12 | - |

Dimensions and weights:

| Length, overall | mm | 2075 | - |
| --- | --- | --- | --- |
| Width (without mirrors) | mm | 850 | - |
| Width (with mirrors) | mm | 1026 | - |
| Height | mm | 1766 | - |
| Seat height | mm | 701 | - |
| Ground clearance | mm | 180 | - |
| Unladen weight, DIN | kg | 185 | - |
| Max permissible weight | kg | 360 | - |
| Tank capacity | ltr | 9.7 | - |

Driving data:

| Fuel consumption at 56mph | llmpg | 97.4 | 88.3 |
| --- | --- | --- | --- |
| Theoretical range | km | 250 plus | 190 |
| Acceleration 0-50 km / h | sec | 5.9 | 3.9 |
| Top speed | mph | 64 | 70 |
| CO2 emission | g/km | 64 | 66 |

Payload:

| Passenger seat | kg | 85 | - |
| --- | --- | --- | --- |
| Luggage bridge | kg | 30 | - |
| Topcase | kg | 20 | - |
| Attaché case | kg | 5 | - |