1. BMW 3 Series Compact:
More Power, New Diesel.

Geneva.  The improvements and modifications enhancing the product substance of the Compact models are now making their world debut in Geneva.  Perhaps the first highlight to be mentioned here is the 1.8-litre diesel engine in the 318td added to the range now enlarged to five different versions of the Compact.  This new power unit supplements the 2.0-litre diesel in the 320d and the three 316ti, 318ti and 325ti spark-ignition models remaining in the range unchanged.  Equipped with the latest common rail technology, the 318td and 320td are expected to give the BMW Compact particular support above all in the target group of dynamic diesel drivers.  As a further highlight, the 325ti and 320td now feature BMW’s new six-speed manual gearbox, with six-speed SMG being available as an option on the 325ti.

BMW’s designers have concentrated on just a few but highly effective “lines” in refining particularly the side and rear view of the Compact now featuring, for example, side-sills with even clearer, more powerful contours giving the car an even sleeker look.  At the rear a new shadow line in the sheet metal adds a further touch full of power and performance, and the grab handle for the rear lid has become longer.  In particular, however, new glass covers on the rear lights now finished in transparent red and orange provide a three-dimensional effect.

325ti with six-speed manual gearbox.

Looking at the technical modifications introduced on the Compact, we must focus in particular on the top model in the Compact series, the 325ti, where the straight-six power unit is now combined with BMW’s new six-speed manual gearbox.  Developing 141 kW/192 bhp at 6,000 rpm, the 2.5-litre engine reaches its maximum torque of 245 Nm (181 lb-ft at 3,500 rpm).  And now the close transmission ratios in the new gearbox enable the driver to choose exactly the right gear at all engine and road speeds, thus conveying maximum power and torque to the rear wheels.  The 325ti reaches its top speed of 235 km/h (146 mph) in fifth gear.  Providing an overdrive function, sixth gear serves in particular to reduce engine speed at high speeds on the road, offering the driver and his passengers the advantage of a lower noise level.  A further advantage is that the 325ti Compact is now even more economical, the straight-six consuming up to four per cent less fuel than before under practical driving conditions thanks to the six-speed gearbox replacing the former five-speed manual transmission.

To consider the specific details, the overall transmission ratio has increased from 4.23:1 on the former five-speed to 5.11:1 on the new six-speed transmission, with the final drive ratio remaining unchanged at 3.23:1.  Lifetime oil remaining in the transmission for the entire service life of the car helps to provide an even higher standard of economy.  And last but not least, power is transmitted by a maintenance-free self-adjusting clutch (SAC).

Again reflecting BMW’s particular style, the 325ti Compact comes with short, crisp and extremely precise gearshift underlining the car’s sporting character particularly on winding roads where the driver is required to frequently shift gears:  With its six gears moving easily into position, this compact performance saloon is the ideal sports car for short and powerful sprints from one bend to the next.

SMG transmission: shifting gears within fractions of a second.

Like all BMW 3 Series with 2.5 and 3.0-litre spark-ignition engines, the 325ti Compact is optionally available with six-speed SMG transmission allowing the driver to shift gears either through paddles on the steering wheel or by briefly flicking the gearshift lever on the centre console forwards or backwards.  This operates the clutch automatically, meaning that the car does not even come with a clutch pedal in this case.

SMG – the Sequential Manual Gearbox – comes from Formula 1 and shifts gears faster than ever before.  Acting as a shift-by-wire system without any kind of mechanical link connecting the gearshift lever and the transmission, SMG shifts gears in just 150 milliseconds in a sequential process that is with one gear following the other on a straight line.  The big advantage, of course, is that the driver is able to leave his hands on the steering wheel and cannot make a mistake when shifting gears since it is no longer possible with this system to leave out a gear when shifting up or down on one gear level, unlike the shifting process with a conventional H-pattern shift gate.  The driver may nevertheless benefit from this option to skip gears in practice, simply by pushing the paddles or the centre gearshift lever several times in a row.  And when shifting down, the system automatically gives gas in between gears in the interest of a smooth gearshift.

Driving with the SMG paddles not only makes things a lot easier for the driver but also offers much greater pleasure when shifting gears in the first place – an advantage particularly drivers of the 3 Series Compact appreciate on the road.  This also applies to drivers who do not want to miss the good old centre gearshift and prefer shifting gears the conventional way, with SMG offering high-speed operation, a smooth gearshift and ultimate precision with both gearshift options.  For SMG is intended primarily for the dyed-in-the-wool sports driver who appreciates an extremely quick gear change but nevertheless wishes to decide himself when to shift gears.  To accelerate all-out with full power, the driver can even leave his foot pressed fully down on the gas pedal when shifting gears with SMG:  Advanced engine electronics interrupt the flow of engine power for fractions of a second, the control unit electro hydraulically shifting gears and opening/closing the clutch.

Sporting or comfortable.

Pressing the sports button, the driver of the 325ti can choose either the more comfortable basic or a sporting and dynamic shift program.  With the sports program active and DSC deactivated, you can really enjoy all of the car’s power when accelerating, simply pressing down the gas pedal quickly and completely to increase start-up engine speed to approximately 4,000 rpm before the system engages the clutch.  This means that even the less experienced driver is able to accelerate all-out from 0–100 km/h in 7.1 seconds.

In the cruise mode the system shifts gears automatically as a function of road speed, gas pedal position and acceleration/deceleration until the driver operates the shift lever or paddles.

BMW’s five-speed automatic transmission is available on all versions of the 
3 Series Compact with the exception of the 318td.  This offers the driver the advantages of adaptive transmission management (ATM) with gearshift points adapted to the driver’s personal style of motoring.  The standard transmission on the 316ti, 318ti and 318td Compact models is BMW’s proven five-speed manual, the 320td and 325ti coming as standard with six-speed manual transmission.

A unique character within the 3 Series.

Viewed from the front, the 3 Series Compact with its separate high-and low-beam headlights is absolutely unique and unmistakable.  And at the same time the Compact’s design language is truly dynamic, firm and tense surfaces with a positive curvature creating subtle lines and shadows.  Striking features such as the classic contour line along the side panel give the 3 Series Compact truly dominating character.

Starting at the rear, the sideline moves down dramatically behind the front wheels, accentuating the car’s dynamic performance and muscle through the strongly contoured wheel lips.  The sills beneath the door openings add to the sporting touch of this muscular performer, stretching the lines of the car and generating a bright contour line giving the Compact even more visible strength and dynamism from the side.

The same applies to the rear-end view:  The shadow line in the tailgate now added here introduces a special feature stretching the look of the rear end and conveying the impression of even more power.  A striking counterpoint is the shadow line formed by the longer grab handle on the tailgate accentuating the width of the car from behind.

Modified rear lights.

Covers in red-orange transparent glass have now replaced the former clear glass covers on the rear lights.  From behind, therefore, the 3 Series Compact conveys an even more impressive feeling of value and progressive style.  With the inner structure of the lights remaining unchanged as one larger and one smaller circle, the new model retains the same fresh touch as its predecessor.  And the three-dimensional look with the lights coming out in their full depth demonstrates the superior function and design features to the last detail.

Top-of-the-class technology for the star among the six-cylinders.

Power and performance naturally comes first and foremost from the engine.  So the 2.5-litre power unit in the top-of-the-range 325ti Compact marks the absolute climax in motoring refinement and engine power, as well as all-round economy and environmental compatibility:  Maximum output of the straight-six power unit is 141 kW/192 bhp at 6,000 rpm, maximum torque is 245 Newton-metres/181 lb-ft at 3,500 rpm.  The key to this outstanding combination of power and muscle is ultra-modern engine technology of the highest standard. BMW’s innovative Bi-VANOS, that is infinite camshaft control of the valves’ intake and outlet timing, ensures an optimum torque curve throughout the entire speed range as a function of engine speed and the position of the gas pedal.  In practice this gives the driver of the 325ti Compact superior torque at low engine speeds combined with high power at high speeds.

Another proven technology is the four-valve drive system with the spark plug right in the middle.  This ensures optimum cylinder charge, as an essential prerequisite for the six-cylinder’s superior output and torque.  The specific arrangement of the two intake and outlet valves also allows more efficient design of the combustion chamber, again contributing to the car’s enhanced fuel economy.  Cylinder-specific knock control on the six-cylinder also helps to save fuel, the sensors detecting any inclination of the engine to knock right from the start and informing the Digital Motor Electronics (DME) accordingly.  Monitoring and masterminding all central engine functions, DME will in this case change the ignition angle and/or the ignition timing immediately for each cylinder, allowing the engine to run smoothly and efficiently on all fuel grades.

The solid-state distributor system, finally, gives each cylinder and spark plug its own ignition coil, ensuring a powerful ignition spark and, as a result, optimum combustion and efficient use of fuel.

Environmental compatibility of the highest standard.

The driver of the BMW 325ti Compact benefits from this supreme technology in several ways:  He enjoys unparalleled performance in a car of this calibre, good fuel economy and outstanding environmental compatibility, the six-cylinder outperforming the EU4 emission standards and thus entitling owners of the car in Germany to a reduced rate of tax.

All-electronic throttle butterfly providing exactly the right power 
and performance in every situation.

In order to dose engine output appropriately with the gas pedal in stop-and-go traffic, whilst at the same time ensuring an immediate response of the car whenever the driver requires high power, the six-cylinder comes with an all-electronic throttle butterfly recognising which gear is currently in mesh and thus applying an individually programmed throttle butterfly control curve.  This also guarantees smooth transition from overrun to part load and vice versa.

Four-cylinder power units with VALVETRONIC.

Yet another highlight in technology is to be admired beneath the engine compartment lid of the two 316ti Compact and 318ti Compact four-cylinder spark-ignition models is BMW’s innovative VALVETRONIC engine management.  The power units from BMW’s engine plant in Hams Hall, Great Britain, equipped with this system no longer require a throttle butterfly under normal operating conditions.  Instead, engine load is controlled by infinite valve lift management serving in particular to reduce fuel consumption under regular driving conditions by up to ten per cent and cut back exhaust emissions accordingly.  As an example, the 316ti Compact developing 85 kW/115 bhp maximum output and reaching a top speed of 201 km/h (125 mph), makes do with just 7.0 litres premium on 100 kilometres (40.3 mpg Imp) in the European test cycle, an excellent figure versus the competition.  In the European extra-urban test cycle, fuel consumption is just 5.4 litres/100 km (52.3 mpg Imp), meaning that in this case the driver would be able to cover 1,188 kilometres (737 miles) before having to refuel.  At the same time VALVETRONIC gives the engine even better dynamic and spontaneous performance, plus extra running smoothness and refinement on low loads.

A further advantage, finally, is the exceptional spontaneity of the engine when accelerating, since engine load management is determined directly on the combustion chamber.

BMW 320td and 318td: diesel-fast and super-economical.

The diesel engines in the 318td and 320td Compact can take any challenge with their fuel-efficient spark-ignition counterparts in terms of both power and economy:  The 2.0-litre direct-injection diesel engine with second-generation common rail technology in the 320td develops maximum output of 
110 kW/150 bhp at 4,000 rpm and maximum torque of 330 Newton-metres/ 243 lb-ft at just 2,000 rpm in the interest of superior performance on the road.  As a result, the 320td Compact offers a standard of performance and motoring refinement available until recently only with genuine sports cars.  And despite this superiority, the engine consumes a mere 5.7 litres of diesel fuel/100 km (49.6 mpg Imp) in the EU cycle.  Being rated in the EU3/D4 emission category, finally, the 320td qualifies the driver for lower road tax in Germany.

With the 320td moving up to a new power category, the new 318td Compact is now rounding off the range at the lower end.  Developing 85 kW/115 bhp at 4,000 rpm and 280 Nm/206 lb-ft at 1,750 rpm, the four-cylinder power unit in the 318td Compact excels through its harmonious refinement, exemplary response and superior fuel economy.  In the EU cycle the 318td consumes just 5.6 litres of diesel fuel on 100 km (50.4 mpg Imp).  And qualifying for the EU3/D4 emission category, the 318td Compact also offers its owner tax relief in Germany.

Nimble and practical.

The 3 Series Compact and the Saloon have the same wheelbase, but the former is 21 cm or 8.3´´ shorter.  It nevertheless boasts creative solutions making the BMW Compact both practical and very convenient in everyday motoring.  Measuring 1,146 millimetres (45.1´´ ) across at its widest point, the strikingly designed tailgate moving up to an almost vertical position is really very practical and meets virtually all requirements.  Even a 19´´ computer monitor packed in its original box or a washing machine will fit inside the luggage compartment – and then you can still close the tailgate!  With the rear-seat backrests being split asymmetrically and with both segments folding down to an almost horizontal position, the driver of the compact benefits from luggage space ranging from 310 to 1,100 litres.  Motorists often required to take along bulky luggage will appreciate the special remote control function opening the tailgate fully automatically (which means that you do not have to first put down what you are carrying in order to then open the tailgate manually).

The storage package available as an option allows the user to discreetly store valuables beneath a folding cover in the parcel shelf where they are transported safely and securely without slipping around.  Shopping bags can be attached to special profile bars in the variable luggage compartment, again to secure them in position.  The umbrella holder beneath the parcel shelf is accessible from the luggage compartment and a 12 volt power socket is also included in the storage package.

Lots of room for luggage – lots of comfort for passengers.

With the Compact offering lots of space and convenience for your luggage, the driver and his passengers should naturally also receive the same kind of treatment:  Homologated as a five-seater, the 3 Series Compact offers rear-seat passengers very convenient entry and exit conditions, the front-seat backrests tilting far to the front and in the process moving forward by about 90 millimetres (3.54´´ ) and even rising up as well.  This gives passengers entering the car an opening 243 millimetres (9.57´´ ) wide at knee level. To improve visibility for the driver, finally, the rear-seat headrests may be folded down.

Trap release on the door windows.

Starting immediately, the Compact models come with a trap release on the door windows, as already featured on the Saloon, Touring and Coupé.  So whenever somebody’s hand or an object gets stuck by mistake between the window and the window frame, the windows moving up electrically will automatically open up immediately.

Full range of equipment – low cost of ownership.

The 3 Series Compact is the premium model in its segment.  This is confirmed, not least, by the Compact’s wide range of chassis and safety features.  The interior equipment, in turn, comprises all the essential features characteristic of the 3 Series, using the most sophisticated materials in perfect finish and incorporating practical comfort features such as the options offered to each driver in programming his or her personal seat, radio or climate settings by remote control from the key to the car.  Apart from the actual price of a car, the cost of insurance, tax, service and repair is crucial to the overall cost of ownership.

Each model within the range of 3 Series Compacts has been specifically optimised on precisely these points.  Low cost of insurance compared with other cars in the market proves that the Compact was designed and built from the start for inexpensive repair in the event of an accident.  And ultimately, low cost of maintenance helps to give a car lasting value in the market.

(Almost) unlimited possibilities to drive a unique original.

The purchaser wishing to personalise his Compact over and above the wide range of sophisticated standard features will find an almost unlimited range of choice within the Compact series:  In all, the car is available with some 70 options and items of special equipment, plus approximately a dozen paintwork colours and upholstery/interior colour combinations as well as several materials and colours for the interior trim, for example on the top of the instrument panel.  So in a nutshell, each and every proud owner is able to give his BMW Compact his very own personal touch.