Specifications BMW 7 Series.
730i/730Li.

| Body d Anzahl Türen / s |  | 730i | 730Li |  |  |
| --- | --- | --- | --- | --- | --- |
| No. of doors/seats |  | 4/5 | 4/5 |  |  |
| Length/width/height (unladen) ) | mm | 5,029/1,902/1,492 | 5,169/1,902/1,492 |  |  |
| Wheelbase | mm | 2,990 | 3,130 |  |  |
| Track, front/rear | mm | 1,578/1,582 | 1,578/1,582 | ; |  |
| Turning circle | m | 12.1 | 12.6 |  |  |
| Fuel tank capacity/range | approx. ltr | 88 | 88 |  |  |
| Cooling system incl. heater | ltr | 11.4 | 11.4 |  |  |
| Engine oil | ltr | 6.5 | 6.5 |  |  |
| Transmission fluid | ltr | Permanent filling | Permanent filling |  |  |
| Final drive fluid | ltr | Permanent filling | Permanent filling |  |  |
| Weight, unladen (EU)1 | kg | 1,790/1,865 | 1,820/1,895 |  |  |
| Max. load (DIN) | kg | 580 | 580 |  |  |
| Max. permissible weight (DIN) | kg | 2,370 | 2,400 |  |  |
| Max. permissible axle load front/rear | kg | 1,105/1,325 | 1,120/1,340 |  |  |
| Max. trailer load2 |  |  |  |  |  |
| braked (12%)/unbraked | kg | 2,000/750 | 2,000/750 |  |  |
| Max. roof load/trailer nose | kg | 100/100 | 100/100 |  |  |
| Luggage comp. capacity, VDA | ltr | 500 | 500 |  |  |
| Drag coefficient | cX x A | 0.28 x 2.37 | 0.28 x 2.37 |  |  |
| Engine |  |  |  |  |  |
| Layout/No. of cylinders/valves |  | R/6/4 | R/6/4 |  |  |
| Engine management |  | MS45 | MS45 |  |  |
| Displacement | cm³ | 2,979 | 2,979 |  |  |
| Bore/stroke | mm | 89.6/80.0 | 89.6/80.0 |  |  |
| Compression ratio | :1 | 10.2 | 10.2 |  |  |
| Fuel grade | RON | 98 | 98 |  |  |
| Max. output | kW | 170 (231) | 170 (231) |  |  |
| At engine speed | min–1 | 5,900 | 5,900 |  |  |
| Max. torque | Nm | 300 | 300 |  |  |
| At engine speed | min–1 | 3,500 | 3,500 |  |  |
| Electronic |  |  |  |  |  |
| Battery/location | Ah/– | 80/boot | 80/boot |  |  |
| Alternator | A/W | 140/1,960 | 140/1,960 |  |  |
| Chassis |  |  |  |  |  |
| Front suspension |  | Double-joint thrust-rod spring strut axle in aluminium; compensation of transverse forces; anti-dive |
| Rear suspension |  | Integral IV multi-arm axle in aluminium; wheel suspension with special effect and anti-squat/anti-dive; pneumatic suspension with self-levelling |
| Driving stability system |  | DSC (incl. ABS, CBC, DBC, ASC); Dynamic Drive (sway stability system) and EDC-C (continuous electronic damper adjustment) as an option |
| Brakes, front |  | Double-piston swing-calliper disc brakes (inner-vented) |
| Diameter | mm | 324 | 324 |  |
| Brakes, rear |  | Double-piston swing-calliper disc brakes (inner-vented) |
| Diameter | mm | 324 | 324 |  |
| Steering |  | Power steering with speed depending support (Servotronic) |
| Overall ratio | :1 | 13.1 | 13.1 |  |
|  |  | 3.0 Turns lock to lock |
| Type of transmission |  | 6-speed Steptronic automatic transmission (ZF 6HP26) |
| Transmission ratio | I | :1 | 4.17 | 4.17 |  |
|  | II | :1 | 2.34 | 2.34 |  |
|  | III | :1 | 1.52 | 1.52 |  |
|  | IV | :1 | 1.14 | 1.14 |  |
|  | V | :1 | 0.87 | 0.87 |  |
|  | VI | :1 | 0.69 | 0.69 |  |
|  | R | :1 | 3.40 | 3.40 |  |
| Final drive ratio | :1 | 3.73 | 3.73 |  |
| Tyres |  | 225/60R17 99W | 225/60R17 99W |  |
| Wheels |  | 8J x 17 LBS | 8J x 17 LBS |  |
| Performance3 |  |  |  |  |
| Power to weight ratio (DIN) | kg/kW | 10.5 | 10.7 |  |
| Output per litre | kW/ltr | 57.1 | 57.1 |  |
| Acceleration 0–100 km/h | sec | 8.1 | 8.3 |  |
| Top speed | km/h | 237 | 237 |  |
| Fuel consumption (EU-cycle) |  |  |  |  |
| In town | ltr/100 km | 15.5 | 15.7 |  |
| Out of town | ltr/100 km | 7.9 | 8.0 |  |
| Overall | ltr /100 km | 10.6 | 10.7 |  |
| CO2 | g/km | 257 | 260 |  |
| Miscellaneous |  |  |  |  |
| Emission classification |  | EU4 | EU4 |  |

Weight of the operable vehicle (DIN) plus 75 kg for driver and luggage.			
2May be increased under certain condition.

3Performance and power figures are based on ROZ 98, fuel economy on ROZ 95.		
These specifications are for the German market. Deviations from the model variants described here are possible in various countries.