5.	The New BMW 630i Coupé/
 	630i Convertible.

A wonderful tradition is back: Following the first BMW 6 Series which entered the market in the late ’70s with a 6 cylinder power unit, the new BMW 630i Coupé/630i Convertible now also boast a 6 cylinder of the highest calibre.

Demand for the BMW 6 Series with a 6 cylinder power unit has always been particularly great in markets the world over. So BMW has responded accordingly, taking up such a model in the range. Displacing three litres, this new power unit is making its world debut in both versions of the 
BMW 6 Series – and at a later point in time it will also replace the straight-six power units in other BMW models.

Displacing 2,996 cc, the new 6 cylinder develops maximum output of 
190 kW/258 bhp at 6,600 rpm and comes with maximum torque of 
300 Newton-metres/221 lb-ft at just 2,500 rpm. With its compression ratio of 10.7:1, the engine is able to run on unleaded fuel varying from 91–98 RON. Average fuel consumption in the BMW 630i Coupé with six-speed manual gearbox is just 9.0 litres/100 km (31.4 mpg Imp) (six-speed automatic transmission: 9.5 litres/29.7 mpg Imp). In the BMW 630i Convertible, in turn, average fuel consumption is 9.6 and, respectively, 9.9 litres/100 km 
(29.4/28.5 mpg Imp).

Compared with the BMW 645Ci, the transmission ratios are somewhat “shorter” on both the manual gearbox and the automatic transmission models. And the customer opting for the BMW 630i also has the choice 
of BMW’s SMG Sequential Manual Gearbox or automatic transmission.

With the driver shifting gears by hand, the new BMW 630i Coupé accelerates to 100 km/h in just 6.5 seconds (automatic transmission model: 6.7 seconds). The BMW 630i Convertible, in turn, performs the same exercise in 6.9 and, respectively, 7.2 seconds. The top speed of all models is 250 km/h or 
155 mph.

Low weight for outstanding performance.

The weight of the new BMW 630i models is down versus the 8 cylinder versions on average by 120 kg or 265 lb, depending on the transmission and type of body. Differences in equipment both outside and inside, in turn, 
are perhaps more significant to the driver of a BMW 630i Coupé or Convertible, since they are clearly visible and distinguish these models from the top-of-the-range versions.

As an example, the BMW 630i comes as standard on 7½ -inch wide and 
17-inch high light-alloy wheels in brand-new styling and running on 
245/50 R17 tyres. And the front brake discs are slightly smaller in diameter than on the BMW 645Ci.

On the body of the car, the new BMW 630i Coupé/630i Convertible differ 
from their “bigger brothers” by chrome-plated tailpipes in round instead of oval design, as well as black instead of chrome-plated kidney rods in the typical BMW radiator grille. Inside, the upholstery of the new 6 cylinder models is an attractive combination of cloth and leather, with complete leather available at extra cost.