9. The New BMW X3 2.0d: 
Making an Attractive Entry into the 
BMW X Family.

The new BMW X3, the first Sports Activity Vehicle (SAV) in the midrange segment, is entering the market with a new entry-level engine as of 
September 2004: Introducing the X3 2.0d, BMW is offering a 4 cylinder 
engine in a utility vehicle for the first time, thus enabling an even larger group 
of customers to enjoy the particular experience of an SAV.

Featuring direct fuel injection, this 2.0-litre common rail diesel of the latest generation develops maximum output of 110 kW/150 bhp at 4,000 rpm and, with maximum torque of 330 Nm/243 lb-ft, ensures a dynamic driving experience in the X3. The fuel economy of the new model proves that agility and economy in an all-wheel-drive vehicle are not a contradiction in terms, 
the X3 2.0d making do with 7.2 litres of diesel fuel/100 km (39.2 mpg Imp) in the European Driving Cycle.

The updated straight-four in the new BMW X3 2.0d offers a standard of flexibility quite impressive in a diesel. Developing injection pressure of up to 1,600 bar, the latest generation of common rail technology provides the engine’s superior maximum torque of 330 Nm or 243 lb-ft at a very low 
2,000 rpm, enabling the X3 2.0d, like its “bigger brothers” to translate all the particular benefits of BMW’s new xDrive all-wheel-drive system into genuine driving dynamics on the road: Electronically controlled, the multiple-plate clutch distributes drive power within fractions of a second between the two axles, ensuring not only excellent traction, but also a very fast response 
in the process for a level of agility never seen before in four-wheel drive.

Perfect harmony: driving dynamics, agility, and economy.

The X3 2.0d offers impressive performance data also in terms of its longitudinal dynamics: Acceleration to 100 km/h comes in 10.2 seconds, 
and the X3 2.0d completes the sprint from 80–120 km/h in fourth gear in just 
8.3 seconds. This and the top speed of 198 km/h or 123 mph proves that 
the new X3 2.0d lives up to the standard of a BMW Sports Activity Vehicle in 
every respect. And the good news is also that this economical drive system gives the vehicle a range of 875 km or 543 miles on just one tank in the EU consumption cycle.

Six-speed gearbox featured as standard.

Efficient use of fuel combined with excellent performance is also a result of the six-speed manual gearbox harmonising perfectly with the two-litre power 
unit. First gear is conceived for superior muscle and pulling power for particularly good acceleration from a standstill and, as a very important feature 
in this class, good setting-off characteristics on a gradient or with a trailer.

The next five gears – with the X3 2.0d reaching its top speed in sixth gear – provide exactly the right ratio for each speed range and level of engine revs, enabling the driver of the X3 2.0d to use the full torque of the engine at all speeds and accelerate all-out. Similarly, he can also drive the X3 in a relaxed, comfortable style, reducing gearshifts to a minimum without forfeiting too much agility.

The six-speed gearbox featured as standard shifts very smoothly and 
comfortably in typical BMW style and with short, precise shift travel, again underlining the dynamic character of this Sports Activity.

The BMW X3 2.0d comes as standard with 235/55 all-season tyres on 
17-inch light-alloy rims in new design. And like all BMW X3s, it naturally features BMW’s intelligent xDrive four-wheel-drive system complete with an electronically controlled multiple-plate clutch. Other standard features are DSC Dynamic Stability Control, DBC Dynamic Brake Control, CBC Cornering Brake Control, as well as two-stage brake lights for enhanced safety. 
And like all BMW Sports Activity Vehicles, the X3 2.0d features BMW’s unique Trailer Stability Control automatically detecting any dangerous sway motion 
of a trailer and intervening whenever appropriate. HDC Hill Descent Control, finally, ensures superior safety and comfort on rough terrain by automatically controlling the speed of the vehicle as well as the intervention of the brakes on a steep downhill gradient.

New features on all X3s.

Starting in September with the launch of the X3 2.0d, further new features will be available in all X3s in the areas of comfort, communication, entertainment and safety. As an example, the BMW Business audio system will also be able to play CDs with MP3 files and the popular Bluetooth mobile phone preparation kit will support all functions of the BMW Assist driver assistance system. The TV function available in conjunction with the Professional navigation system is able to receive not just analogue, but also digital TV signals, and a child seat complying with the ISOFIX standard may now also be fitted on the front passenger’s seat, in which case the airbag function is of course deactivated.