|  | Media Information |
| --- | --- |
|  | 12 February, 2012 |
|  | The new BMW M6 Coupé and Convertible |
|  | V8 M TwinPower Turbo: 560hp, 680Nm, 0-62mph in 4.2 seconds (Coupé) EfficientDynamics technologies improve fuel consumption and lower emissions by 30 per cent Seven-speed M DCT gearbox as standard Specific M chassis incorporating M Drive with Active M Differential and optional M Carbon Ceramic Brakes Extensive standard equipment including M driving environment with Head-up Display |

The new BMW M6 Coupé and M6 Convertible models represent the most recent expression of the BMW M philosophy, having sold over 14,000 examples of the previous generation worldwide.

Powered by the latest V8 M TwinPower Turbo engine producing 560hp, these bold 6 Series flagship models offer searing performance and sporting dynamics, combined with supreme long-distance touring manners and everyday usability.  With near 50:50 weight distribution and optimised aerodynamics the latest BMW M6 offers an intense M experience.

Thanks to BMW’s EfficientDynamics technologies and the range of measures this incorporates, the new M6 is both cleaner and 30 per cent more fuel-efficient than its predecessor, despite being significantly faster and more powerful.

Bespoke M design, a driver-focused cabin and cutting edge in-car technology, makes the new M6 the most desirable yet, whether ordered with the lightweight carbon-fibre roof or the elegant retractable soft top.

| Model | Power hp | Torque Nm | 0 – 62mph Seconds | Top Speed Mph | Combined Mpg | CO2 Emissions g/km |
| --- | --- | --- | --- | --- | --- | --- |
| BMW M6 Coupé | 560 | 680 | 4.2 | 155* | 28.5 | 232 |
| BMW M6 Convertible | 560 | 680 | 4.3 | 155* | 27.4 | 239 |

*  Electronically limited

Expressive design with a sporty edge from BMW M

The classical proportions and elegant design of the current 6 Series Coupé and Convertible have won many admirers since their introduction. Now BMW M gives them a sporty, dynamic update, with aggressive design features defined by the technical considerations of the engineering team. The need for appropriate cooling air, the revised chassis and the pursuit of aerodynamic excellence: all have dictated the creative approach of the designers. The result is bold and powerful with an aggressive stance.

At the front a new M apron with wide air-intake apertures provides the necessary cooling for the engine, while sharply contoured headlamps featuring the characteristic BMW Corona rings shine brightly thanks to the latest Adaptive LED headlight technology. The new M kidney grille, with its black slats and shape inspired by the double spoke alloy wheels, enhances the front end.

To the side, a 30mm increase in the front track has resulted in a significant swelling of the front wheel arches, with the familiar M gills behind them featuring chrome flares and indicator bars with the M logo. At the rear, the now-traditional twin pairs of exhaust pipes sit either side of the aerodynamically optimised diffuser.

The new M6 comes as standard with 19” Star-spoke forged alloy wheels featuring seven double spokes in a two-tone finish. Optional 20” alloy wheels, with five double spokes hinting at the weight saving their lightweight design provides, are also available.

The BMW M6 Coupé once again uses a carbon-fibre reinforced plastic roof panel, lowering the car’s centre of gravity and improving handling agility as a result. In addition, the dark colour of the roof elongates the silhouette of the car when viewed in profile, something that’s further exaggerated by the BMW High-gloss Shadowline trim around the side glass.

The M6 Convertible features the same high quality retractable roof as the 6 Series Convertible, with its ‘fin’ architecture projecting into the rear section, enhancing the silhouette of the car. The heated vertical glass rear window retracts independently of the roof itself. Operation of the roof is via a button on the centre console, and it can be raised and lowered at anything from a standstill to speeds of up to 25mph. Just 19 seconds is all it takes to lower the roof; 24 seconds to raise it once again. Buyers can choose from Black, Beige or Anthracite Silver fleck for the roof material colour.

TwinPower Turbo technology for the most powerful M6 ever

The new BMW M6 Coupé and M6 Convertible are equipped with the same high-revving, turbocharged V8 engine as the M5 Saloon. This revolutionary powerplant not only produces 53hp more than its ten-cylinder predecessor at 560hp, but it also benefits from a greatly improved torque output over a broad band of revs. It’s this 680Nm, available from as low as 1,500rpm to 5,750rpm, that not only gives the new M6 its stunning outright acceleration, but also its commanding flexibility on-road.

The key to this impressive performance is BMW’s M TwinPower Turbo technology, incorporated on the M6 via twin turbochargers built in to the twin scroll principle, including a cross-bank exhaust manifold. This sophisticated, 4.4-litre engine also includes direct fuel injection, VALVETRONIC variable valve timing and Double VANOS continuously variable camshaft control, all of which help it to rev to 7,200rpm – unusually high for a turbocharged engine.

The result is a 0-62mph sprint of just 4.2 seconds for the M6 Coupé, with the M6 Convertible following at 4.3 seconds. Both versions have a top speed limited to 155mph.

This marked increase in performance has gone hand in hand with significant improvements to fuel consumption and emissions. With the adoption of BMW’s

EfficientDynamics technology, the efficiency of the V8 M TwinPower Turbo engine is further improved by Auto Start-Stop, Brake Energy Regeneration and Active Aerodynamics amongst others, helping to reduce consumption and emissions by approximately 30 per cent.  The new BMW M6 Coupé has a combined fuel consumption of 28.5mpg (Convertible 27.4mpg) with CO2 emissions of 232g/km (Convertible 239g/km). Moreover, with an increased fuel tank size of 80 litres, the new BMW M6 offers excellent touring range.

Seven speeds for ultimate gearbox efficiency

The new BMW M6 models use BMW M’s latest seven-speed Double Clutch Transmission (M DCT) with DRIVELOGIC. This advanced transmission features two oil-cooled ‘wet’ clutches, offering near-seamless shifts. The DRIVELOGIC control offers three separate shift programs, both in automatic and manual modes, providing the driver with the best of both worlds whether they are looking for the sportiest selection of gears or driving comfort. M DCT also includes a Launch Control function, while in manual mode gears can be changed via either the M gear selector or via paddles on the M Sport steering wheel.

The M DCT gearbox is part of an advanced powertrain that also includes the M-Differential. This electronically controlled multi-plate limited slip differential ensures the best possible traction at all times, with a locking factor from 0-100 per cent. As with many of the other systems on the new BMW M6, it is linked into the car’s Dynamic Stability Control (DSC) system to ensure maximum driving safety.

M-specific chassis for the most demanding of drivers

BMW’s M division has worked tirelessly on the chassis of the new M6, and the result is a sporting car that combines tremendous ability for high performance driving with everyday usability. Drawing on their vast collective experience and legendary back catalogue, the M engineers have combined their knowledge with the latest technology, honing it over an extensive testing period.

To meet the expectations of the most demanding drivers, the rear axle subframe has been bolted directly to the body, the front axle kinematics redesigned with M-specific settings, and a number of 6 Series suspension components replaced with forged aluminium items. The electro-hydraulically controlled dampers feature BMW’s Variable Damper Control (VDC) with a choice of three settings, so that drivers can tailor the suspension of the M6 to best suit their driving style and environment at any given moment.

The new M6 is steered via a hydraulic rack and pinion system, with a variable ratio to increase low-speed agility while offering outstanding stability at speed. M-specific Servotronic power steering offers ideal weighting for the driver, with a choice of three settings for further personalisation.

BMW’s sophisticated Dynamic Stability Control (DSC) uses many of the cars electronic systems – such as ABS, CBC and DBC – to provide an effective safety net. However, drivers can select the M Dynamic Mode (MDM) that overrides the basic settings, allowing for greater wheel slip and even more sporty driving characteristics.

Personalisation of driver settings via the M buttons

The settings for the DSC, the engine characteristics, DDC, Servotronic and M DCT DRIVELOGIC can all be adjusted via the buttons on the centre console or from within the BMW iDrive system. However, drivers can also assign particular configurations to the ‘M1’ and ‘M2’ buttons located on the steering wheel. This way, for example, the driver can store a ‘sporty’ set up and a ‘comfort’-biased set up that can be accessed immediately at the touch of button.

M Carbon Ceramic Brakes

The new BMW M6 Coupé and M6 Convertible feature as standard a powerful braking system with 400mm front discs and 396mm rear discs, gripped by six-piston callipers on the front axle that can be identified by their dark blue metallic finish.

However, for the first time buyers can choose the latest optional M Carbon Ceramic Brakes, with front discs measuring 410mm in diameter and 396mm on the rear axle. This powerful new braking system offers even better resistance to heat and a reduction in the rotational masses by 19.4kg. The matte gold finish on the brake callipers identifies cars equipped with these outstanding brakes.

The body structure: strength by design

In addition to the aforementioned carbon-fibre reinforced plastic roof the new M6 benefits from a hybrid construction of steel, aluminium and composite materials to give an immensely strong platform that’s remarkably light. In addition to the high strength steels used in the monocoque, the doors and bonnet are fashioned in aluminium while the front wings are formed in plastic. The boot lid, and the roof cover on the convertible, are made from an SMC fibreglass material.

With robust load path structures, large and precisely engineered deformation zones and the latest restraint systems, the new M6 has been engineered with safety as a priority.

In the cabin: sporting luxury

As the ultimate expression of the BMW M ethos, the interior of the new M6 Coupé and M6 Convertible is a blend of luxury appointments and sporting intent. The new M Sport seats, a lightweight design, feature an integrated seat belt system, electric seat adjustment, a pneumatic lumbar adjustment and manually adjustable under thigh support. Active head restraints also feature, and the M logo embossed into the shoulder area is the finishing touch.

The cockpit is finished in fine grain extended Merino leather, with the dynamic styling of the 6 Series interior particularly suited to the role of an M car. There’s more space too, and 460 litres of luggage capacity, 300-350 litres in the M6 Convertible depending on whether the roof is raised or lowered, an increase over its predecessor.

The driver’s environment is particularly sporty, with an instrument facia featuring the latest Black Panel technology, M dials with red needles and white instrumentation and

the M logo. Should the driver raise their eyes they’ll see the M-specific Head-Up Display (HUD) with its digital speedometer readout and speed limit identification, gear and rev counter and shift lights.

Extensive standard equipment and personalisation options

The new BMW M6 offers a particularly high level of standard equipment. In addition to the advanced mechanical package that the car offers, the M6 driver enjoys two-zone climate control, heated and multi-adjustable M Sport seats, the M-specific HUD, Extended Merino leather interior trim and BMW Professional Navigation with 10.2” colour screen. Customers can then further personalise their cars with an upgrade to 20” alloy wheels, M Carbon Ceramic Brakes, Internet, BMW Night Vision and a Bang and Olufsen Advanced audio system.

The new M6 Coupé and Convertible goes on sale in the UK on 15 September 2012, with the Coupé costing £93,795 and the Convertible £98,995.

Ends

The BMW Group

The BMW Group is one of the most successful manufacturers of automobiles and motorcycles in the world with its BMW, MINI, Husqvarna Motorcycles  and Rolls-Royce brands. As a global company, the BMW Group operates 25 production and assembly facilities in 14 countries and has a global sales network in more than 140 countries.

In 2011, the BMW Group sold about1.67 million cars and more than 113,000 motorcycles worldwide. The profit before tax for the financial year 2010 was euro 4.8 billion on revenues amounting to euro 60.5 billion. At 31 December 2010, the BMW Group had a workforce of approximately 95,500 employees.

The success of the BMW Group has always been built on long-term thinking and responsible action. The company has therefore established ecological and social sustainability throughout the value chain, comprehensive product responsibility and a clear commitment to conserving resources as an integral part of its strategy. As a result of its efforts, the BMW Group has been ranked industry leader in the Dow Jones Sustainability Indexes for the last seven years.

www.bmwgroup.com

Facebook: http://www.facebook.com/BMWUK

Twitter: http://twitter.com/BMWGroup

YouTube: http://www.youtube.com/BMWUK

For further information please contact:

Krystyna Kozlowska	BMW Media Relations Assistant

Tel: 01344 480707	Email: Krystyna.Kozlowska@bmw.co.uk

Gavin Ward		BMW Media Relations Manager
Tel:  01344 480829	Email: Gavin.Ward@bmw.co.uk

Wieland Bruch		Product Communications Manager

Tel: 01344 480113	Email: Wieland.Bruch@bmw.co.uk

Graham Biggs		Corporate Communications Director

Tel:  01344 480109	Email:  Graham.Biggs@bmw.co.uk

Press office fax:		01344 480306

Media website:  		www.press.bmwgroup.co.uk
Customer website:	www.bmw.co.uk