| For Release: | December 15, 2005 |
| --- | --- |
| Contact: | David J. Buchko Product Communications Manager 201-307-3789 / dave.buchko@bmwna.com William Scully BMW Product Communications Specialist 201-307-3790 / william.scully@bmwna.com |

# 2006 BMW 3 SERIES COUPES & CONVERTIBLES

## Technical Specifications

Bold within table indicates new specification for 2006.

## General	325Ci Coupe	325Ci Convertible	330Ci Coupe	330Ci Convertible

Curb weight, lb.:

Manual transmission	3219	3560	3285	3616

Automatic transmission	3285	3627	3362	3704

Weight distribution, front/rear, %:

Manual transmission	50.4/49.6	48.9/51.1	50.1/49.9	48.7/51.3

Automatic transmission	51.1/48.9	49.2/50.8	50.6/49.4	49.4/50.6

Wheelbase, in.	107.3

Track, front/rear, in. 	57.9/58.4 1

Length, in.	176.7 1

Width, in.	69.2 1

Height, in.	53.9	54.0 	53.9	54.0 3

## Body	325Ci Coupe	325Ci Convertible	330Ci Coupe	330Ci Convertible

Type	2-door coupe	2-door convertible	2-door coupe	2-door convertible

Aerodynamic drag

coefficient	0.32	0.35	0.32	0.35

EPA size classification	Subcompact	Minicompact	Subcompact	Minicompact

## Accommodations

Seating capacity, persons	5	4	5	4

Shoulder room, front/rear,

in.	54.5/52.7	54.5/45.9	54.5/52.7	54.5/45.9

Head room, front/rear, in.	36.3/36.2	38.0/36.4 3	36.3/36.2	38.0/36.4 3

Leg room, front/rear, in.	41.7/33.2	41.7/32.0	41.7/33.2	41.7/32.0

EPA passenger volume, cu ft.	84.4	80.0	84.4	80.0

EPA cargo volume, cu ft.	9.5 	7.7 	9.5 4	7.7 5

## Engine & electrical

Engine type	DOHC inline 24-valve 6-cylinder, Double VANOS steplessly variable valve timing 1

Bore x stroke, mm/in.	84.0 x 75.0/3.31 x 2.95 	84.0 x 89.6/3.31 x 3.53

Displacement, cc/cu in.	2494/152 6		2979/182 7

Compression ratio	10.5:1 6		10.2:1 7

Power @ rpm, hp	184 @ 6000 6		225 @ 5900 7 (ZHP: 235 @ 5900)

Torque @ rpm, lb-ft.	175 @ 3500 6		214 @ 3500 7 (ZHP: 222 @ 3500)

## Engine & electrical	325Ci Coupe	325Ci Convertible	330Ci Coupe	330Ci Convertible

(cont.)

Engine-management	Siemens MS 43 with knock control (2 sensors); variable valve timing, electronic

system	throttle system, 2-stage intake system, engine cooling & other functions included

in control strategy 1

Fuel requirement	Premium unleaded 1

Fuel capacity, U.S. gal.	16.6 1

Battery capacity, amp-hr.	80 1

Alternator output rating,

amp./W	120/1680 1

## Drivetrain	325Ci Coupe	325Ci Convertible	330Ci Coupe	330Ci Convertible

Drive system	Front engine/rear-wheel drive 1

Manual transmission	Getrag Type B, 5-speed 6	ZF Type H, 6-speed 7

Ratios: 1st	4.23:1 6		4.35:1 7

2nd	2.52:1 6		2.50:1 7

3rd	1.66:1 6		1.66:1 7

4th	1.22:1 6		1.24:1 7

5th	1.00: 1 6		1.00:1 7

6th	–		0.85:1 7

Reverse	4.04: 1 6		3.93:1 7

Final drive ratio	3.15: 1	3.46:1	2.93:1 (ZHP: 3.07:1) 	3.07:1

## Drivetrain (cont.)	325Ci Coupe	325Ci Convertible	330Ci Coupe	330Ci Convertible

Automatic transmission	ZH 5 HP 19, 5-speed STEPTRONIC with Adaptive Transmission Control &

selectable Sport mode 1

Ratios:	1st	3.67:1 1

2nd	2.00:1 1

3rd	1.41:1 1

4th	1.00:1 1

5th	0.74:1 1

Final drive ratio	3.46:1 6		3.38:1 7

## Chassis

Body/frame construction	Unitized steel 1

Front suspension	Struts, arc-shaped forged-aluminum lower arms with hydraulic cushions, coil springs,

twin-tube gas-pressure shock absorbers, anti-roll bar 1

Coupe std., Convertible ZSP: sport calibration; 330Ci ZHP: M sport calibration

Rear suspension	Multi-link system with Central Links, upper & lower lateral links (upper link of cast

aluminum), coil springs, twin-tube gas-pressure shock absorbers, anti-roll bar 1

Coupe std., Convertible ZSP: sport calibration; 330Ci ZHP: M sport calibration

Steering type	Rack & pinion, engine-speed-sensitive power assist 1

Overall ratio	13.7:1 1

Turns lock-to-lock	3.0 1

Turning circle, ft.	34.4 1

4-wheel ventilated disc brakes:

Diameter, front, mm/in.	300/11.8 6		325/12.8 7

Diameter, rear, mm/in.	294/11.6 6		320/12.6 7

ZHP – Performance Package     ZSP – Sport Package

## Chassis (cont.)	325Ci Coupe	325Ci Convertible	330Ci Coupe	330Ci Convertible

Wheels (standard)	Cast alloy, 16 x 7.0	Cast alloy, 17 x 7.0

Wheels (optional)	Cast alloy, 17 x 8.0 (ZSP)	Cast alloy, 17 x 7.5 front/17 x 8.5 rear (ZSP)

Cast alloy, 18 x 8.0 front/18 x 8.5 rear (ZHP)

Tires (standard)	All-season, 205/55R-16 H-rated	All-season, 205/50R-17 V-rated

Tires (optional)	Performance, 225/45R-17 W-rated  	Performance, 225/45ZR-17 front /245/40ZR-17 rear (ZSP) 8

Performance, 225/40ZR-18 front /

255/35ZR-18 rear (opt. or ZHP) 8

All-season run-flat, 205/50R-17 V-rated

Stability-enhancement	Dynamic Stability Control (DSC), including all-speed traction control, Dynamic Traction system

Control, electronic brake proportioning, antilock braking (ABS), Dynamic Brake Control

& cornering/braking stability enhancement

## Performance data

Acceleration, 0-60 mph, sec. :

Manual transmission	7.1	7.7	6.4 (ZHP: 5.9)	6.9

Automatic transmission	8.1	8.9	7.0	7.5

Top speed, mph	129 1  		(ZHP: 155 7  10)

Fuel economy, EPA est.

MPG, city/highway:

Manual transmission	20/29	19/27	20/30	19/28

Automatic transmission	19/27	18/26	19/27	18/25

ZHP – Performance Package     ZSP – Sport Package

# Footnotes

– Specification applies to all models.

– With standard wheels.

– With softtop raised.

– Can be expanded via standard folding rear seats.

– With softtop lowered. Volume with softtop raised & variable softtop-compartment floor adjusted is approximately 15% greater.

– Specification applies to 325Ci models.

– Specification apples to 330Ci models.

– Due to low-profile tires, please note: Wheels, tires and suspension parts are more susceptible to road hazard and consequential damages. Performance tires are not recommended for driving in snow and ice conditions.

– BMW AG test results. Actual acceleration results may vary depending on specification of vehicle; road and environmental conditions; testing procedures and driving style. These results should be used for comparison only, and verification should not be attempted on public roads. BMW urges you to obey all posted speed limits and to please wear your safety belt at all times.

– Electronically limited.

# Text boxes

Company

BMW of North America, LLC

BMW Group Company

Mailing address

PO Box 1227

Westwood, NJ

07675-1227

Office address

300 Chestnut Ridge Road

Woodcliff Lake, NJ

07677-7731

Telephone

(201) 307-3606

Fax

- 307-3607

Internet

bmwusa.com