| For Release: | March 5, 2007 |
| --- | --- |
| Contact: | Thomas J. Plucinsky Product and Technology Communications Manager 201-307-3783 / thomas.plucinsky@bmwna.com William Scully BMW Product Communications Specialist 201-307-3790 / william.scully@bmwna.com |

2007 BMW 6 SERIES

Technical Specifications

Bold within table indicates new specification for 2007.

General	650i	650i
		Coupe	Convertible

Curb weight, lb.:

Manual transmission	3814	4277

Sequential Manual Gearbox

(SMG)	3814	4277

Automatic transmission	3814	4277

Weight distribution, front/rear, %:

Manual transmission	52.6/47.4	49.0/51.0

Sequential Manual Gearbox

(SMG)	52.6/47.4	49.0/51.0

Automatic transmission	52.6/47.4	49.0/51.0

Wheelbase, in.	109.4

Track, front/rear, in.	61.3/62.8 1

Length, in.	190.2 1

Width, in.	73.0 1

Height, in.	54.1 1

Body	650i	650i
		Coupe	Convertible

Type	2-door coupe	2-door convertible

Aerodynamic drag coefficient	0.30	0.32

EPA size classification	Subcompact	Subcompact

Accommodations

Seating capacity, persons	4	4

Shoulder room, front/rear, in.	56.4/49.4 1

Head room, front/rear, in.	37.6/35.6	37.8/36.5

Leg room, front/rear, in.	42.0/30.1	42.0/29.0

EPA interior volume, cu ft.	81.0	82.0

EPA cargo volume, cu ft.	13.0	12.4/10.6

Engine & electrical

Engine type	DOHC 32-valve (4-cam) V-8, Valvetronic variable

intake-valve lift & Double VANOS  steplessly

variable intake- & exhaust-valve timing 1

Bore x stroke, mm/in.	92.0 x 88.3/3.62 x 3.48 1

Displacement, cc/cu in.	4799/293 1

Compression ratio	10.5:1 1

Power @ rpm, hp	360 @ 6300 1

Torque @ rpm, lb-ft.	360 @ 3400 1

Engine-management system	Motronic ME9 with knock control; variable

valve lift & timing, electronic throttle system,

engine cooling & other functions included in

control strategy 1

Fuel requirement	Premium unleaded 1

Fuel capacity, U.S. gal.	18.5 1

Battery capacity, amp-hr.	110 1

Alternator output rating, amp./W	170/2380 1

Drivetrain	650i	650i
		Coupe	Convertible

Drive system	Front engine/rear-wheel drive 1

Manual transmission	ZF Type G, 6-speed 1

Ratios:	1st	4.05:1 1

2nd	2.40:1 1

3rd	1.58:1 1

4th	1.19:1 1

5th	1.00:1 1

6th	0.87:1 1

Reverse	3.68:1 1

Final drive ratio	3.23:1	3.46:1

Sequential Manual Gearbox	Electrohydraulic/electronic controls applied to

6-speed manual transmission (above);

transmission & final drive ratios same as for

manual transmission 1

Automatic transmission	ZF 6 HP 26, 6-speed STEPTRONIC with Adaptive

Transmission Control, selectable Sport & Manual

modes 1

Ratios:	1st	4.17:1 1

2nd	2.34:1 1

3rd	1.52:1 1

4th	1.14:1 1

5th	0.87:1 1

6th	0.69:1 1

Reverse	3.40:1 1

Final drive ratio	3.46:1 1

Chassis	650i	650i
		Coupe	Convertible

Body/frame construction	Unitized; aluminum front-end structure, aluminum

hood & doors, thermoplastic front fenders,

Sheet Molding Compound (SMC) trunklid 1

Front suspension	Struts, double-pivot lower arms, coil springs,

twin-tube gas-pressure shock absorbers, Active

Roll Stabilization; aluminum suspension system,

thrust plate & subframe 1 (Convertible: additional

diagonal braces)

Rear suspension	4-link Integral Link system, coil springs, twin-

tube gas-pressure shock absorbers, Active Roll

Stabilization; aluminum suspension system & sub-

frame 1 (Convertible: additional diagonal braces)

Steering type	Rack & pinion, Servotronic vehicle-speed-sensitive

variable power assist 1

Overall ratio	Mechanically variable; mean ratio is 14.4:1 1

Overall ratio, Active Steering	Electrically/electronically variable over wide range

(optional)	of 10:1 – 18:1 1

Turning circle, ft.	37.4 1

Brakes	4-wheel ventilated discs with lightweight aluminum/

cast-iron rotors, aluminum front/cast-iron rear

calipers 1

Diameter, front, mm/in.	348/13.7 1

Diameter, rear, mm/in.	345/13.6 1

Wheels (standard)	Cast alloy, 18 x 8.0 front/rear 1

Wheels (optional)	Cast alloy, 19 x 8.5 front/19 x 9.0 rear	(Sport Package) 1

Tires (standard)	245/45R-18 front/rear run-flat all-season 1,

Tires (optional)	245/40R-19 front / 275/35R-19 rear

run-flat performance (Sport Package) 1, 6

Stability-enhancement system	Dynamic Stability Control (DSC); includes Dynamic

Traction Control, electronic brake proportioning,

antilock braking (ABS), Dynamic Brake Control,

Brake Fade Compensation, Brake Standby,

Brake Drying, Comfort Stop, Start-off Assistant

& cornering/braking stability enhancement 1

Performance data	650i	650i
		Coupe	Convertible

Acceleration, 0-60 mph, sec. :

Manual transmission	5.3	5.6

Sequential Manual Gearbox

(SMG)	5.3	5.6

Automatic transmission	5.4	5.7

EPA estimated MPG, city/highway:

Manual transmission	17/24	16/22

Sequential Manual Gearbox

(SMG)	16/22	15/21

Automatic transmission	17/25	17/25

# Footnotes

– Specification applies to both models.

– With standard wheels.

– With softtop raised.

– Softtop raised/lowered, variable softtop storage compartment adjusted accordingly.

– VANOS = VAriable NOckenwellen Steuerung = variable camshaft control, or variable valve timing.

– Due to low-profile tires, please note: wheels, tires and suspension parts are more susceptible to road hazard and consequential damages. 6 Series models are not equipped with a spare tire and wheel. Performance tires are not recommended for driving in snow and ice conditions.

– BMW AG test results. Actual acceleration results may vary depending on specification of vehicle; road and environmental conditions; testing procedures and driving style. These results should be used for comparison only, and verification should not be attempted on public roads. BMW urges you to obey all posted speed limits and to please wear your safety belt at all times.

# Text boxes

Company

BMW of North America, LLC

BMW Group Company

Mailing address

PO Box 1227

Westwood, NJ

07675-1227

Office address

300 Chestnut Ridge Road

Woodcliff Lake, NJ

07677-7731

Telephone

(201)  307-3606

Fax

- 307-3607

Internet

bmwusa.com