The new BMW G 450 X.
Contents.

1.	Concept, Requirements and Features. 	 2

2.	Model Designation BMW G 450 X. 	 6

3.	Development, Technology and Design. 	 7

4.	Technical Data. 	12

1.	Concept, Requirements 
and Features.

Over the last 80 years BMW Motorrad has made off-road history time 
and time again. The marque is now closely involved in off-road sports as never before and is premièring an uncompromising, pedigree sport enduro 
in the attractive 450-cc displacement class.  The new BMW G 450 X is a motorcycle exclusively developed for enduro sport and the most demanding competitive races in the world. It’s a machine that is ready to compete the moment it arrives from the factory.

The background to the development of such a machine is the knowledge 
that competition-oriented enduro motorcycles represent a parameter with growth potential in the motorcycle market. Markets such as US, Australia, and Spain, already register – nearly traditional – stable sales in the off-road sector and BMW Motorrad wants to help shape and stimulate this and other markets for the long term. Besides, smaller volume off-road motorcycles open the gateway to both popular and professional motor sport as well as offering enough potential to also help the young generation to rediscover the fascination of motorcycles again. With the launch of the G 450 X, BMW is also pointing the way for the upcoming generation and towards sustainably securing the future of the motorcycle in general.

The engine with the latest fuel injection and computer-controlled three-way catalytic converter is Euro III homologated and already meets the vehicle emissions standards which are becoming ever more rigorous today for sports events as well as for road vehicles. With these measures BMW Motorrad is also taking a further step towards public acceptance of enduro sports in the future. The patented, unrivalled technical features of the new BMW G 450 X make it a driving force and contribute to the advancement of technological competition in this segment.

The introduction of the tough enduro BMW G 650 Xchallenge has already pointed the way: with a frame and swing arm layout for improved offroad traction, low weight, compact chassis and dynamic engine. BMW Motorrad goes still further with the BMW G 450 X and is not content with constructional features traditionally seen in the class. High-tech solutions have been realized in both the engine and chassis in keeping with the cross-country sporting tradition of the house and giving the marque a fascinating exclusive off-road profile.

The concept of the BMW G 450 X is based on keeping the mass con-
centrated as near as possible to the center of gravity and realizing a vehicle configuration that adapts perfectly to the requirements of off-road sport. 
The central element of this concept is the amalgamation of the bearing axle 
of the rear-wheel swing arm with the axis of rotation for the driving pinion 
so there is no change in length of the chain on compression and rebound, minimizing the effects of the final drive on the vehicle’s response. Further consequences of this unequalled technical approach are a noticeably longer swing arm for the same wheelbase as the competition and, with it, maximum traction bringing concrete advantages in enduro sport with its extreme demands on rider and machine.

Fundamental to the overall plan is the saving in length through the alliance 
of the swinging bearing and pinion rotation axis. Not only does it enable 
a longer swing arm, but the modern high-performance DOHC single-cylinder engine with an output of 50 bhp could also be positioned further to the rear. The cylinder was more strongly tilted to the front, thus creating space for long, straight intake tracts. In this way an ideal position was reached for the fuel injection nozzle and dual throttle valve fuel injection system. This also contributed to adapting the engine to meet the requirements of the Euro III exhaust gas norm without loss of performance, which is anything but standard in this motorcycle category. Further concept advantages include optimum protection of the airbox and voluminous air flow due to its placement above the engine in front of the seat. One consequence of the resolutely implemented, centralized concentration of masses close to the centre of gravity is the 8.5-liter tank under the seat. The filler manifold is positioned below an opening in the rear part of the seat. The reserve function is signaled by a warning lamp in the cockpit.

The starter is placed in front of the engine; the battery is protected from dirt and easily accessible directly behind the control head in the upper triangular frame. The air filter is a square, flat wet element, fixed by a drawer mechanism that makes it very easy, safe, clean and extremely fast to change. For this, 
the right cosmetic tank cover (fixed with a quick-release fastener) is removed and the air filter drawer is pulled out.

The intake funnel is positioned at the height of the control head whose 
high-lying position is advantageous in water splashes or wherever there is heavy dust development. The seat of the BMW G 450 X is made from a 
piece of special foam plastic. Foregoing a cover and not having a substructure or sump as its base brings weight advantages.

Another distinctive construction feature is the relocation of the clutch directly onto the crankshaft, a position that enabled an ingenious frame construction: The frame tubes were placed straight ahead of the swing arm pivot, bring-
ing maximum stiffness at the same time as minimum weight and lowest use of material. Further plus points of this overall arrangement resulted for the radiator. This now had enough space to be designed in one piece. This saved additional coolant hoses and and with a low weight, important for an off-road motorcycle.

The development of the BMW G 450 X focussed on the ergonomic shape and design of the active riding configuration. Starting from the steering head to the rear section of the seat, the machine has an extremely slender waistline exactly where the rider sits, offering maximum freedom of movement. Especially in a standing position, the rider benefits because the absence of the tank at this point provides unrestrained clearance and the motorcycle can be kept appreciably slimmer.

In this configuration the G 450 X is the first BMW enduro to be uncompro-misingly developed for professional competitive racing. Like no other vehicle, the advantages of the unique construction features are revealed to the full 
in rugged off-road conditions; features such as the effective concentration of the masses around the center of gravity, the engine effects eliminated by 
the unique swing arm mounting, the resulting low wear of chain and pinion, the extreme handling reminiscent of a 250 series motocross motorcycle 
with prodigious tracking stability, the low weight, the powerful engine and the high-technology spring elements that offer the ambitious enduro sports 
rider a number of package and design benefits in hard competition plus limit-less riding pleasure. Measured by the options it incorporates, the G 450 X 
is the most powerful off-road BMW of all times for hard offroad riding.

A dedicated team of specialist engineers and mechanics, who have also 
taken part in intensive off-road sport privately for many years, has developed this new model for BMW Motorrad under the motto “from passionate professionals for passionate professionals”.

The BMW G 450 X continues the off-road expertise in the field of professional enduro sport already consistently realized in the BMW G 650 Xchallenge. 
It weighs about 40 kilograms less than the G 650 Xchallenge for roughly the same output and, from the first draft to the last detail, is perfectly tailored to the requirements of the ambitious and success-oriented enduro sports rider. As a completely special and absolutely exceptional motorcycle, the BMW G 450 X is a genuine sports machine and it goes without saying that it has all parts required for MOT approval as standard. This means that – unlike other vehicles in this class –  it’s no problem to ride the BMW G 450 X to the track on its own two wheels.

The innovative, patented technology of the single-cylinder sports enduro concept was put to the test in all relevant highly-competitive events through-out the 2007 season by experienced and successful racing professionals such as Sascha Eckert, Simo Kirssi and Joël Smets who were able to harmonize and further develop the concept. Today the motorcycle comes ready for offroad racing and competitions at the highest level and with approval for public road traffic without further modification straight from the factory.

Thanks to great traction at low revs, smooth engine output and fast revving, superior riding qualities with extremely light handling, best balance in slow 
“trial” sections and enormous stability at higher speeds, not only professional or well-versed enduro riders, but even enduro sport novices have no problem in mastering this racing motorcycle.

To corroborate the extremely sporty enduro qualities, BMW Motorrad has 
a works racing team that already took part in different Enduro sports events with the G 450 X during the test phase and will continue to race it in the Enduro world championship of the E2 class for example, or the German cross country championship (GCC).

2.	Model Designation 
BMW G 450 X.

The model designation G stands for a new ‘G’eneration of sporty motorcycles in the mid-range and lower cc segment, distinguished by its consistent lightweight, easy handling, tracking stability and safe riding qualities. For drive power, the focus is placed on powerful, cultivated, dependable and economic single-cylinder engines.

G stands symbolically for a well thought out ‘G’eneral concept and perfection down to the last detail, for the performance of the whole vehicle, for the masterful harmony of all individual components in respect to an impressive whole. G also stands for ‘G’reat riding qualities and pure, unadulterated riding pleasure.

The range of possible uses of the G models covers a wide spectrum. 
From the light allrounder ideal for touring to the agile super moto performer and the robust hard enduro up to the genuine sports enduro with competitive qualities. While the models of the 650 series are based on a common technical basis, but are differentiated by the consistent configuration and exclusive product features for their respective purpose, the high performance machine G 450 X is the first representative of a motorcycle generation 
that shows itself to be uncompromisingly competitive and success oriented, representing the sporty spearhead of the G-series as a result. Common 
to all G models is the high-grade substance of the product and proverbial BMW quality, independent of where it is produced.

Specially tailored to customers’ riding styles and the abilities of the G 450 X, exclusive training is in preparation and will progressively supplement the offers for the new motorcycle.

3.	Development, Technology 
and Design.

From a technical point of view, the BMW G 450 X has no forerunners. 
It is a brand-new development where features such as weight saving plus perfect and uncompromising configuration to the requirements of the competition-oriented offroad racing were at the forefront of the specification for the developer.

Test program.

Enduro racing places an enormous stress on the materials. The transition 
to moto cross sport is fluid, the machines tuned to the limits of performance are strained to the limits so their technology must satisfy the highest of 
all demands. Due to the extreme range of use, the trials of the G 450 X were extremely complex and totally new paths had to be taken in some areas. The testing included the toughest enduro performance with meter-high jumps, freezing cold up to extreme heat, water splashes and continuous racing 
in extremely dusty surroundings with sand and stone impacts. The vehicle must be able to withstand all these conditions reliably and sustainably. Hardly any other type of motorcycle is confronted with such requirements in this combination. The testing program primarily included testing in a real competitive environment as well as numerous bench tests and trials on special test tracks were correspondingly extensive and intensive. From the very outset this meant the BMW G 450 X had to prove itself in the environment where it wants to take part later in contests for the title: on the courses of national and international enduro and cross racing where the slightest weakness of rider or machine can lead to defeat or failure. Long-term trials in terrain in both Spain and Italy rounded off the overall program until serial production was reached.

Engine.

The 449 cc single-cylinder DOHC 4-stroke engine of the G 450 X was developed by BMW. The compact cylinder head of the short-stroke four-valve power unit houses the technical elements of the K 1200 S: for example, the intake valves are operated by follower valves; the outlet control is implemented by tappets. A space-saving configuration distinguished by high engine peeds. Optimum performance that meets the requirements of the Euro III exhaust gas norm is realized by fuel injection with oxygen sensor regulation and a dual throttle valve system which ensure that the engine reacts more sensitively to throttle commands. The crankshaft and conrod are fitted with roller bearings and the weight-optimized two ring piston is forged.

A balance shaft effectively reduces the vibrations typical of a single-cylinder engine. The constant mesh five-speed transmission was widely staggered for optimum connections in racing. The primary coupling sits directly on the crankshaft and is configured as a wet clutch with a clutch diaphragm. In contast to conventional concepts, the BMW G 450 X clutch is considerably more compact and has a smaller diameter with the same number of discs. Contrary to the conventional geared-down clutches, this is possibe because the clutch only needs to transmit a correspondingly reduced torque on the transmission input shaft. The clutch is operated by a cable.

The engine is fed with oil by a wet sump lubrication system. Two oil pumps, 
a pressure pump and a suction pump use the same volumes of oil to lubricate the gearbox and the crankshaft. The two integrated oil sieves and oil filter are easy to access from the left side of the engine for replacement. The volume of oil of approximately one liter can be checked via an inspection glass.

An intermediate shaft with integrated ventilation function transfers the power from the crankshaft to the gearbox and means that the crankshaft of the G 450 X engine turns backwards. The cylinder is tilted forward by approxi-mately 30 degrees, enabling the center of gravity to be moved in the direction of the front wheel thereby benefitting the suspension. A further advantage 
of tilting the cylinder is the creation of space for the intake air ducting that can now come vertically from above and virtually straight, promoting optimum performance.

The engine of the BMW G 450 X, with a compression ratio of 12 : 1, is started by an electric starter; an additional kickstarter is unnecessary thanks to a powerful battery and fuel injection with invariably reliable starting action. An automatic decompression function with a centrifugal force valve lifter reduces the power demanded by the starter. Even when the machine has to travel for longer periods at higher revs in difficult and slow off-road sections, the engine is never excessively thermally loaded thanks to its large-volume, single-piece radiator. A fan behind the cooler provides sufficient air flow rate at low flow speeds.

The production exhaust system is made of stainless steel and the catalytic converter is fitted in the silencer (absorption silencer). For exclusive use in competitive racing, optional purely sporting end silencers are offered as special equipment and it is possible to switch to the extreme “race” mapping stored in the engine control unit.

Despite the powerful alternator and electric starter, the high-performance engine of the BMW G 450 X weighs no more than the aggregate of competitor motorcycles (less than 30 kilograms). The exact power and torque data are not yet fixed.

Chassis.

The chassis of the BMW G 450 X is a completely new development that 
uses selected high-quality components and materials. The years of enduro experience of BMW Motorrad flowed into the development of the chassis. The main consideration in the geometry and overall configuration of the chassis was to meet the especially high demands of off-road racing.  The results are excellent properties in terrain with ease of handling, great maneuverability and extreme tracking stability.

Innovative frame concept.

The frame layout is based on the experiences of the development engineers, the know-how from competitive racing and attendant research and develop-ment work. The knowledge gained from earlier rally sport activities was also incorporated. The frame of the BMW G 450 X is an absolutely new develop-ment that differs in principle from all constructions of the competition. In the main part it consists of thin walled, but high-strength stainless steel precision tubes and is welded to the node points with forged parts deployed for the purpose. No additional surface treatment is necessary. The entire main frame weighs merely 8.6 kilograms and is distinguished by excellent stiffness.

The lower bow of the frame tubes runs directly from the swinging axle straight to the steering head. On the other hand, the upper bow creates a direct con-nection between the suspension strut mount and steering head. The wheel forces are braced centrally on the frame over the suspension strut so that the light rear frame that is bolted to the main frame and is formed by aluminum 
square profiles now only needs to bear the weight of the rider. All in all this construction enables the optimum flow of force, requires minimum use of material, thus allowing a hitherto unrivalled ratio of rigidity to weight.

The 18-inch rear wheel is suspended in a robustly dimensioned two-arm swing arm made from aluminum square profiles which supports a directly linked Öhlins central suspension strut with a generous spring travel of 320 mm. This high-technology element is variably adjustable in pressure and outward stroke damping as well as in the spring pre-tension. The suspension of the 21-inch front wheel is undertaken by a 45 mm upside-down fork 
by Marzocchi that absorbs even the roughest bumps with a spring travel of 300 mm and is also fully adjustable.

A powerful brake system with double-piston floating caliper from Brembo ensures the deceleration of the BMW G 450 X. The front single brake 
disc has a diameter of 260 mm, the rear disc measures 220 mm.

In order to live up to the the harshest off-road conditions, the BMW G 450 X has a light, impact resistant and highly stable plastic underride protection fitted as standard and that has already proved itself in racing. The motorcycle also has a double-butted Magura aluminium handlebar that guarantees optimum control on all surfaces.

Patented swing arm mount.

The real finesse in the chassis sector and a unique feature of the 
BMW G 450 X is the coaxial mount of the swing arm and chain pinion. The swing arm pivot has been mounted through the hollow gearbox output so 
that there is no longer any change in length of the chain on compression and rebound over the entire spring travel. The chain tension remains constant independent of the compression position; the pinion, chain and chain ring are subject to less wear than in conventional constructions. A positive effect on the riding characteristics is that the effect of changing loads on the powertrain is now noticeably reduced.

Thanks to the patented coaxial mounting of the swing arm and drive chain pinion plus a wheelbase at competition level, the swing arm is 30 mm longer, markedly improving the traction properties. The rear wheel remains longer 
in contact with the ground in all situations, keeping the driving force better on the surface. Also, compared with the competition, a significantly greater length adjustment range of the rear wheel results which means different pinion and chain ring combinations can be used with the same chain with no problem.

When a pinion has to be replaced, the swing arm must be removed; however, in comparison to conventional concepts, this is not a particularly time consuming task. An experienced mechanic can replace the pinion in about 15 minutes and, because of the much lower wear of the entire final drive, 
the pinion needs to be replaced less often then by the competition.

Design.

The looks of the BMW G 450 X immediately make clear the affinity to 
BMW Motorrad. The dynamic “Flyline” allows the new motorcycle to be identified as a typical member of the BMW enduro world, the most striking element is the typical family beak – also the distinguishing characteristic shared by all GS models.

The optical appearance also expresses pure sporting performance with the associated aggression. This results in the look and feel of a fascinating vehicle that has the right to “ride to win” in competitive races.

The color concept of the G 450 X is oriented to the G 650 Xchallenge. 
The standard color is “racing white” with blue accents typical of BMW which highlights the affiliation to the G model family and the new, sporty enduro 
line from BMW.

4.	Technical Data.

The exact technical data of the BMW G 450 X have not yet been finally fixed. The maximum output is around 37 kW (50 bhp) with a best torque value of approximately 35 lb-ft. The overall weight with full tank is about 120 kg which means the BMW G 450 X is lighter than the current best weight values in this class. This value is all the more impressive because this is a vehicle with fuel injection, catalytic converter, electric starter and Euro III homologation that points the way to the future of the enduro sport.

The exact geometrical data of the chassis is subject to the last fine tuning activities and will be made known at a later date.