| For Release: | September 1, 2007 |
| --- | --- |
| Contact: | Thomas J. Plucinsky Product and Technology Communications Manager 201-307-3783 / thomas.plucinsky@bmwna.com William Scully BMW Product Information Specialist 201-307-3790 / william.scully@bmwna.com |

### 2008 BMW 3 SERIES SEDANS & SPORTS WAGONS

### Product Highlights

General

•	BMW’s best-selling Series

•	The model lineup includes: 328i Sedan, 328xi Sedan, 328i Sports Wagon, 328xi Sports Wagon, 335i Sedan and 335xi Sedan

•	328i and 328xi Sedans and Sports Wagons powered by BMW’s 3.0-liter smooth, high-performing straight-six engine

•	The 335i and 335xi Sedans are powered by BMW's 6-cylinder, twin-turbocharged engine

## Engines

•	6-cylinder engines designated N52 (normally aspirated) and N54 (turbocharged)

•	Magnesium /aluminum composite construction of N52 engine block

•	The significantly increased loads and cylinder pressures produced by the turbocharged N54 engine requires the use of an aluminum engine structure with cast-iron cylinder sleeves

•	Valvetronic variable valve lift; eliminates conventional throttle, improves power, torque and fuel efficiency (328 models)

•	Electric coolant pump, volume-controlled oil pump

328i Sedan, 328xi Sedan, 328i Sports Wagon and 328xi Sports Wagon

•	230 hp @ 6500 rpm, 200 lb-ft. torque @ 2750 rpm

•	Single-stage induction system and Valvetronic

335i Sedan, 335xi Sedan

•	300 hp @ 5800 rpm, 300 lb-ft. torque @ 1400-5000 rpm

•	Twin turbochargers and direct gasoline injection

Transmissions

•	6-speed manual standard, 6-speed automatic optional on all models

Chassis features

•	Double-pivot strut-type front suspension system (328i/335i RWD models: extensive aluminum components)

•	5-link rear suspension system

•	4-wheel ventilated disc brakes

•	Dynamic Stability Control with many braking functions

•	Available Active Steering (RWD models only); varies steering ratio according to vehicle speed and other factors

•	Run-flat tires standard across the board

•	Standard wheels and tires:

•	328i/xi models – 16-in. wheels with all-season tires

•	335i/xi models – 17-in. wheels with all-season tires

•	Tire Pressure Monitor standard on all models

Exterior design & function

•	Xenon Adaptive headlights standard on 335i/xi models, optional on 328i/xi models

•	Ground lighting in door handles

•	Adaptive Brake Lights

•	Chrome tail pipe tips

Ergonomics, luxury & convenience

•	Dynamic Cruise Control standard; can apply brakes lightly if necessary to maintain set speed

•	Available Active Cruise Control; assists driver in maintaining following distance

•	Leather-wrapped tilt/telescopic steering wheel with multi-function controls

•	Manually adjustable front seats standard in 328i/xi Sedan and Sports Wagon models; power seats optional in 328i/xi models, standard in 335i/xi Sedan models.  Include memory for driver’s seat and exterior mirrors, automatic tilt-down of right-hand exterior mirror for reversing

•	Sport seats with power-adjustable backrest width included in optional Sport Package

•	Automatic climate control with separate left/right temperature settings, automatic recirculation control, mist control, temperature- and volume-controlled rear air outlets, microfilter ventilation and other features

•	Climate-controlled console storage compartment

•	2-way (tilt/slide) power moonroof standard on Sedans, dual-panel Panoramic moonroof standard on Sports Wagons

•	Leatherette upholstery standard, leather available in Premium Package or as stand-alone option

•	Burl Walnut interior trim standard; Light Poplar Natural or Aluminum trim available at no extra cost

•	10-speaker audio system standard in 328i/xi Sedan and Sports Wagon models, 
13-speaker Logic7 system optional in 328i/xi, standard in 335i/xi Sedan models.  Either system has two subwoofers and is MP3 CD-capable (including ID3 tag display of artist and song information)

•	SIRIUS Satellite Radio, HD Radio, and iPod/USB Adapter available as factory options

Safety & security

•	Front- and rear-seat Head Protection System

•	Automatic safety-belt tensioners and force limiters standard on front seats and at rear outboard seating positions

•	BMW Assist, BMW’s system of in-car telematics and customer services, available in Premium Package (with 4-year subscription) or as stand-alone option

Factory options, complete listing

Packages

•	Premium Package:

•	Leather upholstery

•	Auto-dimming interior and exterior mirrors

•	Power-fold exterior mirrors

•	Digital compass in interior mirror

•	BMW Universal Transceiver (3-function garage-door opener)

•	4-way power lumbar support on front seats

•	BMW Assist with 4-year subscription

•	Power front seats with Driver Memory System and auto tilt-down of right exterior mirror for backing up (328i/xi Sedan and Sports Wagon models only; standard 335i/xi Sedan models)

•	Sport Package:

328i and 335i/xi Sedans –

•	Sport suspension

•	Specific wheels and tires:

•  328i Sedan and Sports Wagons, 335xi sedan – 17-in., differentiated front/rear sizes, performance tires

•  335i Sedan – 18-in., differentiated front/rear sizes, performance tires

•	Sport steering wheel and front seats

328xi Sedan and Sports Wagon –

•	Specific 17-in. wheels, same size front/rear, all-season tires

•	Sport steering wheel and front seats

•	Cold Weather Package:

All models –

•	Heated front seats

•	Ski bag

•	Sedans – split folding rear seats

328i Sedan and Sports Wagon and 335i Sedan only – headlight cleaning system (standard on 328xi and 335xi models)

Stand-alone options

•	6-speed STEPTRONIC automatic transmission

•	Paddle Shifters now available on all modeals – steering wheel mounted; require automatic transmission and Sport Package

•	Active Cruise Control

•	Active Steering (328i Sedan and Sports Wagon, 335i Sedan only)

•	Sport wheels and tires (upgrade option on AWD models with Sport package)

•	Park Distance Control

•	Xenon Adaptive headlights with auto-leveling (standard 335i/xi, optional 328i/xi models)

•	Comfort Access

•	Leather upholstery

•	Alternate interior trims

•	Power front seats (standard 335i/xi, optional 328i/xi models)

•	Heated front seats

•	Split folding rear seats and ski bag (Sedans only)

•	BMW On-board Navigation System and iDrive control concept with Voice Command, Real Time Traffic Information, and 6 programmable memory keys

•	SIRIUS Satellite Radio

•	HD Radio

•	iPod/USB Adapter

•	Logic7 sound system (standard 335i/xi models, optional 328i/xi models)

•	Power rear-window and manual rear side-window sunshades (Sedans)

•	Manual rear side-window sunshades (Sports Wagons)

•	BMW Assist

•	Metallic Paint

#      #      #