| For Release: | September 1, 2007 |
| --- | --- |
| Contact: | Thomas J. Plucinsky Product and Technology Communications Manager 201-307-3783 / thomas.plucinsky@bmwna.com William Scully BMW Product Information Specialist 201-307-3790 / william.scully@bmwna.com |

2008 BMW 3 SERIES SEDANS & SPORTS WAGONS

Technical Specifications

General	328i	328xi	328i	328xi	335i		335xi

Sedan	Sedan	Sports	Sports	Sedan	Sedan

Wagon	Wagon

Curb weight, lb.:

Manual transmission	3340	3583	3527	3770	3594		3814

Automatic transmission	3406	3627	3594	3814	3605		3825

Weight distribution, front/rear, %:

Manual transmission	50.5/49.5	52.6/47.4	53.8/46.2	50.9/49.1	51.5/48.5	53.8/46.2

Automatic transmission	51.1/48.9	52.9/47.1	53.9/46.1	51.2/48.8	51.7/48.3	53.9/46.1

Wheelbase, in.	108.7

Track, front/rear, in. (with standard wheels)	59.1/59.6 1

Length, in.	178.2 1

Width, in.	71.5 1

Height, in.	55.9 		55.8

Body	328i	328xi	328i	328xi	335i		335xi

Sedan	Sedan	Sports	Sports	Sedan	Sedan					Wagon	Wagon

Type	4-door sedan 2		5-door wagon 3

Aerodynamic drag coefficient	0.30	0.31	0.30	0.31	0.30		0.31

EPA size classification	Compact	Compact	Small	Small	Compact	Compact

Station	Station

Wagon	Wagon

# Accommodations

Seating capacity, persons	5 1

Shoulder room, front/rear, in.	55.4/55.1 1

Head room, front/rear	38.5/37.5 2		38.5/38.0 3

Leg room, front/rear	41.5/34.6 2		41.1/34.6 3

EPA passenger-compartment

volume, cu ft.	93.0 2		92.6 3

EPA cargo volume, cu ft.	12.0 2, 		16.2/24.8/60.9

Engine & electrical	328i	328xi	328i	328xi	335i		335xi

Sedan	Sedan	Sports	Sports	Sedan	Sedan					Wagon	Wagon

Engine type	DOHC, 24-valve inline 6-cylinder,  Double VANOS  steplessly variable intake- 			& exhaust-valve timing 1

Composite magnesium/aluminum engine block

Aluminum engine block

Valvetronic variable intake-valve lift  7

Turbocharged – twin turbo technology 8

Bore x stroke, mm/in.	85.0 x 88.0/				84 x 89.6/

3.35 x 3.46 7				3.31 x 3.53 8

Displacement, cc/cu in.	2996/183 7				2979/182 8

Compression ratio	10.7 7				10.2 8

Power @ rpm, hp	230@6500 7				300@5800 8

Torque @ rpm, lb-ft.	200@2750 7				300@1400-5000 8

Engine-management system	MSV70 (328 models) MSD80 (335i) with knock control (2 sensors); variable valve 		timing, engine cooling & other functions included in control strategy 1

Fuel requirement	Premium unleaded 1

Fuel capacity, U.S. gal. 	16.1 1

Battery capacity, amp-hr.	70 1

Alternator output rating, amp./W	180/2520 1

Drivetrain	328i	328xi	328i	328xi	335i		335xi

Sedan	Sedan	Sports	Sports	Sedan	Sedan						Wagon	Wagon

Drive system, engine/drive wheels	Front/	Front/	Front/	Front/	Front/	Front/

RWD 	AWD	RWD	AWD	RWD		AWD

Manual transmission	Getrag I,	Getrag H,	Getrag I,	Getrag H,	ZF G,		ZF G,

6-speed	6-speed 	6-speed	6-speed	6-speed	6-speed

Ratios:1st	4.32:1	4.35:1	4.32:1	4.35:1	4.06:1	4.06:1

2nd	2.46:1	2.50:1	2.46:1	2.50:1	2.40:1	2.40:1

3rd	1.66:1	1.67:1	1.66:1	1.67:1	1.58:1	1.58:1

4th	1.23:1  	1.23:1 	1.23:1	1.23:1	1.19:1	1.19:1

5th	1.00:1	1.00:1	1.00:1	1.00:1	1.00:1	1.00:1

6th	0.85:1	0.85:1	0.85:1	0.85:1	0.87:1	0.87:1

Reverse	3.94:1	3.93:1	3.94:1	3.93:1	3.68:1	3.68:1

Final drive ratio	3.23:1	3.38:1	3.23:1	3.38:1	3.08:1	3.08:1

Automatic transmission	GM 6 7				ZF 6HP 19TU 8

6-speed				6-speed

Ratios: 1st	4.07:1 7				4.17:1 8

2nd	2.37:1 7				2.34:1 8

3rd	1.55:1 7				1.52:1 8

4th	1.16:1 7				1.14:1 8

5th	0.85:1 7				0.87:1 8

6th	0.67:1 7				0.69:1 8

Reverse	3.20:1 7				3.40:1 8

Final drive ratio	3.73:1	3.91:1	3.73:1	3.91:1	3.46:1 8

RWD – Rear-wheel drive     AWD – All-wheel drive

Chassis	328i	328xi	328i	328xi	335i		335xi

Sedan	Sedan	Sports	Sports	Sedan	Sedan					Wagon	Wagon

Body/frame construction	Unitized steel 1

Front suspension	Struts, double-pivot lower arms, coil springs, twin-tube gas-pressure

shock absorbers, tubular anti-roll bar, subframe 1

dual forged aluminum lower arms 2

Rear suspension	5-link system, coil springs, twin-tube gas-pressure shock absorbers,

tubular anti-roll bar 1

cast aluminum upper transverse arms 2

Rack-&-pinion steering:

Standard system	Engine-speed-sensitive variable-assist power steering 1

Overall ratio	16.0 	18.2

Optional Active Steering	Vehicle-speed-sensitive ratio & power assist 9

Overall ratio	Electrically/electronically variable over wide range of 10.8:1 – 18.0:1

Turning circle, ft.	36.1 9	38.7 10

ZSP – Sport Package

Chassis (cont.)		328i	328xi	328i	328xi	335i	335xi

Sedan	Sedan	Sports	Sports	Sedan	Sedan						Wagon	Wagon

4-wheel ventilated disc brakes,

vacuum-assisted:

Front, diameter x thickness, mm/in.	300 x 24/				348 x 24/

11.8 x 0.94 7				13.7 x 0.94 8

Caliper material	Aluminum 9	Steel 10

Rear, diameter x thickness, mm/in.	300 x 20/				336 x 22/

11.8 x 0.79 7				13.2 x 0.87 8

Caliper material	Aluminum 9	Steel 10

Light-alloy wheels: standard	16 x 7.0 7				17 x 8.0 8

optional – Sport Package	17 x 8.0 F/	17 x 8.0	17 x 8.0 F/	17 x 8.0	18 x 8.0 F/	17 x 8.0

17 x 8.5 R		17 x 8.5 R		18 x 8.5 R

optional – Sport Package required	NA	17 x 8.0 F/	NA	17 x 8.0 F/	NA		18 x 8.0 F/

17 x 8.5 R		17 x 8.5 R			18 x 8.5 R

Run-flat tires:	standard	205/55R16 7	all-season 1			225/45R17 8

optional –  Sport Package	225/45R17 F	225/45R17	225/45R17 F	225/45R17	225/40R18 F	225/40R18 F			255/40R17 R		255/40R17 R		255/35R18 R	255/35R18 R

optional – Sport Package required	NA	225/45R17 F	NA	225/45R17 F	NA	225/40R18 F				255/40R17 R		255/40R17 R		225/35R18 R

F – Front     R – Rear

Chassis (cont.)	328i	328xi	328i	328xi	335i		335xi

Sedan	Sedan	Sports	Sports	Sedan	Sedan					Wagon	Wagon

Stability-enhancement system	Dynamic Stability Control, including electronic brake proportioning,

antilock braking (ABS), cornering/braking stability enhancement,

Dynamic Brake Control, Brake Fade Compensation, Brake Standby,

Brake Drying & Start-up Assistant, plus –

Dynamic Traction Control 9

Hill Descent Control 10

# Performance data

Acceleration, 0-60 mph, sec.

Manual transmission	6.3	6.9	6.5	7.1	5.4		5.3

Automatic transmission	6.9	7.1	7.1	7.3	5.6		5.4

Top speed,  mph:

Standard	130 1

Sport Package	150	130	150	130	150		150

Sport Package + optional tires	NA	150	NA	150	NA		150

EPA estimated MPG, city/highway:

Manual transmission	18/28	17/25	17/27	17/25	17/26	16/25

Automatic transmission	19/28	17/25	18/27	17/25	17/26	17/25

#      #      #

# Footnotes

– Specification applies to all models.

– Specification applies to all sedans

– Specification applies to both sports wagons

– Does not include compartment under trunk floor, which encloses about 1.8 cu ft.; can be expanded via available folding rear seats.

– Rear seats upright, loaded to top of seats/rear seats upright, loaded to ceiling/ rear seats folded, loaded to ceiling.

– VANOS = VAriable NOckenwellen Steuerung = variable camshaft control, or variable valve timing.

– Specification applies to all 328 models

– Specification applies to both 335 models

– Specification applies to all RWD models

– Specification applies to all AWD models

− BMW AG test results.  Actual acceleration results may vary depending on specification of vehicle; road and environmental conditions; testing procedures and driving style. These results should be used for comparison only, and verification should not be attempted on public roads. BMW urges you to obey all posted speed limits and to please wear your safety belt at all times.

– Electronically limited