| For Release: | October 1, 2007 |
| --- | --- |
| Contact: | Thomas J. Plucinsky Product and Technology Communications Manager 201-307-3783 / thomas.plucinsky@bmwna.com William Scully BMW Product Communications Specialist 201-307-3790 / william.scully@bmwna.com |

2008 BMW Z4 ROADSTERS AND COUPE

Technical Specifications

## General	Z4	Z4	Z4

Roadster	Roadster	Coupe

3.0i	3.0si	3.0si

Curb weight, lb.:

Manual transmission	3020	3086		3108

Automatic transmission	3086	3131		3156

Weight distribution, front/rear, %:

Manual transmission	49.9/50.1	49.9/50.1	49.7/50.3

Automatic transmission	50.6/49.4 	50.6/49.4	50.3/49.7

Wheelbase, in.	98.2

Track, front/rear, in.	58.0/60.0 1

Length, in.	161.1 1

Width, in.	70.1 1

Height, in. (with softtop up)	51.1	51.1		49.9

## Body

Type	2-seat Roadster 	2-seat Coupe

Aerodynamic drag coefficient	0.36 2 (with softtop up) 	0.34

EPA size classification	2-Seater 1

## Accommodations	Z4	Z4	Z4

Roadster	Roadster	Coupe

3.0i	3.0si	3.0si

Seating capacity, persons	2 1

Shoulder room, in.	52.5 1

Head room, in.	37.3 2  (with softtop up)	37.3

Leg room, in.	42.0 1

EPA interior volume, cu ft.	47.6 2 (with softtop up)	47.6

Cargo volume, cu ft.	8.5/9.2 2, 		10.1/12.0

## Engine & electrical

Engine type	DOHC inline 24-valve 6-cylinder,

magnesium/aluminum composite 	construction,

Valvetronic variable intake-valve lift & Double

VANOS  steplessly  variable intake- &

exhaust-valve timing 1

Bore x stroke, mm/in.	85.0 x 88.0/3.35 x 3.46 1

Displacement, cc/cu in.	2996/183 1

Compression ratio	10.7:1 1

Power @ rpm, hp	215 @ 6250	255 @ 6600

Torque @ rpm, lb-ft.	185 @ 2750	220 @ 2750 6

Engine-management system 	MSV70 with knock control (2 sensors);

Valvetronic, variable valve timing, electronic

throttle system, engine cooling & other functions

included in control strategy 1

Induction system	Single-stage	3-stage 6

Fuel requirement	Premium unleaded 1

Fuel capacity, U.S. gal.	14.5 1

Battery capacity, amp-hr.	55 1

Alternator output, amp./W	120/1680 2			155/2170

## Drivetrain	Z4		Z4		Z4

Roadster	Roadster	Coupe

3.0i	3.0si	3.0si

Drive system	Front engine/rear drive 1

Manual transmission	Getrag I,	ZF Type H,	Getrag H,

6-speed	6-speed		6-speed

Ratios:	1st	4.32:1	4.35:1 6

2nd	2.46:1	2.50:1 6

3rd	1.66:1	1.66:1 6

4th	1.23:1	1.23:1 6

5th	1.00:1	1.00:1 6

6th	0.85:1	0.85:1 6

Reverse	3.94:1	3.93:1 6

Final drive ratio	3.38:1	3.23:1		3.46:1

Automatic transmission	ZF 6  HP 19, 6-speed 1

Ratios:	1st	4.17:1 1

2nd	2.34:1 1

3rd	1.52:1 1

4th	1.14:1 1

5th	0.87:1 1

6th	0.69:1 1

Reverse	3.40:1 1

Final drive ratio	3.73:1	3.64:1 6

## Chassis

Body/frame construction	Unitized steel structure with aluminum

hood 1

Front suspension	Struts, arc-shaped forged-aluminum

lower arms with hydraulic cushions,

coil springs, twin-tube gas-pressure

shock absorbers, anti-roll bar; alumi-

num thrust plate and strut-tower braces 1

Rear suspension	Multi-link system with Central Links,

upper & lower lateral links (upper link of

cast aluminum), coil  springs, twin-tube

gas-pressure shock absorbers, anti-roll bar,

steel thrust plate & V-brace 1

## Chassis (cont.)	Z4		Z4		Z4

Roadster	Roadster	Coupe

3.0i	3.0si	3.0si

Steering type	Rack & pinion, vehicle-speed-sensitive

electric power assist 1

Overall ratio	14.2:1 1

Turns, lock-to-lock	3.0 1

Turning circle, ft.	32.2 1

4-wheel ventilated disc brakes,

vacuum-assisted:

Diameter, front, mm/in.	300/11.8 	325/12.8 	325/12.8

Diameter, rear, mm/in.	294/11.6 1

Wheels (standard)	Cast alloy, 17 x 8.0 1

Wheels (optional), front/rear	Cast alloy 1,

18 x 8.0/	18 x 8.0/ 		18 x 8.0/

18 x 8.5	18 x 8.5		18 x 8.5

(ZSP)	(ZSP)		(ZSP)

Run-flat performance tires (standard)	225/45R-17 1,

Run-flat performance tires (optional),

front/rear	225/40R-18/

255/35R-18

(ZSP) 1

Stability-enhancement system	Dynamic Stability Control (DSC), 	including all-

speed traction control, Dynamic Traction

Control, electronic brake proportioning, antilock

braking (ABS), cornering/braking stability

enhancement, Dynamic Brake Control, Brake

Fade Compensation, Brake Standby, Brake

Drying & Start-off Assistant 1

ZSP – Sport Package

## Performance data	Z4		Z4		Z4

Roadster	Roadster	Coupe

3.0i	3.0si	3.0si

Acceleration, 0-60 mph, sec. :

Manual transmission	6.2		5.6 6

Automatic transmission	6.6		5.7 6

Top speed, mph

Manual transmission	149	155 6

Automatic transmission	149	155 6

Fuel economy, EPA est. MPG,

city/highway :

Manual transmission	18/28 1

Automatic transmission	19/28 1

#      #      #

# Footnotes

– Specification applies to all three models

– Specification applies to both Roadster models

– Softtop lowered/raised; German DIN measurement.

– Beneath cargo cover/cover retracted; German DIN measurement

– VANOS = VAriable NOckenwellen Steuerung = variable camshaft control, or variable valve timing.

– Applies to Z4 Roadster 3.0si and Coupe 3.0si

– Due to low-profile tires, please note: Wheels, tires and suspension parts are more susceptible to road hazard and consequential damages. Z4 models are not equipped with a spare tire and wheel. Performance tires are not recommended for driving in snow and ice conditions.

– BMW AG test results. Actual acceleration results may vary depending on specification of vehicle; road and environmental conditions; testing procedures and driving style. These results should be used for comparison only, and verification should not be attempted on public roads. BMW urges you to obey all posted speed limits and to please wear your safety belt at all times.

– Electronically limited.

– Preliminary data

# Text boxes

Company

BMW of North America, LLC

BMW Group Company

Mailing address

PO Box 1227

Westwood, NJ

07675-1227

Office address

300 Chestnut Ridge Road

Woodcliff Lake, NJ

07677-7731

Telephone

(201)  307-3606

Fax

- 307-3607

Internet

bmwusa.com